Proposal for draft Corrigendum 1 to Supplement 3 to the 04 series of amendments of Regulation No. 48

(Installation of lighting and light-signalling devices)

A. 	PROPOSAL

The modifications to the text of Regulation No. 48, including draft Supplement 4 to the 04 series of amendments to Regulation No. 48 (ECE/TRANS/WP.29/2009/91) are marked in bold or strikethrough characters.

Paragraph 3.2.7., insert a reference to footnote 5/ and footnote 5/ to read:

"3.2.7.	a description of ….control gear, or variable intensity control. 5/

____________

5/ This provision only applies to vehicles of the categories M and N.

As from 36 months from the entry into force of Supplement 3 to the 04 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets the requirements of this provision as amended by Supplement 3 to the 04 series of amendments.

Contracting Parties applying this Regulation shall not refuse to grant extensions of approvals to all previous versions of this Regulation which remain valid."

Paragraph 4.4.1., the reference to footnote 5/ and footnote 5/, renumber as footnote 6/

Paragraph 5.2.1., the reference to footnote 6/ and footnote 6/, renumber as footnote 7/

Paragraph 5.15., the reference to footnotes 7/ 8/ and 9/ and footnotes 7/ 8/ and 9/, renumber as footnotes 8/ 9/ and 10/

Paragraph 5.27., insert a reference to footnote 11/ and footnote 11/ to read:

"5.27.	The applicant shall …as specified by the applicant, with the following provisions: 11/

____________

11/ This provision only applies to vehicles of the categories M and N.  As from 36 months from the entry into force of Supplement 3 to the 04 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets the requirements of this provision as amended by Supplement 3 to the 04 series of amendments.  Contracting Parties applying this Regulation shall not refuse to grant extensions of approvals to all previous versions of this Regulation which remain valid."

Paragraph 6.2.4.2., the reference to footnote 10/ and footnote 10/, renumber as footnote 12/

Paragraph 6.2.9., the reference to footnote 11/ and footnote 11/, renumber as footnote 13/

Paragraph 6.3.4.2., the reference to footnote 12/ and footnote 12/, renumber as footnote 14/

Paragraphs 6.3.5., 6.3.6.1.1. and 6.5.8., the reference to footnote 13/ and footnote 13/, renumber as footnote 15/

Paragraph 6.19., the reference to footnote 14/ and footnote 14/, renumber as footnote 16/

Paragraph 6.19.7.1., the reference to footnote 15/ and footnote 15/, renumber as footnote 17/

Paragraphs 6.21.4.1.3. and 6.21.4.2.3., the reference to footnote 16/ and footnote 16/, renumber as footnote 18/

Paragraph 6.22.4.1.2., the reference to footnote 16/ and footnote 16/, renumber as footnote 17/

Paragraph 6.22.7.4.3., the reference to footnote 18/ and footnote 18/, renumber as footnote 20/

Paragraph 6.22.7.4.5., the reference to footnote 19/ and footnote 19/, renumber as footnote 21/

Paragraph 6.22.9.1., the reference to footnote 20/ and footnote 20/, renumber as footnote 22/

Paragraphs 12.19. and 12.20., shall be deleted

Annex 1, paragraph 10.6., insert a reference to footnote 3/ and footnote 3/ to read:

"10.6.	Comments regarding the electrical supply conditions (according to paragraphs 3.2.7 and 5.27 of the regulations)." 3/

____________

3/ This provision only applies to vehicles of the categories M and N.

As from 36 months from the entry into force of Supplement 3 to the 04 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type to be approved meets the requirements of this provision as amended by Supplement 3 to the 04 series of amendments.

Contracting Parties applying this Regulation shall not refuse to grant extensions of approvals to all previous versions of this Regulation which remain valid."

B. 	JUSTIFICATION

The OVIG document GRE-60-04 refers to vehicles of the categories M and N only. This has not been taken into account in the document ECE/TRANS/WP29/2009/22 which was submitted to 147th session of WP.29.

Also transitional provisions refer only to the OVIG part of the document and not to the all Supplement 3 to the 04 series.  The aim of this corrigendum is to clarify the situation.