Corrigenda

Working document ECE/TRANS/WP.29/GRPE/2009/16

Proposal for draft global technical regulation concerning the test procedure for compression-ignition (C.I.) engines to be installed in agricultural and forestry tractors and in non-road mobile machinery with regard to the emissions of pollutants by the engine

Submitted by the expert from the European Commission

Working document ECE/TRANS/WP.29/GRPE/2009/16 as deposited at GRPE secretariat on the 20 March 2009 and released 1 April 2009 with changes by the GRPE secretariat.

http://www.unece.org/trans/main/wp29/wp29wgs/wp29grpe/grpedoc_2009.html

Part A and part B up to Annex 6  – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Short Title | EXHAUST EMISSIONS TEST PROTOCOL OF NON-ROAD MOBILE MACHINERY | EMISSIONS TEST PROTOCOL OF NON-ROAD MOBILE MACHINERY ENGINES |
| 2 | A.STATEMENT OF TECHNICAL RATIONALE AND JUSTIFICATION; 1.TECHNICAL AND ECONOMIC FEASIBILITY; Paragraph 7 | Deposited text: The guidance document has no legal status, it does not introduce any additional requirements… in GRPE/2009/16: The guidance document has no legal status as it does not introduce any additional requirements… | The guidance document has no legal status and it does not introduce any additional requirements … [in order to maintain agreed content] |
| 3 | A. STATEMENT OF TECHNICAL RATIONALE AND JUSTIFICATION; 3. Potential Cost Effectiveness; Paragraph 11 | belive [incorrect spelling] | believe |
| 4 | page 1, footnote | wrong format 1 | 1/ |
| 5 | 7.8.3.4. | Points with negative torque values have to be accounted for as zero work. [sentence mistakenly deleted] | [reintroduce] Points with negative torque values have to be accounted for as zero work. |
| 6 | Table 7.3, second column | Conditions (n = engine speed, T = torque) nref = 0 per cent and Tref = 0 per cent and Tact > (Tref - 0.02 Tmaxmappedtorque) and Tact < (Tref + 0.02 Tmaxmappedtorque) nact ≤ 1.02 nref and Tact > Tref and nact > nref and Tact ≤ Tref' and nact > 1.02 nref and Tref < Tact ≤ (Tref + 0.02 Tmaxmappedtorque) nact < nref and Tact ≥ Tref and nact ≥ 0.98 nref and Tact < Tref and nact < 0.98 nref and Tref > Tact ≥ (Tref – 0.02 Tmaxmappedtorque) [ 4 and have to be replaced by or] | Conditions (n = engine speed, T = torque) nref = 0 per cent and Tref = 0 per cent and Tact > (Tref - 0.02 Tmaxmappedtorque) and Tact < (Tref + 0.02 Tmaxmappedtorque) nact ≤ 1.02 nref and Tact > Tref or nact > nref and Tact ≤ Tref' or nact > 1.02 nref and Tref < Tact ≤ (Tref + 0.02 Tmaxmappedtorque) nact < nref and Tact ≥ Tref or nact ≥ 0.98 nref and Tact < Tref or nact < 0.98 nref and Tref > Tact ≥ (Tref – 0.02 Tmaxmappedtorque) |
| 7 | 8.1.10.2.4 | wrong subdivision in i, ii, iii; editor introduced subdivision where none should be | delete sub division |
| 8 | 9.2.2 | shall be maintained within one of the following ranges(option): (i) between 293 and 303 K (20 and 30 °C) or (ii) between 293 and 325 K (20 to 52°C) The range shall be selected by the Contracting Party. [the half sentence 'in close proximity to the entrance into the dilution tunnel' was lost copying the text from 9.2.3.2 during its introduction by the Editorial Committee] | shall be maintained within one of the following ranges (option): (a) between 293 and 303 K (20 and 30 °C) or (b) between 293 and 325 K (20 to 52°C) in close proximity to the entrance into the dilution tunnel. The range shall be selected by the Contracting Party. use missing half sentence from this paragraph 9.2.3.2 |
| 9 | A.2.4. (b) | …that the σi are the errors | …that the εi are the errors |

Annex A.7 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Title Annex 7 | Emission molar based calculation | Molar based emission calculation |
| 2 | Para A.7.0.1. footnote (2) 2nd line | xdil | xdil/exh |
| 3 | A.7.0.1. footnote (2) 3rd line | xdil | xdil/exh |
| 4 | Eq. (A.7-3) |  |  |
| 5 | A.7.1.2.2.; A.7.1.2.3. | vapor [incorrect spelling] | vapour |
| 6 | Eq. (A.7-28) |  |  |
| 7 | Legend Eq. (A.7-28) |  |  |
| 8 | Legend of Eq. (A.7-28) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 9 | Eq. (A.7-29) |  |  |
| 10 | Legend Eq. (A.7-29) |  |  |
| 11 | Legend Eq. (A.7-29) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 12 | Eq. (A.7-30) |  |  |
| 13 | Legend Eq. (A.7-30) |  |  |
| 14 | Legend Eq. (A.7-30) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 15 | Eq. (A.7-31) |  |  |
| 16 | Legend Eq. (A.7-31) | = mean exhaust gas molar flow rate on a wet basis | = exhaust gas molar flow rate on a wet basis |
| 17 | Legend Eq. (A.7-31) | = mean gaseous emission molar fraction | = mean gaseous emission molar fraction on a wet basis |
| 18 | Legend Eq. (A.7-31) | tcycle = test time interval | Δt = time duration of test interval |
| 19 | Eq. (A.7-32) |  |  |
| 20 | Legend Eq. (A.7-32) |  |  |
| 21 | Legend Eq. (A.7-32) | = mean gaseous emission molar fraction | = mean gaseous emission molar fraction on a wet basis |
| 22 | Para A.7.3.2. 3rd line | xgaswet | xgas |
| 23 | Eq. (A.7-33) |  |  |
| 24 | Eq. (A.7-34) |  |  |
| 25 | Legend Eq. (A.7-34) | xH2O,dry | xH2Odry |
| 26 | Eq. (see A.7-29) | See above errata of Eq. (A.7-29) | See above corrige of Eq. (A.7-29) |
| 27 | Eq. (see A.7-31) | See above errata of Eq. (A.7-31) | See above corrige of Eq. (A.7-31) |
| 28 | Eq. (see A.7-32) | See above errata of Eq. (A.7-32) | See above corrige of Eq. (A.7-32) |
| 29 | A.7.4..4.1.(a): | Changing exhaust flow rate shall be extracted. [the first line of the paragraph has been lost while editing] | If a batch sample from a changing exhaust flow rate is collected, a sample proportional to the changing exhaust flow rate shall be extracted. |
| 30 | Eq. (A.7-45) |  |  |
| 31 | Legend Eq. (A.7-45) | = mean exhaust molar flow rate | = exhaust molar flow rate |
| 32 | Legend Eq. (A.7-45) | tcycle = test interval | Δt = time duration of test interval |
| 33 | Legend eq. (A.7-46): DR 2nd line | mdil () | mdil/exh () |
| 34 | Legend Eq. (A.7-46): DR 2nd line | xdil | xdil/exh |
| 35 | Eq. (A.7-47) |  |  |
| 36 | A.7.7.1. and A.7.7.2. | A.7.7.1. and A.7.7.2 [incorrect numbering] | replace numbering by A.7.6.4. and A.7.6.5. |
| 37 | A.7.8.1. to A.7.8.4. | A.7.8.1. to A.7.8.4. [incorrect numbering] | replace numbering by A.7.7.1. and A.7.7.4. |

Annex A.8 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Eq. (A.8-1) |  |  |
| 2 | Eq. (A.8-2) |  |  |
| 3 | Eq. (A.8-22) |  |  |
| 4 | Legend Eq. (A.8-22) | cCO2ad | cCO2d,a |
| 5 | Eq. (A.8-38) |  |  |
| 6 | Legend Eq. (A.8-38) | pP | pp |
| 7 | Eq. (A.8-39) |  |  |
| 8 | Legend Eq. (A.8-39) | pP | pp |
| 9 | Eq. (A.8-40) |  |  |
| 10 | Eq. (A.8-41) |  |  |
| 11 | Eq. (A.8-42) |  |  |
| 12 | Legend Eq. (A.8-51) | med = mass of equivalent diluted exhaust gas over the cycle [kg] | med = mass of diluted exhaust gas over the cycle [kg] |
| 13 | Annex 8 appendix 1, A.8.1., A8.1.1. to A.8.1.3. | A.8.1., A8.1.1. to A.8.1.3. [incorrect numbering] | replace numbering by A.8.5., A.8.5.1 to A.8.5.3 |
| 14 | Annex 8 appendix 2, A8.2 | A8.2 [incorrect numbering] | replace numbering by A.8.6 |