Corrigenda

Working document ECE/TRANS/WP.29/GRPE/2009/16

Proposal for draft global technical regulation concerning the test procedure for compression-ignition (C.I.) engines to be installed in agricultural and forestry tractors and in non-road mobile machinery with regard to the emissions of pollutants by the engine

Submitted by the expert from the European Commission

Working document ECE/TRANS/WP.29/GRPE/2009/16 as deposited at GRPE secretariat on the 20 March 2009 and released 1 April 2009 with changes by the GRPE secretariat.

http://www.unece.org/trans/main/wp29/wp29wgs/wp29grpe/grpedoc_2009.html

Part A and part B up to Annex 6  – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Short Title | EXHAUST EMISSIONS TEST PROTOCOL OF NON-ROAD MOBILE MACHINERY | EMISSIONS TEST PROTOCOL OF NON-ROAD MOBILE MACHINERY ENGINES |
| 2 | A.STATEMENT OF TECHNICAL RATIONALE AND JUSTIFICATION; 1.TECHNICAL AND ECONOMIC FEASIBILITY; Paragraph 7 | Deposited text: The guidance document has no legal status, it does not introduce any additional requirements… in GRPE/2009/16: The guidance document has no legal status as it does not introduce any additional requirements… | The guidance document has no legal status and it does not introduce any additional requirements … [in order to maintain agreed content] |
| 3 | A. STATEMENT OF TECHNICAL RATIONALE AND JUSTIFICATION; 3. Potential Cost Effectiveness; Paragraph 11 | belive [incorrect spelling] | believe |
| 4 | page 1, footnote | wrong format 1 | 1/ |
| 5 | 7.8.3.4. | Points with negative torque values have to be accounted for as zero work. [sentence mistakenly deleted] | [reintroduce] Points with negative torque values have to be accounted for as zero work. |
| 6 | Table 7.3, second column | Conditions (n = engine speed, T = torque) nref = 0 per cent and Tref = 0 per cent and Tact > (Tref - 0.02 Tmaxmappedtorque) and Tact < (Tref + 0.02 Tmaxmappedtorque) nact ≤ 1.02 nref and Tact > Tref and nact > nref and Tact ≤ Tref' and nact > 1.02 nref and Tref < Tact ≤ (Tref + 0.02 Tmaxmappedtorque) nact < nref and Tact ≥ Tref and nact ≥ 0.98 nref and Tact < Tref and nact < 0.98 nref and Tref > Tact ≥ (Tref – 0.02 Tmaxmappedtorque) [ 4 and have to be replaced by or] | Conditions (n = engine speed, T = torque) nref = 0 per cent and Tref = 0 per cent and Tact > (Tref - 0.02 Tmaxmappedtorque) and Tact < (Tref + 0.02 Tmaxmappedtorque) nact ≤ 1.02 nref and Tact > Tref or nact > nref and Tact ≤ Tref' or nact > 1.02 nref and Tref < Tact ≤ (Tref + 0.02 Tmaxmappedtorque) nact < nref and Tact ≥ Tref or nact ≥ 0.98 nref and Tact < Tref or nact < 0.98 nref and Tref > Tact ≥ (Tref – 0.02 Tmaxmappedtorque) |
| 7 | 8.1.10.2.4 | wrong subdivision in i, ii, iii; editor introduced subdivision where none should be | delete sub division |
| 8 | 9.2.2 | shall be maintained within one of the following ranges(option): (i) between 293 and 303 K (20 and 30 °C) or (ii) between 293 and 325 K (20 to 52°C) The range shall be selected by the Contracting Party. [the half sentence 'in close proximity to the entrance into the dilution tunnel' was lost copying the text from 9.2.3.2 during its introduction by the Editorial Committee] | shall be maintained within one of the following ranges (option): (a) between 293 and 303 K (20 and 30 °C) or (b) between 293 and 325 K (20 to 52°C) in close proximity to the entrance into the dilution tunnel. The range shall be selected by the Contracting Party. use missing half sentence from this paragraph 9.2.3.2 |
| 9 | A.2.4. (b) | …that the σi are the errors | …that the εi are the errors |

Annex A.7 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Title Annex 7 | Emission molar based calculation | Molar based emission calculation |
| 2 | Para A.7.0.1. footnote (2) 2nd line | xdil | xdil/exh |
| 3 | A.7.0.1. footnote (2) 3rd line | xdil | xdil/exh |
| 4 | Eq. (A.7-3) |  |  |
| 5 | A.7.1.2.2.; A.7.1.2.3. | vapor [incorrect spelling] | vapour |
| 6 | Eq. (A.7-28) |  |  |
| 7 | Legend Eq. (A.7-28) |  |  |
| 8 | Legend of Eq. (A.7-28) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 9 | Eq. (A.7-29) |  |  |
| 10 | Legend Eq. (A.7-29) |  |  |
| 11 | Legend Eq. (A.7-29) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 12 | Eq. (A.7-30) |  |  |
| 13 | Legend Eq. (A.7-30) |  |  |
| 14 | Legend Eq. (A.7-30) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 15 | Eq. (A.7-31) |  |  |
| 16 | Legend Eq. (A.7-31) | = mean exhaust gas molar flow rate on a wet basis | = exhaust gas molar flow rate on a wet basis |
| 17 | Legend Eq. (A.7-31) | = mean gaseous emission molar fraction | = mean gaseous emission molar fraction on a wet basis |
| 18 | Legend Eq. (A.7-31) | tcycle = test time interval | Δt = time duration of test interval |
| 19 | Eq. (A.7-32) |  |  |
| 20 | Legend Eq. (A.7-32) |  |  |
| 21 | Legend Eq. (A.7-32) | = mean gaseous emission molar fraction | = mean gaseous emission molar fraction on a wet basis |
| 22 | Para A.7.3.2. 3rd line | xgaswet | xgas |
| 23 | Eq. (A.7-33) |  |  |
| 24 | Eq. (A.7-34) |  |  |
| 25 | Legend Eq. (A.7-34) | xH2O,dry | xH2Odry |
| 26 | Eq. (see A.7-29) | See above errata of Eq. (A.7-29) | See above corrige of Eq. (A.7-29) |
| 27 | Eq. (see A.7-31) | See above errata of Eq. (A.7-31) | See above corrige of Eq. (A.7-31) |
| 28 | Eq. (see A.7-32) | See above errata of Eq. (A.7-32) | See above corrige of Eq. (A.7-32) |
| 29 | A.7.4..4.1.(a): | Changing exhaust flow rate shall be extracted. [the first line of the paragraph has been lost while editing] | If a batch sample from a changing exhaust flow rate is collected, a sample proportional to the changing exhaust flow rate shall be extracted. |
| 30 | Eq. (A.7-45) |  |  |
| 31 | Legend Eq. (A.7-45) | = mean exhaust molar flow rate | = exhaust molar flow rate |
| 32 | Legend Eq. (A.7-45) | tcycle = test interval | Δt = time duration of test interval |
| 33 | Legend eq. (A.7-46): DR 2nd line | mdil () | mdil/exh () |
| 34 | Legend Eq. (A.7-46): DR 2nd line | xdil | xdil/exh |
| 35 | Eq. (A.7-47) |  |  |
| 36 | A.7.7.1. and A.7.7.2. | A.7.7.1. and A.7.7.2 [incorrect numbering] | replace numbering by A.7.6.4. and A.7.6.5. |
| 37 | A.7.8.1. to A.7.8.4. | A.7.8.1. to A.7.8.4. [incorrect numbering] | replace numbering by A.7.7.1. and A.7.7.4. |

Annex A.8 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Eq. (A.8-1) |  |  |
| 2 | Eq. (A.8-2) |  |  |
| 3 | Eq. (A.8-22) |  |  |
| 4 | Legend Eq. (A.8-22) | cCO2ad | cCO2d,a |
| 5 | Eq. (A.8-38) |  |  |
| 6 | Legend Eq. (A.8-38) | pP | pp |
| 7 | Eq. (A.8-39) |  |  |
| 8 | Legend Eq. (A.8-39) | pP | pp |
| 9 | Eq. (A.8-40) |  |  |
| 10 | Eq. (A.8-41) |  |  |
| 11 | Eq. (A.8-42) |  |  |
| 12 | Legend Eq. (A.8-51) | med = mass of equivalent diluted exhaust gas over the cycle [kg] | med = mass of diluted exhaust gas over the cycle [kg] |
| 13 | Annex 8 appendix 1, A.8.1., A8.1.1. to A.8.1.3. | A.8.1., A8.1.1. to A.8.1.3. [incorrect numbering] | replace numbering by A.8.5., A.8.5.1 to A.8.5.3 |
| 14 | Annex 8 appendix 2, A8.2 | A8.2 [incorrect numbering] | replace numbering by A.8.6 |
| 15 | Experts agreed during the NRMM WG Meeting (10 June 2009) to update the mass based emission calculation of Annex A.8 with the NRMM relevant changes in the WHDC gtr regarding the measurement/calculation methods of HC emissions (expected to be introduced within July 2009). |