Corrigenda Rev. 2

Working document ECE/TRANS/WP.29/GRPE/2009/16

Proposal for draft global technical regulation concerning the test procedure for compression-ignition (C.I.) engines to be installed in agricultural and forestry tractors and in non-road mobile machinery with regard to the emissions of pollutants by the engine

Submitted by the expert from the European Commission

Working document ECE/TRANS/WP.29/GRPE/2009/16 as deposited at GRPE secretariat on the 20 March 2009 and released 1 April 2009 with changes by the GRPE secretariat.

http://www.unece.org/trans/main/wp29/wp29wgs/wp29grpe/grpedoc_2009.html

Part A and part B up to Annex 6  – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Short Title | EXHAUST EMISSIONS TEST PROTOCOL OF NON-ROAD MOBILE MACHINERY | EMISSIONS TEST PROTOCOL OF NON-ROAD MOBILE MACHINERY ENGINES |
| 2 | A.STATEMENT OF TECHNICAL RATIONALE AND JUSTIFICATION; 1.TECHNICAL AND ECONOMIC FEASIBILITY; Paragraph 7 | Deposited text: The guidance document has no legal status, it does not introduce any additional requirements… in GRPE/2009/16: The guidance document has no legal status as it does not introduce any additional requirements… | The guidance document has no legal status and it does not introduce any additional requirements … [in order to maintain agreed content] |
| 3 | A. STATEMENT OF TECHNICAL RATIONALE AND JUSTIFICATION; 3. Potential Cost Effectiveness; Paragraph 11 | belive [incorrect spelling] | believe |
| 4 | page 1, footnote | [wrong format] 1 | 1/ |
| 5 | 7.8.3.4. | Points with negative torque values have to be accounted for as zero work. [sentence mistakenly deleted] | [reintroduce] Points with negative torque values have to be accounted for as zero work. |
| 6 | Table 7.3, second column | Conditions (n = engine speed, T = torque) nref = 0 per cent and Tref = 0 per cent and Tact > (Tref - 0.02 Tmaxmappedtorque) and Tact < (Tref + 0.02 Tmaxmappedtorque) nact ≤ 1.02 nref and Tact > Tref and nact > nref and Tact ≤ Tref' and nact > 1.02 nref and Tref < Tact ≤ (Tref + 0.02 Tmaxmappedtorque) nact < nref and Tact ≥ Tref and nact ≥ 0.98 nref and Tact < Tref and nact < 0.98 nref and Tref > Tact ≥ (Tref – 0.02 Tmaxmappedtorque) [ 4 and have to be replaced by or] | Conditions (n = engine speed, T = torque) nref = 0 per cent and Tref = 0 per cent and Tact > (Tref - 0.02 Tmaxmappedtorque) and Tact < (Tref + 0.02 Tmaxmappedtorque) nact ≤ 1.02 nref and Tact > Tref or nact > nref and Tact ≤ Tref' or nact > 1.02 nref and Tref < Tact ≤ (Tref + 0.02 Tmaxmappedtorque) nact < nref and Tact ≥ Tref or nact ≥ 0.98 nref and Tact < Tref or nact < 0.98 nref and Tref > Tact ≥ (Tref – 0.02 Tmaxmappedtorque) |
| 7 | 8.1.10.2.4 (m) | [paragraph m, wrong subdivision in i, ii, iii] | delete sub division [deletion of the i, ii, iii, but not the text, which is contracted into 1 paragraph] |
| 8 | 9.2.2 | shall be maintained within one of the following ranges(option): (i) between 293 and 303 K (20 and 30 °C) or (ii) between 293 and 325 K (20 to 52°C) The range shall be selected by the Contracting Party. [the half sentence 'in close proximity to the entrance into the dilution tunnel' was lost copying the text from 9.2.3.2 during its introduction by the Editorial Committee] | shall be maintained within one of the following ranges (option): (a) between 293 and 303 K (20 and 30 °C) or (b) between 293 and 325 K (20 to 52°C) in close proximity to the entrance into the dilution tunnel. The range shall be selected by the Contracting Party. [use missing half sentence from paragraph 9.2.3.2 ] |
| 9 | A.2.4. (b) | …that the σi are the errors | …that the εi are the errors |

Additional editorial corrections for Part A and part B up to Annex 6

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 10 | 3.1.51. | "PTFE means polytetrafluoroethylene, commonly known as Teflon TM; [The right quotation mark is missing. ] | "PTFE" means polytetrafluoroethylene, commonly known as Teflon TM; |
| 11 | 3.2 | RF not in list of sysmbols | Response factor RF added to list of symbols |
| 12 | Eq. (7-3) in section 7.7.2.1. | [Engine power with wrong subscript nnormi] |  |
| 13 | 7.8.2.3. | (a), (b), (c), (c), (d) [non-sequential numbering] | (a), (b), (c), (d), (e) |
| 14 | Table 8.2 | [wrong multiplier] |  |
| 15 | Equation (8-7) in section 8.1.11.5.4. | [Transcription mistake in subscript] |  |

Annex A.7 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Title Annex 7 | Emission molar based calculation | Molar based emission calculation |
| 2 | Para A.7.0.1. footnote (2) 2nd line | xdil | xdil/exh |
| 3 | A.7.0.1. footnote (2) 3rd line | xdil | xdil/exh |
| 4 | Eq. (A.7-3) |  |  |
| 5 | A.7.1.2.2.; A.7.1.2.3. | vapor | vapour [English spelling] |
| 6 | Eq. (A.7-28) |  |  |
| 7 | Legend Eq. (A.7-28) |  |  |
| 8 | Legend of Eq. (A.7-28) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 9 | Eq. (A.7-29) |  |  |
| 10 | Legend Eq. (A.7-29) |  |  |
| 11 | Legend Eq. (A.7-29) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 12 | Eq. (A.7-30) |  |  |
| 13 | Legend Eq. (A.7-30) |  |  |
| 14 | Legend Eq. (A.7-30) | = instantaneous generic gas molar concentration | = instantaneous generic gas molar concentration on a wet basis |
| 15 | Eq. (A.7-31) |  |  |
| 16 | Legend Eq. (A.7-31) | = mean exhaust gas molar flow rate on a wet basis | = exhaust gas molar flow rate on a wet basis |
| 17 | Legend Eq. (A.7-31) | = mean gaseous emission molar fraction | = mean gaseous emission molar fraction on a wet basis |
| 18 | Legend Eq. (A.7-31) | tcycle = test time interval | Δt = time duration of test interval |
| 19 | Eq. (A.7-32) |  |  |
| 20 | Legend Eq. (A.7-32) |  |  |
| 21 | Legend Eq. (A.7-32) | = mean gaseous emission molar fraction | = mean gaseous emission molar fraction on a wet basis |
| 22 | Para A.7.3.2. 3rd line | xgaswet | xgas |
| 23 | Eq. (A.7-33) |  |  |
| 24 | Eq. (A.7-34) |  |  |
| 25 | Legend Eq. (A.7-34) | xH2O,dry | xH2Odry |
| 26 | Eq. (see A.7-29) |  |  |
| 27 | Eq. (see A.7-31) |  |  |
| 28 | Eq. (see A.7-32) |  |  |
| 29 | A.7.4..4.1.(a): | Changing exhaust flow rate shall be extracted. [the first line of the paragraph had been lost while editing] | If a batch sample from a changing exhaust flow rate is collected, a sample proportional to the changing exhaust flow rate shall be extracted. |
| 30 | Eq. (A.7-45) |  |  |
| 31 | Legend Eq. (A.7-45) | = mean exhaust molar flow rate | = exhaust molar flow rate |
| 32 | Legend Eq. (A.7-45) | tcycle = test interval | Δt = time duration of test interval |
| 33 | Legend eq. (A.7-46): DR 2nd line | mdil () | mdil/exh () |
| 34 | Legend Eq. (A.7-46): DR 3rd line | xdil | xdil/exh |
| 35 | Eq. (A.7-47) |  |  |
| 36 | A.7.7.1. and A.7.7.2. | A.7.7.1. and A.7.7.2 [incorrect numbering] | replace numbering by A.7.6.4. and A.7.6.5. |
| 37 | A.7.8.1. to A.7.8.4. | A.7.8.1. to A.7.8.4. [incorrect numbering] | replace numbering by A.7.7.1. and A.7.7.4. |

Additional editorial corrections for Annex A.7 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 38 | A.7.0.3.; A.7.1.1. | sulfur | sulphur [English spelling] |
| 39 | Eq. (A.7-1) | [No double subscript] |  |
| 40 | Eq.(A.7-3) | [No double subscript] |  |
| 41 | A.7.1.2.3. | If humidity is measured as a relative humidity RHa, the amount of water of an ideal gas xH2O [mol/mol] is calculated as follows [mistyped variable name RHa ] | If humidity is measured as a relative humidity RH%, the amount of water of an ideal gas xH2O [mol/mol] is calculated as follows [replaced by RH%] |
| 42 | Eq. (A.7-4) |  | [As the value of RH% is a per cent value between 0 and 100, the value has to be divided by 100] |
| 43 | A.7.1.4.1. (b) | For the NMHC determination described in paragraph (b) of this paragraph, xTHC[THC-FID] shall be corrected [wrong reference to '(b) of this paragraph' ] | For the NMHC determination described in paragraph A.7.1.4.2., xTHC[THC-FID] shall be corrected [reference '(b) of this paragraph' replaced by 'A.7.1.4.2.'] |
| 44 | A.7.1.4.2. | If the NMHC calculations are omitted as described in paragraph A.7.1.4.(c), the background corrected mass of NMHC [wrong reference 'as described in paragraph A.7.1.4.(c)'] | If the NMHC calculations are omitted, the background corrected mass of NMHC [ reference 'as described in paragraph A.7.1.4.(c)' deleted] |
| 45 | Eq. (A7-6) | [Transcription mistake in subscript] |  |
| 46 | A.7.1.4.2. (b) | (i) The following equation for penetration fractions determined using an NMC configuration as outlined in paragraph 8.1.10.3.4. shall be used: (ii) For penetration fractions determined using an NMC configuration as outlined in paragraph 8.1.10.3.5., the following equation shall be used: (iii) For penetration fractions determined using an NMC configuration as outlined in paragraph 8.1.10.3.6., the following equation shall be used: [Wrongly referenced sections] | (i) The following equation for penetration fractions determined using an NMC configuration as outlined in paragraph 8.1.10.3.4.1. shall be used: (ii) For penetration fractions determined using an NMC configuration as outlined in paragraph 8.1.10.3.4.2., the following equation shall be used: (iii) For penetration fractions determined using an NMC configuration as outlined in paragraph 8.1.10.3.4.3., the following equation shall be used: |
| 47 | Eq. (A.7-57) | [Transcription mistake in subscript; reference should be to mixed conditions] | [Reference to mixed conditions] |
| 48 | Legend Eq. (A.7-57) | pact = actual pressure of the flow rate [Pa] Tact = actual temperature of the flow rate [K] = molar mass of the diluted flow rate [g/mol] | pact = actual pressure of the gas [Pa] Tact = actual temperature of the gas [K] = molar mass of the gas [g/mol] [pact, Tact and Mmix are gas properties] |
| 49 | Legend Eq. (A.7-66) | Where dt = diameter of the SSV throat [m] Mmix = mixture molar mass [kg/mol] = reference molar flow rate [mol/s] [Transcription mistake in subscript] | Where dt = diameter of the SSV throat [m] Mmix = mixture molar mass [kg/mol] = reference molar flow rate [mol/s] |

Annex A.8 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Eq. (A.8-1) |  | now covered by #15 below |
| 2 | Eq. (A.8-2) |  | now covered by #15 below |
| ad 1 | Legend Eq. (A.8-2) | CHC(w/Cutter) | now covered by #15 below |
| ad 2 | Legend Eq. (A.8-2) | CHC(w/oCutter) | now covered by #15 below |
| 3 | Eq. (A.8-22) |  |  |
| 4 | Legend Eq. (A.8-22) | cCO2ad | cCO2d,a |
| ad 3 | Eq. (A.8-37) |  | [the index i at m shall be in italic i] |
| 5 | Eq. (A.8-38) |  | [the index to the pressure variable shall be small and roman p] |
| 6 | Legend Eq. (A.8-38) | pP | pp [the index to the pressure variable shall be small and roman p] |
| 7 | Eq. (A.8-39) |  | [the index to the pressure variable shall be small and roman p] |
| 8 | Legend Eq. (A.8-39) | pP | pp [the index to the pressure variable shall be small and roman p] |
| 9 | Eq. (A.8-40) |  |  |
| 10 | Eq. (A.8-41) |  |  |
| 11 | Eq. (A.8-42) |  |  |
| ad 4 | Legend Eq. (A.8-42) |  |  |
| 12 | Legend Eq. (A.8-51) | med = mass of equivalent diluted exhaust gas over the cycle [kg] | med = mass of diluted exhaust gas over the cycle [kg] |
| 13 | Annex 8 appendix 1, A.8.1., A8.1.1. to A.8.1.3. | A.8.1., A8.1.1. to A.8.1.3. [incorrect numbering] | replace numbering by A.8.5., A.8.5.1 to A.8.5.3 |
| 14 | Annex 8 appendix 2, A8.2 | A8.2 [incorrect numbering] | replace numbering by A.8.6 |
| 15 | Experts agreed during the NRMM WG Meeting (10 June 2009) to update the mass based emission calculation of Annex A.8 with the NRMM relevant changes in the WHDC gtr regarding the measurement/calculation methods of HC emissions (expected to be introduced within July 2009). The original text of A.8.1.1.: Determination of methane and non-methane HC concentration The concentration of NMHC (cNMHC [-]) and CH4 (cCH4 [-]) shall be calculated as follows: (A.8-1) (A.8-2) Where: CHC(w/Cutter)= HC concentration with sample gas flowing through the NMC [ppm] CHC(w/oCutter)= HC concentration with sample gas bypassing the NMC [ppm] ECH4 = methane efficiency, as determined in paragraph 8.1.10.3. [-] EC2H6 = ethane efficiency, as determined in paragraph 8.1.10.3. [-] is replaced by the modified text for A.8.1.1.: Determination of methane and non-methane HC concentration The calculation of NMHC and CH4 depends on the calibration method used. The FID for the measurement without NMC, shall be calibrated with propane. For the calibration of the FID in series with NMC, the following methods are permitted. (a) calibration gas – propane; propane bypasses NMC, (b) calibration gas – methane; methane passes through NMC The concentration of NMHC (cNMHC [-]) and CH4 (cCH4 [-]) shall be calculated as follows for (a): (A.8-1a) (A.8-2a) The concentration of NMHC and CH4 shall be calculated as follows for (b): (A.8-1b) (A.8-2b) Where: cHC(w/NMC) = HC concentration with sample gas flowing through the NMC [ppm] cHC(w/oNMC) = HC concentration with sample gas bypassing the NMC [ppm] RFCH4[THC-FID] = methane response factor as determined in paragraph 8.1.10.1.4. [-] ECH4 = methane efficiency, as determined in paragraph 8.1.10.3. [-] EC2H6 = the ethane efficiency, as determined in paragraph 8.1.10.3. [-] If RFCH4[THC-FID] < 1.05, it may be omitted in equations A.8-1a, A.8-1b and A.8-2b. |

Additional editorial corrections for Annex A.8 – Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 16 | A.8.0.3. | sulfur | sulphur [English spelling] |
| 17 | Eq.(A.8-3) | [No division by 1000, as this factor from the conversion of the unit has been already considered in prior equations, such as Eq. A.8-13, Table A.8-1.] |  |
| 18 | Legend Eq.(A.8-3) | ugas = component specific factor or ratio between densities of gas component and exhaust gas (see paragraph §A.8.2.4.) [wrong reference'(see paragraph §A.8.2.4.)' ]; [missing unit [-]] | ugas = component specific factor or ratio between densities of gas component and exhaust gas [-]; to be calculated with equations (A.8-12) or (A.8-13) ['(see paragraph §A.8.2.4.)' replaced by 'to be calculated with equations (A.8-12) or (A.8-13)']; [added missing unit [-]] |
| 19 | Legend Eq. (A.8-4) |  | [add missing unit [-] to parameter u] |
| 20 | Legend Eq.(A.8-6) | Ha = intake air humidity [g H2O/kg dry air] (see paragraph A.8.1.2.) [Wrong reference] | Ha = intake air humidity [g H2O/kg dry air] [Elimination of wrong reference] |
| 21 | Legend Eq. (A.8-14) | Where; (= molar hydrogen-to-carbon ratio [-] ( = molar sulphur-to-carbon ratio [-] ( = molar oxygen-to-carbon ratio [-] [δ is the nitrogen to-carbon ratio and definition of γ is missing] | Where; ( = molar hydrogen-to-carbon ratio [-] (= molar nitrogen-to-carbon ratio [-] ( = molar oxygen-to-carbon ratio [-] (= atomic sulphur-to-carbon ratio [-] |
| 22 | Legend Eq. (A.8-18), (A.8-19) and (A.8-20) | ( = molar sulphur-to-carbon ratio [-] ( = molar nitrogen-to-carbon ratio [-] [δ is the nitrogen to-carbon ratio and γ is the atomic sulphur to carbon ratio] | ( = molar nitrogen-to-carbon ratio [-] ( = atomic sulphur-to-carbon ratio [-] |
| 23 | Legend Eq. (A.8-24) | Where: ugas = ratio between density of exhaust component and density of air (tabulated values) [-] [Wrong reference to '(tabulated values)'] | Where: ugas = ratio between density of exhaust component and density of air, as given in table A.8.2 or calculated with equation (A.8-35) [-] ['(tabulated values)' replaced by 'as given in table A.8.2 or calculated with equation (A.8-35)'] |
| 24 | Eq. A8-35 |  | For unit alignment of u, the equation shall be divided by 1000. |
| 25 | Eq. (A.8-41) as corrected by #10 above | Where: A0 = 0.0056940 collection constant for dV = diameter of the SSV throat [m] pin = absolute pressure at venturi inlet [kPa] [wrong term 'collection constant for' ; wrong unit for diameter and wrong subscript for the absolute pressure at venturi inlet] | Where: A0 = collection of constants and units conversions = 0.0056940 dV = diameter of the SSV throat [mm] pp = absolute pressure at venturi inlet [kPa] ['collection constant for' replaced by ' collection of constants and units conversions'; Correction of wrong unit for diameter and wrong subscript for the absolute pressure at venturi inlet] |
| 26 | Legend Eq. (A.8-46) | n = number of measurements [-] [wrong symbol for the number of measurements] | N = number of measurements [-] [N is symbol for the number of measurements] |
| 27 | Eq. (A.8-56) and legend | (A.8-56) [N wrongly in Italic and N missing from legend] | (A.8-56) Where N = number of measurements [-] [N corrected to Roman and N now defined in legend] |
| 28 | Eq.(A.8-60) | [N wrongly in Italic ] | [N corrected to Roman] |
| 29 | Legend Eq. (A 8-72) | dv = diameter of the SSV throat [m] [wrong unit] | dv = diameter of the SSV throat [mm] |
| 30 | Legend Eq. (A.8-73) and (A.8-74) | Where: A1 = 25.55152 in units of [Wrong value for constant A1; wrong term 'in units of' '; units wrongly in Italic; units not in square brackets] | Where: A1 = collection of constants and units conversions = 27.43831 [value for constant A1 corrected; 'in units of' replaced by 'collection of constants and units conversions'; units in Roman; units in square brackets] |
|  | Legend Eq. (A.8-73) and (A.8-74) | dV = diameter of the SSV throat [m] [wrong unit for diameter] | dV = diameter of the SSV throat [mm] |

Additional Corrections for guidance text - Corrigendum

| # | WHERE | ERRATA | CORRIGE |
| --- | --- | --- | --- |
| 1 | Example following Eq. (GD.A.7-4a) | MH = 1.01 g/mol | MH = 1.00794 g/mol [Use of un-rounded value] |
| 2 | Example following Eq. (GD.A.7-4a) | sulfur | sulphur [English spelling] |
| 3 | Legend Eq. (A.8-28) | Where: Ha = intake air humidity [g H2O/kg dry air] (see paragraph on wet air) Hd = dilution air humidity [g H2O/kg dry air] (see paragraph on wet air) [Missing paragraph references] | Where: Ha = intake air humidity [g H2O/kg dry air] (see paragraph A.8.1 on wet air) Hd = dilution air humidity [g H2O/kg dry air] (see paragraph A.8.1 on wet air) |
| 4 | Legend (Eq.A.8-33) | Where: Hd = intake air humidity [g H2O/kg dry air] (see paragraph on wet air) [Missing paragraph reference] | Where: Hd = intake air humidity [g H2O/kg dry air] (see paragraph A.8.1 on wet air) |
| 5 | Legend (Eq.A.8-35) | Where: Mgas = molar mass of the gas component [g/mol] (see paragraph on basic data for stoichiometric calculation) [Missing paragraph reference] | Where: Mgas = molar mass of the gas component [g/mol] (see paragraph A.8.1. on basic data for stoichiometric calculation) |

# Footnotes

Rev.2 represents corrections (in colour) to the content of Rev.1 and adds some editorial corrections identified in the mean time