UN/SCETDG/37/INF.38

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 7 June 2010 Thirty-seventh session Geneva, 21–30 June 2010 Item 3 of the provisional agenda Listing, classification and packing

Portable tanks instructions for Division 4.3 liquids

Addendum to document ST/SG/AC.10/C.3/2010/28

Note by the secretariat

The following text, which was part of the original proposal submitted by the United States, did not appear in the official version of ST/SG/AC.10/C.3/2010/28 due to technical reasons and should be added.

Proposal 3

7.	Amend the Guiding Principles for assigning portable tank instructions to Division 4.3 liquids as follows:

| Class or Division | PG | Sub-Risk | Tank Instruction | Notes |
| --- | --- | --- | --- | --- |
| 4.3 Liquids | I | Any other than 6.1/8 | T9 or T15a or T21b |  |
|  | II | Any other than 6.1/8 | T7 |  |
|  | III | Any other than 6.1/8 | T7 |  |
| 4.3 Liquids | I | 6.1 or 8 | T10 or T14a or T21b |  |
|  | II | 6.1 or 8 | T7 or T11a |  |
|  | III | 6.1 or 8 | T7 |  |

a This instruction shall be assigned to n.o.s. substances and may also be assigned based on the absolute vapour pressure of the substance.

b This instruction shall be assigned to Division 4.3 packing group I liquids which may ignite in contact with water or moist air.