UN/SCETDG/37/INF.86/Rev.1

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 29 June 2010 Thirty-seventh session Geneva, 21–30 June 2010 Item 3 of the provisional agenda Listing, classification and packing

Packaging for aerosols

Transmitted by the European Aerosol Federation (FEA)

Proposal for a new Packing Instruction for UN 1950

P2yz PACKING INSTRUCTION P2yz

This instruction applies to UN 1950.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3, are met:

(b) Rigid outer packagings with a maximum net mass as follows:

Fibreboard 55kg

Other than fibreboard 125kg

The provisions of 4.1.1.3 need not be met

(a)

Drums (1A2, 1B2, 1N2, 1H2, 1D, 1G);

Boxes (4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H1, 4H2, 4N)

Packagings shall conform to the packing group II performance level. The packagings shall be designed and constructed to prevent movement of the aerosols and inadvertent discharge during normal conditions of transport.

Special packing provisions:

PP87 For UN 1950 waste aerosols carried in accordance with special provision 327, the packagings shall have a means of retaining any free liquid that might escape during carriage, e.g. absorbent material. The packaging shall be adequately ventilated to prevent the creation of flammable atmosphere and the build-up of pressure.

Consequential amendments:

Replace P003 by “P2yz“ in Column 8 of the UN1950 entry in the dangerous goods list.

Delete “ Nos. 1950 and” in PP17 of P003

Delete PP87 in P003

Delete “PP17” in Column 9 of the UN1950 entry in the dangerous goods list.

Replace reference to P003 by new “P2yz” in chapter 3.3 SP 327