UN/SCETDG/37/INF.86

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 28 June 2010 Thirty-seventh session Geneva, 21–30 June 2010 Item 3 of the provisional agenda Listing, classification and packing

Packaging for aerosols

Proposal for a new Packing Instruction for UN 1950

Transmitted by the European Aerosol Federation (FEA)

P2yz PACKING INSTRUCTION P2yz

This instruction applies to UN 1950.

The following packagings are authorized, provided that the general provisions of 4.1.1 and 4.1.3, are met:

(a) For packagings not exceeding the following conditions:

Fibreboard 55kg net mass

Metal, plastics or wood 125kg net mass

The provisions of 4.1.1.3 need not be met

(b) For packagings exceeding the mass above

Drums (1A2, 1B2, 1N2, 1H2, 1D, 1G);

Boxes (4A, 4B, 4C1, 4C2, 4D, 4F, 4G, 4H1 4H2)

Packagings shall conform to the packing group II performance level. The packagings shall be designed and constructed to prevent movement of the aerosols and inadvertent discharge during normal conditions of transport.

Special packing provisions:

PP87 For UN 1950 waste aerosols carried in accordance with special provision 327, the packagings shall have a means of retaining any free liquid that might escape during carriage, e.g. absorbent material. The packaging shall be adequately ventilated to prevent the creation of flammable atmosphere and the build-up of pressure.

Consequential amendments:

Replace P003 by “P2yz“ in Column 8 of the UN1950 entry in the dangerous goods list.

Delete “UN1950” in PP17 of P003

Delete PP87 in P003

Delete “PP17” in Column 9 of the UN1950 entry in the dangerous goods list.

Replace reference to P003 by new “P2yz” in chapter 3.3 SP 327