|  | .15/88/INF.3 | INF.11E |
| --- | --- | --- |
|  | Economic Commission for Europe Inland Transport Committee Working Party on the Transport of Dangerous Goods Eighty-eighth session Geneva, 3–7 May 2010 Item 6 (a) of the provisional agenda Proposals for amendments to annexes A and B of ADR: pending issues Section 9.7.6 – Rear protection of vehicles Transmitted by the Government of Germany | 19 April 2010 |

Chapter 1.6 – Transitional measures

Transmitted by the Government of France

1.	The WP.15 has adopted the two following transitional measures for entry into force on 1 January 2011 (see document ECE/TRANS/WP.15/204).

2.	Paragraph 1.6.5.4 allowing the adaptation of ECE Regulation No. 105 is modified to read:

“1.6.5.4	As regards the construction of EX/II, EX/III, FL, OX and AT vehicles, the requirements of Part 9 in force up to 31 December 2010 may be applied until 31 March 2012.”

3.	A new transitional measure is introduced in 1.6.5.12 to take into account the modification of 9.2.2.6.3:

“1.6.5.12	EX/III and FL vehicles registered or entering into service before 1 July 2011, the electrical connections of which do not comply with the requirements of 9.2.2.6.3, but comply with the requirements applicable until 31 December 2010, may still be used.”

4.	There is an inconsistency between these provisions because of the defined dates which need to be modified.

5.	Furthermore, in its document ECE/TRANS/WP.29/GRSG/2010/17, OICA proposes to modify ECE Regulation No. 105 to align it with ADR 2011 with an entry into force on 1 January 2012.

Proposal

6.	We propose to modify the transitional measures in 1.6.5.4 and 1.6.5.12 as follows:

“1.6.5.4	As regards the construction of EX/II, EX/III, FL, OX and AT vehicles, the requirements of Part 9 in force up to 31 December 2010 may be applied until 31 December 2011.”

“1.6.5.12	EX/III and FL vehicles registered or entering into service before 1 January 2012, the electrical connections of which do not comply with the requirements of 9.2.2.6.3, but comply with the requirements applicable until 31 December 2010, may still be used.”