REGULATION No. 70

(Rear marking plates for long vehicles)

Proposal for Corrigendum 1 to Supplement 7 to the 01 series of amendments

Regulation No. 70

The modifications to the current text of Regulation No. 70 are .marked in bold or strikethrough characters.

# I.	PROPOSAL

Annex 8, amend to read:

"………

7.	Resistance to cleaning

………

7.2.	Power washing

7.2.1.	When subjected to a continuous spraying action for 60 seconds on the test component in its normal mounting conditions, a test sample shall show no damage to the retro-reflective surface or delamination from the substrate or separation from the sample mounting surface under the following set-up parameters:

(a)	Water/wash solution pressure 8 ± 0.2 MPa;

(b)	Water/wash solution temperature 60° - 5 °C;

(c)	Water/wash solution flow rate 7 to ± 1 l/min;

(d)	The tip of the cleaning wand to be positioned at distance of 600 ± 20 mm away from the retro-reflective surface;

(e)	Cleaning wand to be held at no greater angle than 45 degrees from perpendicular to the retro-reflective surface;

(f)	40 degree nozzle creating wide fan pattern.

………"

II.	JUSTIFICATION

This proposal was already adapted by the GRE at its fifty-eighth session to amend Regulation No.70 (ECE/TRANS/WP.29/GRE/2007/58). At that GRE session we were also adapted the same amendments about Regulation No. 69 (ECE/TRANS/WP.29/GRE/2007/57) and No.104 (ECE/TRANS/WP.29/GRE/2007/59), so the same parts of Regulation No. 69(Annex 8, Paragraph 7.2.1 (c)) and Regulation No.104 (Annex 8, Paragraph 5.2.1 (c)) were already amended to "Water/wash solution flow rate 7 ± 1 l/min".

Editorial error had been indicated from Supplement 7 of this Regulation No. 70.

- - - - -