| Transmitted by the expert from GTB | Informal Document No. GRE-64-26 (64th GRE, 4-7 October 2010 agenda item 16) |
| --- | --- |

Proposal for Corrigendum 1 to the 01 series of amendments to Regulation No. 112 (Headlamps emitting an asymmetrical passing beam)

- Proposal

Annex 2, Figure 12, the note, amend to read:

"The above example corresponds to the marking of a lens of plastic material intended to be used in different types of headlamps, namely:

Either	A headlamp, Class B, with a passing beam designed for both traffic systems and a driving beam with a maximum luminous intensity comprised between 123625 and 145125  candelas (as indicated by the number 30), approved in Germany (E1) in accordance with the requirements of this Regulation in its original form (00),

which is reciprocally incorporated with

A front position lamp approved in accordance with the 02 series of amendments to Regulation No. 7;

Or	A headlamp, Class A, with a passing beam designed for both traffic systems and a driving beam with a maximum luminous intensity comprised between 33750 48375 cd and 41250 64500 cd (as indicated by the number 12.5), approved in Germany (E1) in accordance with the requirements of this Regulation in its original form (00),

which is reciprocally incorporated with

The same front position lamp as above;

Or	even either of the above-mentioned-headlamps approved as a single lamp.

The main body of the headlamp shall bear the only valid approval number, for instance:…"

- Justification

The proposal for the 01 series of amendments submitted by GTB as ECE/TRANS/WP.29/GRE/2009/46 contained incorrect values for the maximum luminous intensity in the example of the approval marking described in Annex2, figure 12. This corrigendum presents the correct values that are calculated as shown in the table below.

Table (for reference only) showing the method to determine the Maximum Intensity Reference Mark

| Max Intensity Reference Mark | Intensity values based upon 43,000 cd max |
| --- | --- |
| Marking | Mid Point | Min | Max |
| 7.5 |  |  | 32250 |
|  | 8.75 |  |  |
| 10 |  | 37625 | 48375 |
|  | 11.25 |  |  |
| 12.5 |  | 48375 | 64500 |
|  | 15 |  |  |
| 17.5 |  | 64500 | 80625 |
|  | 18.75 |  |  |
| 20 |  | 80625 | 96750 |
|  | 22.5 |  |  |
| 25 |  | 96750 | 112875 |
|  | 26.25 |  |  |
| 27.5 |  | 112875 | 123625 |
|  | 28.75 |  |  |
| 30 |  | 123625 | 145125 |
|  | 33.75 |  |  |
| 37.5 |  | 145125 | 166625 |
|  | 38.75 |  |  |
| 40 |  | 166625 | 182750 |
|  | 42.5 |  |  |
| 45 |  | 182750 | 204250 |
|  | 47.5 |  |  |
| 50 |  | 204250 | 215000 |