|  | United Nations | ECE/TRANS/WP.15/AC.2/2011/25 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 31 May 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the
European Agreement concerning the International Carriage
of Dangerous Goods by Inland Waterways (ADN)
(ADN Safety Committee)

Nineteenth session

Geneva, 22-25 August 2011

Item 4 of the provisional agenda

Proposals for amendments to the Regulations annexed to ADN

8.6.3 ,

Transmitted by the Government of Belgium

Introduction

1.	In 8.6.3 the model of the ADN Checklist is given. 7.2.4.10 states that a check list for the cargo in question has to be completed. There is, however, no reference in the model to what is meant by “Name of product”. The model does not say where to find the UN Number, Identification number or Class.

2.	It is proposed, therefore, to add to the model of the ADN Checklist some references to the transport document and to Table C. The “Name of product” is substituted by the terminology found in 5.4.1.1.2.

3.	During discussion the question arose whether the packing group should be added to the ADN Checklist. At least for some products the packing group is considered important information (e.g. for UN 1170 ETHANOL SOLUTION the packing group determines the tank design).

Proposal

New text appears in italics.

| 1 ADN Checklist concerning the observance of safety provisions and the implementation of the necessary measures for loading/unloading - Particulars of vessel ………………………………………….. No. …………………………………………... (name of vessel) (official number) ………………………………………….. (vessel type) - Particulars of loading or unloading operations …………………………………………... ……………………………………………….. (shore loading or unloading installation) (place) …………………………………………... ……………………………………………….. (date) (time) - Particulars of the cargo as indicated in the transport document |
| --- |
| Quantity m3 | Proper shipping name supplemented, when applicable, by the technical name | UN Number or Identification number | Danger, as indicated in column (5) of Table C | Packing Group |
|  | ………… | ……………….. | …………….. | ………. |
|  | ………… | ……………….. | …………….. | ………. |
|  | …… | ……………….. | …………….. | ………. |
| - Particulars of last cargo* |
| Proper shipping name supplemented, when applicable, by the technical name | UN Number or Identification number | Danger, as indicated in column (5) of Table C | Packing Group |
| …………………………. | ……………… | …………… | ………. |
| …………………………. |  | ………. | ………. |
| …………………………. |  | ………. | ………. |

# Footnotes

Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR/ZKR/ADN/WP.15/AC.2/2011/25.

In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106; ECE/TRANS/2010/8, programme activity 02.7 (b)).