UN/SCEGHS/23/INF.3

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals 12 April 2012 Twenty–third session Geneva, 4 (p.m) – 6 July 2012 Item 3 of the provisional agenda Hazard communication issues

Fire extinguishers

Transmitted by the expert from Argentina

I.	Background

1.	By definition, gases under pressure are gases which are contained in a receptacle at a pressure of 200 kPa (gauge) or more, or which are liquefied or liquefied and refrigerated. (Chapter 2.5).

2.	The fire extinguishers are metal containers with an extinguishing agent and a propellant gas but they are not considered to be either aerosols or cylinders under pressure (except the containers of carbon dioxide), where the gas is the extinguishing agent. All of them however are under a pressure between 4 and 75 times greater than 200kPa.

3.	The pressurized gas cylinders have steel walls with a thickness ranging between 5.4 mm and 8.0 mm.

4.	Fire extinguishers have a wall of steel or aluminium with a thickness of 1.5 mm and 2.7 mm, (except for carbon dioxide extinguishers that have a steel wall of 5.4 mm) and this makes them more fragile to shocks or punctures that the pressurized gas cylinders.

5.	The exposure to temperatures higher than 54°C (130°F) can significantly increase the internal pressure with hazard of explosion.

6.	A blow can deform or pierce the wall of the fire extinguisher and can cause an explosion.

II.	Accidents produced by the use of fire extinguishers

Table 1

| Country | Date | Injuries | Deaths | Cause |
| --- | --- | --- | --- | --- |
| Argentina | 2004 | 0 | 1 | Explosion |
| New Zealand | 2005 | 1 | 1 | Valve rupture |
| Peru | 2006 | 0 | 1 | Explosion |
| Chile | 2008 | 0 | 1 | Explosion |
| Spain | 2009 | 0 | 1 | Explosion |
| Spain | 2010 | 0 | 0 | Discharge |
| Spain | 2010 | 0 | 0 | Explosion |
| Spain | 2011 | 1 | 0 | Explosion |
| United States | 2011 | 1 | 0 | Explosion |
| India | 2011 | 3 | 0 | Explosion |

Table 2

| Organization | Date | Injuries | Deaths | Cause |
| --- | --- | --- | --- | --- |
| NEW FLAME | 2001 | 0 | 1 | explosion |
| M.A.C. | 2007 | 0 | 1 | explosion |
| M.A.C. | 2007 | several | 0 | explosion |
| M.A.C. | 2010 | 0 | 0 | explosion |
| CPSC | 2011 | several | 0 | different causes |

References

M.A:C.: Maritime Accident Casebook (Philippines)

New Flame: (United Kingdom)

CPSC: Consumer Product Safety Commission (United States)

III.	Proposal

7.	Add a note under table 2.5.1 to read as follows:

“NOTE: Fire extinguishers fall within the scope of this chapter and should be classified in accordance with the criteria in table 2.5.1 and be labelled with the related hazard communication elements in table 2.5.2.”