Proposal for Supplement 22 to the 02 series of amendments to 
Regulation No. 7 (Position, stop and end-outline lamps)

I.	Proposal

Paragraph 6.1., amend to read:

"6.1.	The light emitted by each of the two devices supplied shall be in the reference axis, of not less than the minimum intensity and of not more than the maximum intensity specified below:

|  | Minimum luminous intensity in cd | Maximum luminous intensity in cd when used as |
| --- | --- | --- |
|  |  | Single lamp | Lamp (single) marked "D" paragraph (4.2.2.6.) |
| 6.1.1. Front position lamps, front end-outline marker lamp A or AM | 4 | 140 | 70 |
| 6.1.2. Front position lamps incorpo-rated in a headlamp or front fog lamp | 4 | 140 | - |
| 6.1.3. Rear position lamps, rear end-outline marker lamp 6.1.3.1. R, R1 or RM1 (steady) | 4 | 17 | 8.5 |
| 6.1.3.2. R2 or RM2 (variable) | 4 | 42 | 21 |
| 6.1.4. Stop-lamps |  |  |  |
| 6.1.4.1. S1 (steady) | 60 | 260 | 130 |
| 6.1.4.2. S2 (variable) | 60 | 730 | 365 |
| 6.1.4.3. S3 (steady) | 25 | 110 | 55 |
| 6.1.4.4. S4 (variable) | 25 | 160 | 80 |

"

II.	Justification

1.	UN Regulation No. 48 does not prohibit reciprocal incorporation of front position lamps with front fog lamps. In some cases, manufacturers need to reciprocally incorporate front position lamps with front fog lamps for construction or style.

2.	For lamps fitted with filament light sources, similar to front position lamps reciprocally incorporated with headlamps, because of the reflector employed by front fog lamps, the maximum intensity limit of the front position lamp should be increased as front position lamps reciprocally incorporated with front fog lamps.