Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods				1 February 2013

Joint Meeting of the RID Committee of Experts and the
Working Party on the Transport of Dangerous Goods

Bern, 18–22 March 2013

Item 3 of the provisional agenda

Standards

Consequential amendments of references to EN standards

Transmitted by the European Committee for Standardisation (CEN)

Introduction

1.	At its session in March 2010 the Joint Meeting adopted the reference to EN ISO 14245:2010 and EN ISO 15995:2010 in RID/ADR 2011, subsection 6.2.4.1 based on a proposal from the Working Group on Standards (see ECE/TRANS/WP.15/AC.1/118, and INF.41).

2.	This amendment followed the intention by CEN to replace EN 13152 and EN 13153 by EN ISO 14245:2010 and EN ISO 15995:2010. This led to a restriction of the applicability for EN 13152:2001 and 13153:2001 till end of 2010 and for EN 13152:2001+A1:2003 and 13153:2001+A1:2003 till end of 2014 in the table in RID/ADR 6.2.4.

3.	In addition to RID/ADR subsection 6.2.4.1 EN 13152 and EN 13153 are also referenced in RID/ADR in

-	4.1.4.1, P200 (15) in context with the 15 years interval for periodic inspections and in

-	4.1.6.15 in context with the special packing provisions for goods of Class 2 and goods of other classes assigned to packing instruction P200.

4.	Taking note of these changes of RID/ADR CEN asks to consider the following consequential amendments for the text of RID/ADR 2015:

Proposal 1

5.	Amend the text of RID/ADR subsection 4.1.4.1, P200 (12), 3.4 as follows:

3.4 	Cylinders having been granted a 15 year interval shall only be fitted with valves designed and manufactured for a minimum 15 year period of use according to EN 13152:2001 + A1:2003 or EN 13153:2001 + A1:2003 EN ISO 14245:2010 or EN ISO 15995:2010. After a periodic inspection, ….

Proposal 2

6.	Amend the text of RID/ADR subsection 4.1.6.15 as follows:

4.1.6.15 In the Table, replace the entries EN 13152:2001 + A1:2003 and EN 13153:2001 + A1:2003 with:

"EN ISO 14245:2010 Gas cylinders – Specifications and testing of LPG cylinder valves – Self closing (ISO 14245:2006)” and with

“EN ISO 15995:2010 Gas cylinders – Specifications and testing of LPG cylinder valves – Manually operated (ISO 15995:2006)”.

Proposal 3

7.	Amend the text of RID/ADR subsection 6.2.4.1 as follows:

6.2.4.1, in the Table, delete the four entries EN 13152:2001, EN 13152:2001 + A1:2003, EN 13153:2001 and EN 13153:2001 + A1:2003.

Justification

8.	All proposals are consequential amendments following the decision of CEN/TC 286 to replace EN 13152 and EN 13153 by EN ISO 14245 and EN ISO 15995. The deletion of the existing references (proposal 3) is required as the latest date for the application of the old standards will have been expired when RID/ADR 2015 will become effective.