|  | United Nations | ECE/TRANS/WP.29/2013/12 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 13 December 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

159th session

Geneva, 12-15 March 2013

Item 4.8.5 of the provisional agenda

1958 Agreement – Consideration of draft amendments

to existing Regulations submitted by GRSG

Proposal for the Supplement 1 to the 02 series of amendments to Regulation No. 118 (Burning behaviour)

Submitted by the Working Party on General Safety Provisions*

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its 103rd session, clarifying the provisions on interior materials which shall be tested (ECE/TRANS/WP.29/GRSG/82, para. 25). It is based on ECE/TRANS/WP.29/GRSG/2012/22, as reproduced in Annex III to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraph 2.2., amend to read:

"2.2.		"Interior compartment" means any compartment intended for passengers, drivers and/or crew bounded by the interior facing surface(s) of:

(a)	The ceiling;

(b)	The floor;

(c)	The front, rear and side walls,

(d)	The doors;

(e)	The outside glazing."

Paragraph 5.2.1., amend to read:

"5.2.1.	The materials inside and no more than 13 mm beyond the interior compartment, materials of the engine compartment and materials of any separate heating compartment used in the vehicle to be type approved shall meet the requirements of Part II of this Regulation."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.