UN/SCETDG/45/INF.48/Rev.1

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 24 June 2014 Forty-fifth session Geneva, 23 June – 2 July 2014 Item 7 (g) of the provisional agenda Miscellaneous proposals for amendments to the Model Regulations on the Transport of Dangerous Goods: packagings

Leakproofness testing procedures – comments on document 2014/34 by the expert from Sweden

Transmitted by the experts from Belgium and The Netherlands

Proposal

- In the first paragraph in 4.1.1.12, amend the first sentence as follows and  add a note:

“4.1.1.12	Every packaging as specified in Chapter 6.1 intended to contain liquids shall successfully undergo a suitable leakproofness test either meeting the appropriate test level indicated in 6.1.5.4.3 or a suitable alternative approved by the competent authority : and be capable of meeting the appropriate test level  indicated in 6.1.5.4.3. :

(a)	Before it is first used for transport;

(b)	After the remanufacturing or reconditioning of any packaging, before it is re-used for transport

NOTE: This can be achieved by the application of a suitable QAP (quality assurance programme) as stipulated in 6.1.1.4.”

The rest of the sub-section remains unchanged.

2.	In the first paragraph in 6.1.1.3 amend the first sentence as follows and add a note:

“6.1.1.3		Every packaging intended to contain liquids shall successfully undergo a suitable leakproofness test either meeting the appropriate test level indicated in 6.1.5.4.3 or a suitable alternative approved by the competent authority : , and be capable of meeting the appropriate test level indicated in 6.1.5.4.3. :

(a)	Before it is first used for transport;

(b)	After the remanufacturing or reconditioning of any packaging, before it is re-used for transport

NOTE: This can be achieved by the application of a suitable QAP (quality assurance programme) as stipulated in 6.1.1.4.”

The rest of the sub-section remains unchanged.

3.	In the first paragraph in 6.5.4.4.2, amend the first sentence as follows and  add a note after indent b):

“6.5.4.4.2	Every metal, rigid plastics and composite IBC for liquids, or for solids which are filled or discharged under pressure, shall undergo a suitable leakproofness test either meeting the appropriate test level indicated in 6.5.6.7.3 or a suitable alternative approved by the competent authority :

- Before it is first used for transport;

(b)	At intervals of not more than two and a half years.”

NOTE: This can be achieved by the application of a suitable QAP (quality assurance programme) as stipulated in 6.5.4.1.1.”

The rest of the sub-section remains unchanged.