UN/SCETDG/46/INF.66

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 4 December 2014 Forty-sixth session Geneva, 1 – 9 December 2014 Item 2 (e) of the provisional agenda Recommendations made by the Sub-Committee on its forty-third, forty-fourth and forty-fifth sessions and pending issues: miscellaneous pending issues

Reference document ST/SG/AC.10/C.3/2014/76 (Sweden)

Proposal agreed by International Confederation of Container Reconditioners (ICCR), International Council of Intermediate Bulk Container Associations (ICIBCA) and International Confederation of Plastics Packaging Manufacturers (ICPP)

1. 	Accept original informal document INF.43 with the addition of:

The following note to 6.1.1.3:

“NOTE: Production testing, performed under a quality assurance programme approved by the competent authority, shall be adequate to ensure leakproofness and packaging capability, in accordance with this Chapter.”.

2.	Insert the following subparagraph (b) in 6.5.4.4.2:

“(b)	After the repair or remanufacturing of the IBC, before it is reused for 		transport.” Existing subparagraph (b) becomes subparagraph (c).

3.	Add a Note to 6.5.4.4.2 as follows:

NOTE: Production testing, performed under a quality assurance program approved by the competent authority, shall be adequate to ensure leakproofness and packaging capability, in accordance with this chapter.