|  | United Nations | ECE/TRANS/WP.15/AC.2/2014/5 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 24 October 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the 
European Agreement concerning the International Carriage 
of Dangerous Goods by Inland Waterways (ADN)

(ADN Safety Committee)

Twenty-fourth session

Geneva, 27–31 January 2014

Item 5 (b) of the provisional agenda

Proposals for amendments to the Regulations annexed to ADN:

Other proposals

Miscellaneous proposals for amendments - entries for 
Table A, 1.6.7 and 7.1.4.1

Transmitted by the Government of Belgium

| Summary |
| --- |
| Executive summary: | Regulate the bulk transport of solid substances belonging to Class 6.1 in general and UN No. 2291 in particular |
| Action to be taken: | Modify Table A, add a new entry to 7.1.4.1 and add a transitional provision |

Introduction

1.	For some time now there has been transport in bulk of lead ore by inland waterway vessels in the port of Antwerp. These substances have been classified as UN No. 2291 LEAD COMPOUND, SOLUBLE, N.O.S belonging to Class 6.1. As Table A of the ADN does not allow bulk transport of such products, a special authorization was delivered by the Belgian national authority in accordance with article 6, § 5 of EU directive 2008/68. This proposal aims at regulating the bulk transport of these substances so that special authorizations will no longer be necessary in the future.

2.	It is proposed to modify the entry for UN No. 2291 in Table A to allow carriage in bulk as indicated in column (8). At the same time a breathing apparatus is compulsory as indicated in column (9). As the special authorization already required the use of double hull vessels for the bulk transport of this product, it is now proposed to extend this to all 6.1 substances for which bulk transport is allowed by means of a new entry in 7.1.4.1.

3.	This new requirement also concerns UN Nos. 1690, 1812 and 2505 for which bulk transport is already allowed under the existing ADN. Consequently, a proposal for a transitional provision has been added.

Proposal

4.	Amend the entry for UN No. 2291 in Table A as follows.

| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) | (12) | (13) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 | T5 | III | 6.1 | 199 274 535 802 | 5 kg | E1 | B | PP, EP A |  |  | 0 |  |

5.	Add the following line to the table in 7.1.4.1 for Class 6.1, after “All goods of packing group II: total 300 000 kg”:

“all goods carried in bulk							0  kg”

6.	Add the following paragraph after 1.6.7.2.1.2:

“1.6.7.2.1.3 	By way of derogation from 7.1.4.1, transport in bulk of substances of Class 6.1, packing group III, may be carried out with single hull vessels until 31.12.2018.”

# Footnotes

Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR/ZKR/ADN/WP.15/AC.2/2014/5.