|  | United Nations | ECE/TRANS/WP.29/GRPE/2015/9 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 10 December 2014 English only |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Pollution and Energy

Seventieth session

Geneva, 13-16 January 2015

Item 12 of the provisional agenda

Fuel Quality (FQ)

Proposal for amendments to the Consolidated Resolution on the Construction of Vehicles (R.E.3)

Submitted by the experts from the Association for Emissions Control by Catalyst, the European Association of Automotive Suppliers, the European Association of Internal Combustion Engine Manufacturers and the International Organization of Motor Vehicle Manufacturers*

The purpose of this proposal, tabled by the experts from the Association for Emissions Control by Catalyst (AECC), the European Association of Automotive Suppliers (CLEPA), the European Association of Internal Combustion Engine Manufacturers (EUROMOT) and the International Organization of Motor Vehicle Manufacturers (OICA), is to propose amendments to the recommendation on market fuel quality, contained in the Consolidated Resolution on the Construction of Vehicles (R.E.3).

I.	Proposal

Annex 4, delete and replace by:

"Annex 4

Recommendation on market fuel quality

1.	Purpose of the recommendation

This recommendation has been developed to inform governments about the appropriate market fuel quality that is protective of vehicle emission control technologies. The regulated vehicle emissions limits and associated market fuel qualities should be consistent with local air quality expectations.

2.	Scope of the recommendation

This recommendation applies to fuel quality parameters that directly affect the performance and durability of engine as well as exhaust emission control equipment and that influence the content of exhaust emissions.

3.	Abbreviations

AQIRP	Air Quality Improvement Research Programme

CEN		European Committee for Standardization

CCR		Conradson Carbon Residue 
 		(indication of fuel tendency to form carbon deposits)

CFPP		Cold Filter Plugging Point 
	(measure for lowest temperature at which a fuel will give trouble-free flow)

FAME		Fatty Acid Methyl Esters
FBP		Final Boiling Point

DPF		Diesel Particulate Filter

HC		Hydrocarbons

JCAP		Japan Clean Air Programme

OBD		On-board diagnostics

MON		Motor Octane Number
PAH		Polycyclic Aromatic Hydrocarbons

PM		Particulate matter

RON		Research Octane Number
RVP		Reid Vapour Pressure
TEL		Tetra Ethyl Lead
VLI		Vapour Lock Index

In this annex and its appendixes, for simplifying the format of the tables, the UN Regulations and their series of amendments are noted in a short form as follow: the YY series of amendments to UN Regulation No. XX is noted "RXX.YY".

4.	Introduction

It is acknowledged that market fuel quality plays a key role in the level and type of pollutant emissions from motor vehicles. Regulations and specifications for market fuel quality are not yet well harmonized (even within a given region) and they are not always fully aligned with the needs of engine technology to help meet pollutant emission regulations in force. As many world regions and cities suffer from poor air quality and move towards more stringent motor vehicle emission regulations, this requires the use of more advanced emission control technology on engines, which drives the crucial need for improved market fuel quality.

This recommendation defines a list of key fuel parameters linked to legally required emissions levels and suggests the minimum fuel quality requirements corresponding to vehicle technologies necessary to achieve and maintain such emission levels. It has to be recognised that other parameters can influence tailpipe pollutant emissions and thus adherence to this list may not be sufficient to enable durable compliance to the relevant emissions standards for all vehicle concepts.

The list of parameters has been herewith linked to emission limits set in the various series of UN Regulations Nos. 83 and 49 up to R83.05 (row B) and R49.03 (row B1) and UN Regulation No. 96 up to R96.02. An extension to cover more recent and more stringent emission limits may be needed in due time to keep this recommendation updated to technical progress.

International fuel standards (e.g. CEN) have been developed from the emission technology-fuel specifications that have been driven by European legislation. These CEN standards, developed on a technical basis between the various stakeholders in CEN, provide for European market fuels that are, essentially, fit for purpose.

The parallel application of appropriate market fuel standards must be an important part of an integrated approach by Contracting Parties to enable improved and long-lasting emission reductions during the lifetime of all motor vehicles.

5. 	Appendix content

Appendix 1 shows the historical development of on-road and non-road emission standards and fuel quality (based on CEN standards).

Appendix 2 details the fuel parameters aligned with the progression of the UN emission standards that require the use of more advanced exhaust after-treatment control technology that are affected by market fuel quality.

Appendix 3 shows the correlation between the series of UN Regulations Nos. 83, 49 and 96 and the parallel Euro standards.

Appendix 4 	indicates a guideline document on good practice for fuel housekeeping.

6. 	Market fuel quality

The clearly demonstrated link between emission standards and market fuel quality – which the European Union, Japan and the United States of America have all followed - should be followed in those world areas that are now introducing for the first time or adopting more stringent emission standards, for on-road motor vehicles and Non-Road Mobile Machinery (NRMM).

6.1.	Gasoline – on road vehicles

| Unleaded Gasoline | R83.03 | R83.05 (row A) | R83.05 (row B) | Test method |
| --- | --- | --- | --- | --- |
| Lead [g/l] | No intentional addition, with a max ≤ 0.013 | No intentional addition, with a max ≤ 0.005 | No intentional addition, with a max ≤ 0.005 | EN 237 |
| Sulphur [mg/kg] | ≤ 500 | ≤ 150 | ≤ 50 1 | EN ISO 20846 EN ISO 20884 |
| Metal Additives [mg/l] | ----------------- Not permitted ----------------- |
| Oxygen [%m/m] | ≤ 2.7 | ≤ 2.7 | ≤ 2.7 | EN 1601 EN 13132 |
| Oxygenates [%v/v] |  |  |  |  |
| - methanol | ≤ 3.0 2 | ≤ 3.0 2 | ≤ 3.0 2 | EN 1601 EN 13132 |
| - ethanol | ≤ 5.0 | ≤ 5.0 | ≤ 5.0 |  |
| - iso-propyl alcohol | ≤ 10.0 | ≤ 10.0 | ≤ 10.0 |  |
| - iso-butyl alcohol | ≤ 10.0 | ≤ 10.0 | ≤ 10.0 |  |
| - tert-butyl alcohol | ≤ 7.0 | ≤ 7.0 | ≤ 7.0 |  |
| - ethers | ≤ 15.0 | ≤ 15.0 | ≤ 15.0 |  |
| - other oxygenates | ≤ 10.0 | ≤ 10.0 | ≤ 10.0 |  |
| RVP [kPa] | 35 - 100 | 45 – 100 | 45 – 100 | EN 13016/l DVPE |
| Density [kg/m3] | 725 – 780 | 720 – 775 | 720 – 775 | EN ISO 3675 EN ISO 12185 |
| RON | ≥ 95 | ≥ 95 | ≥ 95 | EN ISO 5164 |
| MON | ≥ 85 | ≥ 85 | ≥ 85 | EN ISO 5163 |
| Benzene [%v/v] | ≤ 5 | ≤ 1 | ≤ 1 | EN 238 EN 14517 |
| Aromatics [%v/v] | - | ≤ 42 | ≤ 35 | EN 14517 EN15553 |
| Olefins [%v/v] | - | ≤ 18 | ≤ 18 | EN 14517 EN15553 |
| VLI (10VP + E70) | - | 1 050 – 1 250 | 1 050 – 1 250 |  |
| Residue [%v/v] | < 2 | < 2 | < 2 | EN ISO 3405 |
| 1 Corresponds to the United Nations Environment Programme (UNEP) decision taken at the fourth global meeting of the Partnership for Clean Fuels and Vehicles (PCFV), held on 14 and 15 December 2005 in Nairobi, Kenya. 2 Industry recommends no methanol content (non-detectable). |

# 6.2.	Volatility Classes for Unleaded Gasoline

| Class (*) | A | B | C/C1 | D/D1 | E/E1 | F/F1 |
| --- | --- | --- | --- | --- | --- | --- |
| Vapour pressure (kPa) | 45 - 60 | 45 - 70 | 50 - 80 | 60 – 90 | 65 - 95 | 70 - 100 |
| E70 (%)1 | 20 - 48 | 20 - 48 | 22 - 50 | 22 – 50 | 22 – 50 | 22 – 50 |
| E100 (%)1 | 46 - 71 | 46 - 71 | 46 - 71 | 46 – 71 | 46 - 71 | 46 - 71 |
| E150 (% min)1 | 75 | 75 | 75 | 75 | 75 | 75 |
| Final boiling point (°C max) (1) | 210 | 210 | 210 | 210 | 210 | 210 |
| T10 (°C, max)1 | 65 | 60 | 55 | 50 | 45 | 45 |
| T50 (°C, max)1 | 77-100 | 77-100 | 75-100 | 70-100 | 65-100 | 65-100 |
| T90 (°C, max)1 | 130-175 | 130-175 | 130-175 | 130-175 | 130-175 | 130-175 |
| Distillation residue (% V/V) | 2 | 2 | 2 | 2 | 2 | 2 |
| Vapour Lock Index (VLI) (10 VP + 7 E70) (index max) | - | - | C - | D - | E - | F - |
| Vapour Lock Index (VLI) (10 VP + 7 E70) (index max) |  |  | C1 1 050 | D1 1 150 | E1 1 200 | F1 1 250 |
| * "Class" is based on the minimum expected ambient temperature of the market and will vary by season. Implementing country to choose volatility class or classes appropriate to their yearly ambient temperature conditions. 1 E-values or T-values as alternatives. |

# Relation between vapour pressure (VP), E70 and VLI for the ten different volatility classes for unleaded gasoline

# 6.3.	Diesel – on-road vehicles

|  | R83 - 03series and R49.02 (Stage II) | R83.05 (row A) and R49.03 (row A) | R83.05 (row B) and R49.03 (row B) | Test method |
| --- | --- | --- | --- | --- |
| Sulphur [mg/kg] | ≤ 500 | ≤ 350 | ≤ 50 1 | EN ISO 20846 EN ISO 20884 |
| Ash [%m/m] | ≤ 0.01 | ≤ 0.01 | ≤ 0.01 | EN/ISO 6245 |
| Total Contamination [mg/kg] | ≤ 24 | ≤ 24 | ≤ 24 | EN 12662 |
| Cetane Number 2 | ≥ 49 | ≥ 51 | ≥ 51 | EN ISO 5165 |
| Cetane Index 2 | ≥ 46 | ≥ 46 | ≥ 46 | EN ISO 4264 |
| Density [kg/m3] 2 | 820 – 860 | 820 – 845 | 820 – 845 | EN ISO 3675 EN ISO 12185 |
| Viscosity [mm2/s] 2 | 2.0 - 4.5 | 2.0 - 4.5 | 2.0 – 4.5 | EN ISO 3104 |
| Flash Point [°C] | > 55 | > 55 | > 55 | EN ISO 2719 |
| T50 [°C] | - | T65 = 250 min | T65 = 250 min | EN ISO 3405 |
| T85 [°C] | ≤ 350 | ≤ 350 | ≤ 350 | EN ISO 3405 |
| T95 [°C] | ≤ 370 | ≤ 360 | ≤ 360 | EN ISO 3405 |
| PAH [%m/m] | ≤ 11 | ≤ 11 | ≤ 11 | EN 12916 |
| Carbon residue [%m/m] | ≤ 0.3 | ≤ 0.3 | ≤ 0.3 | EN ISO 10370 |
| CFPP [°C] 2 | -44 to +5 | -44 to +5 | -44 to +5 | EN 116 |
| Cloud Point [°C] (severe winter conditions) 2 | -34 to -10 | -34 to -10 | -34 to -10 | EN 23015 |
| Copper strip corrosion (3h at 50°C) [rating] | Class 1 | EN ISO 2160 |
| Water [mg/kg] | ≤ 200 | ≤ 200 | ≤ 200 | EN ISO 12937 |
| Lubricity [micron] | ≤ 460 | ≤ 460 | ≤ 460 | EN ISO 12156-1 |
| Oxidation stability [hours] 3 | > 20 | > 20 | > 20 | EN15751 |
| FAME [%v/v] | 4 | 4 | 4 | EN14214 ASTM D6751 |
| Appearance | Clear and bright, no free water or particulates | D4176 visual inspection |
| Ethanol/Methanol [%v/v] | Non-detectable 5 |  |

1	Corresponds to the United Nations Environment Programme (UNEP) decision taken at the fourth global meeting of the Partnership for Clean Fuels and Vehicles (PCFV), held on 14 and 15 December 2005 in Nairobi, Kenya.

2	Implementing country to choose value appropriate within range for arctic or severe winter conditions. More detailed arctic or severe winter specifications for these parameters to be considered.

3	Applicable for diesel containing more than 2 per cent v/v FAME.

4	Up to 5 per cent v/v FAME permitted if FAME complies with ASTM D6751. Up to 7 per cent v/v FAME permitted if FAME complies with EN14214. Industry recommends that vehicle owners refer to their vehicle handbook.

5	At or below detection limit of method used.

# 6.4.	Diesel – NRMM

|  | R96 Power bands A to C | R96.01 Power bands D to G | R96.02 Power bands H to K | Test method |
| --- | --- | --- | --- | --- |
| Sulphur [mg/kg] | ≤ 2 000 | ≤ 2 000 | ≤ 300 1 | ASTM D5453 |
| Ash [%m/m] | ≤ 0.01 | ≤ 0.01 | ≤ 0.01 | EN/ISO 6245 |
| Total Contamination [mg/kg] | ≤ 24 | ≤ 24 | ≤ 24 | EN 12662 |
| Cetane Number 2 | ≥ 45 | ≥ 45 | ≥ 52 | EN ISO 5165 |
| Density [kg/m3] 2 | 835 – 845 | 835 – 845 | 833 – 837 | EN ISO 3675 ASTM D4052 |
| Viscosity [mm2/s] 2 | 2.0 - 4.5 | 2.0 - 4.5 | 2.0 – 4.5 | EN ISO 3104 |
| Flash Point [°C] | > 55 | > 55 | > 55 | EN ISO 2719 |
| T50 [°C] | - | - | > 250 | EN ISO 3405 |
| T95 [°C] | ≤ 370 | ≤ 370 | 345-350 | EN ISO 3405 |
| Final boiling point [°C] | - | - | ≤ 370 | EN ISO 3405 |
| PAH [%m/m] | ≤ 11 | ≤ 11 | ≤ 11 | EN 12916 |
| Carbon residue [%m/m] | ≤ 0.3 | ≤ 0.3 | ≤ 0.3 | EN ISO 10370 |
| CFPP [°C]2 | -44 to +5 | -44 to +5 | -44 to +5 | EN 116 |
| Cloud Point [°C] (severe winter conditions)2 | -34 to -10 | -34 to -10 | -34 to -10 | EN 23015 |
| Copper strip corrosion (3h at 50°C) [rating] | Class 1 | EN ISO 2160 |
| Water [mg/kg] | ≤ 500 | ≤ 500 | ≤ 500 | EN ISO 12937 |
| Lubricity [micron] | ≤ 460 | ≤ 460 | ≤ 460 | EN ISO 12156-1 |
| Oxidation stability [hours] 3 | > 20 | > 20 | > 20 | EN15751 |
| FAME [%v/v] | 4 | 4 | 4 | EN14214 ASTM D6751 |
| Appearance | Clear and bright, no free water or particulates | D4176 visual inspection |
| Ethanol/Methanol [%v/v] | Non-detectable 5 |  |

1	Already agreed in annex to the Consolidated Resolution on the Construction of Vehicles (R.E.3) for on-road engines only. Industry recommends maximum 50 ppm sulphur.

2	Implementing country to choose value appropriate within range for arctic or severe winter conditions. More detailed arctic or severe winter specifications for these parameters to be considered.

3	Applicable for diesel containing more than 2 per cent v/v FAME.

4	Up to 5 per cent v/v FAME permitted if FAME complies with ASTM D6751. Up to 7 per cent v/v FAME permitted if FAME complies with EN14214. Industry recommends that vehicle owners refer to their vehicle handbook.

5	At or below detection limit of method used.

Annex 4 - Appendix 1

Evolution of the UNECE emission limits

Emission standards have been linked with a revision of the respective European market fuel standards (EN228 and EN590):

On-road standards

| UN Emission Levels | Gasoline | Diesel | Date of application |
| --- | --- | --- | --- |
|  | CO (g/km) | HC+NOx (HC/NOx) (g/km) | PM (g/km) | Fuel standard | CO (g/km) | HC+NOX (HC/NOx) (g/km) | PM (g/km) | Fuel standard |  |
| R83.03 | 2.2 | 0.5 | - | EN228: 1993 | 1.0 | 0.7 | 0.08 | EN590: 1993 | 1996 |
| R83.05 (level A) | 2.3 | 0.2 | 0.15 | - | EN228: 1999 | 0.64 | 0.50 | 0.05 | EN590: 2000 | 2000 |
| R83.05 (level B) | 1.0 | 0.1 | 0.08 | - | EN228: 2004 | 0.5 | 0.30 | 0.025 | EN590: 2004 | 2005 |
| R83.06 | 1.0 | 0.1 | 0.60 | 0.0045 | EN228: 2008 | 0.5 | 0.23 | 0.0045 | EN590: 2008 | 2009 |

| UN Emission Levels |  | Diesel | Date of application |
| --- | --- | --- | --- |
|  | CO (g/kWh) | NMHC (g/kWh) | THC (g/kWh) | NOx (g/kWh) | PM (g/kWh) | Fuel standard |  |
| R49.02 (level B) 1 | 4.0 | - | 1.1 | 7.0 | 0.15 | EN590: 1993 | 1995 |
| R49.03 (level A) 2 | 5.45 | 0.78 | 1.6 | 5.0 | 0.03 | EN590: 2000 | 2000 |
| R49.03 (level B1) 2 | 4.0 | 0.55 | 1.1 | 3.5 | 0.03 | EN590: 2004 | 2005 |
| R49.03 (level B2) 2 | 4.0 | 0.55 | 1.1 | 2.0 | 0.02 | EN590: 2008 | 2008 |

Limits shown for the 13-mode test.

2	Limits shown for the ETC test only.

Non-road standards

| UN Emission Levels | Power band | Net power (P) (kW) | CO (g/kWh) | HC (g/kWh) | NOx (g/kWh) | PM (g/kWh) | Date of application |
| --- | --- | --- | --- | --- | --- | --- | --- |
| R96 | A | P ≥ 130 | 5 | 1.3 | 9.2 | 0.54 | 1995 |
|  | B | 75 ≤ P < 130 | 5 | 1.3 | 9.2 | 0.7 |  |
|  | C | 37 ≤ P < 75 | 6.5 | 1.3 | 9.2 | 0.85 |  |
| R96.01 | E | 130 ≤P ≤560 | 3.5 | 1.0 | 6.0 | 0.2 | 2001 |
|  | F | 75 ≤ P < 130 | 5.0 | 1.0 | 6.0 | 0.3 |  |
|  | G | 37 ≤ P < 75 | 5.0 | 1.3 | 7.0 | 0.4 |  |
|  | D | 18 ≤ P < 37 | 5.5 | 1.5 | 8.0 | 0.8 |  |
| UN Emission Levels | Power band | Net power (P) (kW) | CO (g/kWh) | HC + NOx (g/kWh) | PM) (g/kWh) | Date of application |
| R96.02 | H | 130 ≤ P ≤ 560 | 3.5 | 4.0 | 0.2 | 2008 |
|  | I | 75 ≤ P < 130 | 5.0 | 4.0 | 0.3 |  |
|  | J | 37 ≤ P < 75 | 5.0 | 4.7 | 0.4 |  |
|  | K | 19 ≤ P < 37 | 5.5 | 7.5 | 0.6 |  |

Annex 4 - Appendix 2

Evolution of stringency of gasoline market fuel quality standards

On-road vehicles

| Gasoline | R83.03 | R83.05 (row A) | R83.05 (row B) |
| --- | --- | --- | --- |
| RON | 95 | 95 | 95 |
| MON | 85 | 85 | 85 |
| Lead | 0.013 | 0.005 | 0.005 |
| Sulphur | 500 | 150 | 50 / 10 |
| Benzene | 5 | 1 | 1 |
| Aromatics | - | 42 | 35 |
| Olefins | - | 21 | 18 |
| Oxygen | - | 2.7 | 2.7 |
| RVP | 35 - 100 | 45 - 100 | 45 - 100 |
| VLI | - | 1 050 – 1 250 | 1 050 – 1 250 |
| Density | 725 - 780 | 720 - 775 | 720 - 775 |
| FBP | 215 | 210 | 210 |
| E70 | 15 - 47 | 20 - 50 | 20 - 50 |
| E100 | 40 - 70 | 46 - 71 | 46 - 71 |
| E180 | 85 | - | - |
| Residue | 2 | 2 | 2 |

On-road vehicles

| Diesel | R83.03 R49.03 | R83.05 (level A) R49.05 (level A) | R83.05 (level B) R49.05 (level B1) |
| --- | --- | --- | --- |
| Cetane Number | 49 | 51 | 51 |
| Cetane Index | 46 | 46 | 46 |
| Sulphur | 500 | 350 | 50 / 10 |
| Density | 820 - 860 | 820 - 845 | 820 - 845 |
| Viscosity | 2.0 – 4.5 | 2.0 – 4.5 | 2.0 – 4.5 |
| T50 | Report | T65 = 250 min | T65 = 250 min |
| T85 | 350 max | 350 max | 350 max |
| T95 | 360 max | 360 max | 360 max |
| PAH | 11 | 11 | 11 |
| Flash Point | 55 | 55 | 55 |
| CCR | 0.3 | 0.3 | 0.3 |
| CFPP | -44 to +5 | -44 to +5 | -44 to +5 |
| Cloud Point | -34 to -10 | -34 to -10 | -34 to -10 |
| Water and sediment | - | 0.0024 | 0.0024 |
| Water | 0.02 | 0.02 | 0.02 |
| Ash | 0.01 | 0.01 | 0.01 |
| Lubricity | - | 460 | 460 |

Annex 4 - Appendix 3

Correlation between UN Regulations and Euro standards

On-road vehicles

Correlation between the series of amendments of Regulations Nos. 83 and 49 and Euro emission standards

| UN Regulation No. 49 | Euro standard |  | UN Regulation No. 83 | Euro standard |
| --- | --- | --- | --- | --- |
| R49.02 level B | Euro II |  | R83.03 | Euro 2 |
| R49.03 level A | Euro III |  | R83.05 level A | Euro 3 |
| R49.03 level B1 | Euro IV |  | R83.05 level B | Euro 4 |

Non-road vehicles

Correlation between the series of amendments to Regulation No. 96 and Euro emission standards

| UN Regulation No. 96 | NRMM Directive 97/68/EC |
| --- | --- |
| R96 | Stage I |
| R96.01 | Stage II |
| R96.02 | Stage IIIA |

Annex 4 - Appendix 4

Housekeeping

Some problems encountered by vehicles linked to fuel quality can be caused by adulteration of the fuel in the fuel distribution system, after the fuel has left the refinery gate. Failure to invest in adequate pipeline as well as storage facilities and failure to maintain the equipment can lead to volatility losses, fuel leakage, and contamination by particulates and water. These, in turn, can lead to many of the vehicle problems mentioned previously. Poor maintenance practices at the service station, such as too infrequent replacement of fuel dispenser filters or "dipping" of tanks to check for water, can magnify these problems, including corrosion problems within vehicles. CEN has issued a useful guideline document on good practice for fuel housekeeping: CEN TR/15367."

II.	Justification

1.	The objective of this document is to provide recommendations for the minimum quality of market fuels (i.e. gasoline and diesel) that should be introduced in parallel, and at the same time, with the corresponding emissions standards.  They complement the motor vehicle and NRMM pollutant emission standards that a country or a region may be considering to introduce.

2.	Considering that the current Annex 4 of the Consolidated Resolution on the Construction of Vehicles (R.E.3) set basic recommendations (concerning lead and sulphur in gasoline and sulphur, ash and total contamination in diesel), an additional set of fuel parameters is proposed, to impact:

(a)	the performance and durability of engines and emission control equipment and;

(b)	the parameters that have an impact on human health and the environment, should 	now be included.

3.	For the purpose of these recommendations, the motor vehicle and NRMM pollutant emissions standards are those identified in the various series of amendments to UN Regulations Nos. 83, 49 and 96.

4.	Earlier series of these UN Regulations on engine pollutant emissions may already have been implemented by many countries and such countries may now be considering strengthening their pollutant emission standards. Other countries may be considering, for the first time, introducing such pollutant emission regulations.

5.	Countries or regions that have, so far, not implemented a well-formulated relationship between pollutant emissions standards and high quality market fuels are the focus of these recommendations.

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.

For the EU, maximum 10 ppm sulphur content is mandatory since 1 January 2009.

For the EU, maximum 10 ppm sulphur content is mandatory since 1 January 2009.

See Annex C for the correlation between the series of amendments to UN Regulations Nos. 83, 49 and 96 and the respective European emission standards.

See Appendix 3 to Annex 4 for the correlation between the series of amendments to UN Regulations Nos. 83, 49 and 96 and the respective European emission standards.