Proposal for amendments to ECE/TRANS/WP.29/GRSG/2015/8

Proposal for the 02 Series of amendments to Regulation No. 125 (Forward field of vision of drivers)

The modifications to the ECE/TRANS/WP.29/GRSG/2015/8 are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 5.1.3., amend to read:

"5.1.3.	Except as provided in paragraph 5.1.3.1. or 5.1.3.2., other than the obstructions created by the A pillars, the fixed or movable vent or side window division bars, outside radio aerials, regulated devices for indirect vision and windscreen wipers, there should be no obstruction in the driver's 180° forward direct field of vision below a horizontal plane passing through V1, and above three planes through V2, one being perpendicular to the plane X-Z and declining forward 4° below the horizontal, and the other two being perpendicular to the plane Y-Z and declining 4° below the horizontal (see Annex 4, Appendix, Figure 4).

…"

II.	Justification

- The original proposal amends the provisions on forward field of vision of drivers in Regulation No. 125 to promote and to support the installation of camera-monitor devices on vehicles of category M1.

- This proposal aims at clarifying that only the devices for indirect vision which are regulated shall benefit of this promotion.

__________