Modifications to Annex 1 of the draft Resolution on the common specification of light source categories (ECE/TRANS/WP.29/GRE/2015/28)

Annex 1

Sheets for filament light sources

List of sheets for filament light sources and their sequence in this annex:

| Sheet number(s) |  |
| --- | --- |
| C5W/1 |  |
| C21W/1 to 2 |  |
| H1/1 to 3 |  |
| H3/1 to 4 |  |
| H4/1 to 5 |  |
| H7/1 to 4 |  |
| H8/1 to 4 |  |
| H9/1 to 4 |  |
| H10/1 to 3 |  |
| H11/1 to 4 |  |
| H12/1 to 3 |  |
| H13/1 to 4 |  |
| H14/1 to 4 |  |
| H15/1 to 5 |  |
| H16/1 to 4 |  |
| H17/1 to 6 |  |
| H18/1 to 4 |  |
| H19/1 to 5 |  |
| H20/1 to 4 |  |
| H6W/1 |  |
| H10W/1 to 2 |  |
| H21W/1 to 2 |  |
| H27W/1 to 3 |  |
| HB3/1 to 4 |  |
| HB4/1 to 4 |  |
| HIR1/1 to 3 |  |
| HIR2/1 to 3 |  |
| HS1/1 to 5 |  |
| HS2/1 to 3 |  |
| HS5/1 to 4 |  |
| HS5A/1 to 3 |  |
| HS6/1 to 4 |  |
| P13W/1 to 3 |  |
| P19W/1 to 3 |  |
| P21W/1 to 2 |  |
| P21/4W/1 |  |
| P21/5W/1 to 3 |  |
| P24W/1 to 3 |  |
| P27W/1 to 2 |  |
| P27/7W/1 to 3 |  |
| PC16W/1 to 3 |  |
| PR21W/1 |  |
| PR21/4W/1 |  |
| PR21/5W/1 |  |
| PR27/7W/1 |  |
| PSX26W/1 to 3 |  |
| PY21W/1 |  |
| PY21/5W/1 to 3 |  |
| PY27/7W/1 |  |
| R2/1 to 3 |  |
| R5W/1 |  |
| R10W/1 |  |
| S1/S2/1 to 2 |  |
| S3/1 |  |
| T1.4W/1 |  |
| T4W/1 |  |
| W2.3W/1 |  |
| W3W/1 |  |
| W5W/1 |  |
| W10W/1 |  |
| W15/5W/1 to 3 |  |
| W16W/1 |  |
| W21W/1 to 2 |  |
| W21/5W/1 to 3 |  |
| WP21W/1 to 2 |  |
| WR21/5W/1 |  |
| WT21W/1 to 2 |  |
| WT21/7W/1 to 3 |  |
| WY2.3W/1 |  |
| WY21W/1 to 2 |  |

Category C5W	Sheet C5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| b 1/ | 34.0 | 35.0 | 36.0 | 35.0 ( 0.5 |
| f 2/,3/ | 7.5 4/ |  | 15 5/ | 9 ( 1.5 |
| Cap SV8.5 in accordance with IEC Publication 60061 (sheet 7004-81-4) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 5 | 5 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 5.5 max. | 7.7 max. | 5.5 max. |
|  | Luminous flux | 45 ( 20 % |  |
| Reference luminous flux: 45 lm at approximately 13.5 V |

1/	This dimension corresponds to a distance between two apertures of 3.5 mm diameter each bearing against one of the caps.

2/	The filament shall be housed in a cylinder 19 mm long co-axial with the filament light source and placed symmetrically about the filament light source centre. 
The diameter of the cylinder is for 6 V and 12 V filament light sources: d + 4 mm (for standard filament light sources: d + 2 mm) and for 24 V filament light sources: d + 5 mm, "d" being the nominal diameter of the filament as stated by the manufacturer.

3/	The deviation of the filament centre from the centre of the filament light source shall not be more than ±2.0 mm (for standard filament light sources: ±0.5 mm) measured in the direction of the reference axis.

4/	4.5 mm for 6 V filament light sources.

5/	16.5 mm for 24 V filament light sources.

Category C21W	Sheet C21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| b 1/ | 40.0 | 41.0 | 42.0 | 41.0 ( 0.5 |
| f 2/ | 7.5 |  | 10.5 | 8 ( 1.0 |
| Cap SV8.5 in accordance with IEC Publication 60061 (sheet 7004-81-4) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 26.5 max. |
|  | Luminous flux | 460 ( 15 % |  |
| Reference luminous flux: 460 lm at approximately 13.5 V |

1/	This dimension corresponds to a distance between two apertures of 3.5 mm diameter.

2/	The position of the filament is checked by means of a "Box system"; sheet C21W/2.

Category C21W	Sheet C21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and to the centre of the filament light source's length, whether a filament light source complies with the requirements.

| 12 V | a | h | k |
| --- | --- | --- | --- |
| Filament light sources of normal production | 4.0 + d | 14.5 | 2.0 |
| Standard filament light source | 2.0 + d | 14.5 | 0.5 |

d = nominal filament diameter as stated by the manufacturer.

Test procedure and requirements

1.	The filament light source is placed in a holder (socket) capable of being so rotated through 360° about the reference axis that the front elevation is seen on the screen on to which the image of the filament is projected. The reference plane on the screen shall coincide with the centre of the filament light source. The central axis sought on the screen shall coincide with the centre of the filament light source length.

2.	Front elevation

2.1.	The projection of the filament shall lie entirely within the rectangle when the filament light source is rotated through 360°.

2.2.	The centre of the filament shall not be offset by more than distance "k" from the central axis sought.

Category H1 	Sheet H1/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference axis is perpendicular to the reference plane and passes through the point defined by the dimensions marked with 1.

2/	Both current lead-in legs shall be positioned in the bulb, the longer leg above the filament (the filament light source being viewed as shown in the figure). The internal design should be then such that stray light images and reflections are reduced to the minimum, e.g. by fitting cooling jackets over the non-coiled parts of the filament.

3/	The cylindrical portion of the bulb over length "f" shall be such as not to deform the projected image of the filament to such an extent as appreciably to affect the optical results.

4/	The colour of the light emitted shall be white or selective-yellow.

Category H1 	Sheet H1/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 6 V | 12 V | 24 V | 12 V |
| e 6/,10/ | 25.0 9/ | 25.0 ( 0.15 |
| f 6/,10/ | 4.5 ( 1.0 | 5.0 ( 0.5 | 5.5 ( 1.0 | 5.0 + 0.50 / -0.00 |
| g 7/,8/ | 0.5 d ( 0.5 d | 0.5 d ( 0.25 d |
| h1 | 9/ | 0 ( 0.20 5/ |
| h2 | 9/ | 0 ( 0.25 5/ |
| ( | 45( ( 12( | 45( ( 3( |
| Cap P14.5s in accordance with IEC Publication 60061 (sheet 7004-46-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 55 | 70 | 55 |
| Test Voltage | Volts | 6.3 | 13.2 | 28.0 | 13.2 |
| Objective values | Watts | 63 max. | 68 max. | 84 max. | 68 max. |
|  | Luminous flux ( % | 1,350 | 1,550 | 1,900 |  |
|  |  | 15 |  |
| Reference luminous flux at approximately | 12 V | 1,150 |
|  | 13.2 V | 1,550 |

5/	The eccentricity is measured only in the horizontal and vertical directions of the filament light source as shown in the figure. The points to be measured are those where the projections of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

6/	The viewing direction is the perpendicular to the reference axis contained in the plane defined by the reference axis and the centre of the second pin of the cap.

7/	Offset of filament in relation to bulb axis measured at 27.5 mm from the reference plane.

8/	d: diameter of filament.

9/	To be checked by means of a "Box system", sheet H1/3.

10/	The ends of the filament are defined as the points where, when the viewing direction is as defined in footnote 6/ above, the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the reference axis (special instructions for coiled-coil filaments are under consideration).

Category H1 	Sheet H1/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 6 V | 1.4d | 1.9 d | 0.25 | 6 | 3.5 |
| 12 V |  |  |  | 6 | 4.5 |
| 24 V |  |  |  | 7 | 4.5 |

d = diameter of filament.

The filament position is checked solely in directions A and B as shown on sheet H1/1.

The filament shall lie entirely within the limits shown.

The beginning of the filament as defined on sheet H1/2, footnote 10/, shall lie between lines Z1 and Z2.

Category H3 	Sheet H3/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The colour of the light emitted shall be white or selective-yellow.

2/	Minimum length above the height of the light emitting centre ("e") over which the bulb shall be cylindrical.

3/	The distortion of the base-end portion of the bulb shall not be visible from any direction outside the obscuration angle of 80° max. The shields shall produce no inconvenient reflections. The angle between the reference axis and the plane of each shield, measured on the bulb side, shall not exceed 90°.

Category H3 	Sheet H3/2

4/	The permissible deviation of the ring centre from the reference axis is 0.5 mm in the direction perpendicular to the Z-Z line and 0.05 mm in the direction parallel to the Z-Z line.

5/	The cap shall be pressed in these directions.

Category H3 	Sheet H3/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 6 V | 12 V | 24 V | 12 V |
| e | 18.0 6/ | 18.0 |
| f 8/ | 3.0 min. | 4.0 min. | 5.0 ( 0.50 |
| k | 0 6/ | 0 ( 0.20 |
| h1, h3 | 0 6/ | 0 ( 0.15 7/ |
| h2, h4 | 0 6/ | 0 ( 0.25 7/ |
| Cap PK22s in accordance with IEC Publication 60061 (sheet 7004-47-4) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 55 | 70 | 55 |
| Test voltage | Volts | 6.3 | 13.2 | 28.0 | 13.2 |
| Objective values | Watts | 63 max. | 68 max. | 84 max. | 68 max. |
|  | Luminous flux ( % | 1,050 | 1,450 | 1,750 |  |
|  |  | 15 |  |
| Reference luminous flux at approximately | 12 V | 1,100 |
|  | 13.2 V | 1,450 |

6/	To be checked by means of a "Box system"; sheet H3/4.

7/	For standard filament light sources the points to be measured are those where the projection of the outside of the end turns crosses the filament axis.

8/	The positions of the first and the last turn of the filament are defined by the intersections of the outside of the first and of the last light emitting turn, respectively, with the plane parallel to and 18 mm distant from the reference plane. (Additional instructions for coiled-coil filament are under consideration).

Category H3 	Sheet H3/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament complies with the requirements.

|  | a | c | k | g |
| --- | --- | --- | --- | --- |
| 6 V | 1.8 d | 1.6 d | 1.0 | 2.0 |
| 12 V |  |  |  | 2.8 |
| 24 V |  |  |  | 2.9 |

d = diameter of filament

The filament shall lie entirely within the limits shown.

The centre of the filament shall lie within the limits of dimension k.

Category H4	Sheet H4/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane formed by the seating points of the three lugs of the cap ring.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of the circle of diameter "M".

3/	The colour of the light emitted shall be white or selective-yellow.

4/	The bulb and supports shall not exceed the envelope as in Figure 2. However, where a selective-yellow outer bulb is used the bulb and supports shall not exceed the envelope as in Figure 3.

5/	The obscuration shall extend at least as far as the cylindrical part of the bulb. It shall also overlap the internal shield when the latter is viewed in a direction perpendicular to the reference axis.

Category H4	Sheet H4/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 24 V | 12 V |
| e | 28.5 +0.35/-0.25 | 29.0 ( 0.35 | 28.5 + 0.20 / -0.00 |
| p | 28.95 | 29.25 | 28.95 |
| ( | max. 40° | max. 40° |
| Cap P43t in accordance with IEC Publication 60061 (sheet 7004-39-6) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 6/ | 24 6/ | 12 6/ |
|  | Watts | 60 | 55 | 75 | 70 | 60 | 55 |
| Test voltage | Volts | 13.2 | 28.0 | 13.2 |
| Objective values | Watts | 75 max. | 68 max. | 85 max. | 80 max. | 75 max. | 68 max. |
|  | Luminous flux ( % | 1,650 | 1,000 | 1,900 | 1,200 |  |
|  |  | 15 |  |
| Measuring flux 7/ lm | - | 750 | - | 800 |  |
| Reference luminous flux at approximately | 12 V | 1,250 | 750 |
|  | 13.2 V | 1,650 | 1,000 |

6/	The value indicated in the left hand column relate to the driving-beam filament. Those indicated in the right-hand column relate to the passing-beam filament.

7/	Measuring luminous flux according to the provisions for filament light sources with an internal shield to produce the cut-off.

Category H4	Sheet H4/3

Category H4	Sheet H4/4

# Table of the dimensions (in mm) referred to in the drawings on sheet H4/3

| Reference* | Dimension** | Tolerance |
| --- | --- | --- |
|  |  | Filament light sources of normal production | Standard filament light source |
| 12 V | 24 V | 12 V | 24 V | 12 V | 24 V | 12 V |
| a/26 | 0.8 | (0.35 | (0.20 |
| a/23.5 | 0.8 | (0.60 | (0.20 |
| b1/29.5 | 30.0 | 0 | (0.30 | (0.35 | (0.20 |
| b1/33 | b1/29.5 mv | b1/30.0 mv | (0.30 | (0.35 | (0.15 |
| b2/29.5 | 30.0 | 0 | (0.30 | (0.35 | (0.20 |
| b2/33 | b2/29.5 mv | b2/30.0 mv | (0.30 | (0.35 | (0.15 |
| c/29.5 | 30.0 | 0.6 | 0.75 | (0.35 | (0.20 |
| c/33 | c/29.5 mv | c/30.0 mv | (0.35 | (0.15 |
| d | min. 0.1 | - | - |
| e 13/ | 28.5 | 29.0 | +0.35 -0.25 | (0.35 | +0.20 -0.00 |
| f 11/,12/,13/ | 1.7 | 2.0 | +0.50 -0.30 | (0.40 | +0.30 -0.10 |
| g/26 | 0 | (0.50 | (0.30 |
| g/23.5 | 0 | (0.70 | (0.30 |
| h/29.5 | 30.0 | 0 | (0.50 | (0.30 |
| h/33 | h/29.5 mv | h/30.0 mv | (0.35 | (0.20 |
| IR 11/,14/ | 4.5 | 5.25 | (0.80 | (0.40 |
| IC 11/,14/ | 5.5 | 5.25 | (0.50 | (0.80 | (0.35 |
| p/33 | Depends on the shape of the shield | - | - |
| q/33 | (p+q)/2 | (0.60 | (0.30 |

*	"../26" means dimension to be measured at the distance from the reference plane indicated in mm after the stroke.

**	"29.5 mv" or "30.0 mv" means the value measured at a distance of 29.5 or 30.0 mm from the reference plane.

Category H4	Sheet H4/5

8/	Plane V-V is the plane perpendicular to the reference plane and passing through the reference axis and through the intersection of the circle of diameter "M" with the axis of the reference lug.

9/	Plane H-H is the plane perpendicular to both the reference plane and plane V-V and passing through the reference axis.

10/	30.0 mm for the 24-volt type.

11/	The end turns of the filament are defined as being the first luminous turn and the last luminous turn that are at substantially the correct helix angle. For coiled-coil filaments, the turns are defined by the envelope of the primary coil.

12/	For the passing-beam filament, the points to be measured are the intersections, seen in direction 1, of the lateral edge of the shield with the outside of the end turns defined under footnote 11/.

13/	"e" denotes the distance from the reference plane to the beginning of the passing-beam filament as defined above.

14/	For the driving-beam filament the points to be measured are the intersections, seen in direction 1, of a plane, parallel to plane H-H and situated at a distance of 0.8 mm below it, with the end turns defined under footnote 11/.

Additional explanations to sheet H4/3

The dimensions below are measured in three directions:

1	For dimensions a, b1, c, d, e, f, IR and IC;

2	For dimensions g, h, p and q;

3	For dimension b2.

Dimensions p and q are measured in planes parallel to and 33 mm away from the reference plane.

Dimensions b1, b2, c and h are measured in planes parallel to and 29.5 mm 
(30.0 mm for 24 V filament light sources) and 33 mm away from the reference plane.

Dimensions a and g are measured in planes parallel to and 26.0 mm and 23.5 mm away from the reference plane.

Note: For the method of measurement, see Appendix E of IEC Publication 60809.

Category H7 	Sheet H7/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is defined by the points on the surfaces of the holder on which the three supporting bosses of the cap ring will rest.

2/	The reference axis is perpendicular to the reference plane and crosses the intersection of the two perpendiculars as indicated in Figure 3.

3/	The colour of the light emitted shall be white or selective-yellow.

4/	Notes concerning the filament diameter.

(a)	No actual diameter restrictions apply but the objective for future developments is to have d max. = 1.3 mm for 12 V and d max. = 1.7 for 24 V filament light sources.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

5/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

Category H7 	Sheet H7/2

6/	Glass bulb shall be optically distortion free within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2.

7/	The obscuration shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall moreover extend at least to a plane parallel to the reference plane where (3 crosses the outer bulb surface (view B as indicated on sheet H7/1).

8/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction. (View A as indicated in Figure 1 on sheet H7/1).

No metal parts other than filament turns shall be located in the shaded area as seen in Figure 5.

Category H7 	Sheet H7/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 24 V | 12 V |
| e 9/ | 25.0 10/ | 25.0 ( 0.1 |
| f 9/ | 4.1 10/ | 4.9 10/ | 4.1 ( 0.1 |
| g 12/ | 0.5 min. | u.c. |
| h1 11/ | 0 10/ | 0 ( 0.10 |
| h2 11/ | 0 10/ | 0 ( 0.15 |
| (1 | 40° min. | 40° min. |
| (2 | 50° min. | 50° min. |
| (3 | 30° min. | 30° min. |
| Cap PX26d in accordance with IEC Publication 60061 (sheet 7004-5-7) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 55 | 70 | 55 |
| Test voltage | Volts | 13.2 | 28.0 | 13.2 |
| Objectivevalues | Watts | 58 max. | 75 max. | 58 max. |
|  | Luminous flux | 1,500 ( 10 % | 1,750 ( 10 % |  |
| Reference luminous flux at approximately | 12 V | 1,100 |
|  | 13.2 V | 1,500 |

9/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown in Figure 1 on sheet H7/1, the projection of the outside of the end turns crosses the filament axis. (Special instructions for coiled-coil filaments are under consideration).

10/	To be checked by means of a "Box system", sheet H7/4.

11/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 in sheet H7/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

12/	Offset of filament in relation to bulb axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Category H7 	Sheet H7/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

Dimensions in mm

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 12 V | d + 0.30 | d + 0.50 | 0.2 | 4.6 | 4.0 |
| 24V | d + 0.60 | d + 1.00 | 0.25 | 5.9 | 4.4 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H7/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H7/3, footnote 9/, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Categories H8 and H8B 	Sheet H8/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane formed by the underside of the bevelled lead-in flange of the cap.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 19 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

4/	The colour of the light emitted shall be white or selective-yellow.

5/	Notes concerning the filament diameter.

(a) 	No actual diameter restrictions apply but the objective for future developments is to have d max. = 1.2 mm.

(b) 	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

Categories H8 and H8B 	Sheet H8/2

6/	Glass bulb shall be optically distortion free within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

7/	The obscuration shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall moreover extend at least to a plane parallel to the reference plane where (3 crosses the outer bulb surface (view B as indicated on sheet H8/1).

8/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction. (View A as indicated in Figure 1 on sheet H8/1). No metal parts other than filament turns shall be located in the shaded area as seen in Figure 4.

9/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 in sheet H8/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

10/	Offset of filament in relation to bulb axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Categories H8 and H8B 	Sheet H8/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e 11/ | 25.0 12/ | 25.0 ( 0.1 |
| f 11/ | 3.7 12/ | 3.7 ( 0.1 |
| g | 0.5 min. | u.c. |
| h1 | 0 12/ | 0 ( 0.1 |
| h2 | 0 12/ | 0 ( 0.15 |
| (1 | 50° min. | 50° min. |
| (2 | 40° min. | 40° min. |
| (3 | 30° min. | 30° min. |
| Cap: | H8: PGJ19-1 H8B: PGJY19-1 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 35 | 35 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 43 max. | 43 max. |
|  | Luminous flux | 800 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 600 |
|  | 13.2 V | 800 |

11/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown in Figure 1 on sheet H8/1, the projection of the outside of the end turns crosses the filament axis.

12/	To be checked by means of a "Box system"; sheet H8/4.

Categories H8 and H8B 	Sheet H8/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament complies with the requirements.

| a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| d + 0.50 | d + 0.70 | 0.25 | 4.6 | 3.5 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H8/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H8/3, footnote 11/, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Categories H9 and H9B	Sheet H9/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane formed by the underside of the bevelled lead-in flange of the cap.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 19 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

4/	Notes concerning the filament diameter:

(a)	No actual diameter restrictions apply but the objective for future developments is to have d max. = 1.4 mm.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

Categories H9 and H9B 	Sheet H9/2

5/	Glass bulb shall be optically distortion free within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2.

6/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction. (View A as indicated in Figure 1, sheet H9/1).  No metal parts other than filament turns shall be located in the shaded area as seen in Figure 4.

7/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 on sheet H9/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

8/	Offset of filament in relation to bulb axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Categories H9 and H9B 	Sheet H9/3

| Dimensions in mm | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
|  | 12 V | 12 V |
| e 9/,10/ | 25 | 11/ | (0.10 |
| f 9/,10/ | 4.8 | 11/ | (0.10 |
| g 9/ | 0.7 | (0.5 | (0.30 |
| h1 | 0 | 11/ | (0.10 12/ |
| h2 | 0 | 11/ | (0.15 12/ |
| (1 | 50° min. | - | - |
| (2 | 40° min. | - | - |
| Cap: | H9: PGJ19-5 H9B: PGJY19-5 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 65 | 65 |
| Test voltage | Volts | 13.2 | 12.2 | 13.2 | 12.2 |
| Objective values | Watts | 73 max. | 65 max. | 73 max. | 65 max. |
|  | Luminous flux | 2,100 ( 10 % | 1,650 ( 10 % |  |
| Reference luminous flux at approximately | 12 V | 1,500 |
|  | 12.2 V | 1,650 |
|  | 13.2 V | 2,100 |

9/	The viewing direction is direction A as shown in Figure 1 on sheet H9/1.

10/	The ends of the filament are defined as the points where, when the viewing direction is as defined in footnote 9/ above, the projection of the outside of the end turns crosses the filament axis.

11/	To be checked by means of a "Box system"; sheet H9/4.

12/	The eccentricity is measured only in viewing directions A and B as shown in Figure 1 on sheet H9/1. The points to be measured are those where the projection of the outside of the end turns nearest or furthest from the reference plane crosses the filament axis.

Categories H9 and H9B	Sheet H9/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament complies with the requirements.

| a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| d + 0.4 | d + 0.7 | 0.25 | 5.7 | 4.6 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H9/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H9/3, footnote 10/, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Category H10	Sheet H10/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane defined by the meeting points of cap-holder fit.

2/	The reference axis is perpendicular to the reference plane and concentric with the reference diameter of the cap.

3/	Glass bulb and supports shall not exceed the envelope and shall not interfere with insertion past the filament light source key. The envelope is concentric to the reference axis.

4/	The keyway is mandatory.

5/	The filament light source shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

6/	Glass bulb periphery shall be optically distortion-free axially and cylindrically within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2 and does not need to be verified in the area covered by the obscuration.

7/	The obscuration shall extend to at least angle (3 and shall be at least as far as the undistorted part of the bulb defined by angle (1.

Category H10	Sheet H10/2

| Dimensions in mm 8/ | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| e 9/,10/ | 28.9 | 11/ | (0.16 |
| f 9/,10/ | 5.2 | 11/ | (0.16 |
| h1, h2 | 0 | 11/ | (0.15 12/ |
| (1 | 50° min. | - | - |
| (2 | 52° min. | - | - |
| (3 | 45° | (5° | (5° |
| Cap PY20d in accordance with IEC Publication 60061 (sheet 7004-31-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 42 | 42 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 50 max. | 50 max. |
|  | Luminous flux | 850 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 600 |
|  | 13.2 V | 850 |

8/	Dimensions shall be checked with O-ring removed.

9/	The viewing direction is direction* B as shown in the figure on sheet H10/1.

10/	The ends of the filament are defined as the points where, when the viewing direction* as defined in footnote 9/ above, the projection of the outside of the end turns crosses the filament axis.

11/	To be checked by means of a "Box system", sheet H10/3*.

12/	The eccentricity is measured only in viewing directions* A and B as shown in the figure on sheet H10/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

*	Manufacturers may choose another set of perpendicular viewing directions. The viewing directions specified by the manufacturer are to be used by the testing laboratory when checking filament dimensions and position.

Category H10	Sheet H10/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 12 V | 1.4 d | 1.8 d | 0.25 | 6.1 | 4.9 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H10/1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H10/2 footnote 10/ shall lie between lines Z1 and Z2 and between lines Z3 and Z4.

Categories H11 and H11B	Sheet H11/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane formed by the underside of the bevelled lead-in flange of the cap.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 19 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

4/	The colour of the light emitted shall be white or selective-yellow.

5/	Notes concerning the filament diameter.

(a)	No actual diameter restrictions apply but the objective for future developments is to have d max. = 1.4 mm.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

Categories H11 and H11B 	Sheet H11/2

6/	Glass bulb shall be optically distortion free within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2.

7/	The obscuration shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall, moreover, extend at least to a plane parallel to the reference plane where (3 crosses the outer bulb surface (view B as indicated on sheet H11/1).

8/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction (view A as indicated in Figure 1 on sheet H11/1).  No metal parts other than filament turns shall be located in the shaded area as seen in Figure 4.

9/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 on sheet H11/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

10/	Eccentricity of bulb axis with respect to filament axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Categories H11 and H11B 	Sheet H11/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 24 V | 12 V |
| e 11/ | 25.0 12/ | 25.0 ( 0.1 |
| f 11/ | 4.5 | 5.3 12/ | 4.5 ( 0.1 |
| g | 0.5 min. | u.c. |
| h1 | 0 12/ | 0 ( 0.1 |
| h2 | 0 12/ | 0 ( 0.15 |
| (1 | 50° min. | 50° min. |
| (2 | 40° min. | 40° min. |
| (3 | 30° min. | 30° min. |
| Cap: | H11: PGJ19-2 H11B: PGJY19-2 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 55 | 70 | 55 |
| Test voltage | Volts | 13.2 | 28.0 | 13.2 |
| Objective values | Watts | 62 max. | 80 max. | 62 max. |
|  | Luminous flux | 1,350 ( 10 % | 1,600 ( 10 % |  |
| Reference luminous flux at approximately | 12 V | 1,000 |
|  | 13.2 V | 1,350 |

11/	The ends of the filament are defined as the points where, when the viewing direction is View A as shown in Figure 1 on sheet H11/1, the projection of the outside of the end turns crosses the filament axis.

12/	To be checked by means of a "Box system"; sheet H11/4.

Categories H11 and H11B 	Sheet H11/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament complies with the requirements.

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 12 V | d + 0.3 | d + 0.5 | 0.2 | 5.0 | 4.0 |
| 24 V | d + 0.6 | d + 1.0 | 0.25 | 6.3 | 4.6 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H11/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H11/3, footnote 11/, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Category H12	Sheet H12/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane defined by the meeting points of cap-holder fit.

2/	The reference axis is perpendicular to the reference plane and concentric with the reference diameter of the cap.

3/	Glass bulb and supports shall not exceed the envelope and shall not interfere with insertion past the filament light source key. The envelope is concentric to the reference axis.

4/	The keyway is mandatory.

5/	The filament shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

6/	Glass bulb periphery shall be optically distortion-free axially and cylindrically within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2 and does not need to be verified in the area covered by the obscuration.

7/	The obscuration shall extend to at least angle (3 and shall be at least as far as the undistorted part of the bulb defined by angle (1.

Category H12	Sheet H12/2

| Dimensions in mm 8/ | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| e 9/,10/ | 31.5 | 11/ | (0.16 |
| f 9/,10/ | 5.5 | 4.8 min | (0.16 |
| h1, h2, h3, h4 | 0 | 11/ | (0.15 12/ |
| k | 0 | 11/ | (0.15 13/ |
| (1 | 50° min. | - | - |
| (2 | 52° min. | - | - |
| (3 | 45° | (5° | (5° |
| Cap PZ20d in accordance with IEC Publication 60061 (sheet 7004-31-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 53 | 53 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 61 max. | 61 max. |
|  | Luminous flux | 1,050 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 775 |
|  | 13.2 V | 1,050 |

8/	Dimensions shall be checked with O-ring removed.

9/	The viewing direction is direction A as shown in the figure on sheet H12/1.

10/	The ends of the filament are defined as the points where, when the viewing direction as defined in footnote 9/ above, the projection of the outside of the end turns crosses the filament axis.

11/	To be checked by means of a "Box system"; sheet H12/3.

12/	Dimensions h1 and h2 are measured in viewing direction A, dimension h3 in direction C and dimension h4 in direction B as shown in the figure on sheet H12/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

13/	Dimension k is measured only in viewing direction A.

Category H12	Sheet H12/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

| a1 | a2 | b1 | b2 | c |
| --- | --- | --- | --- | --- |
| 1.6 d | 1.3 d | 0.30 | 0.30 | 2.8 |

d = diameter of filament

For the directions of view A, B and C, see sheet H12/1.

The filament shall lie entirely within the limits shown.

The centre the filament shall lie between the limits of dimensions b1 and b2.

Categories H13 and H13A 	Sheet H13/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

# Figure 1 - Main drawing

1/	The reference plane is the plane formed by the underside of the three radiused tabs of the cap.

2/	The reference axis is perpendicular to the reference plane and crosses the intersection of the two perpendiculars as indicated in Figure 2 on sheet H13/2.

3/	Glass bulb and supports shall not exceed the envelope as indicated.  The envelope is concentric to the reference axis.

4/	The filament light source shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

5/	Plane V-V is the plane perpendicular to the reference plane passing through the reference axis and parallel to plane C.

Categories H13 and H13A 	Sheet H13/2

6/	Glass bulb shall be optically distortion-free axially and cylindrically within the angles ( and (.  This requirement applies to the whole bulb circumference within the angles ( and ( and does not need to be verified in the area covered by the opaque coating.

7/	The opaque coating shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall moreover extend at least to a plane parallel to the reference plane where γ crosses the outer bulb surface (view B as indicated on sheet H13/1).

8/	Offset of passing-beam filament in relation to the bulb axis is measured in two planes parallel to the reference plane where the projection of the outside end turns nearest to and farthest from the reference plane crosses the passing-beam filament axis.

9/	Light shall be blocked over the cap end of the bulb extending to angle (.  This requirement applies in all directions around the reference axis.

Categories H13 and H13A 	Sheet H13/3

10/	Dimensions j, k and p are measured from the centre of the passing-beam filament to the centre of the driving-beam filament.

11/	Dimensions m and n are measured from the reference axis to the centre of the passing-beam filament.

12/	Both filaments axis are to be held within a 2( tilt with respect to the reference axis about the centre of the respective filament.

13/	Note concerning the filament diameters.

(a)	For the same manufacturer, the design filament diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

14/	For both the driving-beam and the passing-beam filament distortion shall not exceed (5 per cent of filament diameter from a cylinder.

15/	The metal free zone limits the location of lead wires within the optical path.  No metal parts shall be located in the shaded area as seen in Figure 6.

Categories H13 and H13A 	Sheet H13/4

| Dimensions in mm | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| d1 13/, 17/ | 1.8 max. | - | - |
| d2 13/, 17/ | 1.8 max. | - | - |
| e 16/ | 29.45 | (0.20 | (0.10 |
| f 1 16/ | 4.6 | (0.50 | (0.25 |
| f 2 16/ | 4.6 | (0.50 | (0.25 |
| g 8/, 17/ | 0.5 d1 | (0.40 | (0.20 |
| h 8/ | 0 | (0.30 | (0.15 |
| j 10/ | 2.5 | (0.20 | (0.10 |
| k 10/ | 2.0 | (0.20 | (0.10 |
| m 10/ | 0 | (0.20 | (0.13 |
| n 10/ | 0 | (0.20 | (0.13 |
| p 10/ | 0 | (0.08 | (0.08 |
| ( | 42° min. | - | - |
| ( | 52° min. | - | - |
| ( | 43° | +0° / -5° | +0° / -5° |
| ( 9/ | 41° | (4° | (4° |
| Cap: | H13: P26.4t H13A: PJ26.4t | in accordance with IEC Publication 60061 (sheet 7004-128-3) |
| Electrical and photometric characteristics 18/ |
| Rated values | Volts | 12 | 12 |
|  | Watts | 55 | 60 | 55 | 60 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 68 max. | 75 max. | 68 max. | 75 max. |
|  | Luminous flux | 1,100 ( 15 % | 1,700 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 800 | 1,200 |
|  | 13.2 V | 1,100 | 1,700 |

16/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown on sheet H13/1, the projection of the outside of the end turns crosses the filament axis.

17/	d1 is the actual diameter of the passing-beam filament. d2 is the actual diameter of the driving-beam filament.

18/	The values indicated in the left-hand columns relate to the passing-beam filament and those indicated in the right-hand columns to the driving-beam filament.

Category H14	Sheet H14/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the points on the surface of the holder on which the three lugs of the cap ring will rest.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the cap ring diameter "M'"

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2.  The envelope is concentric to the reference axis.

Category H14	Sheet H14/2

4/	Glass bulb shall be optically distortion free within the angles (1 and (2 .  This requirement applies to the whole bulb circumference within the angles (1 and (2 and does not need to be verified in the area covered by the obscuration.

5/	The obscuration shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall, moreover, extend at least to a plane parallel to the reference plane where (3 crosses the outer bulb surface (view B as indicated on sheet H14/1).

6/	Eccentricity of bulb with respect to passing-beam filament axis is measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the passing-beam filament axis.

7/	The offset of the filaments with respect to the reference axis is measured only in viewing direction A, B and C as shown in Figure 1 on sheet H14/1.  The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filaments axis.

Category H14	Sheet H14/3

| Dimensions in mm | Filament light source of normal production | Standard filament light sources |
| --- | --- | --- |
| e 8/ | 26.15 | 10/ | ±0.1 |
| f1 8/,9/ | 5.3 | 10/ | ±0.1 |
| f2 8/,9/ | 5.0 | 10/ | ±0.1 |
| g | 0.3 min. |  |  |
| h1 | 0 | 10/ | ±0.1 |
| h2 | 0 | 10/ | ±0.15 |
| h3 | 0 | 10/ | ±0.15 |
| h4 | 0 | 10/ | ±0.15 |
| i | 2.7 |  | - |
| j | 2.5 | 10/ | ±0.1 |
| (1 | 55° min. | - | - |
| (2 | 52° min. | - | - |
| (3 | 43° | 0/-5° | 0/-5° |
| Cap P38t in accordance with IEC Publication 60061 (sheet 7004-133-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 55 | 60 | 55 | 60 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 68 max. | 75 max. | 68 max. | 75 max. |
|  | Luminous flux | 1,150 ± 15 % | 1,750 ± 15 % |  |  |
| Reference luminous flux at approximately | 12 V | 860 | 1,300 |
|  | 13.2 V | 1,150 | 1,750 |

8/	The ends of the filaments are defined as the points where, when the viewing direction is direction A as shown in Figure 1 on sheet H14/1, the projection of the outside of the end turns crosses the filaments axis.

9/	"f1" represents the length of the passing-beam filament and "f2" represents the length of the driving-beam filament.

10/	To be checked by means of a "Box system"; sheet H14/4.

Category H14	Sheet H14/4

Screen projection requirements

This test is used to determine, by checking whether the filaments are correctly positioned relative to the reference axis and the reference plane, whether a filament light source complies with the requirements.

| a1 | a2 | b1 | b2 | c1 | c2 | c3 | i | k |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| d1 +0.5 | 1.6 * d2 | 0.2 | 5.8 | 5.1 | 5.75 | 2.7 | 0.15 |

d1 is diameter of the passing-beam filament and d2 that of the driving-beam filament.

Notes concerning the filaments diameter:

(a)	No actual diameter restrictions apply but the objective for future developments is to have d1 max. = 1.6 mm and d2 max. = 1.6 mm.

(b) 	For the same manufacture, the design diameter of standard filament light sources and filament light sources of normal production shall be the same.

The positions of the filaments are checked solely in directions A, B and C as shown in Figure 1 on sheet H14/1.

The passing-beam filament shall lie entirely in the rectangle A and the driving-beam filament entirely in rectangle B.

The ends of the passing-beam filament as defined on sheet H14/3, footnote 8/ shall lie between lines Z1 and Z2 and between lines Z3 and Z4.

Category H15	Sheet H15/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is defined by the points at which the holder touches the three lugs of the cap ring from the plug side. It is intended for use as an internal reference plane.

The auxiliary reference plane is defined by the points on the surface of the holder on which the three supporting bosses of the cap ring will rest. It is intended for use as an external reference plane.

The cap is designed for use of the (internal) reference plane, but for certain applications the (external) auxiliary reference plane may be used instead.

2/	The reference axis is perpendicular to the reference plane and crosses the intersection of the two perpendiculars as indicated in Figure 2 on sheet H15/1.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 3. The envelope is concentric to the reference axis.

4/	Glass bulb shall be optically distortion free within the angles (1 and (2 as indicated in Figure 4.  This requirement applies to the whole bulb circumference within the angles (1 and (2.

Category H15	Sheet H15/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 24 V | 12 V |
| e | 30.0 + 0.35 / -0.25 | 30.0 + 0.35 / -0.25 | 30.0 + 0.20 / -0.15 |
| (1 | 50°min | 50°min | 50°min |
| (2 | 50°min | 50°min | 50°min |
| r | For details see cap sheet |
| Cap PGJ23t-1 in accordance with IEC Publication 60061 (sheet 7004-155-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 5/ | 24 5/ | 12 5/ |
|  | Watts | 15 | 55 | 20 | 60 | 15 | 55 |
| Test voltage | Volts | 13.2 | 28.0 | 13.2 | 13.2 |
| Objective values | Watts | 19 max. | 64 max. | 24 max. | 73 max. | 19 max. | 64 max. |
|  | Luminous flux | 260 | 1,350 | 300 | 1,500 |  |  |
|  | (10 % |  |  |
| Reference luminous flux at approximately 12 V |  | 1,000 |
| Reference luminous flux at approximately 13.2 V |  | 1,350 |
| Reference luminous flux at approximately 13.5 V | 290 |  |

5/	The values indicated in the left-hand columns relate to the low wattage filament. Those indicated in the right-hand columns relate to the high wattage filament.

Category H15	Sheet H15/3

Category H15	Sheet H15/4

# Table of the dimensions (in mm) referred to in the drawings on sheet H15/3

| Reference* | Dimension** | Tolerance |
| --- | --- | --- |
|  |  | Filament light sources of normal production | Standard filament light source |
| 12 V | 24 V | 12 V | 24 V | 12 V | 24 V | 12 V | 24 V |
| a/24.0 | a/24.5 | 1.8 | (0.35 | (0.20 |
| a/26.0 | 1.8 | (0.35 | (0.20 |
| b1/31.0 | 0 | (0.30 | (0.15 |
| b1/33.5 | b1/34.0 | b1/31.0 mv | (0.30 | (0.15 |
| b2/31.0 | 0 | (0.30 | (0.15 |
| b2/33.5 | b2/34.0 | b2/31.0 mv | (0.30 | (0.15 |
| c1/31.0 | 0 | (0.30 | (0.50 | (0.15 | (0.25 |
| c1/33.5 | c1/34.0 | c1/31.0 mv | (0.30 | (0.50 | (0.15 | (0.25 |
| c2/33.5 | c2/34.0 | 1.1 | (0.30 | (0.50 | (0.15 | (0.25 |
| d | min. 0.1 | - | - |
| f 8/, 9/, 10/ | 2.7 | (0.30 | (0.40 | +0.20 -0.10 | +0.25 -0.15 |
| g/24.0 | g/24.5 | 0 | (0.50 | (0.70 | (0.25 | (0.35 |
| g/26.0 | 0 | (0.50 | (0.70 | (0.25 | (0.35 |
| h/31.0 | 0 | (0.50 | (0.60 | (0.25 | (0.30 |
| h/33.5 | h/34.0 | h/31.0 mv | (0.30 | (0.40 | (0.15 | (0.20 |
| 1R 8/, 11/ | 4.2 | 4.6 | (0.40 | (0.60 | (0.20 | (0.30 |
| 1C 8/, 9/ | 4.4 | 5.4 | (0.40 | (0.60 | (0.20 | (0.30 |
| p/33.5 | p/34.0 | Depends on the shape of the shield | - | - |
| q/33.5 | q/34.0 | p/33.5 | p/34.0 | (1.20 | (0.60 |

*	"…/26.0" means dimension to be measured at the distance from the reference plane indicated in mm after the stroke.

**	"31.0 mv" means the value measured at a distance of 31.0 mm from the reference plane.

Category H15	Sheet H15/5

6/	Plane V-V is the plane perpendicular to the reference plane and passing through the reference axis and through the axis of the reference lug.

7/	Plane H-H is the plane perpendicular to both the reference plane and plane V-V and passing through the reference axis.

8/	The end turns of the filament are defined as being the first luminous turn and the last luminous turn that are at substantially the correct helix angle.

9/	For the high wattage filament, the points to be measured are the intersections, seen in direction 1, of the lateral edge of the shield with the outside of the end turns defined under footnote 8/.

10/	"e" denotes the distance from the reference plane to the beginning of the driving-beam filament as defined above.

11/	For the low wattage filament the points to be measured are the intersections, seen in direction 1, of a plane, parallel to plane H-H and situated at a distance of 1.8 mm above it, with the end turns defined under footnote 8/.

12/	34.0 for the 24 V type.

13/	24.5 for the 24 V type.

Additional explanations to sheet H15/3

The dimensions below are measured in four directions:

1)	For dimensions a, c1, c2, d, e, f, lR and lC;

2)	For dimensions g, h, p and q;

3)	For dimension b1;

4)	For dimension b2.

Dimensions b1, b2, c1 and h are measured in planes parallel to the reference plane at distances of 31.0 mm and 33.5 mm (34.0 mm for 24 V types).

Dimensions c2, p and q are measured in a plane parallel to the reference plane at a distance of 33.5 mm (34.0 mm for 24 V types).

Dimensions a and g are measured in planes parallel to the reference plane at distances of 24.0 mm (24.5 mm for 24 V types) and 26.0 mm.

Categories H16 and H16B 	Sheet H16/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is the plane formed by the underside of the bevelled lead-in flange of the cap.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 19 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

4/	The light emitted shall be white or selective yellow.

5/	Notes concerning the filament diameter.

(a)	No actual diameter restrictions apply but the objective for future developments is to have d max. = 1.1 mm.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

Categories H16 and H16B	Sheet H16/2

6/	Glass bulb shall be optically distortion free within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

7/	The obscuration shall extend at least to angle (3 and shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.

8/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction. (View A as indicated in Figure 1 on sheet H16/1).  No metal parts other than filament turns shall be located in the shaded area as seen in Figure 4.

9/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 in sheet H16/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

10/	Offset of filament in relation to bulb axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Categories H16 and H16B	Sheet H16/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e 11/ | 25.0 12/ | 25.0 ( 0.1 |
| f 11/ | 3.2 12/ | 3.2 ( 0.1 |
| g | 0.5 min. | u.c. |
| h1 | 0 12/ | 0 ( 0.1 |
| h2 | 0 12/ | 0 ( 0.15 |
| (1 | 50° min. | 50° min. |
| (2 | 40° min. | 40° min. |
| (3 | 30° min. | 30° min. |
| Cap: | H16: PGJ19-3 H16B: PGJY19-3 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 19 | 19 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 26 max. | 26 max. |
|  | Luminous flux | 500 +10 % / -15 % |  |
| Reference luminous flux: 370 lm at approximately 12 V | 370 lm |
| Reference luminous flux: 500 lm at approximately 13.2 V | 500 lm |
| Reference luminous flux: 550 lm at approximately 13.5 V | 550 lm |

11/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown in Figure 1 on sheet H16/1, the projection of the outside of the end turns crosses the filament axis.

12/	To be checked by means of a "Box system"; sheet H16/4.

Categories H16 and H16B	Sheet H16/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament complies with the requirements.

| a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| d + 0.50 | d + 0.70 | 0.25 | 3.6 | 2.6 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H16/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H16/3, footnote 11/, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Category H17	Sheet H17/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

For the notes see sheet H17/6

Category H17	Sheet H17/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e | 28.5 + 0.35 / - 0.15 | 28.5 + 0.20 / - 0.0 |
| p | 28.95 | 28.95 |
| α | max. 40° | max. 40° |
| Cap PU43t-4 in accordance with IEC Publication 60061 (sheet 7004-171-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 6/ | 12 6/ |
|  | Watts | 35 | 35 | 35 | 35 |
| Test voltage | Volts | 13.2 | 13.2 | 13.2 | 13.2 |
| Objective values | Watts | 37 max. | 37 max. | 37 max. | 37 max. |
|  | Luminous flux | 900 ( 10 % | 600 ( 10 % |  |  |
| Reference luminous flux at approximately | 12.0 V | 700 | 450 |
|  | 13.2 V | 900 | 600 |

For note 6/ see sheet H17/6

Category H17	Sheet H17/3

Position of the shield

Category H17	Sheet H17/4

Position of filaments

Category H17	Sheet H17/5

Table of the dimensions (in mm) referred to in the drawings on sheets H17/3 and H17/4

| Reference* | Dimension** | Tolerance |
| --- | --- | --- |
|  |  | Filament light sources of normal production | Standard filament light source |
| a/25.0 | 0.3 | (0.40 | (0.20 |
| a/26.0 | 0.3 | (0.35 | (0.20 |
| b1/29.5 | 0.0 | (0.30 | (0.25 |
| b1/33.0 | b1/29.5 mv | (0.30 | (0.15 |
| b2/29.5 | 0.0 | (0.30 | (0.25 |
| b2/33.0 | b2/29.5 mv | (0.30 | (0.15 |
| c/29.5 | 0.5 | (0.25 | (0.15 |
| c/31.0 | c/29.5 mv | (0.25 | (0.15 |
| d | min. 0.1 | - | - |
| e 11/ | 28.5 | +0.35 / -0.15 | +0.20 / -0.0 |
| f 9/, 10/, 11/ | 1.7 | (0.30 | (0.15 |
| g/25.0 | 0 | (0.50 | (0.30 |
| g/26.0 | 0 | (0.40 | (0.25 |
| h/29.5 | 0 | (0.40 | (0.25 |
| h/31.0 | h/29.5 mv | (0.30 | (0.15 |
| lR 9/, 12/ | 4.0 | (0.40 | (0.20 |
| lC 9/, 10/ | 4.2 | (0.40 | (0.20 |
| p/33.0 | Depends on the shape of the shield | - | - |
| q/33.0 | (p+q)/2 | (0.60 | (0.30 |

*	"../25.0" means dimension to be measured at the distance from the reference plane indicated in mm after the stroke.

**	"29.5 mv" means the value measured at a distance of 29.5 mm from the reference plane.

For the notes see sheet H17/6

Category H17	Sheet H17/6

1/	The reference plane is the plane formed by the seating points of the three lugs of the cap ring.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of the circle of diameter "M".

3/	The light emitted from standard filament light sources and from normal production filament light sources shall be white.

4/	The bulb and supports shall not exceed the envelope as in Figure 2.

5/	The obscuration shall extend at least as far as the cylindrical part of the bulb. It shall also overlap the internal shield when the latter is viewed in a direction perpendicular to the reference axis.

6/	The value indicated in the left hand column relate to the driving beam filament. Those indicated in the right-hand column relate to the passing-beam filament.

7/	Plane V-V is the plane perpendicular to the reference plane and passing through the reference axis and through the intersection of the circle of diameter "M" with the axis of the reference lug.

8/	Plane H-H is the plane perpendicular to both the reference plane and plane V-V and passing through the reference axis.

9/	The end turns of the filament are defined as being the first luminous turn and the last luminous turn that are at substantially the correct helix angle.

10/	For the passing beam filament, the points to be measured are the intersections, seen in direction 1, of the lateral edge of the shield with the outside of the end turns defined under note 9/.

11/	"e" denotes the distance from the reference plane to the beginning of the passing filament as defined above.

12/	For the driving beam filament the points to be measured are the intersections, seen in direction 1, of a plane, parallel to plane H-H and situated at a distance of 0.3 mm below it, with the end turns defined under note 9/.

Additional explanations to sheets H17/3 and H17/4

The dimensions below are measured in three directions:

1	For dimensions b1, a, c, d, e, f, lR and lC.

2	For dimensions g, h, p and q.

3	For dimension b2.

Dimensions p and q are measured in planes parallel to and 33.0 mm away from the reference plane.

Dimensions b1, b2 are measured in planes parallel to and 29.5 mm and 33.0 mm away from the reference plane.

Dimensions c and h are measured in planes parallel to and 29.5 mm and 31.0 mm away from the reference plane.

Dimensions a and g are measured in planes parallel to and 25.0 mm and 26.0 mm away from the reference plane.

Note: For the method of measurement, see Appendix E to IEC Publication 60809.

Category H18 	Sheet H18/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is defined by the points on the surfaces of the holder on which the three supporting bosses of the cap ring will rest.

2/	The reference axis is perpendicular to the reference plane and crosses the intersection of the two perpendiculars as indicated in Figure 3.

3/	The colour of the light emitted shall be white or selective-yellow.

4/	Notes concerning the filament diameter.

(a)	No actual diameter restrictions apply but the design target is d max. = 1.3 mm.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

5/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

Category H18 	Sheet H18/2

6/	Glass bulb shall be optically distortion free within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2.

7/	The obscuration shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall moreover extend at least to a plane parallel to the reference plane where (3 crosses the outer bulb surface (view B as indicated on sheet H18/1).

8/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction. (View A as indicated in Figure 1 on sheet H18 /1).

No metal parts other than filament turns shall be located in the shaded area as seen in Figure 5.

Category H18 	Sheet H18/3

|  | Filaments light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e 9/ | 25.0 10/ | 25.0 ( 0.1 |
| f 9/ | 4.810/ | 4.8( 0.1 |
| g 12/ | 0.5 min. | u.c. |
| h1 11/ | 0 10/ | 0 ( 0.10 |
| h2 11/ | 0 10/ | 0 ( 0.15 |
| (1 | 40° min. | 40° min. |
| (2 | 50° min. | 50° min. |
| (3 | 30° min. | 30° min. |
| Cap PY26d-1 in accordance with IEC Publication 60061 (sheet 7004-5-7) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 65 | 65 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 69 max. | 69 max. |
|  | Luminous flux | 1,700 ( 8 % |  |
| Reference luminous flux at approximately | 13.2 V | 1,700 |

9/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown in Figure 1 on sheet H18/1, the projection of the outside of the end turns crosses the filament axis.

10/	To be checked by means of a "Box System", sheet H18/4.

11/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 in sheet H18/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

12/	Offset of filament in relation to bulb axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Category H18 	Sheet H18/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

Dimensions in mm

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 12 V | d + 0.30 | d + 0.50 | 0.2 | 5.3 | 4.7 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H18/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H18/3, note 9, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Category H19	Sheet H19/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

For the notes see sheet H19/5.

Category H19	Sheet H19/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e | 28.5 + 0.35 / - 0.15 | 28.5 + 0.20 / - 0.0 |
| p | 28.95 | 28.95 |
| α | max. 45° | max. 45° |
| Cap PU43t-3 in accordance with IEC Publication 60061 (sheet 7004-171-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 126/ | 126/ |
|  | Watts | 60 | 55 | 60 | 55 |
| Test values | Volts | 13.2 | 13.2 | 13.2 | 13.2 |
| Objective values | Watts | 72 max. | 68 max. | 72 max. | 68 max. |
|  | Luminous flux | 1 750 ( 10% | 1 200 ( 10% |  |  |
| Reference luminous flux at approximately | 13.2 V | 1,750 | 1,200 |

For note 6 see sheet H19/5.

Category H19	Sheet H19/3

Position of shield

Position of filament

Category H19	Sheet H19/4

Table of the dimensions (in mm) referred to in the drawings on sheet H19/3

| Reference* | Dimension** | Tolerance |
| --- | --- | --- |
|  |  | Filament light sources of normal production | Standard filament light source |
| a/26.0 | 0.7 | (0.30 | (0.20 |
| a/24.5 | 0.7 | (0.40 | (0.20 |
| b1/29.5 | 1.0 | (0.30 | (0.25 |
| b1/33.0 | b1/29.5 mv | (0.30 | (0.15 |
| b2/29.5 | 1.0 | (0.30 | (0.25 |
| b2/33.0 | b2/29.5 mv | (0.30 | (0.15 |
| c/29.5 | 1.7 | (0.25 | (0.15 |
| c/33 | c/29.5 mv | (0.25 | (0.15 |
| d | min. 1.1 | - | - |
| e11/ | 28.5 | +0.35 / -0.15 | +0.20 / -0.0 |
| f 9/, 10/, 11/ | 1.4 | (0.30 | (0.15 |
| g/26.0 | 0 | (0.40 | (0.30 |
| g/24.5 | 0 | (0.50 | (0.25 |
| h/29.5 | 0 | (0.40 | (0.25 |
| h/33.0 | h/29.5 mv | (0.30 | (0.15 |
| lR 9/, 12/ | 4.0 | (0.60 | (0.30 |
| lC 9/, 10/ | 5.2 | (0.60 | (0.30 |
| p/33.0 | Depends on the shape of the shield | - | - |
| q/33.0 | (p+q)/2 | (0.60 | (0.30 |

*	"../24.5" means dimension to be measured at the distance from the reference plane indicated in mm after the stroke.

**	"../29.5 mv" means the value measured at a distance of 29.5 mm from the reference plane.

For the notes see sheet H19/5.

Category H19	Sheet H19/5

1/	The reference plane is the plane formed by the seating points of the three lugs of the cap ring.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of the circle of diameter "M".

3/	The light emitted from standard filament light sources and from normal production filament light sources shall be white.

4/	The bulb and supports shall not exceed the envelope as in Figure 2.

5/	The obscuration shall extend at least as far as the cylindrical part of the bulb. It shall also overlap the internal shield when the latter is viewed in a direction perpendicular to the reference axis.

6/	The value indicated in the left hand column relate to the major filament. Those indicated in the right-hand column relate to the minor filament.

7/	Plane V-V is the plane perpendicular to the reference plane and passing through the reference axis and through the intersection of the circle of diameter "M" with the axis of the reference lug.

8/	Plane H-H is the plane perpendicular to both the reference plane and plane V-V and passing through the reference axis.

9/	The end turns of the filament are defined as being the first luminous turn and the last luminous turn that are at substantially the correct helix angle.

10/	For the minor filament, the points to be measured are the intersections, seen in direction 1, of either the lateral edge of the shield or the filament axis with the outside of the end turns defined under note 9.

11/	"e" denotes the distance from the reference plane to the beginning of the minor filament as defined above.

12/	For the major filament the points to be measured are the intersections, seen in direction 1, of a plane, parallel to plane H-H and situated at a distance of 0.3 mm below it, with the end turns defined under note 9.

Additional explanations to sheet H19/3

The dimensions below are measured in three directions:

1	For dimensions b1, a, c, d, e, f, lR and lC.

2	For dimensions g, h, p and q.

3	For dimension b2.

Dimensions p and q are measured in planes parallel to and 33.0 mm away from the reference plane.

Dimensions b1, b2 are measured in planes parallel to and 29.5 mm and 33.0 mm away from the reference plane.

Dimensions c and h are measured in planes parallel to and 29.5 mm and 33.0 mm away from the reference plane.

Dimensions a and g are measured in planes parallel to and 24.5 mm and 26.0 mm away from the reference plane.

Note:	For the method of measurement, reference is made to Appendix E of IEC Publication 60809.

Category H20	Sheet H20/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

1/	The reference plane is defined by the points on the surfaces of the holder on which the three supporting 
bosses of the cap ring will rest.

2/	The reference axis is perpendicular to the reference plane and crosses the intersection of the two perpendiculars as indicated in Figure 3.

3/	The colour of the light emitted shall be white with the restriction according to sheet H20/3.

4/	Notes concerning the filament diameter:

(a)	No actual diameter restrictions apply but the design target is to have d max. = 1.4 mm.

(b)	For the same manufacturer, the design diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

5/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 2. The envelope is concentric to the reference axis.

Category H20	Sheet H20/2

6/	Glass bulb shall be optically distortion free within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2.

7/	The internal design of the filament light source shall be such that stray light images and reflections are only located above the filament itself seen from the horizontal direction. (View A as indicated in Figure 1 on sheet H20/1).

No metal parts other than filament turns shall be located in the shaded area as seen in Figure 5.

Category H20	Sheet H20/3

| Dimensions in mm | Filaments light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e 8/ | 25.0 9/ | 25.0 ( 0.1 |
| f 8/ | 4.8 9/ | 4.8 ( 0.1 |
| g 11/ | 0.5 min. | 0.5 min. |
| h1 10/ | 0 9/ | 0 ( 0.10 |
| h2 10/ | 0 9/ | 0 ( 0.15 |
| (1 | 40° min. | 40° min. |
| (2 | 50° min. | 50° min. |
| Cap PY26d-6 in accordance with IEC Publication 60061 (sheet 7004-5-7) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 70 | 70 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 75 max. | 75 max. |
|  | Luminous flux | 1 250 ( 10 % |  |
| Reference luminous flux at approximately | 12 V | 900 |
|  | 13.2 V | 1250 |
| Chromaticity Coordinates | Objective | x=0.347 | y=0.353 |
|  | Tolerance area | Boundaries | x=0.330 | y=0.150+0.640x |
|  |  |  | x=0.370 | y=0.050+0.750x |
|  |  | Intersection points | x=0.330 | y=0.298 |
|  |  |  | x=0.370 | y=0.327 |
|  |  |  | x=0.370 | y=0.387 |
|  |  |  | x=0.330 | y=0.361 |

8/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown in Figure 1 on sheet H20/1, the projection of the outside of the end turns crosses the filament axis. (Special instructions for coiled-coil filaments are under consideration).

9/	To be checked by means of a "Box System", sheet H20/4.

10/	The offset of the filament with respect to the reference axis is measured only in viewing directions A and B as shown in Figure 1 in sheet H20/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

11/	Offset of filament in relation to bulb axis measured in two planes parallel to the reference plane where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

Category H20	Sheet H20/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

Dimensions in mm

| a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| d + 0.40 | d + 0.70 | 0.25 | 5.7 | 4.6 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet H20/1, Figure 1.

The filament shall lie entirely within the limits shown.

The ends of the filament as defined on sheet H20/3, note 9, shall lie between lines Z1 and Z2 and between Z3 and Z4.

Categories H6W and HY6W	Sheet H6W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 14.25 | 15.0 | 15.75 | 15.0 ( 0.25 |
| Lateral deviation 1/ |  |  | 0.75 | 0.4 max |
| β | 82.5° | 90° | 97.5° | 90° ( 5° |
| (1, (2 2/ | 30° |  |  | 30° min. |
| Cap: | H6W: | BAX9s | in accordance with IEC Publication 60061 (sheet 7004-8-1) |
|  | HY6W: | BAZ9s | in accordance with IEC Publication 60061 (sheet 7004-150-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 6 | 6 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 7.35 max. | 7.35 max. |
|  | Luminous flux | H6W | 125 ( 12 % |  |
|  |  | HY6W | 75 ( 17 % |  |
| Reference luminous flux at approximately 13.5 V | White: 125 lm |
|  | Amber: 75 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	In the area between the outer legs of the angles (1 and (2, the bulb shall have no optically distorting areas and the curvature of the bulb shall have a radius not less than 50 per cent of the actual bulb diameter.

3/	Over the entire length of the cap there shall be no projections or soldering exceeding the permissible maximum diameter of the cap.

4/	The light emitted from filament light sources of normal production shall be white for category H6W and amber for category HY6W.

5/	The light emitted from standard filament light sources shall be white for category H6W and amber or white for category HY6W.

Categories H10W/1 and HY10W	Sheet H10W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 14.25 | 15.0 | 15.75 | 15.0 ( 0.25 |
| Lateral deviation 1/ |  |  | 0.75 | 0.4 max |
| β | 82.5° | 90° | 97.5° | 90° ( 5° |
| (1, (2 2/ | 30° |  |  | 30° min. |
| Cap: | H10W/1 HY10W | BAU9s BAUZ9s | in accordance with IEC Publication 60061 (sheet 7004-150A-1) in accordance with IEC Publication 60061 (sheet 7004-150B-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 10 | 10 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 12 max. | 12 max. |
|  | Luminous flux | H10W/1 | 200 ( 12 % |  |
|  |  | HY10W | 120 ( 17 % |  |
| Reference luminous flux at approximately 13.5 V | White: 200 lm |
|  | Amber: 120 lm |

Categories H10W and HY10W	Sheet H10W/2

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	In the area between the outer legs of the angles (1 and (2, the bulb shall have no optically distorting areas and the curvature of the bulb shall have a radius not less than 50 per cent of the actual bulb diameter.

3/	Over the entire length of the cap there shall be no projections or soldering exceeding the permissible maximum diameter of the cap.

4/	The light emitted from filament light sources of normal production shall be white for category H10W/1 and amber for category HY10W.

5/	The light emitted from standard filament light sources shall be white for category H10W/1 and amber or white for category HY10W.

Categories H21W and HY21W	Sheet H21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 20.0 1/ |  | 20.0 ( 0.25 |
| f | 12 V |  |  | 3.8 | 3.8 + 0 / -1 |
|  | 24 V |  |  | 4.5 |  |
| Lateral deviation 2/ |  |  | 1/ | 0.0 ( 0.15 3/ |
| ( | 82.5° | 90° | 97.5° | 90° ( 5° |
| (1, (2 4/ | 45° |  |  | 45° min. |
| Cap: | H21W: | BAY9s | in accordance with IEC Publication 60061 (sheet 7004-9-1) |
|  | HY21W: | BAW9s | in accordance with IEC Publication 60061 (sheet 7004-149-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 21 | 21 | 21 |
| Test voltage | Volts | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 26.25 max. | 29.4 max. | 26.25 max. |
|  | Luminous flux | H21W | 600 ( 12 % | 600 ( 15 % |  |
|  |  | HY21W | 300 ( 17 % | 300 ( 20 % |  |
| Reference luminous flux at approximately | 12 V | White: 415 lm |
|  | 13.2 V | White: 560 lm |
|  | 13.5 V | White: 600 lm Amber: 300 lm |

1/	To be checked by means of a "Box system", sheet H21W/2.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

3/	The lateral deviation with respect to the plane perpendicular to axis X-X is measured in the position described in paragraph 1. of the test procedure specified on sheet H21W/2.

4/	In the area between the outer legs of the angles (1 and (2, the bulb shall have no optical distorting areas and the curvature of the bulb shall have a radius not less than 50 per cent of the actual bulb diameter.

5/	The light emitted from filament light sources of normal production shall be white for category H21W and amber for category HY21W.

6/	The light emitted from standard filament light sources shall be white for category H21W and amber or white for category HY21W.

Categories H21W and HY21W	Sheet H21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within (7.5°, to the plane through the centre line of the reference pin and the reference axis, whether a filament light source complies with the requirements.

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | d + 1.0 | d +1.0 | f + 1.2 | 0.50 |

d	= actual filament diameter

f	= actual filament length

Test procedures and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament;

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

Categories H27W/1 and H27W/2 	Sheet H27W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the plane formed by the underside of the bevelled lead-in flange of the cap.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of
the 13.10 mm cap diameter.

3/	Glass bulb and supports shall not exceed the size of a theoretical cylinder centred on the reference axis.

4/	The obscuration shall extend over the whole bulb top including the bulb cylindrical portion up to the intersection with (1.

Categories H27W/1 and H27W/2	Sheet H27W/2

Filament dimensions and position

(Dimensions f for all filament light sources)

(Dimensions h1, h2, h3, h4 and k for standard filament light sources only)

| Dimensions in mm | Filament light source of normal production | Standard filament light source |
| --- | --- | --- |
| e | 31.75 6/ | 31.75 ( 0.25 |
| f 8/ | 4.8 max. | 4.2 ( 0.20 |
| k | 0 6/ | 0.0 ( 0.25 |
| h1, h2, h3, h4 7/ | 0 6/ | 0.0 ( 0.25 |
| (1 5/ | 38° nom. | 38° nom. |
| (2 5/ | 44° nom. | 44° nom. |
| Cap: | H27W/1: PG13 H27W/2: PGJ13 | in accordance with IEC Publication 60061 (sheet 7004-107-4) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 27 | 27 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 31 max. | 31 max. |
|  | Luminous flux | 477 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 350 lm |
|  | 13.2 V | 450 lm |
|  | 13.5 V | 477 lm |

5/	Glass bulb shall be optically distortion free within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

6/	To be checked by means of a "Box system", sheet H27W/3.

7/	For standard filament light sources, the points to be measured are those where the projection of the outside of the end turns crosses the filament axis.

8/	The ends of the filament are defined by the intersections of the outside of the first and of the last light emitting turn, respectively, with the plane parallel to and 31.75 mm from the reference plane.

Categories H27W/1 and H27W/2 	Sheet H27W/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

Dimensions in mm

| Reference | a | c | k | g |
| --- | --- | --- | --- | --- |
| Dimensions | d + 1.2 | d + 1.0 | 0.5 | 2.4 |

d = actual diameter of filament

The filament shall lie entirely within the limits shown.

The centre of the filament shall lie within the limits of dimension k.

Categories HB3 and HB3A	Sheet HB3/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is the plane defined by the meeting points of cap-holder fit.

2/	The reference axis is perpendicular to the reference plane and concentric with the reference diameter of the cap.

3/	Glass bulb and supports shall not exceed the envelope and shall not interfere with insertion past the filament light source key.

4/	The keyway is mandatory for category HB3A and optional for category HB3.

5/	The filament light source shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

Categories HB3 and HB3A	Sheet HB3/2

6/	The colour of the light emitted shall be white or selective-yellow.

7/	Glass bulb periphery shall be optically distortion-free axially within the angles (1 and (2. 
This requirement applies to the whole bulb circumference within the angles (1 and (2.

Categories HB3 and HB3A	Sheet HB3/3

| Dimensions in mm 12/ | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| e 9/, 11/ | 31.5 | 10/ | (0.16 |
| f 9/, 11/ | 5.1 | 10/ | (0.16 |
| h1, h2 | 0 | 10/ | (0.15 8/ |
| h3 | 0 | 10/ | (0.08 8/ |
| (1 | 45° min. | - | - |
| (2 | 52° min. | - | - |
| Cap P20d in accordance with IEC Publication 60061 (sheet 7004-31-2) 13/ |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 60 | 60 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 73 max. | 73 max. |
|  | Luminous flux | 1,860 ( 12 % |  |
| Reference luminous flux at approximately | 12 V | 1,300 |
|  | 13.2 V | 1,860 |

8/	The eccentricity is measured only in viewing directions* A and B as shown in the figure on sheet HB3/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

9/	The viewing direction is direction* B as shown in the figure on sheet HB3/1.

10/	To be checked by means of a "Box system"; sheet HB3/4*.

11/	The ends of the filament are defined as the points where, when the viewing direction* as defined in footnote 9/ above, the projection of the outside of the end turns crosses the filament axis.

12/	Dimensions shall be checked with O-ring removed.

13/	Filament light source HB3 shall be equipped with the right-angle cap and filament light source HB3A with the straight cap.

*	Manufacturers may choose another set of perpendicular viewing directions. The viewing directions specified by the manufacturer are to be used by the testing laboratory when checking filament dimensions and position.

Categories HB3 and HB3A	Sheet HB3/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | p | q | r | s | t | u | v |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 12 V | 1.3 d | 1.6 d | 3.0 | 2.9 | 0.9 | 0.4 | 0.7 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet HB3/1.

The filament shall lie entirely within the limits shown.

The beginning of the filament, as defined on sheet HB3/3, footnote 11/, shall lie in volume "B" and the end of the filament in volume "C".

Volume "A" does not involve any filament centre requirement.

Categories HB4 and HB4A	Sheet HB4/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is the plane defined by the meeting points of cap-holder fit.

2/	The reference axis is perpendicular to the reference plane and concentric with the reference diameter of the cap.

3/	Glass bulb and supports shall not exceed the envelope and shall not interfere with insertion past the filament light source key. The envelope is concentric to the reference axis.

4/	The keyway is mandatory for category HB4A and optional for category HB4.

5/	The filament shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

Categories HB4 and HB4A	Sheet HB4/2

6/	The colour of the light emitted shall be white or selective-yellow.

7/	Glass bulb periphery shall be optically distortion-free axially and cylindrically within the angles (1 and (2.  This requirement applies to the whole bulb circumference within the angles (1 and (2 and does not need to be verified in the area covered by the obscuration.

8/	The obscuration shall extend to at least angle (3 and shall be at least as far as the undistorted part of the bulb defined by angle (1.

Categories HB4 and HB4A	Sheet HB4/3

| Dimensions in mm 13/ | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| e 10/, 12/ | 31.5 | 11/ | (0.16 |
| f 10/, 12/ | 5.1 | 11/ | (0.16 |
| h1, h2 | 0 | 11/ | (0.15 9/ |
| h3 | 0 | 11/ | (0.08 9/ |
| g 10/ | 0.75 | (0.5 | (0.3 |
| (1 | 50° min. | - | - |
| (2 | 52° min. | - | - |
| (3 | 45° | (5° | (5° |
| Cap P22d in accordance with IEC Publication 60061 (sheet 7004-32-2) 14/ |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 51 | 51 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 62 max. | 62 max. |
|  | Luminous flux | 1,095 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 825 |
|  | 13.2 V | 1,095 |

9/	The eccentricity is measured only in viewing directions* A and B as shown in the figure on sheet HB4/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

10/	The viewing direction is direction* B as shown in the figure on sheet HB4/1.

11/	To be checked by means of a "Box system"; sheet HB4/4*.

12/	The ends of the filament are defined as the points where, when the viewing direction* as defined in footnote 10/ above, the projection of the outside of the end turns crosses the filament axis.

13/	Dimensions shall be checked with O-ring removed.

14/	Filament light source HB4 shall be equipped with the right-angle cap and filament light source HB4A with the straight cap.

*	Manufacturers may choose another set of perpendicular viewing directions. The viewing directions specified by the manufacturer are to be used by the testing laboratory when checking filament dimensions and position.

Categories HB4 and HB4A	Sheet HB4/4

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | p | q | r | s | t | u | v |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 12 V | 1.3 d | 1.6 d | 3.0 | 2.9 | 0.9 | 0.4 | 0.7 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet HB4/1.

The filament shall lie entirely within the limits shown.

The beginning of the filament as defined on sheet HB4/3 footnote 12/ shall lie in volume "B" and the end of the filament in volume "C".

Volume "A" does not involve any filament centre requirement.

Category HIR1	Sheet HIR1/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is the plane defined by the three supporting bosses on the cap flange.

2/	The reference axis is perpendicular to the reference plane and concentric with the reference diameter of the cap.

3/	Glass bulb and supports shall not exceed the envelope. The envelop is concentric to the reference axis.

4/	The keyway is mandatory.

5/	The filament shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

6/	Glass bulb periphery shall be optically distortion-free axially within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

Category HIR1	Sheet HIR1/2

| Dimensions in mm 11/ | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| e 8/, 10/ | 29 | 9/ | (0.16 |
| f 8/, 10/ | 5.1 | 9/ | (0.16 |
| g 8/ | 0 | +0.7 / -0.0 | +0.4 / -0.0 |
| h1, h2 | 0 | 9/ | (0.15 7/ |
| d | 1.6 max. |  |  |
| (1 | 50° min. | - | - |
| (2 | 50° min. | - | - |
| Cap PX20d in accordance with IEC Publication 60061 (sheet 7004-31-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 65 | 65 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 73 max. | 73 max. |
|  | Luminous flux | 2,500 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 1,840 |
|  | 13.2 V | 2,500 |

7/	The eccentricity is measured only in viewing directions A and B as shown in the figure on sheet HIR1/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

8/	The viewing direction is direction B as shown in the figure on sheet HIR1/1.

9/	To be checked by means of a "Box system"; sheet HIR1/3.

10/	The ends of the filament are defined as the points where, when the viewing direction as defined in footnote 8/ above, the projection of the outside of the end turns crosses the filament axis.

11/	Dimensions shall be checked with O-ring mounted.

Category HIR1	Sheet HIR1/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 12 V | d + 0.4 | d + 0.8 | 0.35 | 6.1 | 5.2 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet HIR1/1.

The ends of the filament as defined on sheet HIR1/2 footnote 10/ shall lie between lines Z1 and Z2 and between lines Z3 and Z4.

Category HIR2	Sheet HIR2/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is the plane defined by the three meeting points of the cap holder fit.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of the reference diameter of the cap.

3/	Glass bulb and supports shall not exceed the envelope. The envelop is concentric to the reference axis.

4/	The keyway is mandatory.

5/	The filament light source shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

6/	Glass bulb periphery shall be optically distortion-free axially within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

Category HIR2	Sheet HIR2/2

| Dimensions in mm 11/ | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| e 8/, 10/ | 28.7 | 9/ | (0.16 |
| f 8/, 10/ | 5.3 | 9/ | (0.16 |
| g 8/ | 0 | +0.7 / -0.0 | +0.4 / -0.0 |
| h1, h2 | 0 | 9/ | (0.15 7/ |
| d | 1.6 max. | - | - |
| (1 | 50° min. | - | - |
| (2 | 50° min. | - | - |
| Cap PX22d in accordance with IEC Publication 60061 (sheet 7004-32-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 55 | 55 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 63 max. | 63 max. |
|  | Luminous flux | 1,875 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 1,355 |
|  | 13.2 V | 1,875 |

7/	The eccentricity is measured only in viewing directions A and B as shown in the figure on sheet HIR2/1. The points to be measured are those where the projection of the outside of the end turns nearest to or furthest from the reference plane crosses the filament axis.

8/	The viewing direction is direction B as shown in the figure on sheet HIR2/1.

9/	To be checked by means of a "Box system"; sheet HIR2/3.

10/	The ends of the filament are defined as the points where, when the viewing direction as defined in footnote 8/ above, the projection of the outside of the end turns crosses the filament axis.

11/	Dimensions shall be checked with O-ring removed.

Category HIR2	Sheet HIR2/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | a1 | a2 | b1 | b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- | --- |
| 12 V | d + 0.4 | d + 0.8 | 0.35 | 6.6 | 5.7 |

d = diameter of filament

The filament position is checked solely in directions A and B as shown on sheet HIR2/1.

The ends of the filament as defined on sheet HIR2/2 footnote 10/ shall lie between lines Z1 and Z2 and between lines Z3 and Z4.

Category HS1	Sheet HS1/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is the plane formed by the seating points of the three lugs of the cap ring.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of the circle of diameter "M".

3/	The colour of the light emitted shall be white or selective-yellow.

4/	The bulb and supports shall not exceed the envelope as in Figure 2. However, where a selective-yellow outer bulb is used the bulb and supports shall not exceed the envelope as in Figure 3.

5/	The obscuration shall extend at least as far as the cylindrical part of the bulb. It shall also overlap the internal shield when the latter is viewed in a direction perpendicular to the reference axis.

Category HS1	Sheet HS1/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 6 V | 12 V | 12 V |
| e | 28.5 + 0.45 / -0.25 | 28.5 + 0.20 / -0.00 |
| p | 28.95 | 28.95 |
| ( | max. 40° | max. 40° |
| Cap PX43t in accordance with IEC Publication 60061 (sheet 7004-34-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 6/ | 12 6/ | 12 6/ |
|  | Watts | 35 | 35 | 35 | 35 | 35 | 35 |
| Test voltage | Volts | 6.3 | 13.2 | 13.2 |
| Objective values | Watts | 35 | 35 | 35 | 35 | 35 | 35 |
|  | ( % | 5 | 5 |
|  | Luminous flux | 700 | 440 | 825 | 525 |  |
|  | ( % | 15 |  |
| Measuring flux 7/ lm | - |  | - | 450 |  |
| Reference luminous flux at approximately | 12 V | 700 | 450 |
|  | 13.2 V | 825 | 525 |

6/	The values indicated in the left hand column relate to the driving-beam.  Those indicated in the right-hand column relate to the passing-beam.

7/	Measuring luminous flux according to the provisions for filament light sources with an internal shield to produce the cut-off.

Category HS1	Sheet HS1/3

Category HS1	Sheet HS1/4

Table of the dimensions (in mm) referred to in the drawings on sheet HS1/3

| Reference* | Dimensions** | Tolerance |
| --- | --- | --- |
|  |  | Filament light sources of normal production | Standard filament light source |
| 6 V | 12 V | 6 V | 12 V | 6 V | 12 V | 12 V |
| a/26 | 0.8 | (0.35 | (0.20 |
| a/25 | 0.8 | (0.55 | (0.20 |
| b1/29.5 | 0 | (0.35 | (0.20 |
| b1/33 | b1/29.5 mv | (0.35 | (0.15 |
| b2/29.5 | 0 | (0.35 | (0.20 |
| b2/33 | b2/29.5 mv | (0.35 | (0.15 |
| c/29.5 | 0.6 | (0.35 | (0.20 |
| c/31 | c/29.5 mv | (0.30 | (0.15 |
| d | min. 0.1 / max. 1.5 | - | - |
| e 13/ | 28.5 | +0.45 / -0.25 | +0.20 / -0.00 |
| f 11/, 12/, 13/ | 1.7 | +0.50 / -0.30 | +0.30 / -0.10 |
| g/26 | 0 | (0.50 | (0.30 |
| g/25 | 0 | (0.70 | (0.30 |
| h/29.5 | 0 | (0.50 | (0.30 |
| h/31 | h/29.5 mv | (0.30 | (0.20 |
| lR 11/, 14/ | 3.5 | 4.0 | (0.80 | (0.40 |
| lC 11/, 12/ | 3.3 | 4.5 | (0.80 | (0.35 |
| p/33 | Depends on the shape of the shield | - | - |
| q/33 | (p+q)/2 | (0.60 | (0.30 |

*	"../26" means dimension to be measured at the distance from the reference plane indicated in mm after the stroke.

**	"29.5 mv" means the value measured at a distance of 29.5 mm from the reference plane.

Category HS1	Sheet HS1/5

8/	Plane V-V is the plane perpendicular to the reference plane and passing through the reference axis and through the intersection of the circle of diameter "M" with the axis of the reference lug.

9/	Plane H-H is the plane perpendicular to both the reference plane and plane V-V and passing through the reference axis.

10/	(Blank).

11/	The end turns of the filament are defined as being the first luminous turn and the last luminous turn that are at substantially the correct helix angle. For coiled-coil filaments, the turns are defined by the envelope of the primary coil.

12/	For the passing-beam filament, the points to be measured are the intersections, seen in direction 1, of the lateral edge of the shield with the outside of the end turns defined under footnote 11/.

13/	"e" denotes the distance from the reference plane to the beginning of the passing-beam filament as defined above.

14/	For the driving-beam filament the points to be measured are the intersections, seen in direction 1, of a plane, parallel to plane H-H and situated at a distance of 0.8 mm below it, with the end turns defined under footnote 11/.

Additional explanations to sheet HS1/3

The dimensions below are measured in three directions:

1	For dimensions a, b1, c, d, e, f, IR and IC;

2	For dimensions g, h, p and q;

3	For dimension b2.

Dimensions p and q are measured in planes parallel to and 33 mm away from the reference plane.

Dimensions b1 and b2 are measured in planes parallel to and 29.5 mm and 33 mm away from the reference plane.

Dimensions a and g are measured in planes parallel to and 25.0 mm and 26.0 mm away from the reference plane.

Dimensions c and h are measured in planes parallel to and 29.5 mm and 31 mm away from the reference plane.

Note: For the method of measurement, see Appendix E of IEC Publication 60809.

Category HS2 	Sheet HS2/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference axis is perpendicular to the reference plane and passes through the intersection of this plane with the axis of the cap ring.

2/	All parts which may obscure the light or may influence the light beam shall lie within angle (.

3/	Angle ( denotes the position of the plane through the inner leads with reference to the reference notch.

4/	In the area between the outer legs of the angles (1 and (2, the bulb shall have no optically distorting areas and the curvature of the bulb shall have a radius not less than 50 per cent of the actual bulb diameter.

Category HS2 	Sheet HS2/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 11.0 5/ |  | 11.0 ( 0.15 |
| f 6/ | 6 V | 1.5 | 2.5 | 3.0 | 2.5 ( 0.15 |
|  | 12 V | 2.0 | 3.0 | 4.0 |  |
| h1, h2 |  | 5/ |  | 0 ( 0.15 |
| ( 2/ |  |  | 40° |  |
| ( 3/ | 75° | 90° | 105° | 90° ( 5° |
| (1 4/ | 15° |  |  | 15° min. |
| (2 4/ | 40° |  |  | 40° min. |
| Cap PX13.5s in accordance with IEC Publication 60061 (sheet 7004-35-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 6 |
|  | Watts | 15 | 15 |
| Test voltage | Volts | 6.75 | 13.5 | 6.75 |
| Objective values | Watts | 15 ( 6 % | 15 ( 6 % |
|  | Luminous flux | 320 ( 15 % |  |
| Reference luminous flux: 320 lm at approximately 6.75 V |

5/	To be checked by means of the "Box system", sheet HS2/3.

6/	In order to avoid rapid filament failure, the supply voltage shall not exceed 8.5 V for 6 V filament light sources and 
15 V for 12 V types.

Category HS2	Sheet HS2/3

Screen projection requirements

This test is used to determine, by checking whether the filament light source complies with the requirements by checking whether the filament light source is correctly positioned relative to the reference axis and reference plane.

| Reference | a1 | a2 | b1 | b2 | c1 (6 V) | c1 (12 V) | c2 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Dimension | d + 1.0 | d + 1.4 | 0.25 | 0.25 | 4.0 | 4.5 | 1.75 |

d= actual filament diameter

The filament shall lie entirely within the limits shown.

The beginning of the filament shall lie between the lines Z1 and Z2.

Category HS5 	Sheet HS5/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the three ramp inside surface.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 23 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 1. The envelope is concentric to the reference axis.

4/	Glass bulb shall be optically distortion free within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

5/	The obscuration shall extend at least to angle (3 and shall extend at least to the cylindrical part of the bulb on the whole top circumference.

Category HS5 	Sheet HS5/2

Category HS5 	Sheet HS5/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e | 26 | 6/ | (0.15 |
| lC 7/ | 4.6 |  | (0.3 |
| k | 0 |  | (0.2 |
| h1, h3 | 0 |  | (0.15 |
| h2, h4 | 0 |  | (0.20 |
| lR 7/ | 4.6 |  | (0.3 |
| j | 0 |  | (0.2 |
| g1, g3 | 0 |  | (0.30 |
| g2, g4 | 2.5 |  | (0.40 |
| γ1 | 50( min. | - | - |
| γ2 | 23( min. | - | - |
| γ3 | 50( min. | - | - |
| Cap P23t in accordance with IEC Publication 60061 (sheet 7004-138-2) |
| Electrical and photometric characteristcs |
| Rated values | Voltage | V | 12 | 12 |
|  | Wattage | W | 35 | 30 | 35 | 30 |
| Test voltage | V | 13.2 | 13.2 |
| Objective values | Wattage | W | 40 max. | 37 max. | 40 max. | 37 max. |
|  | Luminous flux | lm | 620 | 515 |  |  |
|  |  | ( % | 15 | 15 |  |  |
| Reference luminous at approximately | 12 V | 460 | 380 |
|  | 13.2 V | 620 | 515 |

6/	To be checked by means of a "Box system". Sheet HS5/4.

7/	The positions of the first and the last turn of the filament are defined by the intersections of the outside of the first and the outside of the last light-emitting turn, respectively, with the plane parallel to and 26 mm distant from the reference plane.

Category HS5 	Sheet HS5/4

Screen projection requirement

This test is used to determine whether a filament light source complies with the requirements by checking whether:

(a)	The passing-beam filament is correctly positioned relative to the reference axis and the reference plane; and whether

(b)	The driving-beam filament is correctly positioned relative to the passing-beam filament.

| Reference | a | b | c | d | v |
| --- | --- | --- | --- | --- | --- |
| Dimensions | d1+0.6 | d1+0.8 | d2+1.2 | d2+1.6 | 2.5 |

d1 : Diameter of the passing-beam filament

d2 : Diameter of the driving-beam filament

| Reference | h | k |
| --- | --- | --- |
| Dimensions | 6.0 | 0.5 |

The filaments shall lie entirely within the limits shown.

The centre of the filament shall lie within the limits of dimension k.

Category HS5A 	Sheet HS5A/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by three ramps inside surface.

2/	The reference axis is perpendicular to the reference plane and passing through the centre of the 23 mm cap diameter.

3/	Glass bulb and supports shall not exceed the envelope as indicated in Figure 1. The envelope is concentric to the reference axis.

4/	Glass bulb shall be optically distortion free within the angles (1 and (2. This requirement applies to the whole bulb circumference within the angles (1 and (2.

5/	The obscuration shall extend at least to angle (3 and shall extend at least to the cylindrical part of the bulb on the whole top circumference.

Category HS5A 	Sheet HS5A/2

Category HS5A 	Sheet HS5A/3

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | 12 V | 12 V |
| e | 26 | - | - |
| lC 6/ | 4.6 | (0.5 | (0.3 |
| k | 0 | (0.4 | (0.2 |
| h1, h3 | 0 | (0.3 | (0.15 |
| h2, h4 | 0 | (0.4 | (0.2 |
| lR 6/ | 4.6 | (0.5 | (0.3 |
| j | 0 | (0.6 | (0.3 |
| g1, g3 | 0 | (0.6 | (0.3 |
| g2, g4 | 2.5 | (0.4 | (0.2 |
| γ1 | 50( min. | - | - |
| γ2 | 23( min. | - | - |
| γ3 | 50( min. | - | - |
| Cap PX23t in accordance with IEC Publication 60061 (sheet 7004-138A-1) |
| Electrical and photometric characteristics |
| Rated values | Voltage | V | 12 7/ | 12 7/ |
|  | Wattage | W | 45 | 40 | 45 | 40 |
| Test voltage | V | 13.2 | 13.2 |
| Objective Values | Wattage | W | 50 max. | 45 max. | 50 max. | 45 max. |
|  | Luminous flux | lm | 750 | 640 |  |  |
|  |  | ( % | 15 | 15 |  |  |
| Reference luminous at approximately | 12 V | 550 lm | 470 lm |
|  | 13.2 V | 750 lm | 640 lm |

6/	The positions of the first and the last turn of the filament are defined by the intersections of the outside of the first and the outside of the last light-emitting turn, respectively, with the plane parallel to and 26 mm distant from the reference plane.

7/	The values indicated in the left-hand columns relate to the driving-beam filament and those indicated in the right-hand columns to the passing-beam filament.

Category HS6	Sheet HS6/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

# Figure 1 - Main drawings

1/	The reference plane is the plane formed by the underside of the three radiused tabs of the cap.

2/	The reference axis is perpendicular to the reference plane and crosses the intersection of the two perpendiculars as indicated in Figure 2 on sheet HS6/2.

3/	Glass bulb and supports shall not exceed the envelope as indicated.  The envelope is concentric to the reference axis.

4/	The filament light source shall be rotated in the measuring holder until the reference lug contacts plane C of the holder.

5/	Plane V-V is the plane perpendicular to the reference plane passing through the reference axis and parallel to plane C.

Category HS6	Sheet HS6/2

6/	Glass bulb shall be optically distortion-free axially and cylindrically within the angles ( and (. This requirement applies to the whole bulb circumference within the angles ( and ( and does not need to be verified in the area covered by the opaque coating.

7/	The opaque coating shall extend at least to the cylindrical part of the bulb on the whole bulb top circumference.  It shall moreover extend at least to a plane parallel to the reference plane where ( crosses the outer bulb surface as shown in Figure 3 (view in direction B as indicated on sheet HS6/1).

8/	Offset of passing-beam filament in relation to the bulb axis is measured in two planes parallel to the reference plane where the projection of the outside end turns nearest to and farthest from the reference plane crosses the passing-beam filament axis.

9/	Light shall be blocked over the cap end of the bulb extending to angle (.  This requirement applies in all directions around the reference axis.

Category HS6	Sheet HS6/3

10/	Dimensions j, k and p are measured from the centre of the passing-beam filament to the centre of the driving-beam filament.

11/	Dimensions m and n are measured from the reference axis to the centre of the passing-beam filament.

12/	Both filaments axis are to be held within a 2( tilt with respect to the reference axis about the centre of the respective filament.

13/	Note concerning the filament diameters: for the same manufacturer, the design filament diameter of standard (étalon) filament light source and filament light source of normal production shall be the same.

14/	For both the driving-beam and the passing-beam filament distortion shall not exceed (5 per cent of filament diameter from a cylinder.

15/	The metal free zone limits the location of lead wires within the optical path.  No metal parts shall be located in the shaded area as seen in Figure 6.

Category HS6	Sheet HS6/4

| Dimensions in mm | Tolerance |
| --- | --- |
|  | Filament light sources of normal production | Standard filament light source |
| d1 13/, 17/ | 1.4 max. | - | - |
| d2 13/, 17/ | 1.4 max. | - | - |
| e 16/ | 29.45 | (0.20 | (0.10 |
| f1 16/ | 4.4 | (0.50 | (0.25 |
| f2 16/ | 4.4 | (0.50 | (0.25 |
| g 8/, 17/ | 0.5 d1 | (0.50 | (0.30 |
| h 8/ | 0 | (0.40 | (0.20 |
| j 10/ | 2.5 | (0.30 | (0.20 |
| k 10/ | 2.0 | (0.20 | (0.10 |
| m 11/ | 0 | (0.24 | (0.20 |
| n 11/ | 0 | (0.24 | (0.20 |
| p 10/ | 0 | (0.30 | (0.20 |
| ( | 42° min. | - | - |
| ( | 52° min. | - | - |
| ( | 43° | +0° / -5° | +0° / -5° |
| ( 9/ | 41° | (4° | (4° |
| Cap PX26.4t in accordance with IEC Publication 60061 (sheet 7004-128-3) |
| Electrical and photometric characteristics 18/ |
| Rated values | Volts | 12 | 12 |
|  | Watts | 40 | 35 | 40 | 35 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 45 max. | 40 max. | 45 max. | 40 max. |
|  | Luminous flux | 900 ( 15 % | 600 ( 15 % |  |
| Reference luminous flux at approximately | 12 V | 630/420 |
|  | 13.2 V | 900/600 |

16/	The ends of the filament are defined as the points where, when the viewing direction is direction A as shown on sheet HS6/1, the projection of the outside of the end turns crosses the filament axis.

17/	d1 is the actual diameter of the passing-beam filament.

d2 is the actual diameter of the driving-beam filament.

18/	The values indicated in the left-hand columns relate to the driving-beam filament and those in the right-hand columns to the passing-beam filament.

Categories P13W and PW13W	Sheet P13W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.0 mm.

3/	No opaque parts other than filament turns shall be located in the shaded area indicated in Figure 2. This applies to the rotational body within the angles (1 + (2.

Categories P13W and PW13W	Sheet P13W/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
| e 5/ | P13W | 25.0 4/ | 25.0 ( 0.25 |
|  | PW13W | 19.25 4/ | 19.25 ( 0.25 |
| f 5/ | 4.3 4/ | 4.3 ( 0.25 |
| (1 6/ | 30.0° min. | 30.0° min. |
| (2 6/ | 58.0° min. | 58.0° min. |
| P13W Cap PG18.5d-1 PW13W Cap WP3.3x14.5-7 | in accordance with IEC Publication 60061 (sheet 7004-147-1) in accordance with IEC Publication 60061 (sheet 7004-164-2) |
| Electrical and photometric characteristics |
| Rated values | Voltage | V | 12 | 12 |
|  | Wattage | W | 13 | 13 |
| Test voltage | V | 13.5 | 13.5 |
| Objective values | Wattage | W | 19 max. | 19 max. |
|  | Luminous flux | lm | 250 |  |
|  |  | ( | +15 % / –20 % |  |
| Reference luminous flux at approximately 13.5 V | 250 lm |

4/	To be checked by means of a "Box system"; sheet P13W/3.

5/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires, the projection of the outside of the end turns crosses the filament axis.

6/	No part of the cap beyond the reference plane shall interfere with angle (2 as shown in Figure 1 on sheet P13W/1. The bulb shall be optically distortion free within the angles (1+ (2.
These requirements apply to the whole bulb circumference.

Categories P13W and PW13W	Sheet P13W/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | p | q | u1,u2 | r,s | t,v |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 1.7 | 1.9 | 0.3 | 2.6 | 0.9 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 2.45 | 0.6 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet P13W/2, footnote 4/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Sheet P19W/1

Categories P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W, PW19W, PWY19W and PWR19W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	The light emitted from normal production filament light sources shall be white for categories P19W, PS19W and PW19W; amber for categories PY19W, PSY19W and PWY19W; red for categories PR19W, PSR19W and PWR19W (see also footnote 8/).

Sheet P19W/2

Categories P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W, PW19W, PWY19W and PWR19W

| Dimensions in mm 4/ | Filament light sources of normal production | Standard filament light source 8/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e 5/, 6/ | P19W, PS19W, PY19W, PSY19W, PR19W, PSR19W |  | 24.0 |  | 24.0 |
|  | PW19W, PWY19W, PWR19W |  | 18.1 |  | 18.1 |
| f 5/, 6/ |  | 4.0 |  | 4.0 ( 0.2 |
| ( 7/ | 58° |  |  | 58° min. |
| P19W Cap PGU20-1 PY19W Cap PGU20-2 PR19W Cap PGU20-5 PS19W Cap PG20-1 PSY19W Cap PG20-2 PSR19W Cap PG20-5 | in accordance with IEC Publication 60061 (sheet 7004-127-2) |
| PW19W Cap WP3.3x14.5-1 PWY19W Cap WP3.3x14.5-2 PWR19W Cap WP3.3x14.5-5 | in accordance with IEC Publication 60061 (sheet 7004-164-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 19 | 19 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts |  | 20 max. | 20 max. |
|  | Luminous flux | P19W PS19W PW19W | 350 ( 15 % |  |
|  |  | PY19W PSY19W PWY19W | 215 ( 20 % |  |
|  |  | PR19W PSR19W PWR19W | 80 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V | White: 350 lm Amber: 215 lm Red: 80 lm |

4/	For categories PS19W, PSY19W and PSR19W, dimensions may be checked with O-ring removed to assure the correct mounting during testing.

5/	The filament position is checked by means of a "Box system"; sheet P19W/3.

6/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires as showed in the drawing on sheet P19W/1, the projection of the outside of the end turns crosses the filament axis.

7/	No part of the cap beyond the reference plane shall interfere with angle (. The bulb shall be optically distortion free within the angle 2( + 180°.

8/	The light emitted from standard filament light sources shall be white for categories P19W, PS19W and PW19W; white or amber for categories PY19W, PSY19W and PWY19W; white or red for categories PR19W, PSR19W and PWR19W.

Sheet P19W/3

Categories P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W, PW19W, PWY19W and PWR19W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

| P19W, PY19W, PR19W, PS19W, PSY19W, PSR19W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 2.9 | 3.9 | 0.5 | 5.2 | 3.8 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PW19W, PWY19W and PWR19W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 2.5 | 2.5 | 0.4 | 5.2 | 3.8 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet P19W/2, footnote 6/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Category P21W 	Sheet P21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 6, 12 V |  | 31.8 3/ |  | 31.8 ( 0.3 |
|  | 24 V | 30.8 | 31.8 | 32.8 |  |
| f | 12 V | 5.5 | 6.0 | 7.0 | 6.0 ( 0.5 |
|  | 6 V |  |  | 7.0 |  |
| Lateral deviation 1/ | 6, 12 V |  |  | 3/ | 0.3 max. |
|  | 24 V |  |  | 1.5 |  |
| ( | 75° | 90° | 105° | 90° ( 5° |
| Cap BA15s in accordance with IEC Publication 60061 (sheet 7004-11A-9) 2/ |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 27.6 max. | 26.5 max. | 29.7 max. | 26.5 max. |
|  | Luminous flux | 460 ( 15 % |  |
| Reference luminous flux: 460 lm at approximately 13.5 V |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the pins.

2/	Filament light sources with cap BA15d may be used for special purposes; they have the same dimensions.

3/	To be checked by means of a "Box system"; sheet P21W/2.

4/	In this view the filament of the 24 V type may be straight or V-shaped.  If it is straight, the screen projection requirements, sheet P21W/2, apply. If it is V-shaped, the filament ends shall be at the same distance within ±3 mm from the reference plane.

Category P21W 	Sheet P21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within (15°, to the plane through the centre line of the pins (P21W) or of the reference pin (PY21W and PR21W) and the reference axis, whether a filament light source complies with the requirements.

Side elevation 	Front elevation

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 9.0 | 1.0 |

Test procedures and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament.

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

Category P21/4W 	Sheet P21/4W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 31.8 1/ |  | 31.8 ( 0.3 |
| f |  |  | 7.0 | 7.0 + 0 /- 2 |
| Lateral deviation |  |  | 1/ | 0.3 max. 2/ |
| x,y | 1/ | 2.8 ( 0.5 |
| ( | 75° 1/ | 90° 1/ | 105° 1/ | 90° ( 5° |
| Cap BAZ15d in accordance with IEC Publication 60061 (sheet 7004-11C-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 21 | 4 | 21 | 4 | 21/4 |
| Test voltage | Volts | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 26.5 max. | 5.5 max. | 29.7 max. | 8.8 max. | 26.5/5.5 max. |
|  | Luminous flux | 440 | 15 | 440 | 20 |  |
|  | ( % | 15 | 20 | 15 | 20 |  |
| Reference luminous flux: 440 lm and 15 lm at approximately 13.5 V |

1/	These dimensions shall be checked by means of a "Box system"3/ based on the dimensions and tolerances shown above. "x" and "y" refer to the major (high wattage) filament, not to the reference axis. Means of increasing the positioning accuracy of the filament and of the cap-holder assembly are under consideration.

2/	Maximum lateral deviation of the major filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

3/	The "Box system" is the same as for filament light source P21/5W; see sheets P21/5W/2 to 3.

Category P21/5W 	Sheet P21/5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 6, 12 V |  | 31.8 1/ |  | 31.8 ( 0.3 |
|  | 24 V | 30.8 | 31.8 | 32.8 |  |
| f | 6, 12 V |  |  | 7.0 | 7.0 + 0 /- 2 |
| Lateral deviation 2/ | 6, 12 V |  |  | 1/ | 0.3 max. |
|  | 24 V |  |  | 1.5 |  |
| x, y | 6, 12 V |  | 1/ |  | 2.8 ( 0.3 |
| x | 24 V 3/ | -1.0 | 0 | 1.0 |  |
| y | 24 V 3/ | 1.8 | 2.8 | 3.8 |  |
| ( |  | 75° | 90° | 105° | 90° ( 5° |
| Cap BAY15d in accordance with IEC Publication 60061 (sheet 7004-11B-7) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 21 | 5 | 21 | 5 | 21 | 5 | 21/5 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 27.6 max. | 6.6 max. | 26.5 max. | 6.6 max. | 29.7 max. | 11.0 max. | 26.5 and 6.6 max. |
|  | Luminous flux | 440 | 35 | 440 | 35 | 440 | 40 |  |
|  | ( % | 15 | 20 | 15 | 20 | 15 | 20 |  |
| Reference luminous flux: 440 and 35 lm at approximately 13.5 V |
| For the notes see sheet P21/5W/2 |

Category P21/5W 	Sheet P21/5W/2

1/	These dimensions shall be checked by means of a "Box system". See sheets P21/5W/2 and P21/5W/3. "x" and "y" refer to the major (high wattage) filament, not to the reference axis.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

3/	In this view the filaments of the 24 V type may be straight or V-shaped.  If the filaments are straight, the screen projection requirements apply. If they are V-shaped, the ends of each filament shall be at the same distance within ±3 mm from the reference plane.

Screen projection requirements

This test is used to determine, by checking whether:

(a)	The major (high wattage) filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the centres of the pins and the reference axis; and whether

(b)	The minor (low wattage) filament is correctly positioned relative to the major (high wattage) filament, whether a filament light source complies with the requirements.

Test procedure and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. (i.e. 15°). The holder is then so rotated that an end view of the major filament is seen on the screen on which the image of the filament is projected. The end view of that filament shall be obtained within the angular displacement tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical, the reference pin to the right and the major filament seen end-on:

2.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament;

2.2.	The projection of the minor filament shall lie entirely:

2.2.1.	Within a rectangle of width "c" and height "d" having its centre at a distance "v" to the right of and at a distance "u" above  the theoretical position of the centre of the major filament;

2.2.2.	Above a straight line tangential to the upper edge of the projection of the major filament and rising from left to right at an angle of 25°.

2.2.3.	To the right of the projection of the major filament.

3.	Front elevation

The filament light source being placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to axis of the major filament:

3.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "h", centred on the theoretical position of the centre of the filament;

3.2.	The centre of the major filament shall not be offset by more than distance "k" from the reference axis.

3.3.	The centre of the minor filament axis shall not be offset from the reference axis by more than (2 mm ((0.4 mm for standard filament light sources).

Category P21/5W 	Sheet P21/5W/3

Dimensions in mm

| Reference | a | b | c | d | u | v |
| --- | --- | --- | --- | --- | --- | --- |
| Dimensions | 3.5 | 3.0 | 4.8 | 2.8 |

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimensions | 3.5 | 9.0 | 1.0 |

Sheet P24W/1

Categories P24W, PX24W, PY24W, PR24W, PS24W, PSX24W, PSY24W, PSR24W, PW24W, 
	PWY24W and PWR24W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	The light emitted from normal production filament light sources shall be white for categories P24W, PX24W, PS24W, PSX24W and PW24W; amber for categories PY24W, PSY24W and PWY24W; red for categories PR24W, PSR24W and PWR24W (see also footnote 8/).

Sheet P24W/2

Categories P24W, PX24W, PY24W, PR24W, PS24W, PSX24W, PSY24W, PSR24W, PW24W, PWY24W and PWR24W

| Dimensions in mm 4/ | Filament light sources of normal production | Standard filament light source 8/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e 5/, 6/ | P24W, PY24W, PR24W, PS24W, PSY24W, PSR24W, PX24W, PSX24W |  | 24.0 |  | 24.0 |
|  | PW24W, PWY24W, PWR24W |  | 18.1 |  | 18.1 |
| f 5/, 6/ | P24W, PY24W, PR24W, PS24W, PSY24W, PSR24W, PW24W, PWY24W, PWR24W |  | 4.0 |  | 4.0 |
|  | PX24W, PSX24W |  | 4.2 |  | 4.2 |
| ( 7/ | 58.0° |  |  | 58.0° min. |
| P24W Cap PGU20-3 PX24W Cap PGU20-7 PY24W Cap PGU20-4 PR24W Cap PGU20-6 PS24W Cap PG20-3 PSX24W Cap PG20-7 PSY24W Cap PG20-4 PSR24W Cap PG20-6 | in accordance with IEC Publication 60061 (sheet 7004-127-2) |
| PW24W Cap WP3.3x14.5-3 PWY24W Cap WP3.3x14.5-4 PWR24W Cap WP3.3x14.5-6 | in accordance with IEC Publication 60061 (sheet 7004-164-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 24 | 24 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts |  | 25 max. | 25 max. |
|  | Luminous flux | P24W PS24W PW24W | 500 +10/-20 % |  |
|  |  | PX24W PSX24W | 500 +10/-15 % |  |
|  |  | PY24W PSY24W PWY24W | 300 +15/-25 % |  |
|  |  | PR24W PSR24W PWR24W | 115 +15/-25 % |  |
| Reference luminous flux at approximately | 12 V | White: 345 lm |
|  | 13.2 V | White: 465 lm |
|  | 13.5 V | White: 500 lm Amber: 300 lm Red: 115 lm |

4/	For categories PS24W, PSX24W, PSY24W and PSR24W, dimensions may be checked with O-ring removed to assure the correct mounting during testing.

5/	The filament position is checked by means of a "Box system"; sheet P24W/3.

6/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires as showed in the drawing on sheet P24W/1, the projection of the outside of the end turns crosses the filament axis.

7/	No part of the cap beyond the reference plane shall interfere with angle (. The bulb shall be optically distortion free within the angle 2( + 180°.

8/	The light emitted from standard filament light sources shall be white for categories P24W, PX24W, PS24W, PSX24W and PW24W; white or amber for categories PY24W, PSY24W and PWY24W; white or red for categories PR24W, PSR24W and PWR24W.

Sheet P24W/3

Categories P24W, PX24W, PY24W, PR24W, PS24W, PSX24W, PSY24W, PSR24W, PW24W, PWY24W and PWR24W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

| P24W, PY24W, PR24W, PS24W, PSY24W, PSR24W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 2.9 | 3.9 | 0.5 | 5.2 | 3.8 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PW24W, PWY24W, PWR24W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 2.5 | 2.5 | 0.4 | 5.0 | 3.8 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PX24W, PSX24W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 1.9 | 1.9 | 0.35 | 5.0 | 4.0 |
| Standard filament light sources | 1.5 | 1.5 | 0.25 | 4.7 | 4.0 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet P24W/2, footnote 6/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Category P27W 	Sheet P27W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 27.9 3/ |  | 27.9 ( 0.3 |
| f |  |  | 9.9 | 9.9 + 0 / - 2 |
| Lateral deviation 2/ |  |  | 3/ | 0.0 ( 0.4 |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap W2.5x16d in accordance with IEC Publication 60061 (sheet 7004-104-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 27 | 27 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 32.1 max. | 32.1 max. |
|  | Luminous flux | 475 ( 15 % |  |
| Reference luminous flux: 475 lm at approximately 13.5 V |

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system", sheet P27W/2.

Category P27W 	Sheet P27W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within (15°, to the plane through the centres of the keys and the reference axis, whether a filament light source complies with the requirements.

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 11.9 | 1.0 |

Test procedures and requirements.

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament.

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

Category P27/7W 	Sheet P27/7W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 27.9 3/ |  | 27.9 ( 0.3 |
| f |  |  | 9.9 | 9.9 + 0 / -2 |
| Lateral deviation 2/ |  |  | 3/ | 0.0 ( 0.4 |
| x 4/ |  | 5.1 3/ |  | 5.1 ( 0.5 |
| y 4/ |  | 0.0 3/ |  | 0.0 ( 0.5 |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap W2.5x16q in accordance with IEC Publication 60061 (sheet 7004-104-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 27 | 7 | 27 | 7 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 32.1 max. | 8.5 max. | 32.1 max. | 8.5 max. |
|  | Luminous flux | 475 ( 15 % | 36 ( 15 % |  |
| Reference luminous flux: 475 and 36 lm at approximately 13.5 V |

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system", sheets P27/7W/2 and 3.

4/	"x" and 'y" denote the offset of the axis of the minor (low wattage) filament with respect to the axis of the major (high wattage) filament.

Category P27/7W 	Sheet P27/7W/2

Screen projection requirements

This test is used to determine, by checking whether:

(a)	The major (high wattage) filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the centres of the keys and the reference axis; and whether:

(b)	The minor (low wattage) filament is correctly positioned relative to the major (high wattage) filament, whether a filament light source complies with the requirements.

Test procedure and requirements.

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the major filament is seen on the screen on which the image of the filament is projected. The end view of that filament shall be obtained within the angular displacement tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical, the reference key to the right and the major filament seen end-on:

2.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament;

2.2.	The projection of the minor filament shall lie entirely within a rectangle of width "c" and height "d" having its centre at a distance "u" above the theoretical position of the centre of the major filament.

3.	Front elevation

The filament light source being placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to axis of the major filament:

3.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "h", centred on the theoretical position of the centre of the filament;

3.2.	The centre of the major filament shall not be offset by more than distance "k" from the reference axis;

3.3.	The centre of the minor filament axis shall not be offset from the reference axis by more than (2 mm ((0.4 mm for standard filament light sources).

Category P27/7W 	Sheet P27/7W/3

| Reference | a | b | c | d | u |
| --- | --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 4.8 | 5.1 |

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimension | 3.5 | 11.9 | 1.0 |

Sheet PC16W/1

Categories PC16W, PCY16W, PCR16W, PW16W, PWY16W and PWR16W

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	The light emitted from normal production filament light sources shall be white for category PC16W and PW16W; amber for category PCY16W and PWY16W; red for category PCR16W and PWR16W. 
(see also footnote 7/).

Sheet PC16W/2

Categories PC16W, PCY16W, PCR16W, PW16W, PWY16W and PWR16W

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 7/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e 4/, 5/ | PC16W PCY16W PCR16W |  | 18.5 |  | 18.5 |
|  | PW16W PWY16W PWR16W |  | 17.1 |  | 17.1 |
| f 4/, 5/ |  | 4.0 |  | 4.0 ( 0.2 |
| α 6/ | 54° |  |  | 54° min. |
| PC16W Cap PU20d-1 PCY16W Cap PU20d-2 PCR16W Cap PU20d-7 | in accordance with IEC Publication 60061 (sheet 7004-158-1) |
| PW16W Cap WP3.3x14.5-8 PWY16W Cap WP3.3x14.5-9 PWR16W Cap WP3.3x14.5-10 | in accordance with IEC Publication 60061 (sheet 7004-164-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 16 | 16 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts |  | 17 max. | 17 max. |
|  | Luminous flux | PC16W PW16W | 300 ( 15 % |  |
|  |  | PCY16W PWY16W | 180 ( 20 % |  |
|  |  | PCR16W PWR16W | 70 ( 20 % |  |
| Reference luminous flux at approximately | 13.5 V | White: 300 lm Amber: 180 lm Red: 70 lm |

4/	The filament position is checked by means of a "Box system"; sheet PC16W/3.

5/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires as showed in the drawing on sheet PC16W/1, the projection of the outside of the end turns crosses the filament axis.

6/	No part of the cap beyond the reference plane shall interfere with angle (. The bulb shall be optically distortion free within the angle 2( + 180°.

7/	The light emitted from standard filament light sources shall be white for category PC16W and PW16W; white or amber for category PCY16W and PWY16W; white or red for category PCR16W and PWR16W.

Sheet PC16W/3

Categories PC16W, PCY16W, PCR16W, PW16W, PWY16W and PWR16W

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

| PC16W, PCY16W, PCR16W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 2.9 | 3.9 | 0.5 | 5.2 | 3.8 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

| PW16W, PWY16W and PWR16W | a1 | a2 | b1, b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 2.5 | 2.5 | 0.4 | 5.2 | 3.8 |
| Standard filament light sources | 1.5 | 1.7 | 0.25 | 4.7 | 3.8 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet PC16W/2, footnote 5/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Category PR21W 	Sheet PR21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 4/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 12 V |  | 31.8 3/ |  | 31.8 ( 0.3 |
|  | 24 V | 30.8 | 31.8 | 32.8 |  |
| f | 12 V | 5.5 | 6.0 | 7.0 | 6.0 ( 0.5 |
| Lateral deviation 1/ | 12 V |  |  | 3/ | 0.3 max |
|  | 24 V |  |  | 1.5 |  |
| ( | 75° | 90° | 105° | 90° ( 5° |
| Cap BAW15s in accordance with IEC Publication 60061 (sheet 7004-11E-1) |
| Electrical and photometric characteristics |
| Rated values: | Volts | 12 | 24 | 12 |
|  | Watts | 21 | 21 |
| Test voltage: | Volts | 13.5 | 28.0 |  |
| Objective values: | Watts | 26.5 max. | 29.7 max. | 26.5 max. |
|  | Luminous flux: | 110 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 460 lm Red: 110 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

2/	The light emitted from normal production filament light sources shall be red (see also footnote 4/).

3/	To be checked by means of a "Box system", sheet P21W/2.

4/	The light emitted from standard filament light sources shall be white or red.

5/	In this view the filament of the 24 V type may be straight or V-shaped.  If it is straight, the screen projection requirements, sheet P21W/2, apply. If it is V-shaped, the filament ends shall be at the same distance within (3 mm from the reference plane.

Category PR21/4W 	Sheet PR21/4W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production 5/ | Standard filament light source 6/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 31.8 1/ |  | 31.8 ( 0.3 |
| f |  |  | 7.0 | 7.0 + 0 / -2 |
| Lateral deviation |  |  | 1/ | 0.3 max.2/ |
| x,y | 1/ | 2.8 ( 0.5 |
| ( | 75° 1/ | 90° 1/ | 105° 1/ | 90° ( 5° |
| Cap BAU15d in accordance with IEC Publication 60061 (sheet 7004-19-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 4/ | 12 |
|  | Watts | 21 | 4 | 21 | 4 | 21/4 |
| Test voltage | Volts | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 26.5 max. | 5.5 max. | 29.7 max. | 8.8 max. | 26.5/5.5 max. |
|  | Luminous flux | 105 | 4 | 105 | 5 |  |
|  | ( % | 20 | 25 | 20 | 25 |  |
| Reference luminous flux at approximately 13.5 V: | White: 440 lm and 15 lm Red: 105 lm and 4 lm |

1/	These dimensions shall be checked by means of a "Boxsystem"3 based on the dimensions and tolerances shown above. "x" and "y" refer to the major (high wattage) filament, not to the reference axis. Means of increasing the positioning accuracy of the filament and of the cap-holder assembly are under consideration.

2/	Maximum lateral deviation of the major filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

3/	The "Box system" is the same as for filament light source P21/5W; see sheets P21/5W/2 to 3.

4/	The 24-volt filament light source is not recommended for future embodiments.

5/	The light emitted from normal production filament light sources shall be red (see also footnote 6/).

6/	The light emitted from standard filament light sources shall be white or red.

Category PR21/5W 	Sheet PR21/5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production 4/ | Standard filament light source 5/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 12 V |  | 31.8 1/ |  | 31.8 ( 0.3 |
|  | 24 V | 30.8 | 31.8 | 32.8 |  |
| f | 12 V |  |  | 7.0 | 7.0 + 0 / -2 |
| Lateral deviation 2/ | 12 V |  |  | 1/ | 0.3 max. |
|  | 24 V |  |  | 1.5 |  |
| x, y | 12 V |  | 1/ |  | 2.8 ( 0.3 |
| x | 24 V 3/ | -1.0 | 0 | 1.0 |  |
| y | 24 V 3/ | 1.8 | 2.8 | 3.8 |  |
| ( |  | 75° | 90° | 105° | 90° ( 5° |
| Cap BAW15d in accordance with IEC Publication 60061 (sheet 7004-11E-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 21 | 5 | 21 | 5 | 21/5 |
| Test voltage | Volts | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 26.5 max. | 6.6 max. | 29.7 max. | 11.0 max. | 26.5 and 6.6 max. |
|  | Luminous flux ( % | 105 | 8 | 105 | 10 |  |
|  | ± % | 20 | 25 | 20 | 25 |  |
| Reference luminous flux at approximately 13.5 V: | White: 440 lm and 35 lm Red: 105 lm and 8 lm |

1/	See footnote 1/ on sheet P21/5W/2.

2/	See footnote 2/ on sheet P21/5W/2.

3/	See footnote 3/ on sheet P21/5W/2.

4/	The light emitted from normal production filament light sources shall be red (see also footnote 5/).

5/	The light emitted from standard filament light sources shall be white or red.

Category PR27/7W 	Sheet PR27/7W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 6/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 27.9 3/ |  | 27.9 ( 0.3 |
| f |  |  | 9.9 | 9.9 + 0 / -2 |
| Lateral deviation 2/ |  |  | 3/ | 0.0 ( 0.4 |
| x 4/ |  | 5.1 3/ |  | 5.1 ( 0.5 |
| y 4/ |  | 0.0 3/ |  | 0.0 ( 0.5 |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap WU2.5x16q in accordance with IEC Publication 60061 (sheet 7004-104D-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 27 | 7 | 27 | 7 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 32.1 max. | 8.5 max. | 32.1 max. | 8.5 max. |
|  | Luminous flux | 110 ( 20 % | 9 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 475 and 36 lm Red: 110 and 9 lm |

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system", sheets P27/7W/2 and 3.

4/	"x" and 'y" denote the offset of the axis of the minor (low wattage) filament with respect to the axis of the major (high wattage) filament.

5/	The light emitted from normal production filament light sources shall be red (see also footnote 6/).

6/	The light emitted from standard filament light sources shall be white or red.

Category PSX26W	Sheet PSX26W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The reference plane is defined by the meeting points of the cap-holder fit.

2/	No actual filament diameter restrictions apply but the objective is d max. = 1.1 mm.

3/	No opaque parts other than filament turns shall be located in the shaded area indicated in Figure 2. This applies to the rotational body within the angles (1 + (2.

Category PSX26W	Sheet PSX26W/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
| e 5/ | 24.0 4/ | 24.0 ( 0.25 |
| f 5/ | 4.2 4/ | 4.2 ( 0.25 |
| (1 6/ | 35.0° min. | 35.0° min. |
| (2 6/ | 58.0° min. | 58.0° min. |
| Cap PG18.5d-3 | in accordance with IEC Publication 60061 (sheet 7004-147-1) |
| Electrical and photometric characteristics |
| Rated values | Voltage | V | 12 | 12 |
|  | Wattage | W | 26 | 26 |
| Test voltage | V | 13.5 | 13.5 |
| Objective values | Wattage | W | 26 max. | 26 max. |
|  | Luminous flux | lm | 500 |  |
|  |  | ( | +10 % / -10 % |  |
| Reference luminous flux at approximately 12 V | 345 lm |
| Reference luminous flux at approximately 13.2 V | 465 lm |
| Reference luminous flux at approximately 13.5 V | 500 lm |

4/	To be checked by means of a "Box system"; sheet PSX26W/3.

5/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires, the projection of the outside of the end turns crosses the filament axis.

6/	No part of the cap beyond the reference plane shall interfere with angle (2 as shown in Figure 1 on sheet PSX26W/1. The bulb shall be optically distortion free within the angles (1+ (2.
These requirements apply to the whole bulb circumference.

Category PSX26W	Sheet PSX26W/3

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane, whether a filament light source complies with the requirements.

|  | a1 | a2 | b1,b2 | c1 | c2 |
| --- | --- | --- | --- | --- | --- |
| Filament light sources of normal production | 1.7 | 1.7 | 0.30 | 5.0 | 4.0 |
| Standard filament light sources | 1.5 | 1.5 | 0.25 | 4.7 | 4.0 |

The filament position is checked in two mutually perpendicular planes, one of them being the plane through the lead-in wires.

The ends of the filament as defined on sheet PSX26W/2, footnote 4/, shall lie between Z1 and Z2 and between the lines Z3 and Z4.

The filament shall lie entirely within the limits shown.

Category PY21W 	Sheet PY21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 4/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 12 V |  | 31.8 3/ |  | 31.8 ( 0.3 |
|  | 24 V | 30.8 | 31.8 | 32.8 |  |
| f | 12 V |  |  | 7.0 | 7.0 +0 / -2 |
| Lateral deviation 1/ | 12 V |  |  | 3/ | 0.3 max. |
|  | 24 V |  |  | 1.5 |  |
| ( | 75° | 90° | 105° | 90° ( 5° |
| Cap BAU15s in accordance with IEC Publication 60061 (sheet 7004-19-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 26.5 max. | 29.7 max. | 26.5 max. |
|  | Luminous flux | 280 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 460 lm Amber: 280 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

2/	The light emitted from production filament light sources shall be amber (see also footnote 4/).

3/	To be checked by means of a "Box system"; sheet P21W/2.

4/	The light emitted from standard filament light sources shall be amber or white.

5/	In this view the filament of the 24 V type may be straight or V-shaped.  If it is straight, the screen projection requirements, sheet P21W/2, apply. If it is V-shaped, the filament ends shall be at the same distance within ±3 mm from the reference plane.

Category PY21/5W 	Sheet PY21/5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production 3/ | Standard filament light source 4/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 28.6 1/ |  | 28.6 ( 0.3 |
| f |  |  | 7.0 | 7.0 + 0/- 2 |
| Lateral deviation 2/ |  |  | 1/ | 0.3 max. |
| x, y |  | 1/ |  | 2.8 ( 0.3 |
| ( | 75° | 90° | 105° | 90° ( 5° |
| Cap BA15d-3 (100°/130°) in accordance with IEC Publication 60061 (sheet 7004-173-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 5 | 21/5 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 6.6 max. | 26.5 and 6.6 max. |
|  | Luminous flux | 270 | 21 |  |
|  | ( % | 20 | 20 |  |
| Reference luminous flux at approximately 13.5 V | White: 440 lm and 35 lm Amber: 270 lm and 21 lm |

1/	These dimensions shall be checked by means of a "Box system". See sheets PY21/5W/2 and PY21/5W/3. "x" and "y" refer to the major (high wattage) filament, not to the reference axis.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

3/	The light emitted from normal production filament light sources shall be amber (see also note 4/).

4/	The light emitted from standard filament light sources shall be white or amber.

Category PY21/5W 	Sheet PY21/5W/2

Screen projection requirements

This test is used to determine, by checking whether:

(a)		The major (high wattage) filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the centres of the pins and the reference axis; and whether

(b)	The minor (low wattage) filament is correctly positioned relative to the major (high wattage) filament, whether a filament light source complies with the requirements.

Test procedure and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. (i.e. 15°). The holder is then so rotated that an end view of the major filament is seen on the screen on which the image of the filament is projected. The end view of that filament shall be obtained within the angular displacement tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical, the reference pin to the right and the major filament seen end-on:

2.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament;

2.2.	The projection of the minor filament shall lie entirely:

2.2.1.	Within a rectangle of width "c" and height "d" having its centre at a distance "v" to the right of and at a distance "u" above  the theoretical position of the centre of the major filament;

2.2.2.	Above a straight line tangential to the upper edge of the projection of the major filament and rising from left to right at an angle of 25°.

2.2.3.	To the right of the projection of the major filament

3.	Front elevation

The filament light source being placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to axis of the major filament:

3.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "h", centred on the theoretical position of the centre of the filament;

3.2.	The centre of the major filament shall not be offset by more than distance "k" from the reference axis.

3.3.	The centre of the minor filament axis shall not be offset from the reference axis by more than (2 mm ((0.4 mm for standard filament light sources).

Category PY21/5W 	Sheet PY21/5W/3

Dimensions in mm

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimensions | 3.5 | 9.0 | 1.0 |

Category PY27/7W 	Sheet PY27/7W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 6/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 27.9 3/ |  | 27.9 ( 0.3 |
| f |  |  | 9.9 | 9.9 + 0 / -2 |
| Lateral deviation 2/ |  |  | 3/ | 0.0 ( 0.4 |
| x 4/ |  | 5.1 3/ |  | 5.1 ( 0.5 |
| y 4/ |  | 0.0 3/ |  | 0.0 ( 0.5 |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap WX2.5x16q in accordance with IEC Publication 60061 (sheet 7004-104A-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 27 | 7 | 27 | 7 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 32.1 max. | 8.5 max. | 32.1 max. | 8.5 max. |
|  | Luminous flux | 280 ( 15 % | 21 ( 15 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 475 and 36 lm Amber: 280 and 21 lm |

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system", sheets P27/7W/2 and 3.

4/	"x" and 'y" denote the offset of the axis of the minor (low wattage) filament with respect to the axis of the major (high wattage) filament.

5/	The light emitted from filament light sources of normal production shall be amber (see also footnote 6/).

6/	The light emitted from standard filament light sources shall be amber or white.

Category R2 	Sheet R2/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Electrical and photometric characteristics |
| --- |
|  | Filament light sources of normal production | Standard filament light source |
| Rated values | Volts | 6 4/ | 12 4/ | 24 4/ | 12 4/ |
|  | Watts | 45 | 40 | 45 | 40 | 55 | 50 | 45 | 40 |
| Test voltage | Volts | 6.3 | 13.2 | 28.0 | 13.2 |
| Objective values | Watts | 53 max. | 47 max. | 57 max. | 51 max. | 76 max. | 69 max. | 52 +0 % -10 % | 46 (5 % |
|  | Luminous flux | 720 min. | 570 (15 % | 860 min. | 675 (15 % | 1,000 min. | 860 (15 % |  |
| Measuring flux 5/ | - | 450 | - | 450 | - | 450 |  |
| Reference luminous flux at approximately 12 V | 700 | 450 |

1/	The reference axis is perpendicular to the reference plane and passes through the centre of the 45 mm cap diameter.

2/	The colour of the light emitted shall be white or selective-yellow.

3/	No part of the cap shall, by reflection of light emitted by the passing-beam filament, throw any stray rising ray when the filament light source is in the normal operating position on the vehicle.

4/	The values indicated on the left and on the right refer to the driving-beam filament and the passing-beam filament respectively.

5/	Measuring luminous flux according to the provisions for filament light sources with an internal shield to produce the cut-off.

Category R2 	Sheet R2/2

Position and dimensions (in mm) of shield and filaments

The drawings are not mandatory with respect to the design of the shield and filaments.

Category R2 	Sheet R2/3

| Filaments and shield position and dimensions 1/ |
| --- |
| Dimensions in mm | Tolerance |
|  | Filament light sources of normal production | Standard filament light source |
|  | 6 V 12 V 24 V | 12 V |
| a | 0.60 | (0.35 | (0.15 |
| b1/30.0 2/ b1/33.0 | 0.20 b1/30.0 mv 3/ | (0.35 | (0.15 |
| b2/30.0 2/ b2/33.0 | 0.20 b2/30.0 mv 3/ | (0.35 | (0.15 |
| c/30.0 2/ c/33.0 | 0.50 c/30.0 mv 3/ | (0.30 | (0.15 |
| e | 6, 12 V 24 V | 28.5 28.8 | (0.35 | (0.15 |
| f | 6, 12 V 24 V | 1.8 2.2 | (0.40 | (0.20 |
| g | 0 | (0.50 | (0.30 |
| h/30.0 2/ h/33.0 | 0 h/30.0 mv 3/ | (0.50 | (0.30 |
| 1/2(p-q) | 0 | (0.60 | (0.30 |
| IC | 5.5 | (1.50 | (0.50 |
| ( 4/ | 15( nom. |  |  |
| Cap P45t-41 in accordance with IEC Publication 60061 (sheet 7004-95-5) |

1/	The position and dimensions of the shield and filaments shall be checked by means of the method of measurement as described in IEC Publication 60809.

2/	To be measured at the distance from the reference plane indicated in millimetres behind the stroke.

3/	mv = measured value.

4/	The angle ( is only for shield design and has not to be checked on finished filament light sources.

Category R5W and RR5W	Sheet R5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 4/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 17.5 | 19.0 | 20.5 | 19.0 ( 0.3 |
| Lateral deviation 2/ |  |  | 1.5 | 0.3 max. |
| ( | 60° | 90° | 120° | 90° ( 5° |
| Cap: | R5W: BA15s RR5W: BAW15s | in accordance with IEC Publication 60061 | (sheet 7004-11A-9) 1/ (sheet 7004-11E-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 5/ | 12 | 24 | 12 |
|  | Watts | 5 | 5 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 5.5 max. | 7.7 max. | 5.5 max. |
|  | Luminous flux | R5W | 50 ( 20 % |  |
|  |  | RR5W | 5/ | 12 ( 25 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 50 lm Red: 12 lm |

1/	Filament light sources with cap BA15d may be used for special purposes; they have the same dimensions.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

3/	The light emitted from filament light sources of normal production shall be white for category R5W and red for category RR5W (see also footnote 4/).

4/	The light emitted from standard filament light sources shall be white for category R5W; white or red for category RR5W.

5/	Within RR5W no 6 V rated voltage type specified.

Categories R10W, RY10W and RR10W	Sheet R10W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 4/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 17.5 | 19.0 | 20.5 | 19.0 ( 0.3 |
| Lateral deviation 2/ |  |  | 1.5 | 0.3 max. |
| ( | 60° | 90° | 120° | 90° ( 5° |
| Cap | R10W: BA15s RY10W: BAU15s RR10W: BAW15s | in accordance with IEC Publication 60061 | (sheet 7004-11A-9) 1/ (sheet 7004-19-2) (sheet 7004-11E-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 5/ | 12 | 24 | 12 |
|  | Watts | 10 | 10 |
| Test voltage | Volts | 6.75 | 13.5 | 28 | 13.5 |
| Objective values | Watts | R10W RY10W | 11 max. | 14 max. | 11 max. |
|  |  | RR10W | 5/ | 11 max. |  | 11 max. |
|  | Luminous flux | R10W | 125 ( 20 % |  |
|  |  | RY10W | 75 ( 20 % |  |
|  |  | RR10W | 5/ | 30 ( 25 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 125 lm Amber: 75 lm Red: 30 lm |

1/	Filament light sources R10W with cap BA15d may be used for special purposes; they have the same dimensions.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of the reference pin.

3/	The light emitted from filament light sources of normal production shall be white for category R10W, amber for category RY10W and red for category RR10W (see also footnote 4/)

4/	The light emitted from standard filament light sources shall be white for category R10W; white or amber for category RY10W; white or red for category RR10W.

5/	Within RR10W no 6 V rated voltage type specified.

Categories S1 and S2 	Sheet S1/S2/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

1/	The colour of the light emitted shall be white or selective-yellow.

2/	The reference plane is perpendicular to the reference axis and touches the upper surface of the lug having a width of 4.5 mm.

3/	Plane V-V contains the reference axis and the centre line of the lugs.

4/	Plane H-H (the normal position of the shield) is perpendicular to plane V-V and contains the reference axis.

Categories S1 and S2 	Sheet S1/S2/2

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 32.35 | 32.70 | 33.05 | 32.7 ( 0.15 |
| f | 1.4 | 1.8 | 2.2 | 1.8 ( 0.2 |
| l | 4.0 | 5.5 | 7.0 | 5.5 ( 0.5 |
| c 5/ | 0.2 | 0.5 | 0.8 | 0.5 ( 0.15 |
| b 5/ | -0.15 | 0.2 | 0.55 | 0.2 ( 0.15 |
| a 5/ | 0.25 | 0.6 | 0.95 | 0.6 ( 0.15 |
| h | -0.5 | 0 | 0.5 | 0 ( 0.2 |
| g | -0.5 | 0 | 0.5 | 0 ( 0.2 |
| ( 5/, 6/ | -2°30' | 0° | +2°30' | 0° ( 1° |
| Cap BA20d in accordance with IEC Publication 60061 (sheet 7004-12-7) |
| Electrical and photometric characteristics |
| Rated values | Volts | S1 | 6 7/ | 12 7/ | 6 |
|  |  | S2 |  |  | 12 |
|  | Watts | S1 | 25 | 25 | 25 | 25 | 25 | 25 |
|  |  | S2 | 35 | 35 | 35 | 35 | 35 | 35 |
| Test voltage | Volts | S1 | 6.75 | 13.5 | 6.75 |
|  |  | S2 | 6.3 | 13.5 | 13.5 |
| Objective values | Watts | S1 | 25 ( 5 % | 25 ( 5 % | 25 ( 5 % | 25 ( 5 % | 25 ( 5 % | 25 ( 5 % |
|  |  | S2 | 35 ( 5 % | 35 ( 5 % | 35 ( 5 % | 35 ( 5 % | 35 ( 5 % | 35 ( 5 % |
|  | Luminous flux | S1 | 435 ( 20 % | 315 ( 20 % | 435 ( 20 % | 315 ( 20 % |  |
|  |  | S2 | 650 ( 20 % | 465 ( 20 % | 650 ( 20 % | 465 ( 20 % |  |
| Reference luminous flux | S1 | at approximately | 6 V | 398 | 284 |
|  | S2 | at approximately | 12 V | 568 | 426 |
|  |  |  | 13.2 V | 634 | 457 |
|  |  |  | 13.5 V | 650 | 465 |

5/	Dimensions a, b, c and ( refer to a plane parallel to the reference plane and cutting the two edges of the shield at a distance of e + 1.5 mm.

6/	Admissible angular deviation of the shield plane position from the normal position.

7/	Values in the left-hand column refer to the driving-beam filament.  Values in the right-hand column to the passing-beam filament.

Category S3 	Sheet S3/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e 2/ | 19.0 | 19.5 | 20.0 | 19.5 ( 0.25 |
| f | 6 V |  |  | 3.0 | 2.5 ( 0.5 |
|  | 12 V |  |  | 4.0 |  |
| h1, h2 3/ | -0.5 | 0 | 0.5 | 0 ( 0.3 |
| Cap P26s in accordance with IEC Publication 60061 (sheet 7004-36-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 6 |
|  | Watts | 15 | 15 |
| Test voltage | Volts | 6.75 | 13.5 | 6.75 |
| Objective values | Watts | 15 ( 6 % | 15 ( 6 % |
|  | Luminous flux | 240 ( 15 % |  |
| Reference luminous flux: 240 lm at approximately 6.75 V |

1/	The colour of the light emitted shall be white or selective-yellow.

2/	Distance related to the luminous centre.

3/	Lateral deviation of filament axis with respect to the reference axis. It is sufficient to check this deviation in two mutually perpendicular planes.

Category T1.4W 	Sheet T1.4W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 7.6 | 8.3 | 9.0 | 8.3 ( 0.35 |
| Lateral deviation 1/ |  |  | 0.7 | 0.35 max |
| ( | 55° | 70° | 85° | 70° ( 5° |
| Cap P11.5d in accordance with IEC Publication 60061 (sheet 7004-79-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 1.4 | 1.4 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 1.54 max. | 1.54 max. |
|  | Luminous flux | 8 ( 15 % |  |
| Reference luminous flux: 8 lm at approximately 13.5 V |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	The reference axis is perpendicular to the reference plane and passes through the centre of the circle of diameter "M".

Category T4W 	Sheet T4W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 13.5 | 15.0 | 16.5 | 15.0 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.5 | 0.5 max |
| ( |  | 90° |  | 90° ( 5° |
| Cap BA9s in accordance with IEC Publication 60061 (sheet 7004-14-9) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 4 | 4 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 4.4 max. | 5.5 max. | 4.4 max. |
|  | Luminous flux | 35 ( 20 % |  |
| Reference luminous flux: 35 lm at approximately 13.5 V |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis of pins.

2/	Over the entire length of the cap there shall be no projections or soldering extending beyond the permissible maximum diameter of the cap.

Category W2.3W 	Sheet W2.3W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 10.3 | 10.8 | 11.3 | 10.8 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.0 | 0.5 max |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap W2x4.6d in accordance with IEC Publication 60061 (sheet 7004-94-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 2.3 | 2.3 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 2.5 max. | 2.5 max. |
|  | Luminous flux | 18.6 ( 20 % |  |
| Reference luminous flux: 18.6 lm at approximately 13.5 V |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

Category W3W 	Sheet W3W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 11.2 | 12.7.0 | 14.2 | 12.7 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.5 | 0.5 max |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap W2.1x9.5d in accordance with IEC Publication 60061 (sheet 7004-91-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 24 | 12 |
|  | Watts | 3 | 3 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 3.45 max. | 4.6 max. | 3.45 max. |
|  | Luminous flux | 22 ( 30 % |  |
| Reference luminous flux: 22 lm at approximately 13.5 V |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

Category W5W, WY5W and WR5W 	Sheet W5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 3/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 11.2 | 12.7 | 14.2 | 12.7 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.5 | 0.5 max. |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap W2.1x9.5d in accordance with IEC Publication 60061 (sheet 7004-91-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 4/ | 12 | 24 | 12 |
|  | Watts | 5 | 5 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 5.5 max. | 7.7 max. | 5.5 max. |
|  | Luminous flux | W5W | 50 ( 20 % |  |
|  |  | WY5W | 30 ( 20 % |  |
|  |  | WR5W | 4/ | 12 ( 25 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 50 lm Amber: 30 lm Red: 12 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	The light emitted from filament light sources of normal production shall be white for category W5W, amber for category WY5W and red for category WR5W (see also footnote 3/)

3/	The light emitted from standard filament light sources shall be white for category W5W; white or amber for category WY5W; white or red for category WR5W.

4/	Within WR5W no 6 V rated voltage type specified.

Categories W10W and WY10W 	Sheet W10W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 15.5 | 17.0 | 18.5 | 17.0 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.0 | 0.5 max. |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap W2.1x9.5d in accordance with IEC Publication 60061 (sheet 7004-91-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 6 | 12 | 12 |
|  | Watts | 10 | 10 |
| Test voltage | Volts | 6.75 | 13.5 | 13.5 |
| Objective values | Watts | 11 max. | 11 max. |
|  | Luminous flux | White | 125 ( 20 % |  |
|  |  | Amber | 75 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 125 lm Amber: 75 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

Category W15/5W 	Sheet W15/5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

a = major (high wattage) filament

b = minor (low wattage) filament

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 25.0 1/ |  | 25.0 ( 0.3 |
| f |  |  | 7.5 | 7.5 + 0 / -2 |
| Lateral deviation 2/ |  |  | 1/ | 0.3 max. |
| x 3/ |  | 2.8 1/ |  | 2.8 ( 0.3 |
| y 3/ |  | 0.0 1/ |  | 0.0 ( 0.3 |
| ( | -15° 1/ | 0° | +15° 1/ | 0° ( 5° |
| Cap WZ3x16q in accordance with IEC Publication 60061 (sheet 7004-151-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 15 | 5 | 15 | 5 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 19.1 max. | 6.6 max. | 19.1 max. | 6.6 max. |
|  | Luminous flux | 280 ( 15 % | 35 ( 20 % |  |
| Reference luminous flux: 280 lm and 35 lm at approximately 13.5 V |

1/	To be checked by means of a "Box system"; sheets W15/5W/2 and 3.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

3/	"x" and "y" denote the offset of the axis of the minor filament with respect to the axis of the major filament.

Category W15/5W 	Sheet W15/5W/2

Screen projection requirements

This test is used to determine, by checking whether:

(a)	The major filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the axis X-X and the reference axis; and whether:

(b)	The minor filament is correctly positioned relative to the major filament, whether a filament light source complies with the requirements.

Test procedure and requirements.

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the major filament is seen on the screen on which the image of the filament is projected. The end view of that filament shall be obtained within the angular displacement tolerance limits. (±15°).

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the major filament seen end-on:

2.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament;

2.2.	The projection of the minor filament shall lie entirely within a rectangle of width "c" and height "d" having its centre at a distance "u" above the theoretical position of the centre of the major filament.

3.	Front elevation

The filament light source being placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to axis of the major filament:

3.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "h", centred on the theoretical position of the centre of the filament;

3.2.	The centre of the major filament shall not be offset by more than distance "k" from the reference axis.

3.3.	The centre of the minor filament axis shall not be offset from the reference axis by more than (2 mm ((0.4 mm for standard filament light sources).

Category W15/5W 	Sheet W15/5W/3

| Reference | a | b | c | d | u |
| --- | --- | --- | --- | --- | --- |
| Dimensions | 3.3 | 2.8 | 4.8 | 2.8 |

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimensions | 3.3 | 9.5 | 1.0 |

Categories W16W AND WY16W 	Sheet W16W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 18.3 | 20.6 | 22.9 | 20.6 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.0 | 0.5 max. |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap W2.1x9.5d in accordance with IEC Publication 60061 (sheet 7004-91-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 16 | 16 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 21.35 max. | 21.35 max. |
|  | Luminous flux | White | 310 ( 20 % |  |
|  |  | Amber | 190 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 310 lm Amber: 190 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

Category W21W 	Sheet W21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 29.0 2/ |  | 29.0 ( 0.3 |
| f |  |  | 7.5 | 7.5 + 0 / -2 |
| Lateral deviation 1/ |  |  | 2/ | 0.5 max. |
| ( | -15° 2/ | 0° | +15° 2/ | 0° ( 5° |
| Cap W3x16d in accordance with IEC Publication 60061 (sheet 7004-105-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 26.5 max. |
|  | Luminous flux | 460 ( 15 % |  |
| Reference luminous flux: 460 lm at approximately 13.5 V |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	To be checked by means of a "Box system"; see sheet W21W/2.

Category W21W 	Sheet W21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within (15°, to the plane through the axis X-X and the reference axis, whether a filament light source complies with the requirements.

Side elevation 				Front elevation

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 9.5 | 1.0 |

Test procedures and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits, i.e. (15°. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits ((15°).

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament;

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

Category W21/5W 	Sheet W21/5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

a = major (high wattage) filament

b = minor (low wattage) filament

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 25.0 1/ |  | 25.0 ( 0.3 |
| f |  |  | 7.5 | 7.5 + 0 / -2 |
| Lateral deviation 2/ |  |  | 1/ | 0.3 max. |
| x 3/ |  | 2.8 1/ |  | 2.8 ( 0.3 |
| y 3/ |  | 0.0 1/ |  | 0.0 ( 0.3 |
| ( | -15° 1/ | 0° | +15° 1/ | 0° ( 5° |
| Cap W3x16q in accordance with IEC Publication 60061 (sheet 7004-106-4) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 5 | 21 | 5 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 6.6 max. | 26.5 max. | 6.6 max. |
|  | Luminous flux | 440 ( 15 % | 35 ( 20 % |  |
| Reference luminous flux: 440 and 35 lm at approximately 13.5 V |

1/	To be checked by means of a "Box system"; sheets W21/5W/2 and 3.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

3/	"x" and "y" denote the offset of the axis of the minor filament with respect to the axis of the major filament.

Category W21/5W 	Sheet W21/5W/2

Screen projection requirements

This test is used to determine, by checking whether:

(a)	The major filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the axis X-X and the reference axis; and whether:

(b)	The minor filament is correctly positioned relative to the major filament, whether a filament light source complies with the requirements.

Test procedure and requirements.

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the major filament is seen on the screen on which the image of the filament is projected. The end view of that filament shall be obtained within the angular displacement tolerance limits (±15°).

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the major filament seen end-on:

2.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament;

2.2.	The projection of the minor filament shall lie entirely within a rectangle of width "c" and height "d" having its centre at a distance "u" above the theoretical position of the centre of the major filament.

3.	Front elevation

The filament light source being placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to axis of the major filament:

3.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "h", centred on the theoretical position of the centre of the filament;

3.2.	The centre of the major filament shall not be offset by more than distance "k" from the reference axis;

3.3.	The centre of the minor filament axis shall not be offset from the reference axis by more than (2 mm ((0.4 mm for standard filament light sources).

Category W21/5W 	Sheet W21/5W/3

| Reference | a | b | c | d | u |
| --- | --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 4.8 | 2.8 |

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimension | 3.5 | 9.5 | 1.0 |

Categories WP21W and WPY21W	Sheet WP21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 27.9 3/ |  | 27.9 ( 0.3 |
| f | 5.5 | 6.0 | 7.0 | 6.0 ( 0.5 |
| Lateral deviation 2/ |  |  | 3/ | 0.0 ( 0.4 |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap: | WP21W: WY2.5x16d WPY21W: WZ2.5x16d | in accordance with IEC Publication 60061 | (sheet 7004-104B-1) (sheet 7004-104C-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 26.5 max. |
|  | Luminous flux | WP21W | 460 ( 15 % |  |
|  |  | WPY21W | 280 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V | White: 460 lm Amber: 280 lm |

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system"; sheet WP21W/2.

4/	The light emitted from filament light sources of normal production shall be white for category WP21W and amber for category WPY21W (see also footnote 5/).

5/	The light emitted from standard filament light sources shall be white for category WP21W and white or amber for category WPY21W.

Categories WP21W and WPY21W 	Sheet WP21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within (15°, to the plane through the centre line of the keys and the reference axis, whether a filament light source complies with the requirements.

Side elevation 				Front elevation

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 9.0 | 1.0 |

Test procedures and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament.

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

Category WR21/5W 	Sheet WR21/5W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

a = major (high wattage) filament

b = minor (low wattage) filament

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 25.0 1/ |  | 25.0 ( 0.3 |
| f |  |  | 7.5 | 7.5 + 0 / -2 |
| Lateral deviation 2/ |  |  | 1/ | 0.3 max. |
| x 3/ |  | 2.8 1/ |  | 2.8 ( 0.3 |
| y 3/ |  | 0.0 1/ |  | 0.0 ( 0.3 |
| ( | -15° 1/ | 0° | 15° 1/ | 0° ( 5° |
| Cap WY3x16q in accordance with IEC Publication 60061 (sheet 7004-106-4) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 5 | 21 | 5 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 6.6 max. | 26.5 max. | 6.6 max. |
|  | Luminous flux | 105 ( 20 % | 8 ( 25 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 440 lm and 35 lm Red: 105 lm and 8 lm |

1/	To be checked by means of a "Box system"; sheets W21/5W/2 and 3.

2/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

3/	"x" and "y" denote the offset of the axis of the minor filament with respect to the axis of the major filament.

4/	The light emitted from normal production filament light sources shall be red (see also footnote 5/).

5/	The light emitted from standard filament light sources shall be white or red.

CategoriesWT21W and WTY21W	Sheet WT21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source 5/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 12 V |  | 27.9 3/ |  | 27.9 ( 0.3 |
|  | 24 V | 26.9 | 27.9 | 28.9 |  |
| f |  |  | 7.5 | 7.5 + 0 / - 2 |
| Lateral deviation 2/ | 12 V |  |  | 3/ | 0.0 ( 0.4 |
|  | 24 V |  |  | 1.5 |  |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap: | WT21W: WUX2.5x16d WTY21W: WUY2.5x16d | in accordance with IEC Publication 60061 | (sheet 7004-176-1) (sheet 7004-177-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 24 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 26.5 max. | 29.7 max. | 26.5 max. |
|  | Luminous flux | WT21W | 460 ( 15 % |  |
|  |  | WTY21W | 280 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 460 lm Amber: 280 lm |

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system", sheets WT21W/2.

4/	The light emitted from filament light sources of normal production shall be white for category WT21W and amber for category WTY21W (see also note 5/).

5/	The light emitted from standard filament light sources shall be white for category WT21W and white or amber for category WTY21W.

Categories WT21W and WTY21W	Sheet WT21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the centres of the keys and the reference axis, whether a filament light source complies with the requirements.

Test procedures and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament.

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

Categories WT21/7W and WTY21/7W 	Sheet WT21/7W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production 6/ | Standard filament light source 7/ |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 27.9 3/ |  | 27.9 ( 0.3 |
| f |  |  | 7.5 | 7.5 + 0 / - 2 |
| Lateral deviation 2/ |  |  | 3/ | 0.0 ( 0.4 |
| x 4/ |  | 5.1 3/ |  | 5.1 ( 0.5 |
| y 4/ |  | 0.0 3/ |  | 0.0 ( 0.5 |
| ( | 75° 3/ | 90° | 105° 3/ | 90° ( 5° |
| Cap: | WT21/7W: WZX2.5x16q WTY21/7W: WZY2.5x16q | in accordance with IEC Publication 60061 | (sheet 7004-180-1) (sheet 7004-181-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 7 | 21 | 7 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 8.5 max. | 26.5 max. | 8.5 max. |
|  | Luminous flux | 440 ( 15 % | 35 ( 20 % |  |
|  |  | 280 ( 20 % | 22 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 440 and 35 lm Amber: 280 and 22 lm |

For the notes see sheet WT21/7W/2.

Categories WT21/7W and WTY21/7W 	Sheet WT21/7W/2

1/	The reference axis is defined with respect to the reference keys and is perpendicular to the reference plane.

2/	Maximum lateral deviation of the major (high wattage) filament centre from two mutually perpendicular planes both containing the reference axis and one containing the axis through the reference keys.

3/	To be checked by means of a "Box system", sheets WT21/7W/2 and 3.

4/	"x" and 'y" denote the offset of the axis of the minor (low wattage) filament with respect to the axis of the major (high wattage) filament.

5/	If the minor filament is positioned using an asymmetric support similar to the one shown then the reference key and support structure shall be located on the same side of the filament light source.

6/	The light emitted from filament light sources of normal production shall be white for category WT21/7W and amber for category WTY21/7W (see also note 7/).

7/	The light emitted from standard filament light sources shall be white for category WT21/7W and white or amber for category WTY21/7W.

Screen projection requirements

This test is used to determine, by checking whether:

- The major (high wattage) filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within ±15°, to the plane through the centres of the keys and the reference axis;  and whether:

- The minor (low wattage) filament is correctly positioned relative to the major (high wattage) filament, whether a filament light source complies with the requirements.

Test procedure and requirements.

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits. The holder is then so rotated that an end view of the major filament is seen on the screen on which the image of the filament is projected. The end view of that filament shall be obtained within the angular displacement tolerance limits.

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical, the reference key to the right and the major filament seen end-on:

2.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament;

2.2.	The projection of the minor filament shall lie entirely within a rectangle of width "c" and height "d" having its centre at a distance "u" above the theoretical position of the centre of the major filament.

3.	Front elevation

The filament light source being placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to axis of the major filament:

3.1.	The projection of the major filament shall lie entirely within a rectangle of height "a" and width "h", centred on the theoretical position of the centre of the filament;

3.2.	The centre of the major filament shall not be offset by more than distance "k" from the reference axis;

3.3.	The centre of the minor filament axis shall not be offset from the reference axis by more than ±2 mm (±0.4 mm for standard filament light sources).

Category WT21/7W AND WTY21/7W 	Sheet WT21/7W/3

Side elevation

| Reference | a | b | c | d | u |
| --- | --- | --- | --- | --- | --- |
| Dimensions | 3.5 | 3.0 | 4.8 | 5.1 |

Front elevation

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimensions | 3.5 | 9.5 | 1.0 |

Category WY2.3W 	Sheet WY2.3W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e | 10.3 | 10.8 | 11.3 | 10.8 ( 0.3 |
| Lateral deviation 1/ |  |  | 1.0 | 0.5 max. |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap W2x4.6d in accordance with IEC Publication 60061 (sheet 7004-94-2) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 2.3 | 2.3 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 2.5 max. | 2.5 max. |
|  | Luminous flux | 11.2 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V | White: 18.6 lm Amber: 11.2 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	The light emitted from production filament light sources shall be amber (see also footnote 3/).

3/	The light emitted from standard filament light sources shall be amber or white.

Category WY21W 	Sheet WY21W/1

The drawings are intended only to illustrate the essential dimensions (in mm) of the filament light source.

| Dimensions in mm | Filament light sources of normal production | Standard filament light source |
| --- | --- | --- |
|  | Min. | Nom. | Max. |  |
| e |  | 29.0 2/ |  | 29.0 ( 0.3 |
| f |  |  | 7.5 | 7.5 + 0 / -2 |
| Lateral deviation 1/ |  |  | 2/ | 0.5 max. |
| ( | -15° | 0° | +15° | 0° ( 5° |
| Cap WX3x16d in accordance with IEC Publication 60061 (sheet 7004-105-3) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 21 | 21 |
| Test voltage | Volts | 13.5 | 13.5 |
| Objective values | Watts | 26.5 max. | 26.5 max. |
|  | Luminous flux | 280 ( 20 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 460 lm Amber: 280 lm |

1/	Maximum lateral deviation of filament centre from two mutually perpendicular planes both containing the reference axis and one containing axis X-X.

2/	The light emitted from filament light sources of normal production shall be amber (see also footnote 4/).

3/	To be checked by means of a "Box system"; sheet WY21W/2.

4/	The light emitted from standard filament light sources shall be amber or white.

Category WY21W 	Sheet WY21W/2

Screen projection requirements

This test is used to determine, by checking whether the filament is correctly positioned relative to the reference axis and reference plane and has an axis perpendicular, within (15°, to the plane through the axis X-X and the reference axis, whether a filament light source complies with the requirements.

Side elevation     					Front elevation

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 9.5 | 1.0 |

Test procedures and requirements

1.	The filament light source is placed in a holder capable of being rotated about its axis and having either a calibrated scale or fixed stops corresponding to the angular displacement tolerance limits, i.e. (15°. The holder is then so rotated that an end view of the filament is seen on the screen on to which the image of the filament is projected. The end view of the filament shall be obtained within the angular displacements tolerance limits ((15°).

2.	Side elevation

The filament light source placed with the cap down, the reference axis vertical and the filament seen end-on, the projection of the filament shall lie entirely within a rectangle of height "a" and width "b", having its centre at the theoretical position of the centre of the filament.

3.	Front elevation

The filament light source placed with the cap down and the reference axis vertical, the filament light source being viewed in a direction at right angles to the filament axis:

3.1.	The projection of the filament shall lie entirely within a rectangle of height "a" and width "h", having its centre at the theoretical position of the centre of the filament.

3.2.	The centre of the filament shall not be offset by more than distance "k" from the reference axis.

# Text boxes

f

b

Ø 11 max.

Reference axis

Ø 3.5

Reference axis

Ø 3.5

f

b

Ø 15 max.

Central axis sought

Reference axis

k

k

h

a

8.5 max.

Filament axis

44 max.

E

B

D

A

A

B

d

g

Reference axis

Reference plane

Section D-E

Bulb axis

27.5

3

Permissible offset of filament axis

h2

h1

Nominal position of filament light source holder studs

Obscuration angle

limits of cap

Section A-B

ε

ε

View C

Second pin

Reference pin

Reference axis

Reference plane

Filament axis

Reference axis

C

120°

20

7.5 1/

e

f

3/

2/

1/

4/

reference plane

25.0 mm to

Reference axis

Z1

Z2

b1

b2

c1

c2

a1

a2

Reference axis

Reference plane

Reference notch

Shields

32 max

80° max.

3 min.2/

e

1/

3/

Ø 12.5 max

Definition: Ring centre and reference axis4/

9.6

Top view

Filament position and dimensions

B

Top view

Top view

C

Z

View B

Z

Definition of Z - Z

Z

Definition of Z - Z

Z

Z

View B

Z

Z

B

A

B

9.6

2.5

C

A

Reference axis

Ring centre

Reference notch

reference  plane

h1

Filament axis

Filament centre

Reference axis

Filament

axis

h2

h3

h4

Z

f

k

18.0 to

Reference mark

r = 2.5

5/

5/

View A: measuring h2

View B: measuring k, h1, h3, f

View C: measuring h4

20.8

Reference axis

Views A and C

View B

18.0 to

reference plane

a

a

c

a

g

g

k

Reference lug

Passing-beam

Driving-beam

Axis of bulb

Figure 1 – Main drawing

Reference plane

Reference axis

Earth

Reference plane1/

Reference axis2/

Maximum filament light source outlines4/

Figure 3

Figure 2

M

p

e

3/

5/

α

α

5

5

14

18

55

20

60

Ø 38.2

Ø 28

Ø 38.2

Ø 22

Ø 34.5

Ø 45

IC

H

H

p

q

Position of shield

Axis of bulb

Reference axis

The drawing is not mandatory with

respect to the design of the shield

H9/

V8/

V

V

H

29.5 10/

33.0

H

b1

b1

b2

e

15°

d

Position of filaments

V 8/

H 9/

Reference axis

e

V

Axis of passing-beam filament

Axis of driving-beam filament

IR

IC

V

29.510/

33.0

H

H

23.5

26.0

g

c

a

c

h

h

a

g

V

b1

d

d

Reference axis

f

View from A

View from C

Reference axis

Reference plane1/

Figure 1 – Main drawing

C     A

V

3/

4/

Reference axis

Reference plane

Reference axis

V

V

B

Figure 2 – Maximum filament light source outline5/

Figure 3 – Definition of reference axis2/

V

R  =  13

55°

55°

50°

25.0

44.0

Ø 15.0

3.5

Ø 20.0

Ø 26.1

e

f

Reference axis

Reference plane

First filament turn

Filament axis

View from A

View from B

ɣ2

ɣ3

ɣ1

25.0

50°

3.0

Figure 5 – Metal free zone8/

Figure 4 – Distorsion free area and black top6/,7/

Reference plane

Filament axis

Reference axis

Filament axis

View from A

Bulb axis

e

f

h1

h2

g

g

Figure 6 – Permissible offset of filament axis

(for standard filament light sources only)

Figure 7 – Bulb eccentricity

25 mm to

reference plane

Reference axis

Z1

Z2

Z3

Z4

b1

b2

c2

c1

a1

a2

Category H8

Category H8B

Reference axis2/

Reference axis2/

Reference plane1/

5/

4/

5/

4/

f

e

A

A

B

B

Figure 1 - Main drawings

f

e

Reference plane

Reference axis

50°

44.0

25.0

4

Figure 2 – Maximum filament light source outline3/

Ø 25.0

Ø 19.0

Ø 15.0

Reference axis

Reference plane

First filament turn

Filament axis

View A

View B

ɣ1

ɣ3

ɣ2

25.0

50°

3.0

Figure 4 – Metal free zone8/

Figure 3 – Distorsion free area6/ and black top7/

Reference plane

Filament axis

Reference axis

Filament axis

View A

Bulb axis

e

f

h1

h2

g

g

Figure 5 – Permissible offset of filament axis9/

(for standard filament light sources only)

Figure 6 – Bulb eccentricity10/

25.0 mm to

reference plane

Reference axis

Z1

Z2

Z3

Z4

b1

b2

c2

c1

a1

a2

Category H9

Category H9B

Reference axis2/

Reference axis2/

Reference plane1/

Figure 1 – Main drawings

e

f

4/

4/

e

f

A

A

B

B

5/

5/

Reference plane

Reference axis

50°

44.0

25.0

4.1

Figure 2 – Maximumfilament light source outline3/

Ø 25.0

Ø 19.0

Ø 15.0

Reference plane

Reference plane

Reference axis

Reference axis

First filament turn

Filament axis

Filament axis

Filament axis

View B

Figure 3 – Distorsion free area5/

View A

View A

Figure 4 – Metal free zone6/

Figure 6 – Bulb eccentricity8/

Figure 5 – Permissible offset of filament axis7/

(for standard filament light sources only)

Bulb axis

ɣ1

ɣ2

50°

3.0

e

f

25.0

h1

h2

g

g

25.0 mm to

reference plane

Reference axis

Z1

Z2

Z3

Z4

b1

b2

c2

c1

a2

a1

f

e

h2

h1

2.0

3/

4/

e

e

f

A

B

ɣ3

ɣ1

ɣ2

55.0 max.

Reference lug

Plane C5/

Reference axis2/

Reference diameter

Reference plane1/

Reference plane

Reference axis

Filament axis

Reference plane

Bulb axis

View A

View A

Distorsion free area6/ and black top7/

Offset filament

Ø 19.81 max.

31.5

Reference axis

reference plane

28.9 mm to

Z1

Z2

Z3

Z4

b1

b2

c1

c2

a2

a1

Reference axis2/

Reference axis2/

Reference plane1/

Category H11

Category H11B

Figure 1 – Main drawings

5/

5/

4/

4/

A

A

B

B

e

e

f

f

Reference plane

Reference axis

Figure 2 - Maximum filament light source outline3/

Ø 25.0

Ø 19.0

Ø 15.0

50°

4.1

25.0

44.0

Reference plane

Reference plane

Reference axis

Reference axis

Filament axis

Filament axis

View A

View A

Filament axis

View B

Distorsion free area6/ and black top7/

Bulb axis

Figure 4 – Metal free zone8/

Figure 6 – Bulb eccentricity10/

Figure 5 – Permissible offset of filament axis9/

(for standard filament light sources only)

ɣ1

ɣ2

ɣ3

50°

3.0

25.0

f

e

h1

h2

g

g

Fist filament turn

25.0 mm to

reference plane

a2

a1

Z1

Z2

Z3

Z4

b1

b2

c2

c1

Reference axis

55.0 max.

3/

4/

B

2/

2/

2/

C

2.0

Reference lug

Plane C5/

Reference axis2/

Reference diameter

Reference plane1/

Reference plane

Reference plane

Bulb axis

Filament axis

Filament centre

Ø 19.81 max.

View A

View B

View B

Distorsion free area6/ and black top7/

Offset filament

View C

e

View B

31.5

ɣ1

ɣ2

ɣ3

31.5

h4

h3

h1

h1

h2

f

k

A

Reference axis

View A

Views B and C

reference plane

31.5 to

a1

a1

a2

b1

b2

c

a1

c

Bulb axis

Plane C

B

4/

5/

3/

V

V

Reference lug

e

e

Reference plane1/

Reference axis2/

Driving

Ground

Passing

Category H13

Category H13A

56.0 max.

4.28

A

26.4  max.

56.0 max.

Bulb axis

4/

Reference lug

V

V5/

4.28

B

A

26.4  max.

Driving

Ground

Passing

3/

Plane C

C

Reference axis2/

View from C

Bulb axis

Bulb axis

Bulb axis

Filament axis

Filament axis

Reference axis

Reference axis

Reference plane

View from B

View from A

Reference plane

Figure 2 – Definition of reference axis2/

Figure 3 – Undistorted area6/ and opaque coating7/

Figure 4 – Bulb offset8/

Figure 5 – Light blocking toward cap9/

h

h

g

g

29.45

29.45

R=13.21

30°

30°

δ

ß

ɣ

θ

Passing-beam filament axis

Driving-beam

filament axis

Reference axis

Passing-beam filament axis

Reference axis

Driving-beam

filament axis

View from A

View from B

Metal free zone15/

Filament centers

V

e

f1

d1

m

k

j

n

p

f2

d2

1.25

max.

1.25

max.

V

n

p

m

Figure 6 – Position and dimensions of filaments 10/, 11/, 12/, 13/, 14/

Ø 33.1

Passing-beam

Driving-beam

Reference lug

Earth

Reference axis2/

Reference plane1/

Reference axis

Figure 2 – Maximum filament light source outline3/

Reference plane

Figure 1 – Main drawing

B

M

A

C

55.0B

26.15

55°

Bulb axis

e

f1

Ø 33.1

Ø 26.4

Reference axis

View B

Reference plane

View A

Reference axis

Bulb axis

Reference plane

Figure 3 – Distorsion free area4/ and black top5/

Figure 4 – Bulb eccentricity6/

Passing-beam

filament axis

Passing-beam

filament axis

Driving-beam

filament axis

Reference axis

View B

Reference plane

View A

Reference axis

Bulb axis

Reference plane

Figure 3 – Distorsion free area4/ and black top5/

Figure 4 – Bulb eccentricity6/

Passing-beam

filament axis

Passing-beam

filament axis

Driving-beam

filament axis

Reference axis

View B

Reference plane

View A

Reference axis

Bulb axis

Reference plane

Figure 3 – Distorsion free area4/ and black top5/

Figure 4 – Bulb eccentricity6/

Passing-beam

filament axis

Passing-beam

filament axis

Driving-beam

filament axis

Driving-beam

filament axis

View A

Views B, C

Reference axis

Reference plane

Figure 5 – Offset of filament axis7/

(for standard filament light sources only)

ɣ1

ɣ2

ɣ3

g

g

e

f1

h1

h1

h3

h4

h2

h3

h2

h4

i

j

26.5

f2

26.15 to reference plane

c2

c1

c3

View A

For passing-beam filament

For driving-beam filament

Reference axis

Reference axis

b1

b2

z1

z2

z3

z4

c3/2

B

B

A

A

a1

a1

a2

a2

Views B, C

k

i

Reference axis2/

Reference plane1/

Bulb axis

Reference axis

Auxiliary

reference plane1/

High wattage

Low wattage

Ground

Figure 1 – Main drawing

Figure 3 - Maximum filament light source outlines3/

Ø 22

Bulb axis

Reference axis2/

Reference lug

Ø 31.5

Ø 23

50°

30.0

55

4.5

e

r

30°

30°

30.0

ɣ1

ɣ2

Reference plane

V

V

Figure 2 – Definition of reference axis7/

Figure 4 - Distorsion free area4/

Reference axis

Position of the shield

Reference axis

The drawing is not mandatory with

respect to the design of the shield

Position of the filaments

Axis of bulb

Reference axis

H7/

V6/

H7/

V6/

Axis of low wattage filament

V

V

V

V

V

H

H

H

p

q

p

q

c1

c2

d

f

h

V

1R

1C

15°

15°

e

a

g

g

h

31.0

33.5

33.5

12/

12/

31.0

24.0

13/

26.0

Axis of high wattage filament

b1

Reference axis2/

Reference axis2/

Reference plane1/

Reference plane

Reference axis

Category H16

Category H16B

Figure 1 – Main drawing

Figure 2 - Maximum filament light source outline3/

50°

44.0

25.0

4

Ø 25.0

Ø 19.0

Ø 15.0

e

e

f

f

A

A

B

B

5/

5/

4/

4/

Reference plane

Reference plane

First filament turn

Reference axis

Reference axis

Filament axis

Filament axis

Bulb axis

Filament axis

View B

View A

View A

25.0

3.0

50°

ɣ2

ɣ1

ɣ3

e

f

h1

h2

g

g

Figure 3 - Distorsion free area6/ and black top7/

Figure 4 – Metal free zone8/

Figure 5 – Permissible offset of filament axis9/

(for standard filament light sources only)

Figure 6 – Bulb eccentricity10/

c2

reference plane

25.0 mm to

Reference axis

a1

a2

Z1

Z2

Z3

Z4

b1

c1

b2

Driving-beam

Reference lug

Passing-beam

M

Earth

Axis of the bulb

Reference axis2/

Reference axis

Reference plane1/

Figure 1 –

Main drawing

Figure 2 - Maximum filament light source outlines4/

Ø 38.2

Ø 28

Ø 22

5/

3/

55

18

14

5

α

α

e

p

p

e

Axis of bulb

Reference axis

H8/

V7/

b2

b1

b1

d

d

p

q

q

p

H

H

V

V

29.5

33.0

Reference axis

Axis of driving-beam filament

Axis of passing-beam filament

H8/

V7/

H

V

V

h

h

g

g

e

a

c

1R

1C

25

26

29.5

31.0

f

Reference plane1/

Reference axis

Reference axis

Reference axis

View from A

View from C

Figure 1 - Main drawing

Figure 2 - Maximum filament light source outline 5/

Figure 3 - Definition of reference axis 2/

3/

4/

Reference plane

e

f

V

V

V

V

B

C

A

55°

55°

50°

R = 13

44.0

25.0

3.5

Ø 26.1

Ø 20.0

Ø 15.0

Figure 6 - Permissible offset of filament axis
(for standard filament light sources only)

Figure 7 - Bulb eccentricity

View from A

Filament axis

Filament axis

Filament axis

Reference axis

Reference axis

View from B

Reference plane

Reference plane

Bulb axis

View from A

First filament turn

Figure 5 - Metal free zone8/

Figure 4 - Distortion free area and black top6/, 7/

ɣ2

ɣ1

ɣ3

25.0

50°

3.0

e

f

h2

h1

g

g

Reference axis

reference plane

25.0 mm to

Major filament

Minor filament

Earth

Axis of the bulb

Reference axis

Reference plane1/

Figure 1 - Main drawing

Figure 2 - Maximum filament light source outlines4/

Reference lug

M2/,7/

p

e

Reference axis2/

( 27

50

5/

3/

( 22

5

14

18

( 38.2

α

α

α

Bulb axis

Reference axis

b1

q

p

d

d

q

p

H

b1

b2

H8/

V7/

H

V

V

29.5

33.0

Reference axis

Axis of major filament

Axis of minor filament

H8/

V7/

V

H

h

g

e

a

c

f

1R

1C

24.5

26

29.5

33.0

g

h

V

Reference plane1/

View from A

View from C

Figure 1 - Main drawing

V

V

e

f

Reference axis

4/

3/

C

A

B

Reference axis

Reference axis

Reference plane

Figure 2 - Maximum filament light source outline5/

Figure 3 - Definition of reference axis2/

V

V

55°

55°

R=13

44.0

25.0

3.5

50°

Ø26.1

Ø20.0

Ø15.0

Figure 4 - Distortion free area6/

Reference plane

Reference axis

View from B

First filament turn

Filament axis

Figure 5 - Metal free zone7/

View from A

Reference plane

Reference axis

Filament axis

Figure 6 - Permissible offset of filament axis (for standard filament light sources only)

f

e

h2

h1

View from A

Bulb axis

Filament axis

Figure 7 - Bulb eccentricity

g

g

ɣ2

ɣ1

25.0

3.0

50°

25.0 mm to reference plane

Reference axis

Z1

Z2

Z3

Z4

c1

c2

b1

b2

a1

a2

28.0 max.

HY6W

H6W

3/

Ø 9.25 max.

4/, 5/

Reference plane

Reference axis

e

ß

ɣ1

ɣ2

Ø 9.25 max.

28.0 max.

4/, 5/

3/

H10W/1

HY10W

ɣ1

ɣ2

e

Reference plane

Reference axis

ß

X

X

33.0 max.

Ø 9.25 max.

5/, 6/

Reference plane

Reference axis

e

ß

HY21W

H21W

ɣ1

ɣ2

Reference axis

Side elevation

Front elevation

reference plane

20.0 to

k

k

h

b

a

a

(13.0 max.

Reference axis2/

Reference axis2/

Reference plane1/

Reference plane1/

ɣ1

ɣ1

ɣ2

ɣ2

B

B

A

A

e

e

3/

3/

4/

4/

44.5 max.

44.5 max.

Ø 13.0 max.

Ø 13.0 max.

Category H27W/1

Category H27W/2

Reference axis

Filament axis

Filament axis

31.75 to

reference plane

h1

h3

h2;h4

View A

View B

k

f

Reference axis

reference plane

31.75  to

g

g

k

k

a

a

a

c

55.0 max.

55.0 max.

View A

View A

3/

3/

A

B

B

e

e

4/

4/

Ø 19.68 max.

Ø 19.68 max.

Reference axis2/

Reference axis2/

Reference plane1/

Reference lug

Reference lug

Plane C5/

Plane C5/

2.0

2.0

Reference diameter

Reference diameter

Category HB3

Category HB3A

A

Reference axis

Reference plane

Reference plane

Bulb axis

Filament centre

Distorsion free area7/

Filament position and dimensions

6/

ɣ1

ɣ2

h2

h3

h1

e

f

31.5

Reference axis

31.5 mm to reference plane

Reference plane

B

C

A

v

s

u

r

t

p

q

p

q

Category HB4

Category HB4A

55.0 max.

55.0 max.

View A

View A

Ø 19.8 max.

Ø 19.81 max.

3/

3/

4/

4/

B

B

A

A

Plane C5/

Plane C5/

Reference axis2/

Reference axis2/

Reference diameter

Reference diameter

Reference lug

Reference lug

2.0

2.0

Reference plane1/

e

e

31.5

ɣ1

ɣ2

ɣ3

6/

8/

Bulb axis

Reference plane

Bulb eccentricity

Distorsion free area7/ and black top8/

Bulb axis

Filament axis

g

h1

h2

h3

f

e

Reference plane

Reference axis

Filament centre

Filament position and dimensions

Reference axis

31.5 mm to reference plane

Reference plane

p

q

p

q

C

B

t

v

u

r

s

A

65.0 max.

Ø 19.81 max.

3/

4/

6/

e

e

d

f

A

B

Reference lug

Reference plane

Plane C5/

Reference axis2/

Reference diameter

Reference plane1/

6.0

View A

View B

Bulb axis

Reference axis

h1

h2

ɣ1

ɣ2

29.0

g

29.0 mm to reference plane

Reference axis

b2

b1

Z1

Z4

Z2

Z3

c1

c2

a2

a1

60.0 max.

3/

4/

6/

e

d

f

Reference axis2/

Reference diameter

Reference plane1/

View A

View B

Ø 19.8 max.

Reference lug

Plane C5/

Reference plane

Filament axis

Reference axis

Reference axis

h1

h2

28.7

Bulb axis

6.0

ɣ1

ɣ2

B

A

e

g

28.7 mm to reference plane

Reference axis

b2

b1

c1

c2

Z1

Z2

Z3

Z4

a1

a2

Reference lug

Driving-beam

Passing-beam

Axis of bulb

Reference axis2/

Reference plane1/

Figure 1 – Main drawing

Earth

M

p

e

α

α

3/

5/

Maximumfilament  light source outlines4/

Reference axis

Reference plane

Figure 2

Figure 3

Ø 38.2

Ø 28

Ø 22

Ø 45

Ø 38.2

Ø 34.5

5

14

18

55

5

20

60

Figure 2

Figure 3

Maximum lamp outlines 4/

Axis of bulb

Position of shield

Reference axis

Reference axis

Reference axis

The drawing is not mandatory with

respect to the design of the shield

33.0

29.5

V8/

H9/

H9/

b2

15°

b1

b1

H

H

H

V

V

p

q

d

d

q

q

V8/

H

Position of filaments

V

V

29.5

31.0

26

25

c

c

a

a

h

g

e

h

g

V

f

1R

1C

Axis of passing-beam filament

Axis of driving-beam filament

View B

View A

Reference plane

View A

View B

Reference axis1/

Reference notch

Filament position

Filament axis

26.1 max.

e

A

B

f

ß3/

α2//

ɣ2

ɣ14/

h1

h2

Ø 10max

Reference axis

11.0 mm to

reference plane

Reference axis

Z2

Z1

b1

b2

c2

c1

a1

a2

Reference axis2/

A

50 max.

e

3/

4/

5/

B

Reference plane1/

Ø 24.5 max

Reference axis2/

Earth

Driving-beam

Passing-beam

Figure 1 – Main drawing

Figure 2 - Distorsion free area4/ and black top5/

Reference axis2/

ɣ1

ɣ2

ɣ3

G3

View B of driving-beam filament

View A of passing-beam filament

Top view of driving-beam filament

Top view of passing-beam filament

Reference axis

Reference axis

Filament centre

Filament centre

Figure 3 – Filament position and dimensions

1R

1C

g1

h1

h3

h4

h2

g3

g2

g4

k

i

e

e

Side elevation

26.0 mm to reference

Dimensions in millimeters

Driving-beam filament

Passing-beam filament

Reference axis

d

b

c

v

a

Front elevation

Reference axis

26.0 mm to reference

k

k

h

A

50 max.

B

e

e

3/

4/

5/

Reference plane1/

Reference plane1/

Reference axis2/

Reference axis2/

Ø 24.5 max.

Earth

Driving-beam

Passing-beam

ɣ1

ɣ2

ɣ3

Figure 1 – Main drawing

Figure 2 - Distorsion free area4/ and black top5/

Filament centre

Filament centre

Reference axis

Reference axis

View B - Driving-beam filament

View A - Passing-beam filament

1R

1C

k

j

g1

g3

h1

h3

e

e

g2

h2

h44

g4

Passing-beam filament axis

Driving-beam filament axis

Reference axis

Top view of driving-beam and passing-beam filament

Figure 3 – Filament position and dimensions

56.0 max.

5.75

3 x 120°

Plane C4/

V5/

V

3/

e

A

Bulb axis

Reference axis2/

Reference plane1/

Reference lug

Driving

Ground

Passing

Ø 26.4 max.

Reference axis

30°

30°

R = 13.21

Figure 2 – Definition of reference axis2/

V

Figure 4 – Bulb offset8/

Bulb axis

Bulb axis

Bulb axis

View from B

View from A

Filament axis

Filament axis

Reference axis

Reference plane

h

h

g

g

Reference plane

ß

ɣ

δ

Figure 3 - Undistorted area6/ and opaque coating7/

θ

29.45

Figure 5 – Light blocking toward9/ cap

29.45

1.25 max.

1.25 max.

e

V

V

f1

m

d1

k

j

f2

d2

m

n

n

p

p

Metal free zone15/

View from A

View from B

Reference axis

Filament centres

Reference axis

Passing-beam

filament axis

Passing-beam

filament axis

Driving-beam

filament axis

Driving-beam

filament axis

Figure 6 – Position and dimensions of filaments10/, 11/, 12/, 13/, 14/

44.0 max.

37.0 max.

Reference plane1/

Reference plane

Reference axis

Reference axis

Ø 16.6 max.

Ø 16.6 max.

f

f

e

e

2/

α1

α1

α2

α2

View B

40°

Figure 1 – Main drawing P13W

Figure 3 – Main drawing PW13W

Figure 2 – Metal free zone3/

Enlarged centre of view B

View A

Reference axis

View A

u1

u2

z4

z3

z2

z1

t

v

r

s

q

p

e

36 max.

f

e

Ø 18.5 max.

Reference axis

Reference plane1/

3/

2/

α

P19W,

PY19W,

PR19W,

PS19W,

PSY19W,

PSR19W

Ø 18.5 max.

e

f

37 max.

Reference plane

α

PW19W,

PWY19W,

PWR19W

Reference axis

.

37 max

e

f

Reference axis

Ø18.5 max.

Reference plane

Reference axis

Z2

Z1

Z3

Z4

b1

b2

c1

e

a2

a1

c2

45 max.

e

ß

4/

f

Reference axis

Reference plane

Ø 26.5 max.

Reference axis

31.8 to

reference plane

k

k

h

b

a

a

45 max.

Ø 26.5 max.

Reference axis

Reference pin

Reference plane

e

x

b

b

b

a

a

a

ß

y

f

a = major (high wattage) filament

b = minor (low wattage) filament

a = major (high wattage) filament

b = minor (low wattage) filament

Ø 26.5 max.

45 max.

3/

e

x

b

a

a

b

y

ß

f

Reference plane

Reference axis

Reference pin

a

b

Reference axis

Side elevation

Low wattage filament

High wattage filament

31.8 to

reference plane

b

v

c

25°

a

u

d

Front elevation

Reference axis

31.8 to

reference plane

k

k

h

a

e

f

3/

2/

Ø 18.5 max.

Ø 18.5 max.

f

e

37 max.

α

α

Reference axis

Reference axis

Reference axis

Reference plane1/

PW24W,

PWY24W,

PWR24W

P24W,

PX24W,

PY24W, PR24W

PS24W,

PSX24W,

PSY24W, PSR24W

36 max.

Reference axis

b2

b1

e

c2

c1

Z2

Z1

Z3

Z4

a1

a2

Reference axis1/

Reference plane

Reference key

44 max.

e

f

ß

Ø 26.5 max

Reference axis

Side elevation

Front elevation

27.9 to

reference plane

k

k

h

b

a

a

Ø 26.5 max.

44 max.

a = major (high wattage) filament

b = minor (low wattage) filament

Reference plane

Reference axis1/

Reference key

e

x

a

a

b

b

b

a

y

ß

f

Ø 27.9 to

reference plane

Reference axis

Side elevation

Low wattage filament

High wattage filament

Ø 27.9 to

c

b

a

d

u

Ø 27.9 to

reference plane

Reference axis

Front elevation

k

k

h

a

28 max.

37.0 max.

Ø 16.6  max.

Ø 16.6  max.

f

f

e

e

3/

2/

α

α

Reference plane1//

Reference plane

Reference axis

Reference axis

PC16W,

PCY16W,

PCR16W

PW16W,

PWY16W,

PWR16W

e

b2

b1

c1

c2

Z4

Z3

Z2

Z1

a2

a1

Reference axis

Reference axis

Reference pin

Reference plane

Ø 26.5 max.

45 max.

e

2/

5/

ß

f

a = major (high wattage) filament

b = minor (low wattage) filament

45 max.

Ø 26.5 max.

Reference axis

Reference plane

Reference pin

e

b

a

a

b

a

b

x

ß

y

f

4/

5/

45.0 max.

Ø 26.5 max.

a = major (high wattage) filament

b = minor (low wattage) filament

Reference axis

Reference plane

Reference pin

3/

4/

e

x

b

a

b

b

a

a

y

f

ß

a = major (high wattage) filament

b = minor (low wattage) filament

44 max.

Ø 26.5 max.

e

x

a

a

a

b

b

b

y

5/

ß

Reference axis1/

Reference plane

Reference key

44.0 max.

Reference plane1/

Ø 18.5 max.

0.45 max.

Reference axis

Reference axis

View A

View B

f

e

e

2/

α2

α1

Figure 1 – Main drawing

Figure 2 – Metal free zone3/

40°

Filament

Enlarged centre of view A

Enlarged centre of view B

24.0 mm to

reference plane

b2

b1

c1

c2

Z2

Z1

Z3

Z4

Reference axis

a2

a1

45 max.

Ø 26.5 max.

e

2/

5/

Reference plane

Reference pin

Reference axis

f

ß

Reference plane

Reference pin

Reference axis

β

b

A

a

b

A

a

b

A

a

y

a

A

a

a

A

a

a

A

a

e

x

Ø 26.5 max.

42 max.

Low wattage filament

c

25°

d

Reference axis

u

v

High wattage filament

Side elevation

28.6 to

reference plane

b

a

28.6 to

reference plane

h

=

=

k

k

Reference axis

a

Front elevation

| Reference | a | b | c | d | u | v |
| --- | --- | --- | --- | --- | --- | --- |
| Dimensions | 3.5 | 3.0 | 4.8 | 2.8 |

a

28.6 to

reference plane

h

=

=

k

k

Reference axis

b

Front elevation

| Reference | a | b | c | d | u | v |
| --- | --- | --- | --- | --- | --- | --- |
| Dimensions | 3.5 | 3.0 | 4.8 | 2.8 |

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimensions | 3.5 | 9.0 | 1.0 |

a = major (high wattage) filament

b = minor (low wattage) filament

Reference axis

Ø 26.5 max.

44 max.

e

x

a

a

a

b

b

b

5/

ß

y

Reference plane

f

Reference key

Reference axis1/

50 max.

e

3/

2/

Ø 41.0 max.

Passing-beam filament

Passing-beam

Driving-beam

Earth

Reference plane

Driving-beam filament

Top view

Reference axis

Reference plane

View from

View from

Shield

View from

V

0°   H

H

H

H

X

X   195°

V

V

X

X

30.0

33.0

b1

b2

e

f

p

q

LC

c

h

g

(

(

(

(

(

a

ɣ

Reference axis

3/

Reference plane

Reference pin

Ø 19 max.

30 max.

R5W

RR5W

ß

ß

e

ß

ß

ß

30 max.

Ø 19 max.

3/

Reference plane

Reference pin

Reference axis

e

R10W

RY10W

RR10W

54 max.

Reference axis

Lug width 3 mm

Reference axis

Reference axis

Reference plane2/

1/

e

Driving-beam filament

Passing-beam filament

Driving-beam filament

Passing-beam filament

Position and dimensions of filaments

Filament axis

Filament

axis

Filament axis

Shield

Position of shield3/,4/

g

h

a

c

b

b

f

l

H

H

V

V

ß

ß

Ø 36 max.

e + 1.5

Shield

Reference axis

Filament axis

Position of shield 3/, 4/

Filament axis

Reference axis

3, 4

34 max.

e

1/

f

h1

h2

Ø 26 max.

Reference axis

Reference plane

11.7 max.

Ø 5.8 max.

Reference plane2/

Reference plane

e

X

X

ß

20°

M

Ø 8.8 max.

21.5 max.

e

2/

Reference plane

Reference axis

ß

20 max.

14.5 max.

e

Ø 5 max.

Reference plane

Reference axis

X

X

ß

Ø 10.29 max.

26.8 max.

20.7 max.

e

X

X

ß

Reference plane

Reference axis

26.8 max.

20.7 max.

Ø 10.29 max.

e

X

X

ß

Reference plane

Reference axis

2/

31.7 max.

25.5 max.

e

7.1 mm

Ø 13.5 max.

Reference axis

Reference plane

Reference axis

X

X

ß

39 max.

8.5 max.

Ø 20.5 max.

Reference plane

Reference axis

Reference boss

f

X

X

y

ß

x

e

b

b

b

a

a

a

Side elevation

Dimensions in millimeters

Reference axis

Low wattage filament

High wattage filament

25.0 to

reference plane

c

b

d

a

u

Front elevation

Reference axis

25.0 to

reference plane

k

k

h

a

38.1 max.

32 max.

e

7.1 mm

Ø 15.7 max.

Reference axis

Reference plane

Reference axis

X

X

ß

43 max.

4.5 max.

Ø 20.5 max.

f

e

X

X

ß

Reference plane

Reference boss

Reference axis

Reference axis

k

k

h

a

a

b

29.0 to

reference plane

y

39 max.

8.5 max.

Ø 20.5 max.

Reference axis

Reference boss

Reference plane

X

X

ß

b

b

b

a

a

a

e

x

Reference axis

Side elevation

Low wattage filament

High wattage filament

25.0 to

reference plane

c

b

a

d

u

Front elevation

Reference axis

25.0 to

reference plane

k

k

h

a

44 max.

e

4/

Reference plane

Reference axis1/

Reference key

ß

f

Ø 26.5 max.

Reference axis

k

k

h

b

a

a

27.9 to

reference plane

39 max.

8.5 max.

Ø 20.5 max.

Reference plane

Reference axis

Reference boss

b

b

b

a

a

a

e

x

4/,5/

f

ß

y

X

X

Reference key

Reference plane

Reference axis

β

ø 20.5 max.

44 max.

e

4/

f

Reference axis

27.9 to

Reference plane

Side elevation

Front elevation

| Reference | a | b | h | k |
| --- | --- | --- | --- | --- |
| Dimension | 3.5 | 3.0 | 9.5 | 1.0 |

reference plane

k

k

h

b

a

a

ø 20.5 max.

6/

Support5/

Reference key5/

Reference plane

Reference axis

44 max.

β

y

a = major (high wattage) filament

b = minor (low wattage) filament

f

e

a

a

a

b

b

b

Reference axis

Low wattage filament

High wattage filament

27.9 to

reference plane

c

b

d

u

a

Reference axis

k

k

h

a

27.9 to

reference plane

20 max.

14.5 max.

e

2/

X

X

ß

Reference axis

Reference plane

Ø 5 max.

4.5 max.

43 max.

e

2/

X

X

ß

Ø 20.5 max.

f

Reference plane

Reference boss

Reference axis

Reference axis

k

k

h

b

a

a

29.0 to

reference plane