## Slide 1: FIA MOBILITY & TOURISM Gerd Preuss, FIA Representative at UNECE, WP 29 ECE-TRANS-WP29 2018-10-24 LED Replacement Light Sources
Informal document GRE-80-30
(80th GRE, 23-26 October 2018,
agenda item 5)

## Slide 2
Introduction
Notes: National Automobile Associations (ACN)
Clubs, Associations or Federations (ASN)

## Slide 3
Connecting Vehicles
Ensuring smooth development of future car connectivity, while providing motorists with informed free choice
Safeguarding mobility
Supporting efficient and affordable mobility for all
Increasing road safety
Promoting 5-star drivers in 5-star cars on 5-star roads Light Sources are means to increase road safety
Protecting the environment
Offering intelligent mobility solutions that mitigate the impact
of transportation on the environment
FIA Region I Policy priorities

## Slide 4: LED Replacement Light Sources
      FIA supports a Regulation on Technical Requirements for LED Replacements
      Technical Arguments for LED:
      Higher Safety with LED
      Disadvantages of Incandescent Lamps
      Advantages of LED lamps
      Consumer Views

## Slide 5: LED Replacement Light Sources as Replacement for Incandescent Lamps
      FIA supports a proposal submitted by the Task Force on Substitutes and Retrofits (TF SR) which introduces requirements for the use of light emitting diode (LED) substitute light sources in the new LSD UN Regulation
LED Replacement Light Sources

## Slide 6
    Technical Arguments: Higher Safety with LED
      15,5 % of all vehicles have one or more lamp defects
      13,1 % of all vehicles equipped with lamp diagnostic systems have also one or more lamp defects
      70 % to 87 % of all car head lights in Germany are equipped with incandescent lamps
      The risk of fatal accidents is three times higher during night than by daylight (Source: DESTATIS)
ADAC lighting check 2017 on 5.819 vehicles in Germany (October 2017)
Chart: Light systems of head lights
| LED | Xenon | unknown | Halogen
Lights systems of headlights | 0.01 | 0.12 | 0.17 | 0.7
LED Replacement Light Sources
Notes: https://www.adac.de/infotestrat/ratgeber-verkehr/sicher-unterwegs/lichttest/lichttest_2017.aspx?ComponentId=306758&SourcePageId=8749&quer=lichttest
Es wurden im Oktober 2017 über 5.800 Fahrzeuge (n=5.819) untersucht im Rahmen des ADAC Licht-Tests.

## Slide 7
    Technical Arguments: Higher Safety with LED
    Test: LED Replacements switch on faster than incandescent lamps
Incandescent Lamp
Time Delay of Break Light with Incandescent Lamp compared to LED
time in ms æ
LED Replacement Light Sources
      Time advantage up to 260ms to full brightness
      Distance advantage up to 3,5m at 50 km/h, leads to less time loss in response time for the driver/vehicle behind

## Slide 8
    Technical Arguments: Higher Safety with LED
    Replacements in Low Beam Head Lights
      More brightness
      Better contrast
      Higher range
    LED Replacements fulfill already many requirements in light distri- bution of UNECE regulations for incandescent filament lamps
Halogen
LED Replacement Light Sources
BMW MINI with Philips H4 Halogen
BMW MINI with
Nighteye H4 LED light source
Notes: Welche Anforderungen, welche Artikel und welche Paragraphen?

## Slide 9
Technical Arguments: Higher Safety with LED
Tested with Free-form Reflector: BMW MINI (H4)
Light Distribution Low Beam – Driver´s View
Philips H4 Halogen
Philips H4 Halogen
Philips H4 LED light source
Philips H4 LED light source
Nighteye H4 LED light source
Nighteye H4 LED light source
LED Replacement Light Sources in Vehicles
Notes: Driver view

## Slide 10
Test: Free-form Reflector in BMW MINI (H4) with Bird’s Eye View and Low Beam Range
LED Replacement Light Sources
Technical Arguments: Higher Safety with LED
1lux isoline till 190 m
Philips H4 LED light source
1lux isoline till 140 m
Philips H4 Halogen
1lux isoline till 172 m
Nighteye H4 LED light source

## Slide 11
Free-form Reflector: BMW MINI (H4)
Table UN ECE Reg. 112 Low Beam
Functions | Min [cd] | Max [cd] | Philips H4 Halogen [cd] | N.i.O | Philips H4 LED light source [cd] | N.i.O | Nighteye H4 LED light source [cd] | N.i.O
Range: |  |  |  |  |  |  |  | 
75R | 10100 | - | 8605 | * | 16959 |  | 9274 | *
50R | 10100 | - | 10841 |  | 29970 |  | 13925 | 
50V | 5100 | - | 6022 |  | 21536 |  | 4836 | *
25L | 1700 | - | 2631 |  | 6793 |  | 3274 | 
25R | 1700 | - | 3324 |  | 7241 |  | 7788 | 
Zone IV | 2500 | - | 12520 |  | 39143 |  | 16468 | 
Glare Values: |  |  |  |  |  |  |  | 
B 50L | - | 350 | 251 |  | 163 |  | 190 | 
BR | - | 1750 | 199 |  | 205 |  | 316 | 
75L | - | 10600 | 2434 |  | 5670 |  | 890 | 
50L | - | 13200 | 4733 |  | 11932 |  | 2894 | 
Zone III | - | 625 | 548 |  | 681 | * | 3760 | *
Zone I | - | 2*E(50R) | 11978 |  | 35887 |  | 12455 | 
Visibleness Values: |  |  |  |  |  |  |  | 
1 (8L - 4O) | 65 | - | 77 |  | 67 |  | 106 | 
2 (H - 4O) | 65 | - | 116 |  | 93 |  | 133 | 
3 (8R - 4O) | 65 | - | 136 |  | 64 | * | 232 | 
4 (4L - 2U) | 125 | - | 166 |  | 92 | * | 140 | 
5 (H - 2U) | 125 | - | 205 |  | 120 | * | 164 | 
6 (4R - 2U) | 125 | - | 201 |  | 153 |  | 273 | 
7 (8L - V) | 65 | - | 290 |  | 325 |  | 339 | 
8 (4L - V) | 125 | - | 309 |  | 490 |  | 238 | 
LED Replacement Light Sources
Technical Arguments: Higher Safety with LED
Notes: glare values = Blendwert
Sichtbarkeitswerte = visibleness values (der Scheinwerfer soll auch von der Seite sichtbar sein, um die Fahrzeugbegrenzung erkennbar zu machen. Dazu ist eine gewisse Lichtstreuung zur Seite erforderlich)

## Slide 12
    Technical Arguments: Higher Safety with LED
      Lower failure rates
      Better view at night
      Easier detection of pedestrians
      Higher protection for motorcycles
      Faster signalling of braking procedures
      Retrofitting for present vehicle fleet
      Better equipment for older vehicles
      Shock proof lamps for trailors
Osram H7 LED Retrofit lamp
in Hyundai i30 head light
Philips LED Replacement Light Sources in
VW Golf VI Variant rear light with clear cover
LED Replacement Light Sources

## Slide 13
    Technical Arguments: Disadvantages of incandescent lamps
    Incandescent filament lamps are sensitive to
      Voltage Fluctuation
      Vibration
      Shock Force
      Life time requirements
      This leads to defects of lamps and less safety if not replaced in time
H7 Halogen incandescent filament lamp
LED Replacement Light Sources

## Slide 14
    Technical Arguments: Advantages of LED lamps
    LED lamps are robust in terms of
      Voltage fluctuations
      Vibrations
      Shock forces
      Life time requirements
      Further advantages of LED lamps are
      Lower power consumption
      Less heat emission
NightEye H4 LED Retrofit lamp
LED Replacement Light Sources
https://www.adac.de/infotestrat/technik-und-zubehoer/licht/lichttechniken/
      All reports are available at (in german only):
Notes: e.g. Eco Innovation for LED in Europe

## Slide 15
    Consumers View
    LED Replacemts are already available on the market and in some markets outside Europe, they are already „allowed“
      Consumers have no understanding for prohibition of LED Replacements in vehicle use in Europe
      Consumers in Europe cannot make a distinction betwenn good and bad performing LED replacement light sources, due to missing regulative technical requirements
    A Regulation for LED Replacements developed by GRE, will give industry safety guidelines with benefits for both: the consumer and the vehicle safety
LED Replacement Light Sources
R22 Example (Helmets)