## Slide 1: GTB
Substitute Light Sources
Equivalence Reports for W5W and WY5W (12V and 24V)
In support of document ECE/TRANS/WP.29/GRE/2019/10
Transmitted by the expert from GTB | Informal document GRE-81-04 (81st GRE, 15 - 18 April 2019, agenda item 5)

## Slide 2: Equivalence Report
W5W, WY5W (12V, 24V)
According to Regulation No. 128
Equivalence Requirements GRE-80-02

## Slide 3: Checklist for Equivalence of Parameters W5W, WY5W (12V and 24V)
Parameters Check
3.1. Parameters with the same values
3.1.1. Holder (as in in accordance with the given IEC Publication 60061) 
3.1.2. Maximum lamp outline dimensions 
3.1.3. Electrical connector n/a
3.1.4. Test voltage 
3.1.5. Objective luminous flux 
3.1.6. Colour of emitted light 
3.1.7. Light centre length 
3.1.8. Distortion free zone (if any) n/a
3.2. Parameters with similar values
3.2.1. Normalized luminous intensity distribution see page 4 and 5 
3.2.2. Size and position of the light-emitting-area see page 6 
3.2.3. Homogeneity of the light-emitting-area see page 6 
3.3. Parameters with different values
3.3.1. Maximum electrical power consumption 2W for 12V (2.5W for 24V) 
3.3.2. The minimum voltage range R128 Annex 4 (9-16V (12V) and [16]-32V(24V)) 
3.3.3. The spectral content R128 par. 3.12.4.** [in combination with functional interlock]
3.3.4. Functional interlock between light source and application IEC Cap: WX2.1x9.5d 
3.4. Additional parameters
3.4.1. Thermal behaviour R128 Annex 4 
Requirements regarding failure detection
4.1 Failure detection 30 …. 185 mA 
4.2 Failure behaviour below 10 mA 
no flash R128 3.12.3.** 
** GRE-adopted proposal GRE/2018/39

## Slide 4: Normalised Intensity Distribution W5W

## Slide 5: Normalised Intensity Distribution WY5W

## Slide 6: Size, Position and Homogeneity of the Light-Emitting-Area W5W, WY5W
< 50%
< 50%
> 20%
> 20%
> 15%
> 15%

## Slide 7
END