Informal document No. 8 - d

[Document 4]

### Progressing break test

（1） Progressing break test :after the test vehicle has reached the prescribed maximum speed the vehicle is slowed down to 20 km/h by operating the brake according to either braking method A or B and then a rapid braking is applied.

Braking A：moderate braking

Braking B：firm braking

（2） Test vehicle ： mini van type vehicle

（3） Seats ： A CRS equipped a webbing sensor is attached to the right seat in the second row from front.

： A CRS equipped with a vehicle sensor is attached to the left seat in the second row from front.

： № CRS is attached to the central seat in the second row from front.

（4） Dummy ： VIP3C

（Conclusions）

1．In the progressing brake test, CRS with a vehicle sensor and CRS with a webbing sensor are equivalent in safety.

2．Although the maximum displacement of CRS with a vehicle sensor reaches 18mm,this does not pose  any safety problems.

| № | Speed test method | Vehicle body G (sensor on floor) Max G | Sample | Forward displacement of dummy head： mm(head position before and after testing) | Webbing displacement from ELR： mm |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | Braking A or B | Rapid braking |  |
| 1 | Max speed： 50km Braking A | Braking A： 0.3G Rapid braking： 1.1Ｇ | CRS with vsir | 0 | 10 | 0 |
|  |  |  | CRS with wsir | 0 | 0 | 0 |
|  |  |  | Without CRS | 0 | 325 | --- |
| 2 | Max speed： 50km Braking A | Braking A： 0.28G Rapid braking： 1.1Ｇ | CRS with vsir | 0 | 0 | 0 |
|  |  |  | CRS with wsir | 0 | 1 | 0 |
| 3 | Max speed： 50km Braking B | Braking B： 0.33Ｇ Rapid braking：0.76Ｇ | CRS with vsir | 0 | 12 | 0 |
|  |  |  | CRS with wsir | 0 | 2 | 0 |
|  |  |  | Without CRS | 0 | 413 | --- |
| 4 | Max speed： 50km Braking B | Braking B： 0.33Ｇ Rapid braking： 1.1Ｇ | CRS with vsir | 0 | 13 | 0 |
|  |  |  | CRS with wsir | 0 | 2 | 0 |
| 5 | Max speed： 40km Braking A | Braking A： 0.22Ｇ Rapid braking： 1.2Ｇ | CRS with vsir | 0 | 0 | 0 |
|  |  |  | CRS with wsir | 0 | 0 | 0 |
|  |  |  | Without CRS | 0 | 220 | --- |
| 6 | Max speed： 40km Braking A | Braking A： 0.3Ｇ Rapid braking： 1.2Ｇ | CRS with vsir | 0 | 18 | 0 |
|  |  |  | CRS with wsir | 0 | 2 | 0 |
| 7 | Max speed： 40km Braking B | Braking B： 0.4Ｇ Rapid braking： 1.1Ｇ | CRS with vsir | 0 | 0 | 0 |
|  |  |  | CRS with wsir | 0 | 2 | 0 |
|  |  |  | Without CRS | 0 | 138 | --- |
| 8 | Max speed： 40km Braking B | Braking B： 0.35Ｇ Rapid braking： 1.2Ｇ | CRS with vsir | 0 | 18 | 4 |
|  |  |  | CRS with wsir | 0 | 3 | 0 |

Graph