## Slide 1: Challenges and Potential of Methane at Moonidih – A Status Review
D.GANGOPADHYAY, Director(Tech) P&P, BCCL
J.S.MAHAPATRA, Project Officer, Moonidih

## Slide 2
The mine is located in South-Central part of Jharia Coalfield in
Dhanbad district of Jharkhand state.
Dhanbad Railway Station is about 10 km from the mine. Dhanbad-Chas
section of National Highway passes through North-western part of
Moonidih. Birsa Munda Airport, Ranchi is the nearest airport at a distance
of about 170 Km.
The area lies between latitudes 230 42’47” to 23045’42”N and
longitudes 86o19’ 21” to 86o22’26” E.
Boundaries of the Mine
North & North East : Pootkee Balliary Project
South & South West : Damodar River/ Parbatpur Block
East : Bhagaband Block/ Tata leasehold
West : Kapuria Block/ Jarian Nala
LOCATION OF MOONIDIH COLLIERY
Notes: Kakatiya longwall project

## Slide 3
MOONIDIH

## Slide 4: PROJECT BACKGROUND
This mine was designed in early 1960’s by Polish Consultants under Technical Collaboration for horizon mining system to produce coking coal from seams XVIII to XV Bottom for a production capacity of 2.1 MTPA.
It is the first mine in India to introduce fully mechanized Self-advancing Powered Support Longwall technology in the year 1978.
This mine has achieved the production level of 1.2 MTPA in the FY -1989.
The infrastructural facilities for production are fully developed including pit head washery.

## Slide 6
7.40m
404.34m
4.16m ( 432.39 – 436.55m)
47.98m
0.33m ( 463.88 – 464.21m)
30.84m
1.42m ( 495.05 – 496.47m)
95.06m
2.93m ( 591.33 – 594.46m)
141.03m
2.19m ( 735.49 – 737.57m)
3.61m ( 738.02 – 743.63m)
0.54m
RL = 185.39M
XVIII SEAM
XVII TOP SEAM
XVII BOTTOM SEAM
XVI TOP SEAM
XV TOP SEAM (COAL)
XV BOTTOM SEAM (COAL)
[Not to Scale]
SURFACE
RMR – 49
Rock Load – 4.19
RMR – 58
Rock Load – 2.50t/m2
RMR –56.67
Rock Load – 2.67t/m2
RMR – 37.4
SEAM SEQUENCE

## Slide 7: Present Status
Seam No. | Parting | Grade | Status | Depth
XVIII(XVIIIA) |  | S-1 to W-1 | 9 Panels worked in Jarma Sector) | 80--590
XVII Top(L-10) | 32-63m | S-1 to W-IV | Worked with B-Series of Panels | 120-640
XVII Bot.(L-9) | 14-47m | S-II to UG | Worked with C-Series of Panels | 140-650
XVI Comb.(L-6/L-5) | 96-101m | S-II to W-II | Worked with F-Series of Panels | 
XVI Top(L-6) | 73-125m | W-1 to W-IV | Extraction in Panel D-12 going on. | 230-780
XVI Bot.(L-5) | 28m | S-1 to UG | Worked with E-Series of Panels | 240-790
XV Top(XVI C) | 87-128 M | S-II to W-IV | VIRGIN(Touched at 500 mH) | 360-900
XV Bot(XVI B) | <1 TO 12M | S-I to W-IV | VIRGIN | 365-905
XV Comb( XVI C/B) |  | S-I to W-IV | VIRGIN | 360-740

## Slide 8
Sl. No. | Particulars | Shaft No.1 | Shaft No. 2
1 | Diameter | 7.5m | 7.5 m
2 | Depth at which horizons are opened. | 280m, 400m and 500m | 220 m, 280 m, 400 m and 500 m
3 | No. of compartment | 2 | 2
4 | Hoisting Arrangement | 2 nos. 4 decked cage in each of the two compartments | In one compartment. 2 skips each of 10 tonnes capacity Second compartment equipped with single deck cage to act as emergency winder for men.
5 | Winders | i) Koepe (K-6000) 1600 KW winder | Koepe (WEF-6) Winder MAMC make, 1600 kW
 |  | ii) Koepe (WEF-6) winder, MAMC make, 1600 KW | 
6 | Purpose | Intake, Man & Material winding upto 400 m horizon and coal hoisting facility also available from 400m horizon through one winder (K-6000) & upto 500 m Horizon through second winder (WEF-6). | Production from 400m horizon and ventilation return.
7 | Capacity of the container | Cages Man – 80 (20 men per deck) Coal – 10 tes per cage in 4 decks (each containing coal filled in 2.5 Te Mine Car). | 2 Skip each of 10 tonnes capacity.
Technical parameters of the Outlets

## Slide 9: TECHNICAL INFORMATION OF MAIN MECHNICAL VENTILATOR
TYPE | MV2-3 (DOUBLE STAGE AXIAL FAN)
MAKE | MAMC, INDIA
VOLTAGE | 6.6KV
CURRENT | RATED-165AMPS, RUNNING-70AMP
MOTOR | 1600KW, SYNCHRONUS MOTOR
CAPACITY | 52-264 M3/SEC., RUNNING AT PRESENT AT 211M3/SEC
EFFICIENCY | 74% (Maximum)
NO. OF BLADES | 32 IN TWO STAGE ( 2X16)
POWER FACTOR | 0.9 LEADING ( PRESENT BY RUNNING)
BLADE ANGLE | 150-450 (RUNNING-450)
DESIGNED WATER GAUSE | 135-400 MM ( PRESENT-135MM)
IMPELLER DIA | 3000 MM

## Slide 10: Methane & Moonidih

## Slide 11: Make of Gas at Moonidih Degree of Gassiness at Moonidih
The gassiness of the seams at Moonidih Underground Project (XVIII to XV) is Degree – III.
(“Gassy seam of degree – III“ means a coal seam or part thereof lying within the precincts of a mine not being an opencast working in which the rate of emission of inflammable gas per tons of coal produced exceeds ten cubic meters).
Methane gas blowers have been encountered at various places while working XVIII, XVII Top, XVII Bot., XVI Top and XVI Comb. Seam at Moonidih Underground Project.

## Slide 12: In-situ Gas Contents
The report of three bore holes in different seams suggest following facts:
It shows that gas content of XVI top seam is about 8- 10 cum/ton and XV seam is about 15 cum/ton.
With increase of depth, gas content also increases.
It has also been observed that, gas emission increases as we move towards Singra Sector which is towards dip side of property.

## Slide 13
CENTRAL MINE PLANNING & DESIGN INSTITUTE GAS ABSORBRNT REPORT OF MOONIDIH, CBM LABORATORY
BORE HOLE NO. | SEAM NO. | SAMPLE NO. | DEPTH/ CORE INTERVAL | Q1 LOST GAS(CC) | Q2 DESORBED GAS(CC) | Q3 RESIDUAL GAS(CC) | AS RECEVED (M³/TON)
MSG-14 | XVII(T) | G-03 | 598.90-599.90 | 244.4 | 506.5 | 191.0 | 0.58
MSG-14 | XVII(T) | G-04 | 599.9-602.90 | 271.4 | 507.5 | 176.2 | 0.60
MSG-14 | XVII(B) | G-05 | 617.90-620.90 | 262.1 | 489.8 | 138.4 | 0.80
MSG-38 | XI | G-24 | 1138.70-1141.70 | 1242.0 | 5654.5 | 543.4 | 4.28
MSG-38 | XIII | G-19 | 1057.20-1060.20 | 1013.1 | 10050.5 | 483.6 | 7.39
MSG-38 | XIII | G-20 | 1060.20-1063.20 | 1279.8 | 10219.8 | 475.1 | 8.25
MSG-13 | XV(T) | G-07 | 799.50-801.00 | 1785.30 | 7370.50 | 315.14 | 8.27
MSG-38 | XVI(T) | G-10 | 772.70-775.70 | 2073.0 | 11121.3 | 456.1 | 8.78
MSG-13 | XIII | G-11 | 878.00-881.00 | 2939.40 | 9052.32 | 400.78 | 8.86
MSG-13 | XIV | G-09 | 842.00-845.00 | 1851.80 | 8222.23 | 291.51 | 8.95
MSG-13 | XV(T) | G-04 | 791.00-793.50 | 1754.90 | 7891.80 | 300.60 | 9.03
MSG-13 | XV(T) | G-06 | 796.50-799.50 | 2359.50 | 8551.70 | 334.40 | 9.06
MSG-13 | XV(T) | G-05 | 793.50-796.50 | 2247.80 | 7377.40 | 297.00 | 9.20
MSG-13 | XIV | G-10 | 875.00-878.00 | 1939.80 | 9053.30 | 296.36 | 9.97
MSG-13 | XIV | G-08 | 839.00-842.00 | 1702.40 | 8912.66 | 289.94 | 10.04
MSG-13 | XV(T) | G-03 | 788.00-791.00 | 1902.10 | 10263.0 | 281.30 | 11.21
MSG-38 | XIV | G-18 | 1036.70-1039.70 | 2801.7 | 19728.7 | 536.4 | 13.50
MSG-38 | XV(T) | G-13 | 916.70-919.00 | 1925.8 | 15767.6 | 407.1 | 14.16
MSG-38 | XII | G-22 | 1111.70-1114.70 | 2113.7 | 21008.9 | 540.1 | 14.41
MSG-38 | XV(T) | G-14 | 919.70-922.70 | 1839.1 | 15913.6 | 383.1 | 14.93
MSG-38 | XV(B) | G-16 | 934.70-937.70 | 1893.1 | 20021.4 | 409.4 | 16.78
MSG-38 | XII | G-23 | 1114.70-1117.70 | 2558.8 | 21297.0 | 422.6 | 19.47
MSG-38 | XII | G-21 | 1108.70-1111.70 | 2089.3 | 20228.7 | 384.0 | 19.64
MSG-38 | XV(B) | G-15 | 931.70-934.70 | 2029.2 | 20027.4 | 354.0 | 19.69
MSG-38 | X | G-28 | 1195.70-1198.70 | 2321.4 | 27364.5 | 449.8 | 22.26
MSG-38 | X | G-27 | 1192.70-1195.70 | 2234.6 | 27278.9 | 427.7 | 23.48
MSG-38 | X | G-29 | 1198.70-1201.70 | 2571.2 | 29920.6 | 446.1 | 24.53

## Slide 14: Methane in sealed off area

## Slide 15: Sealed off areas in Moonidih Mine
Sl. No | Seam; no. of sealed off panels | Depth of working (m) | Panel name | Seam thickness (m) | Panel starting date | Date of finish of panel
1 | XVIII Seam, 9 panels | 480 | A1, A2, A3, A4, A5, A6, A6a, A7, A8 | 2.7 | 27.09.1994 | 04.09.1997
2 | XVII (Top seam); 32 panels | 220-280 | T1 to T6 | 1.7 | 20.09.1974 | 09.06.1980
 |  |  | ML-I/1 to ML-I/7 | - | 28.08.1979 | 21.10.1990
 |  |  | ML-II/1 to ML-II/6 | - | 25.07.1980 | 12.07.1991
 |  |  | B32 | - | 24.07.1997 | 18.09.1998
3 | XVII (Bottom seam), 2 panels | 280-400 | C1, C2 |  | 11.09.1989 | 21.09.1995
4 | XVI (Top seam), 11 panels | 400-500 | ML-III/1, ML-III/2, ML-IV/1, ML-IV/2, D8, D9, D10, D11, D12, D13, D14A | 2.8 | 14.10.1985 | 06.08.2010
5 | XVI (Bottom seam), 6 panels | 400-500 | E1, E2, E3, E4, E5, E6 | - | 11.09.1989 | 13.02.2004
6 | XVI (Combined seam), 7 panels | 450-600 | F1, F2, F3-A, F3-B, F4, F5, F6 | 2.7 | 05.09.1992 | 04.08.2008
 | Total = 67 panels |  |  |  |  | 

## Slide 16: Methane in sealed off area XVIII Seam
Name of Panel | Panel length (m) | Starting date | Completion date | Percentage of Methane in sealed off
A1 | 216 | 27.09.1994 | 22.07.1996 | 93.5
A7 | 217M | 06.11.1996 | 30.03.1998 | 81.38
A2 | 342M | 17.08.1998 | 03.06.1999 | 71.23
A3 | 516M | 06.04.2000 | 26.02.2001 | 82.15
A4 | 539M | 31.05.2001 | 21.03.2002 | 78.75
A5 | 593M | 13.07.2002 | 31.03.2003 | 94.15
A8 | 615M | 01.06.2004 | 31.03.2005 | 91.76
A6 | 165M | 27.06.2005 | 11.01.2006 | 72.9
A6a | 240M | 05.02.2007 | 04.09.2007 | 66.5

## Slide 17: Methane in sealed off area XVI TOP Seam
Name of Panel | Panel length (m) | Starting date | Completion date | Percentage of Methane in sealed off
D1 | 968 | 11.10.1985 | 24.03.1987 | 4.75
D2 | 1022 | 10.10.1987 | 31.03.1989 | 43.58
D8 | 685 | 26.10.1995 | 10.07.1998 | 54.58
D11 | 694 | 08.01.2003 | 31.05.2004 | 50.03
D14A | 242 | 22.12.2008 | 06.08.2010 | 37.51
F4 | 415 | 03.09.2004 | 11.02.2005 | 5.91
F5 | 434 | 19.09.2005 | 05.03.2007 | 12.67
F6 | 425 | 08.10.2007 | 04.08.2008 | 34.56

## Slide 18: Methane in sealed off area XVI Bottom Seam
Name of Panel | Panel length (m) | Starting date | Completion date | Percentage of Methane in sealed off
E4 | 420 | 26.03.1999 | 12.07.2000 | 36.61
E5 | 655 | 19.11.2002 | 13.02.2004 | 19.15

## Slide 19: Methane in sealed off area XVII Seam
Name of Panel | Panel length (m) | Starting date | Completion date | Percentage of Methane in sealed off | 
B1 | 136 | 20.09.1974 |  | 80 | Manual
B3 | 94 | 01.06.1975 |  | 71.2 | Manual
B5 | 164 | 07.02.1976 |  | 67.86 | Manual
B7 | 162 | 25.09.1976 |  | 69.05 | Manual
B8 | 174 | 02.02.1977 |  | 49.49 | Manual
B9 | 66 | 31.03.1977 |  | 48.78 | Manual
B17 | 530 | 27.11.1979 | 20.12.1980 | 10 | 
B21 | 650 | 06.05.1981 | 17.03.1983 | 5.65 | 
B22 | 750 | 02.12.1983 | 25.02.1985 | 7.15 | 
B24 | 740 | 25.03.1985 | 06.04.1987 | 10.65 | 
B25 | 422 | 03.07.1987 | 03.01.1989 | 48 | 
B27 | 290 | 06.06.1989 | 21.10.1990 | 10.15 | 
B28 | 288 | 04.07.1989 | 21.04.1990 | 78.79 | 
B38 | 160 | 04.01.1991 | 12.07.1991 | 33.81 | 
B32 | 285 | 15.06.1995 | 15.06.1997 | 78.06 | 
B33 | 273 | 24.07.1997 | 18.09.1998 | 69.85 | 

## Slide 20: PRESENT MINING OPERATIONS
Seam XVI T

## Slide 21: Present Status of Seam XVI T
The operation of Seam XVI T has been outsourced through a Global Bid mechanism.
The target was to achieve a production of 3.5 MTY in 5 Years by Longwall retreating with caving.
At present, Panel - D12 is being worked in this seam.
Two Roadheaders are deployed for Gate Road Development.
Gas emission varying from 22-35 cum/Min in tail gate of D12 Panel has been observed during the extraction process.
.D-12 panel is likely to be completed by May 2017.

## Slide 22: PART PLAN OF MOONIDIH COLLIERY

## Slide 23: Gas Emission during depillaring by Longwall in D-12 Panel
Gas emission from goaf started after first local fall at 22 meter of face retreat and came out through tail gate.
Up to 300 meter gas percentage coming out from goaf was within permissible limit.
The gas percentage went on increasing and at 440 meter gas coming from goaf was more than five percent and it was up to 9 percent behind last power support in tail gate.
After mixing with ventilation air percentage of methane in top gate return air went up to 1.7 – 2 %.
During that time Production had to be suspended for some days owing to statutory restrictions.

## Slide 25
Chart: 29-03-2016 D-12 Tail gate road Methane concentration

## Slide 26: Steps taken to deal with Methane in D-12 Longwall panel
Air quantity was increased from 2000 Cu/M to 2700 Cu/M. Increased leakage of ventilation air through goaf swept more methane to tail gate and thus resulted into concentration in tail gate road .
To reduce leakage of less ventilation air through goaf, support gaps were blocked by brattice cloth starting from main gate barrier pillar up to middle of face. With this there was minor reduction in gas percentage.
With increase of air in D12 panel and reducing of air in other parts of mine resulted in Methane gas emission problem in other districts.

## Slide 27
Again air quantity was reduced so as to minimise leakage of air through goaf. Quantity of methane coming from goaf was reduced but, the overall return percentage remained unchanged due to reduction of total ventilation air
As advised by CIMFR, pressure balancing was attempted but no improvement noticed.
During periodic weighting, it was observed that gas emission from goaf increases comparing to normal operation period.
No major gas percentage increase observed due to coal cutting.However, due to support advance and immediate fall of roof gas emission from goaf increases. So cutting speed is restricted to control gas emission.

## Slide 28
Channel is made by brattice cloth to rise side of AFC tail end for making an escape route for methane gas from goaf to tail gate to a distance of about twenty five meter
Diverting air from face to side of last power support in tail gate to mix with methane gas for diluting thorough the channel.
One auxiliary fan is installed in main intake side to supply fresh air up to mixing point near AFC tail end for further dilution of gas. By this way air quantity in bottom gate is reduced to 1500 cuM and leakage air in goaf also reduced, whereas total quantity in top gate remains 2000 CuM .So dilution of methane gas is more effective.
Two numbers of LMD are installed. LMD1 is to sense the air near AFC tail end which is the last electrical and moving part of PSLW equipment. LMD2 is to sense the air in the vicinity of last reach of shearer drum while cutting near tail end.
Two numbers of compressesd air blowers were installed to break methane layering where ever required.
One more LMD was installed to assess gas percentage in brattice channel.
Systems adopted to dilute Methane gas and make safe the active working zone

## Slide 29
IMPACT OF HIGH GAS EMISSION ON PRODUCTION
Gas emission from 22-35 cum/Min in tail gate of D12 Panel has been encountered.
It has resulted in suspension of production process at times to comply with the requirements of providing adequate ventilation.
The process of face operation had to be slowed down at times to control the gas emission
All these have resulted in a loss of about 700 hours on production Panel D-12. Assuming the cycle time of one cut at 2 hours, the total loss comes out to 350 cuts.
The loss of production on the above account comes to about 1.57 Lte. At a sale price of Rs. 2570/Te(earlier prevailing rate), the loss is pegged at about Rs. 40 Crs.
In addition, the high make of gas continues to cast its shadow on the safety of mining operations, as the mine has a very large extent.

## Slide 30: XV SEAM PROJECT
PROPOSED MINING OPERATIONS

## Slide 31: PROPOSALS
Seam proposed to be approached by a pair of drifts from surface
XV seam is split into two sections i.e XV Top & XV Bottom.
XV Top section is proposed to be worked by Longwall retreating (caving) using two legged Power Shield Supports.
  After extraction of Top section, XV Bottom section shall be worked by Longwall Retreating (caving) under settled goaf of XV Top section. A parting of minimum 3mtrs shall be maintained between Top & Bottom sections.
  XV Seam will be worked under the goaved out area of XVIII, XVII Top and XVII Bot. seams which are filled up with gas.
  It is proposed to work five panels in XV Top section & five panels in XV Bottom during the contract period.
  The lengths of these panels vary from 878 mtrs to 3238 mtrs with a face width of 250 mtrs.

## Slide 32: SALIENT FEATURES OF THE PROJECT (XV Seam)
S.No. | Panel No. | Section | Face length(m) | Panel length(m) | Reserves(LT)
1 | 1 | TOP | 250 | 928 | 9.54
2 | 2 | TOP | 250 | 1987 | 20.42
3 | 3 | TOP | 250 | 2408 | 24.75
4 | 4 | TOP | 250 | 2930 | 30.12
5 | 5 | TOP | 250 | 3238 | 33.29
6 | 1 | BOTTOM | 239.1 | 878 | 8.64
7 | 2 | BOTTOM | 239.1 | 1938 | 19.07
8 | 3 | BOTTOM | 239.1 | 2359 | 23.22
9 | 4 | BOTTOM | 239.1 | 2881 | 28.36
10 | 5 | BOTTOM | 239.1 | 3189 | 31.39
TOTAL |  |  |  |  | 228.8

## Slide 33: Problem faced to maintain Adequate Ventillation

## Slide 34: Statutory Provisions for ventilation quantity and to deal with Methane gas
CMR Reg - 130. Standard of ventilation
(i) In every ventilating district, not less than six cubic meters per minute of air per person Employed in the district on the largest shift or not less than 2.5 cubic meters per Minute of air per daily tone output whichever is larger.
(iii) The percentage of inflammable gas does not exceed 0.75 in the general body of the Return air of any ventilating district and 1.25 in any place in the mine;
136A. Velocity of Air Current
  The velocity of air current measured in meters per minute at the maximum span of along wall face in Third degree shall be not less than 75m/min.

## Slide 35
DGMS Circular42/1974, CMR 136A
  Maximum air velocities in longwall face is 4 m/s i.e. 240 m/min
Reg 145. Determination of percentage of inflammable gas and of environmental conditions
  (e) If any determination in any ventilating district shows the percentage of Inflammable gas to exceed once and a quarter, the supply of electric energy shall be cut off immediately from all cables and apparatus in the district, and a written report thereof submitted to the Regional Inspector forthwith.

## Slide 36: Constraints to Ventilation Quantity in Seam XVI Top
• At present, gas emission is about 24 cum/Min in tail gate of D12 Panel.
• Considering deployment of man power in largest shift of about 40 persons, quantity of air will be 240CuM/min
• Considering production desired to achieve target of 2500 ton/day, quantity will be 7500Cum/Min.
• To maintain gas percentage of 0.5% in normal period air quantity required is 4800CuM/min, air velocity at face will reach to 8 m/sec, very high as per circular.
• Quantity of about 2000 cum/min is practicable but not sufficient to dilute gas to the required level.

## Slide 37: Constraints to Ventilation Quantity in Seam XV
The in-situ gas content of Seam XV T and XV B is much more than Seam XVI T.
It is envisaged that the gas emission from Seam XV T and XV B will be much more than that of Seam XVI T (i.e. 24 Cum/Min)
It is proposed to initially work Seam XV T and then Seam XV B.
Gas will be accumulated in the goaf of XV T.
As the parting between XV T and XV B is only 3 m, caving will happen and the gas trapped in goaf of Seam XV T will be released in working of Seam XV B.
This excessive gas may become un-controllable with normal ventilation techniques.

## Slide 38: Proposal
Given the amount of gas emission present in Moonidih mine, pre-drainage of gas is necessary.
Thus, a CBM Project is deemed suitable for Moondih Mine.
Advantages:
It will result in safe and smooth operations of the mine.
It may enhance the production capacity of the mine.
The present technology available is adequate to technically and commercially drain-out the gas.
Adequate market is available for selling out the gas.
It will also result in cut-down on “green-house” gas emissions.

## Slide 39: THANK YOU