##### UNITED

NATIONS

Distr.

GENERAL

TRADE/WP.7/GE.2/2003/10

15 April 2003

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

COMMITTEE FOR TRADE, INDUSTRY AND

ENTERPRISE DEVELOPMENT

Working Party on Agricultural Quality Standards

###### Specialized Section on Standardization of

Dry and Dried Produce (Fruit)

50th session, 24-27 June 2003, Geneva

Item 4(a) of the provisional agenda

REVISION OF THE STANDARD LAYOUT FOR

DRY AND DRIED FRUIT

DETERMINATION OF THE MOISTURE CONTENT FOR DRIED FRUIT

Transmitted by Spain

Note by the secretariat:  The rapporteur (Spain) has prepared a new document which includes comments from other delegations. The document is based on an informal document (TRADE/WP.7/GE.2/2002/INF.5), which was distributed at the last session. Additions to that document are shown in bold/underlined and deletions are crossed out.

# ANNEX I

# DETERMINATION OF THE MOISTURE CONTENT FOR DRIED FRUITS

### METHOD 1 - LABORATORY REFERENCE METHOD

1.	Scope and application

This reference method serves to determine the moisture for dried fruits, as dried or desiccated apricots, figs, prunes, dates, grapes, apples, pears, etc.

2.	Reference

This method is based on the method prescribed by AOAC: AOAC Official Method 934.06 - Moisture in Dried Fruits

3.	Definition

Moisture content for dried fruits: conventionally, loss in mass measured under the operating conditions specified in AOAC Official Method 934.06. The moisture content is expressed as percentage by mass (grams per 100 grams).

4.	Principle

Determination of the moisture content of a test portion by drying in an oven 6 h at 70 ± 1º C under pressure < 100 mm Hg (13.3 kPa).

5.	Apparatus (see AOAC Official Method 934.06)

5.1	Analytical balance sensitive to 1 mg or better.

5.2	Mechanical mill or food chopper

5.3	Non-corrosive metal dish, provided with well-fitting lid, about 8.5 cm of diameter, allowing the test portion to be spread to about 0.2 g/cm2  or less.

5.4	Electric vacuum oven with thermostatic control capable of being regulated in normal operation at 70 ± 1º C under pressure < 100 mm Hg (13.3 kPa.).

5.6	Desiccator containing an effective desiccant.

5.7	Steam-bath

6.	Procedure

Follow the operating conditions as specified in AOAC Official Method 934.06 for Moisture in Dried Fruits, with the following additional specifications, concerning the preparation of the test sample:

Homogenize the laboratory sample and take a minimum of 100 g of dried fruits as a test sample. With non-pitted stone fruits (apricots, prunes, peaches, dates, etc), remove the stones using the rest as a test sample.

Grind or chop the test sample to obtain small particles, using either a mechanical mill or food chopper, without overheating the product, or cut and grind by hand if necessary, using knife, scissors, mortar and pestle or similar.

Use 5.0 to 10 g of the ground or chopped product as a test portion. Mix the test portion with circa 2 g of finely divided glass fiber filter or of washed sand, with the help of a spatula, and weigh to nearest  0,01 g.

When necessary, moisten the test portion sand with a few milliliters of hot water, mix the test portion with circa 2 g finely divided glass fiber filter or with washed sand, with the help of a spatula, and heat the open dish on the steam-bath to near dryness, before complete the drying in the vacuum oven.

When necessary, moisten the test portion and the glass fiber filter or the washed sand with a few milliliters of hot water, mix thoroughly with the help of the spatula, and heat the open dish on the steam-bath to near dryness, before complete the drying in the vacuum oven.

Carry out two determinations on the same test sample.

7.	Expression of results and test report

The moisture content, W, as percentage by mass of the sample (grams per 100 grams), is equal to:

M1 - M0

W =     ------------  x 100

M1 - M2

where

M0 is the mass, in grams, of the dish and lid. ,  ,

M1 is the mass, in grams, of the dish and lid, and the test portion before drying. 1,  2

M1 is the mass, in grams, of the dish and lid, and the test portion after drying. 1,  2

Take as a result the arithmetic mean of the results of the two determinations, if the difference between the results  is smaller than 0.2%. The result has to be reported  to one decimal place.

The test report shall show the method used and the results obtained. It shall mention any operating details not specified or optional, and incidents, likely to have influenced the results. It shall also include all the information necessary for the complete identification of the sample.

8.	Repeatability

The difference between the results of two determinations carried out simultaneously or in rapid succession by the same analyst, using the same apparatus and in the same laboratory, should not be greater than 0.2 g of moisture per 100 g of sample.

METHOD 2:  RAPID METHOD

1.	Scope and application

This rapid method serves to determine the moisture for dried fruits.

2.	Reference

This method is based on the method prescribed by AOAC: AOAC Official Method 972.20 - Moisture in Prunes and Raisins (Moisture Meter Method). This method is also commonly used as unofficial method for the determination of moisture content in other kinds of dried fruits.

3.	Definition

Moisture content for dried fruits: conventionally, correlation between moisture content and conductance-temperature measured under the operating conditions specified in AOAC Official Method 972.20. The moisture content is expressed as percentage by mass (grams per 100 grams).

4.	Principle

Determination of the conductance and temperature of a test portion by the moisture tester meter and under the operating conditions specified in AOAC Official Method 972.20. The moisture tester meter has to be calibrated according to the laboratory method, for each kind of dried fruit, taken into account the variety or commercial type and the type of presentation (whole, pitted, slabs, dices, etc) and, when necessary, the crop year and/or the origin.

5.	Apparatus (see AOAC Official Method 972.20)

5.1	Moisture tester meter type A series

5.2	Thermometer (if not incorporated to the moisture tester meter)

5.3	Mechanical mill or food chopper

6.	Procedure

Follow the operating conditions as specified in AOAC Official Method 972.20 - Moisture in Prunes and Raisins (Moisture Meter Method).

Carry out the determination on two test portions

7.	Expression of results and test report

7.1	Result

The result should be the arithmetic mean of the two determinations. Report the result to one decimal place.

7.2	Test report

The test report must state the method used and the results obtained. The report must contain all the information necessary for the complete identification of the sample.

# Footnotes

Weigh to the nearest 0.001 g. 0,01 g.

In case, plus the glass fibre or washed sand, and spatula

After heating on the oven for 2 hours and cooling in the desiccator

It is also possible to employ other rapid methods based on different conductance methods, or on the principle of loss of mass by heating with apparatus including an halogen or infra-red lamp and a built-in analytical balance, always at condition that the method and the apparatus has to be calibrated according the laboratory method.

# Text boxes

E

Economic and Social

Council