CORRIGENDUM Ref. Sales No.: E.99-VIII.1 (ST/SG/AC.10/1/Rev.11) April 2000 New York and Geneva

RECOMMENDATIONS ON THE TRANSPORT

OF DANGEROUS GOODS

Model Regulations

(Eleventh revised edition)

Corrigendum 2

Page 3

Transport of Radioactive material: Change the number of the paragraph: for "19" read "18".

Part 2

Page 54

2.2.3 (b)	Second line, delete "O" after "formula:".

Page 85

2.5.3.2.4	In the column "Diluent type A (%)" for "1,1-DI-(tert-BUTYLPEROXY)-3, 3, 5- TRIMETHYLCYCLOHEXANE", delete "( 23" and add it in the column "Diluent type B (%)".

Page 86

2.5.3.2.4	Rearrange the entries for DI-(2-ETHYLHEXYL) PEROXYDICARBONATE in decreasing concentration order.

Page 87

2.5.3.2.4	For "DI-n-PROPYL PEROXYDICARBONATE" add the following entries: in the column "Concentration (%)": "( 100"; in the column "Packing Method": "OP3"; in the column "Control Temperature ( °C)": "- 25"; in the column "Emergency Temperature ( °C)": "-15 " ; and in the column "Number  (Generic entry)": "3113".

Page 116

2.7.7.2.1 (a)	For "Tbq" read "TBq".

ST/SG/AC.10/1/Rev.11/Corr.2 ENGLISH (Corrigendum 1 applies to the English version only)

Page 132

2.7.7.2.2	In the column, "Activity concentration for exempt material", for "9 ( 10 -1 " read "1 ( 10-1", in the last two rows of the table.

Part 3

Page 148	Explanations for column 9:

In the second, third and forth paragraph, replace "Chapter 4.1" with "sub-section 4.1.4.1", "sub-section 4.1.4.2" and "sub-section 4.1.4.3" respectively.

Page 162

UN 0503	For "pyrotechnic" read "PYROTECHNIC" three times in column (2).

Page 177

UN 1418	Packing group III: For "IC08" read "IBC08" in column (8).

Page 186

UN 1658	NICOTINE SULPHATE, SOLID: For "IBC05" read "IBC08" in column (8).

UN 1664	NITROTOLUENES, SOLID: For "IBC05" read "IBC08" in column (8).

UN 1665	NITROXYLENES, SOLID: For "IBC05" read "IBC08" in column (8).

Page 187

UN 1693	TEAR GAS SUBSTANCE, SOLID, N.O.S. packing group II: For "IBC05" read "IBC08" in column (8).

Page 188

UN 1708	TOLUIDINES, SOLID: For "IBC05" read "IBC08" in column (8).

UN 1711	XYLIDINES, SOLID: For "IBC05" read "IBC08" in column (8).

Page 189

UN 1740	Packing group II: For "IBC05" read "IBC08" in column (8).

Page 191

UN 1781	In column (8), for "ICB02" read "IBC02".

Page 199

UN 1989	Packing group II: For "IBCC02" read  "IBC02" in column (8).

Page 202

UN 2054	In column (8), delete "IBC03" and "LP01".

Page 217

UN 2511	"2-CHLOROPROPIONIC ACID, SOLID," in column (3), for "6.1" read "8".

Page 223

UN 2698	Delete "PP29" in column (9).

Page 227

UN 2772	In column (10), for "TP14" read "T14".

Page 275

SP 238		Delete the following sentence:

"Batteries should be protected against short circuits and shall be securely packed in strong outer packagings".

Page 280

SP 294	Replace "P406" with "P407".

Part 4

Page 287

4.1.1.10	UN 1155: In column "Vp55 (kPa)", for "100" read "199".

Page 291

P001	Under "Single packagings" "Drums", replace "1N" with "1N1".

Page 292

P001		In the column "Single packagings (cont'd)" under "Jerricans" delete "other metal, non-removable head (1N1); for this entry, delete "60 l " under "Packing group I", "Packing group II" and "Packing group III".

In the column "Single packagings (cont'd)" under "Jerricans" delete "other metal, removable head (1N2); for this entry, delete "60 l */ " under "Packing group I" and "60 l" under "Packing group II" and  "Packing group III".

In the column "Single packagings (cont'd)", under "Composite packagings", for "or in a steel, aluminium, wood, fibreboard or plywood box" in the last paragraph, read "or in a steel, aluminium, wood or fibreboard box or in wickerwork hamper".

Under "Special packing provisions", delete the following sentence: "PP20 For UN 2217, any siftproof, tearproof receptacle may be used".

Page 294

P002	In the column "Single packagings (cont'd)" under "Composite packagings", delete "plywood" after "wood" in the last paragraph and add "or in wickerwork hamper" after "fibreboard box".

In the column "Single packagings (cont'd)" under "Composite packagings", for "6PD2 5/" and "6PG2 5/", read "6PG2 5/"and "6PD2 5/" respectively, in the last paragraph before "or in solid or expanded plastics packaging...".

Under "Special packing provisions", add the following sentence: "PP20 For UN 2217, any siftproof, tearproof receptacle may be used".

Page 317

P301 (2)	For "the pressure vessel shall have a minimum design gauge pressure of 5,170 kPa" read "the pressure vessel shall have a minimum design gauge pressure of 2680 kPa and a minimum burst pressure of 5170 kPa".

Page 321

P404	In the list of UN numbers, delete "1370" and add "2441".

P404(1) 	Inner packagings: Replace "capacity of not more than" with "maximum net mass of".

Page 325

P410		In the column "Single packagings (cont'd)", add "3/" after "natural wood with sift proof walls (4C2)".

Page 328

P502, PP28	Correct PP28 to read as follows:

"For UN 1873, only glass inner packagings and glass inner receptacles are authorized respectively for combination packagings and composite packagings."

Page 339

P905		Additional requirements 1 (b): Replace "(Class 2.2)" with "(Division 2.2)".

Page 342

IBC04	Delete "B2".

IBC05	Delete "B3".

Page 346

IBC520		For "Type of IBC 1/" in the heading of column 3, read "Type of IBC".

For "Control temperature 2/" in the heading of column 5, read  "Control temperature".

Page 349

LP01 and

LP02	 	Replace "Plastics" with "Rigid plastics" and "Fibreboard" with "Rigid fibreboard" under "Large outer packagings".

Page 350

LP101 and

LP102		Replace "Plastics" with "Rigid plastics" and "Fibreboard" with "Rigid fibreboard" in the third column.

Page 352

4.1.5.18	For "101" read "P101".

Page 353

4.1.7.1.2	For "520" read "P520".

Page 360

4.2.1.13.6	In the third line, delete the word "substance" before "peroxide".

Part 6

Page 419

6.1.4.3.2	Replace the word "solded" with "soldered".

Page 475

6.5.3.1.1	Replace the word "carriage" with "transport".

Page 503

6.7.1.3		For "T34" read  "T23".

Alphabetical index

Page 625

In the column "Substance or article", for "HYDROGEN CYANIDE, SOLUTION in ALCOHOL with not more than 45 % hydrogen cyanide" for, "in" read "IN".

_________