#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2000/22

14 April 2000

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT

# OF DANGEROUS GOODS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Eighteenth session, 3-14 July 2000,

agenda item 5 (a))

MISCELLANEOUS DRAFT AMENDMENTS TO THE MODEL REGULATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Listing and classification

Proposal for a new entry for Calcium Hypochlorite in Division 5.1

Transmitted by the expert from Japan

Background

1.	It has been several decades from the begining of the manufacture of Calcium Hypochlorite in Japan. Recently some accidents occured on transporting the Calcium Hypochlorites (including hydrated material, UN 2880), so shipping companies began not to accept the cargo of such  Calcium Hypochlorite.   Japanese manufacturers are under the severe situation for exporting. Japanese materials have had no accident on transporting for more than 25years.

2.  	There are three entries (UN 1748, 2208 and 2880) of Calcium Hypochlorites, but there is no entry for Calcium hypochlorite with more than 10% water.

3.  	We succeeded in the development of Calcium hypochlorite with higher moisture content to ensure safe transport of the substance.

GE.00-

Now we are transporting by sea about 10 thousand tons/year of Calcium hypochlorite with more than 10% water contents for more than 50 countries over the world without any accident during transportion. It seems tough situation for the substance to continue to transport as OXYDIZING SOLID, N.O.S.(UN 1479) .

4.	The Expert from Japan proposes that new entry for Calcium hypochlorite with more than 10% water to include in Dangerous Goods List in Chapter 3.2 of the Model Regulation.  The attached data sheet for the substance not specifically listed by name in the List support this position.

Proposal

5.  	(a) 	Add an entry 3XXX in the Dangerous Goods List as follows:

| UN No. | Name and Description | Class or division | Subsid- iary Risks | UN packing group | Special provi-sions | Limited quantities | Packagings and IBCs | Portable tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction | Special provisions | Portable tank instruction | Portable tank special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| 3xxx | CALCIUM HYPOCHLORITE, HYDRATED, with more than 10% water | 5.1 |  | II |  | 500 g | P002 |  |  |  |

(b)	Amend the entry in the alphabetical index to read :

CALCIUM HYPOCHLORITE, HYDRATED, 	5.1  	3XXXX

with more than 10% water

* * * *  *

Figure 1

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by . . . . Japan. . . . . . . . . . . . .                       Date       31 March 20000

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1.     SUBSTANCE IDENTITY

1.1	Chemical name       Calcium hypochlorite, hydrated, with more than 10% water

1.2	Chemical formula       Ca(ClO)2   n H2O

1.3	Other names/synonyms

1.4.1	UN number 		1.4.2	CAS number   7778-54-1

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2 () Calcium hypochlorite, hydrated, or Calcium

hypochlorite, Hydrated mixture, with more than 10% water

1.5.2	class/division    5.1/oxdizing agent                    subsidiary risk(s)   No 		             packing group   II

1.5.3	proposed special provisions, if any      No

1.5.4	proposed packing instruction(s)           No

Section 2.     PHYSICAL PROPERTIES

2.1	Melting point or range	Not applicable

2.2	Boiling point or range	Not applicable

2.3	Relative density at :

2.3.1	15 C

2.3.2	20 C	      about 1(bulk density) for granular

2.3.3	50 C

2.4	Vapour pressure at :

2.4.1	50 C	        Not applicable

2.4.2	65 C	        Not applicable

2.5		Viscosity at 20C((    Not applicable

2.6		Solubility in water at 20C    about 20g/100 ml

2.7		Physical state at 20C (2.2.1.1)      Solid	solid/liquid/gas((

2.8	Appearance at normal carriage temperatures, including colour and odour

White or pale yellowish granular or tablet , chlorine odour

2.9	Other relevant physical properties                    Not known

Section 3.     FLAMMABILITY

3.1		Flammable vapour

3.1.1	Flash point (2.3.3*)        Not applicable

3.1.2	Is combustion sustained? (2.3.1.2*)    No                               yes/no

3.2		Autoignition temperature              Not applicable

3.3		Flammability range (LEL/UEL)   Not applicable

3.4		Is the substance a flammable solid? (2.4.2 *)               No

3.4.1	If yes, give details

Section 4.     CHEMICAL PROPERTIES

4.1		Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?		No	yes/no

If yes, state

4.1.1	Inhibitor/stabilizer used

4.1.2	Alternative method

4.1.3	Time effective at 55C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.1 *)        No	yes/no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.4 *)      No             	yes/no

4.3.1	If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.1)           No	yes/no

If yes, state

4.4.1	exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is the temperature control required? (2.4.2.3.4 */)             No	yes/no

4.4.2	proposed control temperature for a 50 kg package	°C

4.4.3	proposed emergency temperature for a 50 kg package	°C

4.5	Is the substance pyrophoric? (2.4.3 *)                        No	yes/no

4.5.1	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.3 */)        No	yes/no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.1 */)            No	yes/no

If yes state

4.7.1	exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is the temperature control required? (2.5.3.4.1 */)        No	yes/no

4.7.2	proposed control temperature for a 50 kg package	°C

4.7.3	proposed emergency temperature for a 50 kg package	°C

4.8    Does the substance in contact with water emit flammable gases? (2.4.4 * /)              No	yes/no

4.8.1	If yes give details

4.9	Does the substance have oxidizing properties (2.5.1 */)                   Yes	yes/no

4.9.1	If yes, give details

A  mean burning time by a 3:2 mixture of potassium bromate and cellulose : 16.8sec

A mean burning time by a 4:1 mixture of test sample and cellulose :   17.9sec

A mean burning time by a 1:1 mixture of test sample and cellulose : 110sec

Packaging group of this substance was classfied  as 2, based the above results .

4.10	Corrosivity (2.8 */) to:                    Not known

4.10.1	mild steel      Not known 	mm/year   at        Not known	°C

4.10.2	aluminium    Not known	mm/year   at        Not known	°C

4.10.3	other packaging materials

(specify)	    Not known	mm/year   at	°C

Not known	mm/year   at	°C

4.11	Other relevant chemical properties                 Not known

Section 5.     HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1 *)  1)                         850mg/kg	Animal species       rat

5.2	LD 50, dermal (2.6.2.1.2 *) 2)        LDL0=2000mg/kg	Animal species      rabbit

5.3	LC 50, inhalation (2.6.2.1.3 *)     Not known   mg/litre	Exposure time     Not known	 hours

or        Not known   ml/m3	Animal species    Not known

5.4	Saturated vapour concentration at 20 C (2.6.2.2.4.3 ()	   not applicable

- 5.5	Skin exposure (2.8 *) results   	Exposure time     Not known	 hours/minutes

Not known	Animal species    Not known

5.6	Other data	 Mutation test(Ames test) 3)       :   Negative

5.7	Human experience      No

Section 6.     SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1     Fire (include suitable and unsuitable extinguishing agents)

Wear suitable protective equipments containing self-contained breathing apparatus.

Suitable extinguishing agents : a large amout of water

Unsuitable extinguishing agents : a small amount of water, CO2, foam and dry  chmical

6.1.2	Spillage

Collect spill to other container as much as possible and flush with plenty of water.

Dissolve collected spill in a  plenty of water and reduce the solution  by adding reducing

solution.

6.2	Is it proposed to transport the substance in :

6.2.1	Intermediate Bulk Containers (6.5 () ?	   No	yes/no

6.2.2	Portable tanks (6.6*) ?                                 No	yes/no

If yes, give details in Sections 7 and/or 8.

Section 7.     INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.1)

7.1	Proposed type(s)

Section 8.     MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.2)

8.1	Description of proposed tank (including IMO tank type if known)

8.2	Minimum test pressure

8.3	Minimum shell thickness

8.4	Details of bottom openings, if any

8.5	Pressure relief arrangements

8.6	Degree of filling

8.7	Unsuitable construction materials

References         1) Pesticide & Toxic Chemical News,  vol.9,  p21(1980)

2) National Technical Information Service, OTS0570606

3) Food and Chemical Toxicology, vol.22, p623(1984)

___________

# Footnotes

( 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

((	See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

(( 	See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

( 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

( 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

___________

# Text boxes

STSTE

Secretariat