#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2000/27

18 April 2000

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT

# OF DANGEROUS GOODS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Eighteenth session, 3-14 July 2000,

agenda item 5 (a))

MISCELLANEOUS DRAFT AMENDMENTS TO THE MODEL REGULATIONS ON THE TRANSPORT OF DANGEROUS GOODS

Listing and classification

2-Methylbutyraldehyde

Transmitted by the expert from Germany

# Background

Considerable quantities of 2-Methylbutyraldehyde are transported in Germany. Therefore the expert from Germany is of the opinion that this substance should be listed as a new entry in the Dangerous Goods List, Chapter 3.2 of the UN Recommendations.

The determination of the flash point, made by the "PTB" in Germany, shows for the above mentioned substance a flash point of - 3,5° C (see Annex 1 in ST/SG/AC.10/C.3/2000/27/Add.1)).

Details on other physical/chemical properties are recorded in the enclosed data sheet 
(see Annex 2 in ST/SG/AC.10/C.3/2000/27/Add.1).

## GE.00-

## Proposal

The Dangerous Goods List, chapter 3.2 should be amended as follows:

| UN No. (1) | Name and description (2) | Class or division (3) | Subsid- iary risk (4) | UN packing group (5) | Special provi- sions (6) | Limited quantities (7) | Packagings and IBC’s | Portable tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction (8) | Special Provi_ sions (9) | Portable tank instruction (10) | Portable tank special provisions (11) |
| XXXX | 2-METHYLBUTYR- ALDEHYDE | 3 |  | II |  | 1 L | P001 IBC02 |  | T4 | TP1 |

______

# Text boxes

STSTE

Secretariat