#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2000/37

11 April 2000

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT

# OF DANGEROUS GOODS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Eighteenth session, 3-14 July 2000,

# agenda item 3 (a))

# TRANSPORT IN BULK IN PORTABLE TANKS AND FREIGHT CONTAINERS

# Miscellaneous draft amendments to Chapters  4.2 and 6.6

# Refrigerant gases

# Section 4.2.4 Portable tank instructions

Transmitted by the expert from Italy

Introduction

In revising the Tables of RID/ADR concerning filling degrees and test pressures it was discovered that some values, referring to refrigerant gases, were incorrect.

A proposal for amending RID/ADR was then presented to the RID/ADR Joint Meeting (document TRANS/WP.15/AC.1/1999/32), stating also that, if agreed, the relevant proposals will be submitted to the UN Sub-Committee of Experts.

The proposal was adopted at the last Joint Meeting (13-24 March 2000).

GE.00-

Proposal 1

In the portable tank instructions T50 point 4.2.4.2.6 change the maximum filling ratio for:

Refrigerant gas R 404 A    from   0.82 Kg/l  to  0.84 Kg/l

Refrigerant gas R 407 A    from   0.94 Kg/l  to  0.95 Kg/l

Refrigerant gas R 407 B    from   0.93 Kg/l  to  0.95 Kg/l

Justification

The values given in the portable tank instructions T50 are based on the UN Recommendations, Rev.10, originated by ST/SG/AC.10/C.3/R.774, dated 25 April 1996.

The data sheets attached to this document show the following values of density at 50 °C:

R 404 A	0.89 Kg/l

R 407 A	1.00 Kg/l

R 407 B	1.00 Kg/l

Therefore according to point 4.2.2.7.2 of general provision for the use of portable tank maximum filling degrees are:

R 404 A	0.95 ( 0.89 = 0.84

R 407 A	0.95 ( 1.00 = 0.95

R 407 B	0.95 ( 1.00 = 0.95

Proposal 2

In the portable tank instructions T50 point 4.2.4.2.6 change the values of maximum allowable working pressure as follows:

R 404 A	Small            		none			none

Bare              from	28.2 bar	to	28.3 bar

Sunshield      from	25.2 bar	to	25.3 bar

Insulated       from	22.1 bar	to	22.5 bar

R 407 A	Small            from	32.3 bar	to	31.3 bar

Bare              from	29.0 bar	to	28.1 bar

Sunshield      from	25.7 bar	to	25.1 bar

Insulated       		none			none

R 407 B	Small            from	34.0 bar	to	33.0 bar

Bare              from	30.5 bar	to	29.6 bar

Sunshield      from	27.0 bar	to	26.5 bar

Insulated       		none			none

R 407 C	Small            from	30.2 bar	to	29.9 bar

Bare              from	27.0 bar	to	26.8 bar

Sunshield      from	24.1 bar	to	23.9 bar

Insulated       from	21.4 bar	to	21.3 bar

Justification

According to point 6.7.3.1 of requirements for the design, construction, inspection and testing of portable tanks intended for the transport of non-refrigerated liquefied gases, the maximum allowable working pressure is the absolute vapour pressure of non-refrigerated liquefied gas at the design reference temperature minus 1 bar.

The values of the absolute vapour pressures at 65 °C, 60 °C, 55 °C et 50 °C from the calculation program “NIST THERMODYNAMIC PROPERTIES OF REFRIGERANTS AND REFRIGERANT MIXTURES (Rev. 5.10)” are:

R 404 A	65 °C		32.55 bar	rounded  up to		32.6 bar

60 °C		29.29 bar	rounded  up to		29.3 bar

55 °C		26.28 bar	rounded  up to		26.3 bar

50 °C		23.50 bar	rounded  up to		23.5 bar

R 407 A	65 °C		32.29 bar	rounded  up to		32.3 bar

60 °C		29.07 bar	rounded  up to		29.1 bar

55 °C		26.08 bar	rounded  up to		26.1 bar

50 °C		23.32 bar	rounded  up to		23.4 bar

R 407 B	65 °C		33.92 bar	rounded  up to		34.0 bar

60 °C		30.55 bar	rounded  up to		30.6 bar

55 °C		27.42 bar	rounded  up to		27.5 bar

50 °C		24.53 bar	rounded  up to		24.6 bar

R 407 C	65 °C		30.82 bar	rounded  up to		30.9 bar

60 °C		27.73 bar	rounded  up to		27.8 bar

55 °C		24.86 bar	rounded  up to		24.9 bar

50 °C		22.22 bar	rounded  up to		22.3 bar

Therefore the values of the test pressure should be:

R 404 A	Small		31.6 bar

Bare		28.3 bar

Sunshield	25.3 bar

Insulated	22.5 bar

R 407 A	Small		31.3 bar

Bare		28.1 bar

Sunshield	25.1 bar

Insulated	22.4 bar

R 407 B	Small		33.0 bar

Bare		29.6 bar

Sunshield	26.5 bar

Insulated	23.6 bar

R 407 C	Small		29.9 bar

Bare		26.8 bar

Sunshield	23.9 bar

Insulated	21.3 bar

# _____________

# Text boxes

STSTE

Secretariat