Distr.

GENERAL

TRANS/WP.29/GRSP/2000/9/Add.1

8 February 2001

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicles Regulations (WP.29)

Working Party on Passive Safety (GRSP)

(Twenty-ninth session, 7-11 May 2001,

agenda item 2.2.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 14

(Safety-belt anchorages)

### Addendum 1

Transmitted by the Expert from the International Organization of

Motor Vehicles Manufacturers (OICA)

Note: The text reproduced below was prepared by the expert from OICA in order to update his proposal.

____________

__________

Note: This document is distributed to the Experts on Passive Safety only.

GE.01-

Paragraph 4.2.4., amend to read:

"..... in paragraphs 4.2.1. to 4.2.3. of this Regulation .....”

Paragraph 4.3.2., amend to read:

"...... plane of the vehicle.  A pre-load of 1,000 N + 250 N may be applied; this pre-load will be included in the total test load.”

Paragraph 4.3.3., amend to read:

"..... as rapidly as possible: within a maximum of 3 seconds.  The belt anchorages must withstand .......”

Annex 3, amend to read:

"Annex 3

(All dimensions are in mm)

Cloth-covered Loan, thickness: 25

### Figure 1

Cloth-covered Loan, thickness: 25

Strap connecting block to

anchorage points

(dimensions in mm)

Figure 2”

________________