#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2001/4

23 March 2001

# ORIGINAL : ENGLISH

# COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND  ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Nineteenth session, 2-6 July 2001,

# agenda item 3 (b))

TANKS

Miscellaneous proposals

Requirements for the design, construction, inspection and testing of portable tanks

Transmitted by the expert from Spain

In the case of using bursting discs, preceding to a safety valve, it is convenient to take into account the decrease of the section that takes place in the way of the bursting disc, when it is fragmented or closed, if it is not destroyed.

The ASME code settles down in the section VIII Div. 1 UG-129 some prescriptions in this respect.

About this aspect, it is indicated the necessity of marking the valve or the bursting disc, or on a plate or plates, it must include the name of the constructor’s valve and the name of the constructor’s bursting disc, the factor of combined capacity, that it is the one that it is necessary to multiply, m3/h of the safety valve to obtain the real capacity of the combined the device.

GE.01-

Therefore, it is proposed to add a paragraph at 6.7.2.12.2. that says:

“In the case of a combined device of a safety valve preceded of a bursting disc, the steam flow through the bursting disc cannot be minor than the flow through the valve and at such effect.

A factor of combined capacity of 0.9 should be applied as minimum to the capacity of m3/h of the valve given by the manufacturer of it.”

_________

# Text boxes

STSTE

Secretariat