UN/SCETDG/19/INF.36

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Nineteenth session,

2-6 July 2001, agenda item 8(b))

EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

Classification of ammonium nitrate emulsions, suspensions an gels

New entry for ammonium nitrate emulsions in Class 1

Transmitted by the expert from Sweden

1.	BACKGROUND

During the Madrid Working Group, 18-20 April 2001, on classification of Ammonium Nitrate Emulsions, suspensions or gels, intermediate for blasting explosives (ANE:s), a number of changes were proposed on the entry for UN 3375.

These changes affect our earlier document ST/SG/AC.10/C.3/2001/23. Therefore the author proposes some modifications of the earlier proposal using the documents ST/SG/AC.10/C.3/2001/6 (chairman WG) and ST/SG/AC.10/C.3/2001/19 (UK)

2.	MODIFIED PROPOSALS

2.1	To create a new entry in 1.5 D as follows:

UN

No.

(1)

Name and description

(2)

Class or Division

(3)

Subsi-diary risk

(4)

UN packing group

(5)

Special provi-sions

(6)

Limited quantities

| (7) | Packagings and IBC’s | Portable tanks |
| --- | --- | --- |

Packing instruc-tion

(8)

Special provi-sion

(9)

PT instruc-tion

(10)

PT

special provision

(11)

05xy

AMMONIUM NITRATE EMULSION or SUSPENSION or GEL, intermediate for blasting explosives

|  | 1.5 | D | II |
| --- | --- | --- | --- |

3XX

| 3XY | NONE |
| --- | --- |

P101

IBC99

T99

TP9

2.2	Create a new special provision 3XY as follows:

	This entry may only be used for substances that do not pass the 8(b), 8(c) or 8(d) tests and that passes the demands in Test Series 5 (see Manual of Tests and Criteria, Part I).

2.3	Create a new special provision 3XX as follows:

This entry applies to non sensitised emulsions, suspensions and gels consisting primarily of a mixture of ammonium nitrate and a fuel phase, intended to produce a Type E blasting explosive only after further processing prior to use. The mixture typically has the following composition:

60 - 85 % ammonium nitrate; 5 - 30% water; 2 - 8% fuel;  0.5  - 4 % emulsifier or thickening agent; 0 - 10 % soluble flame suppressants and trace additives. Other inorganic nitrate salts may replace part of the ammonium nitrate.

___________