UN/SCETDG/19/INF.37

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Nineteenth session,

2-6 July 2001, agenda item 8(b))

EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

Classification of ammonium nitrate emulsions, suspensions an gels

# Further evaluation of the Vented Pipe Test

# Transmitted by the expert from Sweden

1.	BACKGROUND

During the Madrid Working Group, 18-20 April 2001, on classification of Ammonium Nitrate Emulsions, suspensions or gels, intermediate for blasting explosives (ANE:s), Sweden agreed to coordinate further tests with the Vented Pipe Test.

A small ad-hoc group was formed consisting of both industry and authority representatives from Norway, Spain, Sweden and USA. After a further meeting in Kiruna, 25 April, Finnish industry agreed to join this group.

2.	The Ad-hoc group commission

- Define a reference ANE to use for the further work

-	A reference ANE to be used as a reference between test facilities and countries has been suggested. This is attached as Annex 1.

- Evaluate different fire source, theoretically and in some tests

-	The base should be the 6(c)-test and evaluation of wooden or liquid sources should be made

- Evaluate some variations of the test vessel

-	Size, shall (to begin with) be based upon the US Vented Pipe

-	The strength of the test vessel related to bursting pressure compared with  tanks for transportation. (awaiting data)

-	Variations in the orifice size (3” and 5” was tested in November 2000)

-	Length of the venting pipe (or totally stop using a pipe?)

- Evaluate some variations in ANE

-	Different Sodium Nitrate amounts

-	Differences in the Water contents

- Test volume or filling grade of ANE in test vessel

- Test parameters

-	During testing the following should be observed/measured;

-	Video recording, 2 cameras at different angles from the test set-up

-	Meteorological data, such as wind speed, air temperature, relative humidity and air pressure

-	Temperature measurement in the fire (2 gauges) and in the test vessel

3.	COMMITMENTS
	
In Madrid we agreed to:

-	That Sweden should co-ordinate tests with the vented pipe

-	Present a program for the Ad-hoc group to UN, as a INF-paper, to the July meeting (2001)

-	Propose in that program that test results should be available as a formal paper in July 2002

### ANNEX 1

Reference emulsion - Vented Pipe Test

Formulation

Oxidizer solution Ammonium nitrate: 83% Water: 17% Fuel phase Oil: 80% SMO 10% Atsurf 5000: 10%

## Emulsion matrix

Oxidizer solution  :	94.4%

Fuel Phase          :	5.6%

### Specifications:

The given specifications are recommendations, and other raw materials can be used as long as they have similar properties.

Ammoniumnitrate-liquor:

| Producer | Any |
| --- | --- |
| Name | AN liquor |
| pH (1mol/l @25oC) | 4,0 – 6,5 |
| Chloride | Max 10 ppm |
| Fe3+ | Max 10 ppm |
| Sulphate (SO42-) | Max 10 ppm |
| Organic matter | Max 15 ppm |

Atsurf 5000:

| Producer | Uniquema |
| --- | --- |
| Polymeric emulsifier, non ionic |  |
| Acid number | 29.0-33.0 mg KOH/g |

###### SMO :

| Producer | Croda |
| --- | --- |
| Name | Anfomul S4 |
| Acid value | 6.8 mg KOH/g |
| Hydroxyl value | 211 mg KOH/g |
| Saponification value | 154.7 mg KOH/g |
| Water content | 0.27 % (w/w) |

Oil :

Producer:  	Nynäs or orthers

Name	:	Nytex 810 or equivalent

|  |  | Value | Method |
| --- | --- | --- | --- |
| Density (15ºC) | kg/dm3 | 0.901 | D 4052 |
| Viscosity (40ºC) | CSt | 22 | D 445 |
| Viscosity (100ºC) | CSt | 3.7 | D 445 |
| Flashpoint | ºC | 178 | D 93 |
| Pourpoint | ºC | -42 | D 97 |
| Neutralisation no | Mg KOH/g | <0.01 | D 974 |
| Sulphur | Wt% | 0.03 | D 2622 |
| Aniline point | ºC | 74 | D 611 |
| Refractive index 20ºC |  | 1.493 | D1747 |
| VGC |  | 0.860 | D 2501 |
| UV abs at 260 nm |  | 1.0 | D 2008 |
| Ca | % | 16 | IR Method |
| Cn | % | 40 | IR Method |
| Cp | % | 44 | IR Method |
| Aromatic content | % | 10 | D 2140 |
| DMSO extracted compounds | % | 2 | IP 346 |

### Emulsion matrix properties:

Density: 1.4 kg/dm3

Viscosity: (To be determined later) (Brookfield RV or LV, spindle 7, @ 20 rpm @ 20 oC)

_______