# UN/SCETDG/20/INF.20

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Twentieth session, 3-12 December 2001,

agenda item 7 (d))

# DRAFT AMENDMENTS TO THE MODEL REGULATIONS

# ON THE TRANSPORT OF DANGEROUS GOODS

# Listing and Classification

#### Proposal for schematic classification of Organometallic Substances

#### Transmitted by the International Council of Chemical Associations (ICCA)

1:	Introduction

This information paper contains a first draft on schematic classification of organometallic substances. The intent of this paper is to inform the UN sub-committee and to collect comments from the various delegations.  A brief introduction may be given, but it is not the intent to discuss this paper during this December session.

A formal proposal, incorporating the comments received, will be submitted for the July 2002 session.

** First DRAFT **

1.		Introduction

In the UN model regulations, organometallic substances are classified in division 4.2 as pyrophoric substances or, in diluted form, in division 4.3 as water reactive substances. These substances can be designated to a number of UN entries, but not in a systematic way. In practise the same product may be transported under different UN numbers which causes confusion. Also some UN entries may be used for both solid and liquid substances. The problem was already partly highlighted in Information paper 43, December 1994, of the UN CETDG. Over the last two years, relevant industries discussed these problems and developed a systematic classification procedure for organometallic substances as submitted by this proposal.

2.		Appropriate UN numbers

The designation of an appropriate UN number to organometallic compounds is not based on a generic entry system. These materials can be assigned to the following available appropriate UN entries:

Division 4.2

- pyrophoric substance; the current UN numbers are based on physical state (solid/liquid) and nature (organic or inorganic) of the substances,

- pyrophoric organometallic compounds n.o.s (one UN number for both solid and liquid),

- n.o.s entries for pyrophoric metal alkyls, on the bases of their general chemical nature (alkyls general, alkyl halides, alkyl hydrides and aryl hydrides),

- n.o.s. entries for pyrophoric metal alkyls with specified metal part,

- metal alkyls listed by chemical name

Division 4.3

- organometallic compound or compound solution or compound dispersion, water reactive, flammable

- organometallic compound, solid, water reactive, flammable

A table of currently available UN numbers is given in Annex 1. In practise, the number of possibilities result in a non unambiguous UN number assignment. For example, a pyrophoric solution of a metal alkyl compound can be assigned to UN number 2845 (Pyrophoric liquid, n.o.s.) or UN 3203 (Pyrophoric organometallic compounds, n.o.s) or UN 2003, Metal alkyl, n.o.s. In order to classify organometallic substances in a systematic way, ICCA proposes the a procedure to achieve consistent classification. Justification is given below.

3.		Justification  of classification scheme proposed

In the proposed scheme for classifying organometallic substances the following aspects are incorporated:

- individual UN entries for solid and liquid substances, which is currently not the case

- clear distinction between pyrophoric and non pyrophoric organometallic substances and formulations

- clear distinction between water reactive and non water reactive organometallic substances and formulations

- systematic assignment of packagings, IBCs and tanks (if applicable), in line with the current requirements for these substances

In the scheme, the non pyrophoric water reactive substances have to be evaluated on :

a) flammability for the liquids and

b) self-heating properties for the solids (and not flammability properties).

On a): the determination of the flash point to assess flammability properties of liquids is not possible due to the reactive properties of organometallic substances in air. Therefore, it is proposed to use the flash point of the solvent used in the formulation.

On b): for non pyrophoric, water reactive solid organometallic substances the self-heating properties are relevant, because these substances react with oxygen. Also according the precedence of hazards table 2.0.3.3, self-heating of 4.2 takes precedence over flammability 4.1.

All the UN entries proposed for deletion are covered by the proposed organometallic substances, defined as substances having a metal-carbon bond. Nevertheless it is proposed to remain the old UN entries in the alphabetic list with reference to the relevant new UN number. For the new generic entries proposed, the wording organometallic “substance” which covers the current descriptions: compounds, solutions, dispersions because it is not always obvious which description should be used.

In case a organometallic substance is not classified according to the flow chart in division 4.2 or 4.3, classification in other classes has to be evaluated. This is also applicable for the substances classified by the proposed scheme.

4.		Proposals

4.1	Insert in chapter 2.4., under introductory notes, the following new note:

NOTE 3: Because Organometallic substances, defined as substances containing a metal-carbon bond,  can be classified in division 4.2 or 4.3 with additional subsidiary risks, depending on the properties of the substance, a specific classification flow chart for these substances is given in 2.4.5

4.2	Insert the following new flowchart in new 2.4.5

Figure 2.4.2: Flowchart scheme for organometallic substances (substances containing metal-carbon bonds)

4.3	Delete the following new UN numbers in chapter 3, Dangerous Goods List:

1366 	Diethylzinc

1370	Dimethylzinc

2003	Metal alkyls water-reactive N.O.S. or Metal aryls water reactive, N.O.S

2005	Magnesium diphenyl

2445	Lithium alkyls

3049	Metal alkyl halides, water-reactive, N.O.S.,  Metal aryl halides, water-reactive, N.O.S

3050	Metal alkyl hydrides, water-reactive, N.O.S.,  Metal aryl hydrides, water-reactive, N.O.S

3051	Aluminium alkyls

3052	Aluminium alkyl halides (liquid + solid)

3053	Magnesium alkyls

3076	Aluminium alkyl hydrides

3203	Pyrophoric organometallic compound, water reactive, N.O.S (solid + liquid)

3207	Organic metallic compound or compound solution or compound dispersion, water reactive,

flammable, N.O.S

3372	Organic metallic compound solid, water reactive, flammable, N.O.S

4.4	Insert the following new UN numbers in chapter 3, Dangerous Goods List:

| UN No. (1) | Name and description (2) | Class or division (3) | Subsid-iary risk (4) | UN packing group (5) | Special provi-sions (6) | Limited quantities (7) | Packagings and IBCs | Portable tanks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | Packing instruction (8) | Special provisions (9) | Portable tank instruction (10) | Portable tank special provision (11) |
| xxx1 | Organometallic substance, solid, pyrophoric | 4.2 |  | I | 274 | NONE | P404 |  |  |  |
| xxx2 | Organometallic substance, liquid, pyrophoric | 4.2 |  | I | 274 | NONE | P400 |  | T21 | TP2 TP7 TP9 |
| xxx3 | Organometallic substance, solid, pyrophoric, water reactive | 4.2 | 4.3 | I | 274 | NONE | P404 |  |  |  |
| xxx4 | Organometallic substance, liquid, pyrophoric, water reactive | 4.2 | 4.3 | I | 274 | NONE | P400 |  | T21 | TP2 TP7 TP9 |
| xxx5 | Organometallic substance, solid, water reactive | 4.3 |  | I | 274 | NONE | P403 IBC04 |  |  |  |
|  |  | 4.3 |  | II | 274 | 500 g | P410 IBC04 |  |  |  |
|  |  | 4.3 |  | III | 223 274 | 1 kg | P410 IBC06 |  |  |  |
| xxx6 | Organometallic substance, liquid, water reactive | 4.3 |  | I | 274 | NONE | P402 IBC99 |  | T13 | TP2 TP7 TP9 |
|  |  | 4.3 |  | II | 274 | 500 g | P001 IBC01 | B2 | T7 | TP2 TP7 |
|  |  | 4.3 |  | III | 223 274 | 1 kg | P001 IBC02 | B4 | T7 | TP2 TP7 |
| xxx7 | Organometallic substance, solid, water reactive, self-heating | 4.3 | 4.2 | I | 274 | NONE | P403 IBC04 |  |  |  |
|  |  | 4.3 | 4.2 | II | 274 | 500 g | P410 IBC04 |  |  |  |
|  |  | 4.3 | 4.2 | III | 223 274 | 1 kg | P410 IBC06 |  |  |  |
| xxx8 | Organometallic substance, liquid, water reactive, flammable | 4.3 | 3 | I | 274 | NONE | P402 IBC99 |  | T13 | TP2 TP7 TP9 |
|  |  | 4.3 | 3 | II | 274 | 500 g | P001 IBC01 | B2 | T7 | TP2 TP7 |
|  |  | 4.3 | 3 | III | 223 274 | 1 kg | P001 IBC02 | B4 | T7 | TP2 TP7 |
| xxx9 | Organometallic substance, solid, self-heating | 4.2 |  | II | 274 | 500 g | P410 IBC06 | B2 |  |  |
|  |  | 4.2 |  | III | 223 274 | 1 kg | P002 IBC08 | B3 |  |  |

5.		Consequential amendments

5.1	Amend the following entries in the alphabetical index of substances and articles

| Entry | To be read as |
| --- | --- |
| DIETHYLZINC, 4.2, 1366 | Diethylzinc, see 4.2, xxx4 |
| DIMETHYLZINC, 4.2, 1370 | Dimethylzinc, 4.2, xxx4 |
| Metal alkyls, water-reactive, N.O.S, 4.2, 2003 | Metal alkyls, water-reactive N.O.S, see 4.2, xxx3 or xxx4 |
| Metal aRYLs, water-reactive, N.O.S, 4.2, 2003 | Metal aryls, water-reactive N.O.S, see 4.2, xxx3 or xxx4 |
| Magnesium diphenyl, 4.2, 2005 | Magnesium diphenyl, see 4.2, xxx1 |
| Lithium alkyls, 4.2, 2445 | Lithium alkyls, see 4.2, xxx4 |
| Metal alkyl halides, water-reactive, N.O.S., 4.2, 3049 | Metal alkyl halides, water-reactive, N.O.S, see 4.2, xxx4 |
| Metal aryl halides, water-reactive, N.O.S, 4.2, 3049 | Metal aryl halides, water-reactive, N.O.S, see 4.2, xxx4 |
| Metal alkyl hydrides, water-reactive, N.O.S., 4.2, 3050 | Metal alkyl hydrides, water-reactive, N.O.S, see 4.2, xxx4 |
| Metal aryl hydrides, water-reactive, N.O.S, 4.2, 3050 | Metal aryl hydrides, water-reactive, N.O.S, see 4.2, xxx4 |
| Aluminium alkyls, 4.2, 3051 | Aluminium alkyls, see 4.2, xxx4 |
| Aluminium alkyl halides, liquid, 4.2, 3052 | Aluminium alkyl halides, liquid see 4.2, xxx4 |
| Aluminium alkyl halides, solid, 4.2, 3052 | Aluminium alkyl halides, solid see 4.2, xxx3 |
| Magnesium alkyls, 4.2, 3053 | Magnesium alkyls, see 4.2, xxx4 |
| Alminium alkyl hydrides, 4.2, 3076 | Aluminium alkyl hydrides, see 4.2, xxx4 |
| Pyrophoric organometallic compound, water reactive, liquid, N.O.S, 4.2, 3203 | Pyrophoric organometallic compound, water reactive, liquid, N.O.S, see 4.2, xxx4 |
| Pyrophoric organometallic compound, water reactive, solid, N.O.S, 4.2, 3203 | Pyrophoric organometallic compound, water reactive, solid, N.O.S, see 4.2, xxx3 |
| Organic metallic compound dispersion, water reactive, flammable, N.O.S, 4.3, 3207 | Organic metallic compound dispersion, water reactive, flammable, N.O.S, see 4.3, xxx8 |
| Organic metallic compound SOLUTION, water reactive, flammable, N.O.S, 4.3, 3207 | Organic metallic compound solution, water reactive, flammable, N.O.S, see 4.3, xxx8 |
| Organic metallic compound solid, water reactive, flammable, N.O.S, 4.3, 3372 | Organic metallic compound solid, water reactive, flammable, N.O.S, see 4.3, xxx7 |

5.2	Insert the new UN numbers, as shown in 4.4, in the alphabetical index of substances and articles

5.3	In 3.1.2.2 select an other example instead of UN 3207

In 3.1.2.8.1.3: select an other example for UN 2003 Metal Alkyl, water reactive, N.O.S. (triethylgallium)

5.4	Change UN numbers in packing instruction P404 (2005 into xxx1, 3203 into xxx3, 3052 into xxx3)

Annex 1

Possible UN numbers for organometallic compounds, division 4.2

Proper shipping name							UN number

Pyrophoric liquid, organic, N.O.S					2845

Pyrophoric solid, organic, N.O.S					2846

Pyrophoric liquid, inorganic, N.O.S					3194

Pyrophoric solid, inorganic, N.O.S					3200

Pyrophoric organometallic comp, water reactive, N.O.S (solid + liquid)	3203

Metal alkyls/aryls, water reactive, N.O.S					2003

Metal alkyl/aryl halides, water reactive, N.O.S				3049

Metal alkyl/aryl hydrides, water reactive, N.O.S.				3050

Aluminium alkyls							3051

Aluminium alkyl halides (solid + liquid)				3052

Aluminium alkyl hydrides						3076

Magnesium alkyls							3053

Lithium alkyls								2445

Magnesium diphenyl							2005

Diethylzinc								1366

Dimethylzinc								1370

Possible UN numbers for organometallic compounds, division 4.3

Organic metallic compound or compound solution or

compound dispersion, water reactive, flammable, N.O.S			3207

Organic metallic compound solid, water reactive, flammable, N.O.S	3372

──────────────────

# Text boxes

Organometallic substance/formulation/

solution

Is the substance pyrophoric ?

test N.2 (solid)

test N.3 (liquid)

Is the substance water reactive ?

test N.5

Is the substance water reactive ?

test N.5

Division 4.3, PG I or II or III.

Is the substance a

solid ?

Is the substance self heating ?

test N.4

Is the flash point

of the diluent

≤ 60.5 °C ?

Organometallic substance,  solid, pyrophoric

UN XXX1

Organometallic substance,  liquid, pyrophoric

UN XXX2

Organometallic substance,  solid, pyrophoric, water reactive UN XXX3

Organometallic substance,  liquid, pyrophoric, water reactive UN XXX4

Organometallic substance,  solid, water reactive

UN XXX5

Organometallic substance,  solid, water reactive, self-heating UN XXX7

Organometallic substance,  liquid, water reactive

UN XXX6

Organometallic substance,  liquid, water reactive, flammable UN XXX8

No

No

No

No

No

Yes

Yes

Yes

Yes

Yes

No

Yes

liquid

liquid

solid

solid

Substance does not have to be classified in division 4.2 or in division 4.3

Organometallic substance,  solid, self-heating

UN XXX9

Is the substance self heating ?

test N.4

Yes

Is the substance a

solid ?

Yes

No

No