# UN/SCETDG/20/INF.38

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

(Twentieth session, 3-12 December 2001,

agenda item 3 (b))

TANKS

Miscellaneous Proposals

Transport of solids in portable tanks

Transmitted by the Expert from the United States of America

Background

1.	In ST/SG/AC.10/C.3/2001/55 the expert from the United States of America agreed to draft a list of tank code assignments for solid dangerous goods that are not currently authorized for transport in portable tanks in the Dangerous Goods List.  Annex 2 of this paper provides a draft listing.  The draft list of tank assignments was developed on the basis of the rationalized approach provided in Annex 1.

2.	Tank assignments were not considered for the following items:

- explosives and desensitized explosives;

- certain blasting explosives and ammonium nitrate;

- Division 6.2 substances and Genetically Modified Micro-organisms, UN 3245;

- UN 3255, tert-Butyl hypochlorite and UN 2907, Isosorbide dinitrate mixture, which should be  forbidden from transport in portable tanks;

- articles; and

- substances where it is not practical to transport them in portable tanks, including:

UN 2211, Polymeric beads, expandable

UN 3314, Plastics moulding compound

UN 2000, Celluloid

UN 1379, Paper, Unsaturated oil treated

UN 1386, Seed cake

UN 1365, Cotton, wet

UN 2793, Ferrous metal borings, shavings, turnings or cuttings

UN 2217, Seed cake

UN 1364, Cotton, waste oily

UN 2002, Celluloid, scrap

UN 2006, Plastics, nitrocellulose based, self-heating, n.o.s.

UN 2016, Ammunition toxic, non-explosive

3.	As there are a few solids which are currently assigned tank codes in the Model Regulations, it is proposed that these tank codes be changed in accordance with the rationalized approach for consistency.  A list of these solids with their current and proposed T-Codes is provided in Annex 3.

4.	This paper does not include proposed assignments of tank provisions (TPs) for solids.  The Sub-committee is invited to consider what TPs should apply to solids in tanks.  The TPs which exist in the Recommendations generally apply to liquids and are considered to be inappropriate for solids.  The following are examples of provisions which may be appropriate as TPs for solids:

- The substance should be so loaded that the weight is evenly distributed within the tank.

- The tank shall not be filled in excess of its maximum permissible gross mass.

- If the substance is offered for transport under elevated temperature conditions, the degree of filling prescribed in 4.2.1.9.5.1 shall not be exceeded (e.g. current TP3 and TP7).

5.  Additional tank code assignments or amendments may be necessary on the basis of the paper from the Netherlands, UN/SCETDG/20/INF.17 Correct assignment of UN Numbers to substances and solutions

with respect to physical state (liquid or solid).

##### Annex 1

Rationalized Approach to Assignment of Tank Instructions for Solids

Following is a proposed rationalized approach for the assignment of solids to portable tanks:

| Tank Instructions for Solids – Rationalized Approach |
| --- |
| Class | PG | TI | TP |
| 4.1 | I | Forbidden |
|  | II | T3 |  |
|  | III | T1 |  |
| 4.2 | I | T21 |  |
|  | II | T3 |  |
|  | III | T1 |  |
| 4.3 | I | T6 | TP3, TP7 |
|  | II | T3 |  |
|  | III | T1 |  |
| 5.1 | II | T3 |  |
|  | III | T1 |  |
| 6.1 | I | T6 |  |
|  | II | T3 |  |
|  | III | T1 |  |
| 8 | I | T6 |  |
|  | II | T3 |  |
|  | III | T1 |  |
| 9 | I | T3 |  |
|  | II | T1 |  |

Annex 2

Proposed T-Codes for Solids not Currently Assigned T-Codes

| UN# | Name | Class | PG | Sub-Risk | TI |
| --- | --- | --- | --- | --- | --- |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | II |  | T3 |
| 1323 | FERROCERIUM | 4.1 | II |  | T3 |
| 1341 | PHOSPHORUS SESQUISULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 |
| 1343 | PHOSPHORUS TRISULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 |
| 3242 | AZODICARBONAMIDE | 4.1 | II |  | T3 |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | II |  | T3 |
| 3270 | NITROCELLULOSE MEMBRANE FILTERS, with not more than 12.6% nitrogen, by dry mass | 4.1 | II |  | T3 |
| 1437 | ZIRCONIUM HYDRIDE | 4.1 | II |  | T3 |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 |
| 2556 | NITROCELLULOSE WITH ALCOHOL (not less than 25% alcohol, by mass, and not more than 12.6% nitrogen, by dry mass) | 4.1 | II |  | T3 |
| 2555 | NITROCELLULOSE WITH WATER (not less than 25% water, by mass) | 4.1 | II |  | T3 |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | II |  | T3 |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 |
| 3097 | FLAMMABLE SOLID, OXIDIZING, N.O.S. | 4.1 | II | 5.1 | T3 |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | II | 6.1 | T3 |
| 1868 | DECABORANE | 4.1 | II | 6.1 | T3 |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | II | 6.1 | T3 |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | II | 8 | T3 |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | II | 8 | T3 |
| 1339 | PHOSPHORUS HEPTASULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 |
| 1345 | RUBBER SCRAP or RUBBER SHODDY, powdered or granulated, not exceeding 840 microns and rubber content exceeding 45% | 4.1 | II |  | T3 |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | III |  | T1 |
| 1330 | MANGANESE RESINATE | 4.1 | III |  | T1 |
| 1328 | HEXAMETHYLENETETRAMINE | 4.1 | III |  | T1 |
| 1324 | FILMS, NITROCELLULOSE BASE, gelatin coated, except scrap | 4.1 | III |  | T1 |
| 1314 | CALCIUM RESINATE, FUSED | 4.1 | III |  | T1 |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 |
| 2213 | PARAFORMALDEHYDE | 4.1 | III |  | T1 |
| 1869 | MAGNESIUM or MAGNESIUM ALLOYS with more than 50% magnesium in pellets, turnings or ribbons | 4.1 | III |  | T1 |
| 1332 | METALDEHYDE | 4.1 | III |  | T1 |
| 1353 | FIBRES or FABRICS IMPREGNATED WITH WEAKLY NITRATED NITROCELLULOSE, N.O.S. | 4.1 | III |  | T1 |
| 2538 | NITRONAPHTHALENE | 4.1 | III |  | T1 |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | III |  | T1 |
| 2956 | 5-tert-BUTYL-2,4,6-TRINITRO-m-XYLENE (MUSK XYLENE) | 4.1 | III |  | T1 |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 |
| 3241 | 2-BROMO-2-NITROPROPANE-1,3-DIOL | 4.1 | III |  | T1 |
| 2687 | DICYCLOHEXYLAMMONIUM NITRITE | 4.1 | III |  | T1 |
| 2001 | COBALT NAPHTHENATES, POWDER | 4.1 | III |  | T1 |
| 2714 | ZINC RESINATE | 4.1 | III |  | T1 |
| 2878 | TITANIUM SPONGE GRANULES or TITANIUM SPONGE POWDERS | 4.1 | III |  | T1 |
| 1318 | COBALT RESINATE, PRECIPITATED | 4.1 | III |  | T1 |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | III | 8 | T1 |
| 1338 | PHOSPHORUS, AMORPHOUS | 4.1 | III |  | T1 |
| 1313 | CALCIUM RESINATE | 4.1 | III |  | T1 |
| 1312 | BORNEOL | 4.1 | III |  | T1 |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | III |  | T1 |
| 2858 | ZIRCONIUM, DRY, coiled wire, finished metal sheets, strip (thinner than 254 microns but not thinner than 18 microns) | 4.1 | III |  | T1 |
| 3097 | FLAMMABLE SOLID, OXIDIZING, N.O.S. | 4.1 | III | 5.1 | T1 |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | III | 8 | T1 |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | III | 6.1 | T1 |
| 2717 | CAMPHOR, synthetic | 4.1 | III |  | T1 |
| 1334 | NAPHTHALENE, CRUDE or NAPHTHALENE, REFINED | 4.1 | III |  | T1 |
| 3251 | ISOSORBIDE-5-MONONITRATE | 4.1 | III |  | T1 |
| 1346 | SILICON POWDER, AMORPHOUS | 4.1 | III |  | T1 |
| 2715 | ALUMINIUM RESINATE | 4.1 | III |  | T1 |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | III | 6.1 | T1 |
| 3254 | TRIBUTYLPHOSPHANE | 4.2 | I |  | T21 |
| 1855 | CALCIUM, PYROPHORIC or CALCIUM ALLOYS, PYROPHORIC | 4.2 | I |  | T21 |
| 2846 | PYROPHORIC SOLID, ORGANIC, N.O.S. | 4.2 | I |  | T21 |
| 2881 | METAL CATALYST, DRY | 4.2 | I |  | T21 |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | I |  | T21 |
| 1854 | BARIUM ALLOYS, PYROPHORIC | 4.2 | I |  | T21 |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | I |  | T21 |
| 2546 | TITANIUM POWDER, DRY | 4.2 | I |  | T21 |
| 1383 | PYROPHORIC METAL, N.O.S. or PYROPHORIC ALLOY, N.O.S. | 4.2 | I |  | T21 |
| 3200 | PYROPHORIC SOLID, INORGANIC, N.O.S. | 4.2 | I |  | T21 |
| 3255 | tert-BUTYL HYPOCHLORITE | 4.2 | I | 8 | T21 |
| 2870 | ALUMINIUM BOROHYDRIDE | 4.2 | I | 4.3 | T21 |
| 2441 | TITANIUM TRICHLORIDE, PYROPHORIC or TITANIUM TRICHLORIDE MIXTURE, PYROPHORIC | 4.2 | I | 8 | T21 |
| 2005 | MAGNESIUM DIPHENYL | 4.2 | I |  | T21 |
| 3342 | XANTHATES | 4.2 | II |  | T3 |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | II |  | T3 |
| 1369 | p-NITROSODIMETHYLANILINE | 4.2 | II |  | T3 |
| 1385 | SODIUM SULPHIDE, ANHYDROUS or SODIUM SULPHIDE with less than 30% water of crystallization | 4.2 | II |  | T3 |
| 2940 | 9-PHOSPHABICYCLONONANES (CYCLOOCTADIENE PHOSPHINES) | 4.2 | II |  | T3 |
| 2318 | SODIUM HYDROSULPHIDE with less than 25% water of crystallization | 4.2 | II |  | T3 |
| 2881 | METAL CATALYST, DRY | 4.2 | II |  | T3 |
| 1923 | CALCIUM DITHIONITE (CALCIUM HYDROSULPHITE) | 4.2 | II |  | T3 |
| 1374 | FISH MEAL (FISH SCRAP), UNSTABILIZED | 4.2 | II |  | T3 |
| 1431 | SODIUM METHYLATE | 4.2 | II | 8 | T3 |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | II | 8 | T3 |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | II | 8 | T3 |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | II | 6.1 | T3 |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | II | 6.1 | T3 |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | II | 5.1 | T3 |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | II | 8 | T3 |
| 1929 | POTASSIUM DITHIONITE (POTASSIUM HYDROSULPHITE) | 4.2 | II |  | T3 |
| 2546 | TITANIUM POWDER, DRY | 4.2 | II |  | T3 |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | II |  | T3 |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | II |  | T3 |
| 1384 | SODIUM DITHIONITE (SODIUM HYDROSULPHITE) | 4.2 | II |  | T3 |
| 3341 | THIOUREA DIOXIDE | 4.2 | II |  | T3 |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | II |  | T3 |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | II |  | T3 |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | II |  | T3 |
| 1382 | POTASSIUM SULPHIDE, ANHYDROUS or POTASSIUM SULPHIDE with less than 30% water of crystallization | 4.2 | II |  | T3 |
| 2004 | MAGNESIUM DIAMIDE | 4.2 | II |  | T3 |
| 1361 | CARBON, animal or vegetable origin | 4.2 | II |  | T3 |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | II |  | T3 |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | III |  | T1 |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | III | 8 | T3 |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | III | 8 | T3 |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | III | 8 | T3 |
| 1376 | IRON OXIDE, SPENT or IRON SPONGE, SPENT obtained from coal gas purification | 4.2 | III |  | T1 |
| 3341 | THIOUREA DIOXIDE | 4.2 | III |  | T1 |
| 1932 | ZIRCONIUM SCRAP | 4.2 | III |  | T1 |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGETABLE or SYNTHETIC, N.O.S. with oil | 4.2 | III |  | T1 |
| 1361 | CARBON, animal or vegetable origin | 4.2 | III |  | T1 |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | III |  | T1 |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | III |  | T1 |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | III |  | T1 |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | III | 5.1 | T1 |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | III |  | T1 |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | III | 6.1 | T1 |
| 3174 | TITANIUM DISULPHIDE | 4.2 | III |  | T1 |
| 2210 | MANEB or MANEB PREPARATION with not less than 60% maneb | 4.2 | III | 4.3 | T1 |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | III |  | T1 |
| 2546 | TITANIUM POWDER, DRY | 4.2 | III |  | T1 |
| 3342 | XANTHATES | 4.2 | III |  | T1 |
| 1363 | COPRA | 4.2 | III |  | T1 |
| 1362 | CARBON, ACTIVATED | 4.2 | III |  | T1 |
| 2881 | METAL CATALYST, DRY | 4.2 | III |  | T1 |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | III |  | T1 |
| 2009 | ZIRCONIUM, DRY, finished sheets, strip or coiled wire | 4.2 | III |  | T1 |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | III | 6.1 | T1 |
| 1360 | CALCIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 1402 | CALCIUM CARBIDE | 4.3 | I |  | T9 |
| 1404 | CALCIUM HYDRIDE | 4.3 | I |  | T9 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | I | 8 | T6 |
| 1419 | MAGNESIUM ALUMINIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | I | 6.1 | T6 |
| 2013 | STRONTIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 1714 | ZINC PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 2012 | POTASSIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 2011 | MAGNESIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 1397 | ALUMINIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 1433 | STANNIC PHOSPHIDES | 4.3 | I | 6.1 | T6 |
| 2010 | MAGNESIUM HYDRIDE | 4.3 | I |  | T9 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | I | 4.2 | T6 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | I | 4.2 | T6 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | I | 4.2 | T6 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | I | 4.2 | T6 |
| 1870 | POTASSIUM BOROHYDRIDE | 4.3 | I |  | T9 |
| 1432 | SODIUM PHOSPHIDE | 4.3 | I | 6.1 | T6 |
| 1423 | RUBIDIUM | 4.3 | I |  | T9 |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | I | 4.1 | T9 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | I | 4.1 | T9 |
| 1389 | ALKALI METAL AMALGAM | 4.3 | I |  | T9 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | I |  | T9 |
| 1414 | LITHIUM HYDRIDE | 4.3 | I |  | T9 |
| 1427 | SODIUM HYDRIDE | 4.3 | I |  | T9 |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION | 4.3 | I |  | T9 |
| 1407 | CAESIUM | 4.3 | I |  | T9 |
| 2463 | ALUMINIUM HYDRIDE | 4.3 | I |  | T9 |
| 1410 | LITHIUM ALUMINIUM HYDRIDE | 4.3 | I |  | T9 |
| 1392 | ALKALINE EARTH METAL AMALGAM | 4.3 | I |  | T9 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | I |  | T9 |
| 2806 | LITHIUM NITRIDE | 4.3 | I |  | T9 |
| 1413 | LITHIUM BOROHYDRIDE | 4.3 | I |  | T9 |
| 1415 | LITHIUM | 4.3 | I |  | T9 |
| 1420 | POTASSIUM METAL ALLOYS | 4.3 | I |  | T9 |
| 1426 | SODIUM BOROHYDRIDE | 4.3 | I |  | T9 |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | I |  | T9 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | T3 |
| 1400 | BARIUM | 4.3 | II |  | T3 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | II | 8 | T3 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | II | 6.1 | T3 |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | II | 6.1 | T3 |
| 3133 | WATER-REACTIVE SOLID, OXIDIZING, N.O.S. | 4.3 | II | 5.1 | T3 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | II | 4.2 | T3 |
| 1401 | CALCIUM | 4.3 | II |  | T3 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | II |  | T3 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | T3 |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | T3 |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 | II |  | T3 |
| 1405 | CALCIUM SILICIDE | 4.3 | II |  | T3 |
| 2624 | MAGNESIUM SILICIDE | 4.3 | II |  | T3 |
| 2830 | LITHIUM FERROSILICON | 4.3 | II |  | T3 |
| 2835 | SODIUM ALUMINIUM HYDRIDE | 4.3 | II |  | T3 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | II |  | T3 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | II |  | T3 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | T3 |
| 3078 | CERIUM, turnings or gritty powder | 4.3 | II |  | T3 |
| 1394 | ALUMINIUM CARBIDE | 4.3 | II |  | T3 |
| 2805 | LITHIUM HYDRIDE, FUSED SOLID | 4.3 | II |  | T3 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | II |  | T3 |
| 1390 | ALKALI METAL AMIDES | 4.3 | II |  | T3 |
| 1402 | CALCIUM CARBIDE | 4.3 | II |  | T3 |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | II |  | T3 |
| 1417 | LITHIUM SILICON | 4.3 | II |  | T3 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | II | 4.2 | T3 |
| 1340 | PHOSPHORUS PENTASULPHIDE, free from yellow and white phosphorus | 4.3 | II | 4.1 | T3 |
| 1405 | CALCIUM SILICIDE | 4.3 | III |  | T1 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | III |  | T1 |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 | III |  | T1 |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 | III |  | T1 |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 | III |  | T1 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | III |  | T1 |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | T1 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | III |  | T1 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | III | 4.2 | T1 |
| 1435 | ZINC ASHES | 4.3 | III |  | T1 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | III | 8 | T1 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | III |  | T1 |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 | III |  | T1 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | T1 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | T1 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | T1 |
| 3133 | WATER-REACTIVE SOLID, OXIDIZING, N.O.S. | 4.3 | III | 5.1 | T1 |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | III | 6.1 | T1 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | III | 6.1 | T1 |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 | III |  | T1 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | III | 4.2 | T1 |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | I | 8 | T6 |
| 3100 | OXIDIZING SOLID, SELF-HEATING, N.O.S. | 5.1 | I | 4.2 | T6 |
| 3137 | OXIDIZING SOLID, FLAMMABLE, N.O.S. | 5.1 | I | 4.1 | T6 |
| 2466 | POTASSIUM SUPEROXIDE | 5.1 | I |  | T6 |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 | I |  | T6 |
| 2547 | SODIUM SUPEROXIDE | 5.1 | I |  | T6 |
| 2072 | AMMONIUM NITRATE FERTILIZER, N.O.S. | 5.1 | I |  | T6 |
| 1491 | POTASSIUM PEROXIDE | 5.1 | I |  | T6 |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | I | 6.1 | T6 |
| 1504 | SODIUM PEROXIDE | 5.1 | I |  | T6 |
| 3121 | OXIDIZING SOLID, WATER-REACTIVE, N.O.S. | 5.1 | I | 4.3 | T6 |
| 1475 | MAGNESIUM PERCHLORATE | 5.1 | II |  | T3 |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | II |  | T3 |
| 1496 | SODIUM CHLORITE | 5.1 | II |  | T3 |
| 1495 | SODIUM CHLORATE | 5.1 | II |  | T3 |
| 1494 | SODIUM BROMATE | 5.1 | II |  | T3 |
| 1473 | MAGNESIUM BROMATE | 5.1 | II |  | T3 |
| 1472 | LITHIUM PEROXIDE | 5.1 | II |  | T3 |
| 1471 | LITHIUM HYPOCHLORITE, DRY or LITHIUM HYPOCHLORITE MIXTURE | 5.1 | II |  | T3 |
| 2468 | TRICHLOROISOCYANURIC ACID, DRY | 5.1 | II |  | T3 |
| 2465 | DICHLOROISOCYANURIC ACID, DRY or DICHLOROISOCYANURIC ACID SALTS | 5.1 | II |  | T3 |
| 1439 | AMMONIUM DICHROMATE | 5.1 | II |  | T3 |
| 1462 | CHLORITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1463 | CHROMIUM TRIOXIDE, ANHYDROUS | 5.1 | II | 8 | T3 |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1509 | STRONTIUM PEROXIDE | 5.1 | II |  | T3 |
| 1450 | BROMATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1457 | CALCIUM PEROXIDE | 5.1 | II |  | T3 |
| 1484 | POTASSIUM BROMATE | 5.1 | II |  | T3 |
| 1485 | POTASSIUM CHLORATE | 5.1 | II |  | T3 |
| 3212 | HYPOCHLORITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 3247 | SODIUM PEROXOBORATE, ANHYDROUS | 5.1 | II |  | T3 |
| 1490 | POTASSIUM PERMANGANATE | 5.1 | II |  | T3 |
| 1489 | POTASSIUM PERCHLORATE | 5.1 | II |  | T3 |
| 1488 | POTASSIUM NITRITE | 5.1 | II |  | T3 |
| 1493 | SILVER NITRATE | 5.1 | II |  | T3 |
| 1512 | ZINC AMMONIUM NITRITE | 5.1 | II |  | T3 |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | II | 8 | T3 |
| 1449 | BARIUM PEROXIDE | 5.1 | II | 6.1 | T3 |
| 1469 | LEAD NITRATE | 5.1 | II | 6.1 | T3 |
| 2573 | THALLIUM CHLORATE | 5.1 | II | 6.1 | T3 |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | II | 6.1 | T3 |
| 2741 | BARIUM HYPOCHLORITE with more than 22% available chlorine | 5.1 | II | 6.1 | T3 |
| 2719 | BARIUM BROMATE | 5.1 | II | 6.1 | T3 |
| 1446 | BARIUM NITRATE | 5.1 | II | 6.1 | T3 |
| 1448 | BARIUM PERMANGANATE | 5.1 | II | 6.1 | T3 |
| 2464 | BERYLLIUM NITRATE | 5.1 | II | 6.1 | T3 |
| 1515 | ZINC PERMANGANATE | 5.1 | II |  | T3 |
| 3100 | OXIDIZING SOLID, SELF-HEATING, N.O.S. | 5.1 | II | 4.2 | T3 |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1502 | SODIUM PERCHLORATE | 5.1 | II |  | T3 |
| 1503 | SODIUM PERMANGANATE | 5.1 | II |  | T3 |
| 2721 | COPPER CHLORATE | 5.1 | II |  | T3 |
| 2723 | MAGNESIUM CHLORATE | 5.1 | II |  | T3 |
| 1514 | ZINC NITRATE | 5.1 | II |  | T3 |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED, or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% but not more than 10% water | 5.1 | II |  | T3 |
| 1516 | ZINC PEROXIDE | 5.1 | II |  | T3 |
| 1513 | ZINC CHLORATE | 5.1 | II |  | T3 |
| 1506 | STRONTIUM CHLORATE | 5.1 | II |  | T3 |
| 1508 | STRONTIUM PERCHLORATE | 5.1 | II |  | T3 |
| 1453 | CALCIUM CHLORITE | 5.1 | II |  | T3 |
| 3121 | OXIDIZING SOLID, WATER-REACTIVE, N.O.S. | 5.1 | II | 4.3 | T3 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1487 | POTASSIUM NITRATE AND SODIUM NITRITE MIXTURE | 5.1 | II |  | T3 |
| 1452 | CALCIUM CHLORATE | 5.1 | II |  | T3 |
| 1476 | MAGNESIUM PEROXIDE | 5.1 | II |  | T3 |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | II |  | T3 |
| 1456 | CALCIUM PERMANGANATE | 5.1 | II |  | T3 |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 | II |  | T3 |
| 2626 | CHLORIC ACID, AQUEOUS SOLUTION with not more than 10% chloric acid | 5.1 | II |  | T3 |
| 2627 | NITRITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 |
| 2072 | AMMONIUM NITRATE FERTILIZER, N.O.S. | 5.1 | II |  | T3 |
| 1455 | CALCIUM PERCHLORATE | 5.1 | II |  | T3 |
| 1442 | AMMONIUM PERCHLORATE | 5.1 | II |  | T3 |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | III |  | T1 |
| 1466 | FERRIC NITRATE | 5.1 | III |  | T1 |
| 1492 | POTASSIUM PERSULPHATE | 5.1 | III |  | T1 |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | III |  | T1 |
| 2208 | CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 10% but not more than 39% available chlorine | 5.1 | III |  | T1 |
| 1444 | AMMONIUM PERSULPHATE | 5.1 | III |  | T1 |
| 2072 | AMMONIUM NITRATE FERTILIZER, N.O.S. | 5.1 | III |  | T1 |
| 1465 | DIDYMIUM NITRATE | 5.1 | III |  | T1 |
| 1438 | ALUMINIUM NITRATE | 5.1 | III |  | T1 |
| 2070 | AMMONIUM NITRATE FERTILIZERS: uniform non-segregating mixtures of nitrogen/phosphate or nitrogen/ potash types or complete fertilizers of nitrogen/phosphate/ potash type, with more than 70% but less than 90% ammonium nitrate and not more than 0.4% total c | 5.1 | III |  | T1 |
| 1505 | SODIUM PERSULPHATE | 5.1 | III |  | T1 |
| 2069 | AMMONIUM NITRATE FERTILIZERS: uniform non-segregating mixtures of ammonium nitrate/ammonium sulphate, with more than 45% but not more than 70% ammonium nitrate and not more than 0.4% total combustible material | 5.1 | III |  | T1 |
| 2068 | AMMONIUM NITRATE FERTILIZERS: uniform non-segregating mixtures of ammonium nitrate with calcium carbonate and/or dolomite, with more than 80% but less than 90% ammonium nitrate and not more than 0.4% total combustible material | 5.1 | III |  | T1 |
| 2469 | ZINC BROMATE | 5.1 | III |  | T1 |
| 2726 | NICKEL NITRITE | 5.1 | III |  | T1 |
| 1451 | CAESIUM NITRATE | 5.1 | III |  | T1 |
| 1474 | MAGNESIUM NITRATE | 5.1 | III |  | T1 |
| 1499 | SODIUM NITRATE AND POTASSIUM NITRATE MIXTURE | 5.1 | III |  | T1 |
| 2067 | AMMONIUM NITRATE FERTILIZERS: uniform non-segregating mixtures of ammonium nitrate with added matter which is inorganic and chemically inert towards ammonium nitrate, with not less than 90% ammonium nitrate and not more than 0.2% combustible material (inc | 5.1 | III |  | T1 |
| 2720 | CHROMIUM NITRATE | 5.1 | III |  | T1 |
| 1507 | STRONTIUM NITRATE | 5.1 | III |  | T1 |
| 1511 | UREA HYDROGEN PEROXIDE | 5.1 | III | 8 | T1 |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | III | 8 | T1 |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | III | 6.1 | T1 |
| 1500 | SODIUM NITRITE | 5.1 | III | 6.1 | T1 |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S | 5.1 | III |  | T1 |
| 1942 | AMMONIUM NITRATE with not more than 0.2% combustible substances, including any organic substance calculated as carbon, to the exclusion of any other added substance | 5.1 | III |  | T1 |
| 2722 | LITHIUM NITRATE | 5.1 | III |  | T1 |
| 1486 | POTASSIUM NITRATE | 5.1 | III |  | T1 |
| 2724 | MANGANESE NITRATE | 5.1 | III |  | T1 |
| 2725 | NICKEL NITRATE | 5.1 | III |  | T1 |
| 1498 | SODIUM NITRATE | 5.1 | III |  | T1 |
| 1872 | LEAD DIOXIDE | 5.1 | III |  | T1 |
| 2728 | ZIRCONIUM NITRATE | 5.1 | III |  | T1 |
| 1479 | OXIDIZING SOLID, N.O.S. | 5.1 | III |  | T1 |
| 1454 | CALCIUM NITRATE | 5.1 | III |  | T1 |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 |
| 1467 | GUANIDINE NITRATE | 5.1 | III |  | T1 |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | I |  | T6 |
| 1575 | CALCIUM CYANIDE | 6.1 | I |  | T6 |
| 2642 | FLUOROACETIC ACID | 6.1 | I |  | T6 |
| 2630 | SELENATES or SELENITES | 6.1 | I |  | T6 |
| 2629 | SODIUM FLUOROACETATE | 6.1 | I |  | T6 |
| 2628 | POTASSIUM FLUOROACETATE | 6.1 | I |  | T6 |
| 1698 | DIPHENYLAMINE CHLOROARSINE | 6.1 | I |  | T6 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 |
| 1570 | BRUCINE | 6.1 | I |  | T6 |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 1614 | HYDROGEN CYANIDE, STABILIZED, containing less than 3% water and absorbed in a porous inert material | 6.1 | I |  | T6 |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 1565 | BARIUM CYANIDE | 6.1 | I |  | T6 |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 2249 | DICHLORODIMETHYL ETHER, SYMMETRICAL | 6.1 | I |  | T6 |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 3048 | ALUMINIUM PHOSPHIDE PESTICIDE | 6.1 | I |  | T6 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | I |  | T6 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | I |  | T6 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | I |  | T6 |
| 1889 | CYANOGEN BROMIDE | 6.1 | I | 8 | T6 |
| 1699 | DIPHENYLCHLOROARSINE, SOLID | 6.1 | I |  | T6 |
| 2570 | CADMIUM COMPOUND | 6.1 | I |  | T6 |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | I | 8 | T6 |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | I | 8 | T6 |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | I | 5.1 | T6 |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | I | 4.3 | T6 |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | I | 4.1 | T6 |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 1692 | STRYCHNINE or STRYCHNINE SALTS | 6.1 | I |  | T6 |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | I | 4.2 | T6 |
| 2471 | OSMIUM TETROXIDE | 6.1 | I |  | T6 |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 1713 | ZINC CYANIDE | 6.1 | I |  | T6 |
| 1626 | MERCURIC POTASSIUM CYANIDE | 6.1 | I |  | T6 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | I |  | T6 |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 2316 | SODIUM CUPROCYANIDE, SOLID | 6.1 | I |  | T6 |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | I |  | T6 |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2567 | SODIUM PENTACHLOROPHENATE | 6.1 | II |  | T3 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | II |  | T3 |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 1678 | POTASSIUM ARSENITE | 6.1 | II |  | T3 |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2671 | AMINOPYRIDINES (o-, m-, p,) | 6.1 | II |  | T3 |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2657 | SELENIUM DISULPHIDE | 6.1 | II |  | T3 |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 1636 | MERCURY CYANIDE | 6.1 | II |  | T3 |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 2863 | SODIUM AMMONIUM VANADATE | 6.1 | II |  | T3 |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | II | 5.1 | T3 |
| 2859 | AMMONIUM METAVANADATE | 6.1 | II |  | T3 |
| 1651 | NAPHTHYLTHIOUREA | 6.1 | II |  | T3 |
| 2673 | 2-AMINO-4-CHLOROPHENOL | 6.1 | II |  | T3 |
| 2931 | VANADYL SULPHATE | 6.1 | II |  | T3 |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 2587 | BENZOQUINONE | 6.1 | II |  | T3 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 |
| 2645 | PHENACYL BROMIDE | 6.1 | II |  | T3 |
| 2647 | MALONONITRILE | 6.1 | II |  | T3 |
| 2861 | AMMONIUM POLYVANADATE | 6.1 | II |  | T3 |
| 2649 | 1,3-DICHLOROACETONE | 6.1 | II |  | T3 |
| 2570 | CADMIUM COMPOUND | 6.1 | II |  | T3 |
| 1617 | LEAD ARSENATES | 6.1 | II |  | T3 |
| 1684 | SILVER CYANIDE | 6.1 | II |  | T3 |
| 2027 | SODIUM ARSENITE, SOLID | 6.1 | II |  | T3 |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 |
| 1679 | POTASSIUM CUPROCYANIDE | 6.1 | II |  | T3 |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | II | 4.2 | T3 |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S | 6.1 | II | 4.1 | T3 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | II | 4.3 | T3 |
| 1895 | PHENYLMERCURIC NITRATE | 6.1 | II |  | T3 |
| 2727 | THALLIUM NITRATE | 6.1 | II | 5.1 | T3 |
| 1751 | CHLOROACETIC ACID, SOLID | 6.1 | II | 8 | T3 |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | II | 8 | T3 |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | II | 8 | T3 |
| 1567 | BERYLLIUM POWDER | 6.1 | II | 4.1 | T3 |
| 1885 | BENZIDINE | 6.1 | II |  | T3 |
| 1704 | TETRAETHYL DITHIOPYROPHOSPHATE | 6.1 | II |  | T3 |
| 1691 | STRONTIUM ARSENITE | 6.1 | II |  | T3 |
| 1707 | THALLIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 |
| 1712 | ZINC ARSENATE, ZINC ARSENITE or ZINC ARSENATE AND ZINC ARSENITE MIXTURE | 6.1 | II |  | T3 |
| 2864 | POTASSIUM METAVANADATE | 6.1 | II |  | T3 |
| 1688 | SODIUM CACODYLATE | 6.1 | II |  | T3 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | II |  | T3 |
| 1685 | SODIUM ARSENATE | 6.1 | II |  | T3 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | II |  | T3 |
| 1894 | PHENYLMERCURIC HYDROXIDE | 6.1 | II |  | T3 |
| 1639 | MERCURY NUCLEATE | 6.1 | II |  | T3 |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 1683 | SILVER ARSENITE | 6.1 | II |  | T3 |
| 3155 | PENTACHLOROPHENOL | 6.1 | II |  | T3 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 1687 | SODIUM AZIDE | 6.1 | II |  | T3 |
| 1665 | NITROXYLENES, SOLID | 6.1 | II |  | T3 |
| 1586 | COPPER ARSENITE | 6.1 | II |  | T3 |
| 1587 | COPPER CYANIDE | 6.1 | II |  | T3 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 1590 | DICHLOROANILINES, SOLID | 6.1 | II |  | T3 |
| 1597 | DINITROBENZENES, SOLID | 6.1 | II |  | T3 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 |
| 1606 | FERRIC ARSENATE | 6.1 | II |  | T3 |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 |
| 1653 | NICKEL CYANIDE | 6.1 | II |  | T3 |
| 1674 | PHENYLMERCURIC ACETATE | 6.1 | II |  | T3 |
| 1658 | NICOTINE SULPHATE, SOLID | 6.1 | II |  | T3 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 1585 | COPPER ACETOARSENITE | 6.1 | II |  | T3 |
| 1656 | NICOTINE HYDROCHLORIDE, solid | 6.1 | II |  | T3 |
| 1657 | NICOTINE SALICYLATE | 6.1 | II |  | T3 |
| 1652 | NAPHTHYLUREA | 6.1 | II |  | T3 |
| 1638 | MERCURY IODIDE | 6.1 | II |  | T3 |
| 1637 | MERCURY GLUCONATE | 6.1 | II |  | T3 |
| 1607 | FERRIC ARSENITE | 6.1 | II |  | T3 |
| 1634 | MERCURY BROMIDES | 6.1 | II |  | T3 |
| 1608 | FERROUS ARSENATE | 6.1 | II |  | T3 |
| 1630 | MERCURY AMMONIUM CHLORIDE | 6.1 | II |  | T3 |
| 1629 | MERCURY ACETATE | 6.1 | II |  | T3 |
| 1627 | MERCUROUS NITRATE | 6.1 | II |  | T3 |
| 1625 | MERCURIC NITRATE | 6.1 | II |  | T3 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 |
| 1620 | LEAD CYANIDE | 6.1 | II |  | T3 |
| 1664 | NITROTOLUENES, SOLID | 6.1 | II |  | T3 |
| 1642 | MERCURY OXYCYANIDE, DESENSITIZED | 6.1 | II |  | T3 |
| 1572 | CACODYLIC ACID | 6.1 | II |  | T3 |
| 1631 | MERCURY BENZOATE | 6.1 | II |  | T3 |
| 1646 | MERCURY THIOCYANATE | 6.1 | II |  | T3 |
| 1645 | MERCURY SULPHATE | 6.1 | II |  | T3 |
| 1644 | MERCURY SALICYLATE | 6.1 | II |  | T3 |
| 1677 | POTASSIUM ARSENATE | 6.1 | II |  | T3 |
| 1643 | MERCURY POTASSIUM IODIDE | 6.1 | II |  | T3 |
| 1624 | MERCURIC CHLORIDE | 6.1 | II |  | T3 |
| 1641 | MERCURY OXIDE | 6.1 | II |  | T3 |
| 1574 | CALCIUM ARSENATE AND CALCIUM ARSENITE MIXTURE, SOLID | 6.1 | II |  | T3 |
| 1623 | MERCURIC ARSENATE | 6.1 | II |  | T3 |
| 1659 | NICOTINE TARTRATE | 6.1 | II |  | T3 |
| 1622 | MAGNESIUM ARSENATE | 6.1 | II |  | T3 |
| 1621 | LONDON PURPLE | 6.1 | II |  | T3 |
| 1640 | MERCURY OLEATE | 6.1 | II |  | T3 |
| 1611 | HEXAETHYL TETRAPHOSPHATE | 6.1 | II |  | T3 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | II |  | T3 |
| 1573 | CALCIUM ARSENATE | 6.1 | II |  | T3 |
| 1618 | LEAD ARSENITES | 6.1 | II |  | T3 |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 |
| 1562 | ARSENICAL DUST | 6.1 | II |  | T3 |
| 1561 | ARSENIC TRIOXIDE | 6.1 | II |  | T3 |
| 1559 | ARSENIC PENTOXIDE | 6.1 | II |  | T3 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | II |  | T3 |
| 1555 | ARSENIC BROMIDE | 6.1 | II |  | T3 |
| 1554 | ARSENIC ACID, SOLID | 6.1 | II |  | T3 |
| 1558 | ARSENIC | 6.1 | II |  | T3 |
| 1546 | AMMONIUM ARSENATE | 6.1 | II |  | T3 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 |
| 2862 | VANADIUM PENTOXIDE, non-fused form | 6.1 | III |  | T1 |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 |
| 2871 | ANTIMONY POWDER | 6.1 | III |  | T1 |
| 2875 | HEXACHLOROPHENE | 6.1 | III |  | T1 |
| 2876 | RESORCINOL | 6.1 | III |  | T1 |
| 2853 | MAGNESIUM FLUOROSILICATE | 6.1 | III |  | T1 |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | III |  | T1 |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 | III |  | T1 |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 | III |  | T1 |
| 2855 | ZINC FLUOROSILICATE | 6.1 | III |  | T1 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | III |  | T1 |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 1550 | ANTIMONY LACTATE | 6.1 | III |  | T1 |
| 2854 | AMMONIUM FLUOROSILICATE | 6.1 | III |  | T1 |
| 1548 | ANILINE HYDROCHLORIDE | 6.1 | III |  | T1 |
| 1551 | ANTIMONY POTASSIUM TARTRATE | 6.1 | III |  | T1 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 2570 | CADMIUM COMPOUND | 6.1 | III |  | T1 |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2716 | 1,4-BUTYNEDIOL | 6.1 | III |  | T1 |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2516 | CARBON TETRABROMIDE | 6.1 | III |  | T1 |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE | 6.1 | III |  | T1 |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2713 | ACRIDINE | 6.1 | III |  | T1 |
| 2674 | SODIUM FLUOROSILICATE | 6.1 | III |  | T1 |
| 2660 | NITROTOLUIDINES (MONO) | 6.1 | III |  | T1 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 2659 | SODIUM CHLOROACETATE | 6.1 | III |  | T1 |
| 2655 | POTASSIUM FLUOROSILICATE | 6.1 | III |  | T1 |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 2233 | CHLOROANISIDINES | 6.1 | III |  | T1 |
| 2512 | AMINOPHENOLS (o-, m-, p-) | 6.1 | III |  | T1 |
| 2505 | AMMONIUM FLUORIDE | 6.1 | III |  | T1 |
| 2473 | SODIUM ARSANILATE | 6.1 | III |  | T1 |
| 2446 | NITROCRESOLS | 6.1 | III |  | T1 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 |
| 2237 | CHLORONITROANILINES | 6.1 | III |  | T1 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | III |  | T1 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | III |  | T1 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 2020 | CHLOROPHENOLS, SOLID | 6.1 | III |  | T1 |
| 1884 | BARIUM OXIDE | 6.1 | III |  | T1 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | III |  | T1 |
| 2433 | CHLORONITROTOLUENES, SOLID | 6.1 | III |  | T1 |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 |
| 1616 | LEAD ACETATE | 6.1 | III |  | T1 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | I |  | T6 |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | I |  | T6 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | I |  | T6 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | I |  | T6 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | I |  | T6 |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | I | 5.1 | T6 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | I |  | T6 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | I | 6.1 | T6 |
| 1905 | SELENIC ACID | 8 | I |  | T6 |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | I | 4.3 | T6 |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | I | 4.1 | T6 |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | I | 4.2 | T6 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | I |  | T6 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | II |  | T3 |
| 2680 | LITHIUM HYDROXIDE MONOHYDRATE | 8 | II |  | T3 |
| 2682 | CAESIUM HYDROXIDE | 8 | II |  | T3 |
| 2691 | PHOSPHORUS PENTABROMIDE | 8 | II |  | T3 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | II |  | T3 |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | II |  | T3 |
| 2583 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with more than 5% free sulphuric acid | 8 | II |  | T3 |
| 2678 | RUBIDIUM HYDROXIDE | 8 | II |  | T3 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | II |  | T3 |
| 1756 | CHROMIC FLUORIDE, SOLID | 8 | II |  | T3 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | II |  | T3 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | II |  | T3 |
| 1839 | TRICHLOROACETIC ACID | 8 | II |  | T3 |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | II |  | T3 |
| 2033 | POTASSIUM MONOXIDE | 8 | II |  | T3 |
| 1794 | LEAD SULPHATE with more than 3% free acid | 8 | II |  | T3 |
| 1847 | POTASSIUM SULPHIDE, HYDRATED with not less than 30% water of crystallization | 8 | II |  | T3 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | II |  | T3 |
| 1770 | DIPHENYLMETHYL BROMIDE | 8 | II |  | T3 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | II | 6.1 | T3 |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | II | 5.1 | T3 |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | II | 4.3 | T3 |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | II | 4.2 | T3 |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | II | 4.1 | T3 |
| 1806 | PHOSPHORUS PENTACHLORIDE | 8 | II |  | T3 |
| 1725 | ALUMINIUM BROMIDE, ANHYDROUS | 8 | II |  | T3 |
| 2670 | CYANURIC CHLORIDE | 8 | II |  | T3 |
| 2506 | AMMONIUM HYDROGEN SULPHATE | 8 | II |  | T3 |
| 1825 | SODIUM MONOXIDE | 8 | II |  | T3 |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | II |  | T3 |
| 2509 | POTASSIUM HYDROGEN SULPHATE | 8 | II |  | T3 |
| 1813 | POTASSIUM HYDROXIDE, SOLID | 8 | II |  | T3 |
| 1823 | SODIUM HYDROXIDE, SOLID | 8 | II |  | T3 |
| 1727 | AMMONIUM HYDROGENDIFLUORIDE, SOLID | 8 | II |  | T3 |
| 1726 | ALUMINIUM CHLORIDE, ANHYDROUS | 8 | II |  | T3 |
| 1807 | PHOSPHORUS PENTOXIDE | 8 | II |  | T3 |
| 2508 | MOLYBDENUM PENTACHLORIDE | 8 | III |  | T1 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | III |  | T1 |
| 1805 | PHOSPHORIC ACID, SOLID | 8 | III |  | T1 |
| 3253 | DISODIUM TRIOXOSILICATE | 8 | III |  | T1 |
| 1773 | FERRIC CHLORIDE, ANHYDROUS | 8 | III |  | T1 |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | III |  | T1 |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | III |  | T1 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | III |  | T1 |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | III |  | T1 |
| 1907 | SODA LIME with more than 4% sodium hydroxide | 8 | III |  | T1 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | III |  | T1 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | III | 6.1 | T1 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | III |  | T1 |
| 2578 | PHOSPHORUS TRIOXIDE | 8 | III |  | T1 |
| 2905 | CHLOROPHENOLATES, SOLID or PHENOLATES, SOLID | 8 | III |  | T1 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | III |  | T1 |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 | III |  | T1 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | III |  | T1 |
| 2865 | HYDROXYLAMINE SULPHATE | 8 | III |  | T1 |
| 2802 | COPPER CHLORIDE | 8 | III |  | T1 |
| 2507 | CHLOROPLATINIC ACID, SOLID | 8 | III |  | T1 |
| 2503 | ZIRCONIUM TETRACHLORIDE | 8 | III |  | T1 |
| 2475 | VANADIUM TRICHLORIDE | 8 | III |  | T1 |
| 2331 | ZINC CHLORIDE, ANHYDROUS | 8 | III |  | T1 |
| 1910 | CALCIUM OXIDE | 8 | III |  | T1 |
| 2698 | TETRAHYDROPHTHALIC ANHYDRIDES with more than 0.05% of maleic anhydride | 8 | III |  | T1 |
| 2967 | SULPHAMIC ACID | 8 | III |  | T1 |
| 2812 | SODIUM ALUMINATE, SOLID | 8 | III |  | T1 |
| 2809 | MERCURY | 8 | III |  | T1 |
| 2803 | GALLIUM | 8 | III |  | T1 |
| 2440 | STANNIC CHLORIDE PENTAHYDRATE | 8 | III |  | T1 |
| 3335 | AVIATION REGULATED SOLID, N.O.S. | 9 |  |  | T1 |
| 2969 | CASTOR BEANS or CASTOR MEAL or CASTOR POMACE or CASTOR FLAKE | 9 | II |  | T3 |
| 2212 | BLUE ASBESTOS (crocidolite) or BROWN ASBESTOS (amosite, mysorite) | 9 | II |  | T3 |
| 3152 | POLYHALOGENATED BIPHENYLS, SOLID or POLYHALOGENATED TERPHENYLS, SOLID | 9 | II |  | T3 |
| 3258 | ELEVATED TEMPERATURE SOLID, N.O.S., at or above 240 °C | 9 | III |  | T1 |
| 2590 | WHITE ASBESTOS (chrysotile, actinolite, anthophyllite, tremolite) | 9 | III |  | T1 |
| 2216 | FISH MEAL (FISH SCRAP), STABILIZED | 9 | III |  | T1 |
| 2071 | AMMONIUM NITRATE FERTILIZERS: uniform non-segregating mixtures of nitrogen/phosphate or nitrogen/ potash types or complete fertilizers of nitrogen/phosphate/ potash type, with not more 70% ammonium nitrate and not more than 0.4% total added combustible material | 9 | III |  | T1 |
| 1931 | ZINC DITHIONITE (ZINC HYDROSULPHITE) | 9 | III |  | T1 |
| 1841 | ACETALDEHYDE AMMONIA | 9 | III |  | T1 |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S. | 9 | III |  | T1 |

Annex 3

Proposed T-Codes for Solids Currently Assigned T-Codes in the Dangerous Goods List

| UN# | Name | Class | PG | Sub-Risk | EXISTING | PROPOSED |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | TI | TP | TI |
| 1422 | POTASSIUM SODIUM ALLOYS | 4.3 | I |  | T9 | TP3 TP7 | T6 |
| 1428 | SODIUM | 4.3 | I |  | T9 | TP3 TP7 | T6 |
| 2257 | POTASSIUM | 4.3 | I |  | T9 | TP3 TP7 | T6 |
| 1445 | BARIUM CHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 |
| 1447 | BARIUM PERCHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 |
| 1470 | LEAD PERCHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 |
| 1811 | POTASSIUM HYDROGENDIFLUORIDE | 8 | II | 6.1 | T7 | TP2 | T3 |
| 2076 | CRESOLS, SOLID | 6.1 | II | 8 | T7 | TP2 | T3 |
| 3203 | PYROPHORIC ORGANOMETALLIC COMPOUND, WATER-REACTIVE, N.O.S., solid | 4.2 | I | 4.3 | T21 | TP2 TP7 TP9 | T21 |