INF.39 (E)

##### ECONOMIC COMMISSION FOR EUROPE

##### INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Geneva, 10-14 September 2001)

## Report of the working group on document TRANS/WP.15/AC.1/2001/23

## Harmonisation with the 12th revised edition of the UN Recommendations

This amendments apply only to the English version.

PART 4

Document TRANS/WP.15/AC.1/2001/23: Adopted with the following modifications:

4.1.1	Replace "4.1.8" and "4.1.9" with "4.1.8.2" and "4.1.9.1.5" respectively.

4.1.3.6	Amend the beginning of the paragraph to read: "All cylinders, bundles of cylinders, pressure drums and tubes conforming to packing instruction P200 and to the construction requirements of Chapter 6.2 are authorized…".

4.1.3.8.1	Add "of the country of origin 2" after "the competent authority" at the end of the first sentence and a footnote "2" to read as follows:

"2	If the country of origin is not a contracting party to ADR, the competent authority of the first country contracting party to ADR reached by the consignment."

Renumber subsequent footnotes accordingly.

4.1.3.8.1 (e)	Add "or to the transport unit" after "handling devices".

4.1.3.8.2	Replace at the end "carried with the large and robust articles" with "attached to the transport document".

In the Note, replace at the end "quantity thresholds" with "quantities according to 3.4.6".

4.1.4.1	P001: 	Under "Special packing provisions specific to RID and ADR", delete RR1. (This special 	packing provision is now new special provision PP81).

P402(1): In the existing text of ADR, delete at the end: "Filling shall not be greater than 90% of the capacity of the cylinder".

P406: 		In the existing text of ADR, delete additional requirement 3.

P601:	In the existing text of ADR, delete "(see also the Table of 4.1.4.4)" at the end of the first sentence.

P650:	Amend as follows:

Add the following sentence after "DIAGNOSTIC SPECIMENS.":

"Packages containing substances carried in refrigerated liquid nitrogen shall, in addition, bear a label conforming to model No. 2.2."

(Note: This sentence is the existing text for SP634)

Add the following paragraph at the end of the existing text under "General provisions":

"If any substances have leaked and been spilled in a vehicle or container, it may not be reused until after it has been thoroughly cleaned and, if necessary, disinfected or decontaminated. Any other goods and articles carried in the same vehicle or container shall be examined for possible contamination.".

(Note: This paragraph is the existing text for CV13 in 7.5.11).

Consequential amendment in Table A of Chapter 3.2:

For UN 3373, delete: "634" in Column (6), "4" in Column (15) and "CV13" in Column (18).

P802:	Delete PP79.

P904(1): Add "packing instruction" before "P001 or P002".

P907:	Delete.

4.1.7.2.3	Delete.

4.1.7.2.4	Renumber this paragraph as 4.1.7.2.3.

----------------------------------