#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2002/14

3 April 2002

# ORIGINAL : ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-first session, 1-10 July 2002

# agenda item 6 (b))

PACKAGINGS

### Miscellaneous proposals

Substances in the Dangerous Goods List that are allocated P003

Proposed changes to LP02

Transmitted by the expert from the United Kingdom

Background

- Packing Instruction P003 was developed for a range of substances and articles where it is recognised that UN packaging is not required.  Although there are no package limitations by mass or volume because this is a ‘P’ number, the upper capacity limit of 400Kg/450 litres is considered to apply.

( This is the lower capacity limit for the definition of large packagings in 1.2.1.)

- There are occasions when a number of the substances allocated to this instruction need to be carried in quantities greater than 400Kg/450 litres particularly when they are waste e.g. aerosols, fire extinguishers etc.

- The expert from the United Kingdom believes that to solve this, LP02 should be added to all the UN numbers that attract P003 as shown in the Annex to this paper. On the attached Annex is a list of all those UN numbers that in the opinion of the expert from the United Kingdom should be subject to this provision. Those UN numbers on the Annex which are shown with an * refer to those entries in the Model Regulations that already attract LP02.

# Proposal

4.   	Add “LP02” to all the UN numbers that attract P003 shown in the Annex to this paper.

GE.02-

##### ANNEX

| 1044 | FIRE EXTINGUISHERS with compressed or liquefied gas | 2.2 |  |  | 225 | 120 ml | P003 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1057 | LIGHTERS or LIGHTER REFILLS containing flammable gas | 2.1 |  |  | 201 | NONE | P003 |  |
| 1327 | HAY, STRAW or BHUSA | 4.1 |  |  | 281 | 3 kg | P003 IBC08 | PP19 B6 |
| 1363* | COPRA | 4.2 |  | III | 29 | NONE | P003 IBC08 LP02 | PP20 B3, B6 |
| 1364* | COTTON WASTE, OILY | 4.2 |  | III |  | NONE | P003 IBC08 LP02 | PP19 B3, B6 |
| 1365* | COTTON, WET | 4.2 |  | III | 29 | NONE | P003 IBC08 LP02 | PP19 B3, B6 |
| 1386* | SEED CAKE with more than 1.5% oil and not more than 11% moisture | 4.2 |  | III | 29 | NONE | P003 IBC08 LP02 | PP20 B3, B6 |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | 6.1 | III | 39 223 | 1 kg | P003 IBC08 | PP20 B4 |
| 1845 | CARBON DIOXIDE, SOLID (DRY ICE) | 9 |  | III | 297 | NONE | P003 | PP18 |
| 1856 | RAGS, OILY | 4.2 |  |  | 29 117 | NONE | P003 IBC08 | PP19 B6 |
| 1950 | AEROSOLS | 2 |  |  | 63 190 277 | see SP277 | P003 | PP17 |
| 2037 | RECEPTACLES, SMALL, CONTAINING GAS (GAS CARTRIDGES) without a release device, non-refillable | 2 |  |  | 191 277 303 | see SP277 | P003 | PP17 |
| 2793* | FERROUS METAL BORINGS, SHAVINGS, TURNINGS or CUTTINGS in a form liable to self-heating | 4.2 |  | III | 223 | NONE | P003 IBC08 LP02 | PP20 B3, B6 |
| 2800 | BATTERIES, WET, NON-SPILLABLE, electric storage | 8 |  |  | 238 | 1 L | P003 | PP16 |
| 2857 | REFRIGERATING MACHINES containing non-flammable, non-toxic, liquefied gas or ammonia solutions (UN 2672) | 2.2 |  |  | 119 | NONE | P003 | PP32 |
| 3150 | DEVICES, SMALL, HYDROCARBON GAS POWERED or HYDROCARBON GAS REFILLS FOR SMALL DEVICES with release device | 2.1 |  |  |  | NONE | P003 |  |
| 3164 | ARTICLES, PRESSURIZED, PNEUMATIC or HYDRAULIC (containing non-flammable gas) | 2.2 |  |  | 283 | 120ml | P003 |  |
| 3358 | REFRIGERATING MACHINES containing flammable, non-toxic, liquefied gas | 2.1 |  |  | 291 | NONE | P003 | PP32 |
| 3360 | FIBRES, VEGETABLE, DRY | 4.1 |  |  | 291 172 99 | NONE | P003 | PP19 |

# Text boxes

STSTE

Secretariat

ST/SG/AC.10/C.3/2002/14

page 2