#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2002/33

12 April 2002

# ORIGINAL : ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

##### Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Twenty-first session, 1-10 July 2002

agenda item 4)

TRANSPORT OF SOLID SUBSTANCES IN BULK IN CONTAINERS

Transport of solids in portable tanks

Transmitted by the expert from the United States of America

1.	At the twentieth session of the Sub-Committee, the expert from the United States of America agreed to coordinate the development of requirements for the transport of solid dangerous goods in portable tanks and to lead a correspondence group to review proposed requirements and develop a proposal for submission to the twenty-first session.  Many solids are not currently authorized for transport in portable tanks in the Model Regulations.  Consignors that transport solid dangerous goods are required to acquire competent authority approvals to transport their solids in tanks which imposes unnecessary burdens and delays.  Adoption of this proposal will result in the assignment of tank codes for the majority of solids dangerous goods listed in the Dangerous Goods List that are suitable and safe for transport in portable tanks.  In developing the assignments, a rationalized approach was developed (see Annex 1) and other regulations that provide portable tank requirements for solids were considered (e.g.  IMDG Code, ADR/RID and 49 CFR).  Annex 2 of this paper provides proposed assignments that are based on the rationalized approach that is provided in Annex 1.  As there are a few solids that are currently assigned tank codes in the Model Regulations, it is proposed that these tank codes be changed in accordance with the rationalized approach for consistency where necessary.  Annex 3 is a list of currently assigned tank provisions that would need to be changed in the Model Regulations based on the rationalized approach.  There are a number of proposed portable tank assignments for solid substances that may require further consideration by the Sub-Committee based on comments that were provided by correspondence group members. To facilitate the review of these substances, Annex 4 is provided.  Annex 4 provides a list of substances and proposed tank assignments where one or more correspondence group members provided a comment relative to the tank assignment.

GE.02-

- Tank assignments were not considered appropriate for the following items:

- explosives and desensitized explosives;

- certain blasting explosives and ammonium nitrate (this will be handled by a separate proposal);

- Division 6.2 substances;

- UN 3255, tert-Butyl hypochlorite and UN 2907, Isosorbide dinitrate mixture, which should be forbidden from transport in portable tanks;

- articles; and

- substances where it was not considered practical to transport them in portable tanks, including but not limited to:

UN 3314, Plastics moulding compound

UN 2000, Celluloid

UN 1379, Paper, Unsaturated oil treated

UN 1386, Seed cake

UN 1365, Cotton, wet

UN 2793, Ferrous metal borings, shavings, turnings or cuttings

UN 2217, Seed cake

UN 1364, Cotton, waste oily

UN 2002, Celluloid, scrap

UN 2006, Plastics, nitrocellulose based, self-heating, n.o.s.

UN 2016, Ammunition toxic, non-explosive

3.  	This paper proposes the following new portable tank special provision (TP) for solids.  The Sub-committee is invited to consider this TP and take a decision on whether it is necessary for solids.

"TPXX  The portable tank shall not be loaded with solid substances that are at a temperature outside of the portable tank’s design temperature range or that would exceed the portable tank’s maximum permissible gross mass when loaded in the portable tank.  The substance should be so loaded that the weight is evenly distributed within the tank to prevent unsafe handling and transport conditions. If the substance is offered for transport under elevated temperature conditions, the degree of filling requirements prescribed in 4.2.1.9.5.1 and the requirements of 4.2.1.18 shall be met."

Additionally it is proposed that Division 4.3 PG I solids be assigned TP 7.

4. 	At its twentieth session the Sub-Committee indicated that portable tank requirements for molten substances and solids that are loaded molten and transported in the solid state should also be addressed. Provisions for these substances are proposed as follows:

Add a new paragraph 4.2.1.18 as follows:

"4.2.1.18  Additional provisions applicable to the transport of elevated temperature substances and solid substances transported above their melting point but below 100°C

4.2.1.18.1  Solid substances transported above their melting point but below 100°C and elevated temperature substances that are not assigned a portable tank instruction in column (10) of the Dangerous Goods List may be transported in portable tanks provided that the solid substances are:

(a)	classified in Division 6.1 or Classes 8 or 9 and have no subsidiary risk other than that of Division 6.1 or Class 8; and

(b)	are in packing group II or III; or

(c)	the solid substances are authorized for transport in portable tanks by the competent authority in accordance with the provisions of 6.7.1.3.

4.2.1.18.2  Unless otherwise indicated in the Dangerous Goods List of Chapter 3.2, portable tanks used for the transport of these solid substances shall conform to the provisions of portable tank instruction T4 for solid substances of packing group III or T7 for solid substances of packing group II. An equally suitable portable tank may be selected according to 4.2.5.2.5. The maximum degree of filling (in %) shall be determined according to 4.2.1.9.5 (TP3).  The shell shall be thermally insulated to ensure that the temperature of its outer surface excluding openings and their closures does not exceed 70 °C."

(Annexes in English only)

Annex 1

Proposed rationalized approach for the assignment of tank instructions for solids

The following is a proposed rationalized approach for the assignment of solids to portable tanks:

| Tank Instructions for Solids – Rationalized Approach |
| --- |
| Class/SR | PG | TI | TP |
| 4.1 | I | Not Authorized |  |
|  | II | T3** | TPXX |
|  | III | T1* | TPXX |
| 4.2 | I | T21* | TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 4.3 | I | T6* | TP7, TPXX |
| 4.3/6.1 | I | Not Authorized |  |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 5.1 | I | Not Authorized |  |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 5.2 | I | Not Authorized |  |
|  | II | T23*** | TPXX |
| 6.1 | I | T6 | TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 8 | I | T6 | TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 9 | II | T3 | TPXX |
|  | III | T1 | TPXX |

* 	Some substances in this category are not assigned a T-Code on the basis of the risk posed in transport.

**	Wetted substances that may possess explosive properties are not authorized. Some substances in this category are not assigned a T-Code on the basis of the risk posed in transport.

***	Only Type F organic peroxides are authorized.

Annex 2

Proposed T-Codes for Solids not Currently Assigned T-Codes

| UN# | Name/Description | Class | PG | SR | Proposed UN T-Code | Proposed TP Note(s) |
| --- | --- | --- | --- | --- | --- | --- |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | II |  | T3 | TPXX |
| 1323 | FERROCERIUM | 4.1 | II |  | T3 | TPXX |
| 1341 | PHOSPHORUS SESQUISULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 | TPXX |
| 1343 | PHOSPHORUS TRISULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 | TPXX |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 1437 | ZIRCONIUM HYDRIDE | 4.1 | II |  | T3 | TPXX |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | II |  | T3 | TPXX |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | II | 6.1 | T3 | TPXX |
| 1868 | DECABORANE | 4.1 | II | 6.1 | T3 | TPXX |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | II | 6.1 | T3 | TPXX |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | II | 8 | T3 | TPXX |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | II | 8 | T3 | TPXX |
| 1339 | PHOSPHORUS HEPTASULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 | TPXX |
| 1345 | RUBBER SCRAP or RUBBER SHODDY, powdered or granulated, not exceeding 840 microns and rubber content exceeding 45% | 4.1 | II |  | T3 | TPXX |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 1326 | HAFNIUM POWDER, WETTED with not less than 25% water | 4.1 | II |  | T3 | TPXX |
| 1352 | TITANIUM POWDER, WETTED with not less than 25% water | 4.1 | II |  | T3 | TPXX |
| 1358 | ZIRCONIUM POWDER, WETTED with not less than 25% water | 4.1 | II |  | T3 | TPXX |
| 1871 | TITANIUM HYDRIDE | 4.1 | II |  | T3 | TPXX |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | III |  | T1 | TPXX |
| 1330 | MANGANESE RESINATE | 4.1 | III |  | T1 | TPXX |
| 1328 | HEXAMETHYLENETETRAMINE | 4.1 | III |  | T1 | TPXX |
| 1314 | CALCIUM RESINATE, FUSED | 4.1 | III |  | T1 | TPXX |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 2213 | PARAFORMALDEHYDE | 4.1 | III |  | T1 | TPXX |
| 1869 | MAGNESIUM or MAGNESIUM ALLOYS with more than 50% magnesium in pellets, turnings or ribbons | 4.1 | III |  | T1 | TPXX |
| 1332 | METALDEHYDE | 4.1 | III |  | T1 | TPXX |
| 2538 | NITRONAPHTHALENE | 4.1 | III |  | T1 | TPXX |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 2687 | DICYCLOHEXYLAMMONIUM NITRITE | 4.1 | III |  | T1 | TPXX |
| 2001 | COBALT NAPHTHENATES, POWDER | 4.1 | III |  | T1 | TPXX |
| 2714 | ZINC RESINATE | 4.1 | III |  | T1 | TPXX |
| 2878 | TITANIUM SPONGE GRANULES or TITANIUM SPONGE POWDERS | 4.1 | III |  | T1 | TPXX |
| 1318 | COBALT RESINATE, PRECIPITATED | 4.1 | III |  | T1 | TPXX |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | III | 8 | T1 | TPXX |
| 1338 | PHOSPHORUS, AMORPHOUS | 4.1 | III |  | T1 | TPXX |
| 1313 | CALCIUM RESINATE | 4.1 | III |  | T1 | TPXX |
| 1312 | BORNEOL | 4.1 | III |  | T1 | TPXX |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | III |  | T1 | TPXX |
| 3097 | FLAMMABLE SOLID, OXIDIZING, N.O.S. | 4.1 | III | 5.1 | T1 | TPXX |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | III | 8 | T1 | TPXX |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | III | 6.1 | T1 | TPXX |
| 2717 | CAMPHOR, synthetic | 4.1 | III |  | T1 | TPXX |
| 1334 | NAPHTHALENE, CRUDE or NAPHTHALENE, REFINED | 4.1 | III |  | T1 | TPXX |
| 1346 | SILICON POWDER, AMORPHOUS | 4.1 | III |  | T1 | TPXX |
| 2715 | ALUMINIUM RESINATE | 4.1 | III |  | T1 | TPXX |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | III | 6.1 | T1 | TPXX |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 1350 | SULPHUR | 4.1 | III |  | T1 | TPXX |
| 3254 | TRIBUTYLPHOSPHANE | 4.2 | I |  | T21 | TPXX |
| 2881 | METAL CATALYST, DRY | 4.2 | I |  | T21 | TPXX |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | I |  | T21 | TPXX |
| 1854 | BARIUM ALLOYS, PYROPHORIC | 4.2 | I |  | T21 | TPXX |
| 1383 | PYROPHORIC METAL, N.O.S. or PYROPHORIC ALLOY, N.O.S. | 4.2 | I |  | T21 | TPXX |
| 3200 | PYROPHORIC SOLID, INORGANIC, N.O.S. | 4.2 | I |  | T21 | TPXX |
| 2870 | ALUMINIUM BOROHYDRIDE | 4.2 | I | 4.3 | T21 | TPXX |
| 3342 | XANTHATES | 4.2 | II |  | T3 | TPXX |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | II |  | T3 | TPXX |
| 1369 | p-NITROSODIMETHYLANILINE | 4.2 | II |  | T3 | TPXX |
| 1385 | SODIUM SULPHIDE, ANHYDROUS or SODIUM SULPHIDE with less than 30% water of crystallization | 4.2 | II |  | T3 | TPXX |
| 2940 | 9-PHOSPHABICYCLONONANES (CYCLOOCTADIENE PHOSPHINES) | 4.2 | II |  | T3 | TPXX |
| 2318 | SODIUM HYDROSULPHIDE with less than 25% water of crystallization | 4.2 | II |  | T3 | TPXX |
| 1923 | CALCIUM DITHIONITE (CALCIUM HYDROSULPHITE) | 4.2 | II |  | T3 | TPXX |
| 1374 | FISH MEAL (FISH SCRAP), UNSTABILIZED | 4.2 | II |  | T3 | TPXX |
| 1431 | SODIUM METHYLATE | 4.2 | II | 8 | T3 | TPXX |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | II | 8 | T3 | TPXX |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | II | 8 | T3 | TPXX |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | II | 6.1 | T3 | TPXX |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | II | 6.1 | T3 | TPXX |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | II | 5.1 | T3 | TPXX |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | II | 8 | T3 | TPXX |
| 1929 | POTASSIUM DITHIONITE (POTASSIUM HYDROSULPHITE) | 4.2 | II |  | T3 | TPXX |
| 2546 | TITANIUM POWDER, DRY | 4.2 | II |  | T3 | TPXX |
| 2881 | METAL CATALYST, DRY | 4.2 | II |  | T3 | TPXX |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | II |  | T3 | TPXX |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | II |  | T3 | TPXX |
| 1384 | SODIUM DITHIONITE (SODIUM HYDROSULPHITE) | 4.2 | II |  | T3 | TPXX |
| 3341 | THIOUREA DIOXIDE | 4.2 | II |  | T3 | TPXX |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 1382 | POTASSIUM SULPHIDE, ANHYDROUS or POTASSIUM SULPHIDE with less than 30% water of crystallization | 4.2 | II |  | T3 | TPXX |
| 2004 | MAGNESIUM DIAMIDE | 4.2 | II |  | T3 | TPXX |
| 1361 | CARBON, animal or vegetable origin | 4.2 | II |  | T3 | TPXX |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 1378 | METAL CATALYST, WETTED with a visible excess of liquid | 4.2 | II |  |  | TPXX |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | III | 8 | T3 | TPXX |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | III | 8 | T3 | TPXX |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | III | 8 | T3 | TPXX |
| 1376 | IRON OXIDE, SPENT or IRON SPONGE, SPENT obtained from coal gas purification | 4.2 | III |  | T1 | TPXX |
| 3341 | THIOUREA DIOXIDE | 4.2 | III |  | T1 | TPXX |
| 1932 | ZIRCONIUM SCRAP | 4.2 | III |  | T1 | TPXX |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGETABLE or SYNTHETIC, N.O.S. with oil | 4.2 | III |  | T1 | TPXX |
| 1361 | CARBON, animal or vegetable origin | 4.2 | III |  | T1 | TPXX |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | III | 5.1 | T1 | TPXX |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | III |  | T1 | TPXX |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | III | 6.1 | T1 | TPXX |
| 3174 | TITANIUM DISULPHIDE | 4.2 | III |  | T1 | TPXX |
| 2210 | MANEB or MANEB PREPARATION with not less than 60% maneb | 4.2 | III | 4.3 | T1 | TPXX |
| 3342 | XANTHATES | 4.2 | III |  | T1 | TPXX |
| 1362 | CARBON, ACTIVATED | 4.2 | III |  | T1 | TPXX |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | III |  | T1 | TPXX |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | III |  | T1 | TPXX |
| 2546 | TITANIUM POWDER, DRY | 4.2 | III |  | T1 | TPXX |
| 2881 | METAL CATALYST, DRY | 4.2 | III |  | T1 | TPXX |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | III | 6.1 | T1 | TPXX |
| 1402 | CALCIUM CARBIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1404 | CALCIUM HYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | I | 8 | T6 | TP7, TPXX |
| 2010 | MAGNESIUM HYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | I | 4.2 | T6 | TP7, TPXX |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | I | 4.2 | T6 | TP7, TPXX |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | I | 4.2 | T6 | TP7, TPXX |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | I | 4.2 | T6 | TP7, TPXX |
| 1870 | POTASSIUM BOROHYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1423 | RUBIDIUM | 4.3 | I |  | T6 | TP7, TPXX |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | I | 4.1 | T6 | TP7, TPXX |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | I | 4.1 | T6 | TP7, TPXX |
| 1422 | POTASSIUM SODIUM ALLOYS | 4.3 | I |  | T6 | TP7, TPXX |
| 1428 | SODIUM | 4.3 | I |  | T6 | TP7, TPXX |
| 2257 | POTASSIUM | 4.3 | I |  | T6 | TP7, TPXX |
| 1389 | ALKALI METAL AMALGAM | 4.3 | I |  | T6 | TP7, TPXX |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | I |  | T6 | TP7, TPXX |
| 1414 | LITHIUM HYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1427 | SODIUM HYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION | 4.3 | I |  | T6 | TP7, TPXX |
| 1407 | CAESIUM | 4.3 | I |  | T6 | TP7, TPXX |
| 2463 | ALUMINIUM HYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1410 | LITHIUM ALUMINIUM HYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1392 | ALKALINE EARTH METAL AMALGAM | 4.3 | I |  | T6 | TP7, TPXX |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | I |  | T6 | TP7, TPXX |
| 2806 | LITHIUM NITRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1413 | LITHIUM BOROHYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1415 | LITHIUM | 4.3 | I |  | T6 | TP7, TPXX |
| 1420 | POTASSIUM METAL ALLOYS | 4.3 | I |  | T6 | TP7, TPXX |
| 1426 | SODIUM BOROHYDRIDE | 4.3 | I |  | T6 | TP7, TPXX |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | I |  | T6 | TP7, TPXX |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | T3 | TPXX |
| 1400 | BARIUM | 4.3 | II |  | T3 | TPXX |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | II | 8 | T3 | TPXX |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | II | 6.1 | T3 | TPXX |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | II | 6.1 | T3 | TPXX |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | II | 4.2 | T3 | TPXX |
| 1401 | CALCIUM | 4.3 | II |  | T3 | TPXX |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | T3 | TPXX |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | T3 | TPXX |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 1405 | CALCIUM SILICIDE | 4.3 | II |  | T3 | TPXX |
| 2624 | MAGNESIUM SILICIDE | 4.3 | II |  | T3 | TPXX |
| 2830 | LITHIUM FERROSILICON | 4.3 | II |  | T3 | TPXX |
| 2835 | SODIUM ALUMINIUM HYDRIDE | 4.3 | II |  | T3 | TPXX |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | II |  | T3 | TPXX |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | T3 | TPXX |
| 3078 | CERIUM, turnings or gritty powder | 4.3 | II |  | T3 | TPXX |
| 1394 | ALUMINIUM CARBIDE | 4.3 | II |  | T3 | TPXX |
| 2805 | LITHIUM HYDRIDE, FUSED SOLID | 4.3 | II |  | T3 | TPXX |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | II |  | T3 | TPXX |
| 1390 | ALKALI METAL AMIDES | 4.3 | II |  | T3 | TPXX |
| 1402 | CALCIUM CARBIDE | 4.3 | II |  | T3 | TPXX |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 1417 | LITHIUM SILICON | 4.3 | II |  | T3 | TPXX |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | II | 4.2 | T3 | TPXX |
| 1340 | PHOSPHORUS PENTASULPHIDE, free from yellow and white phosphorus | 4.3 | II | 4.1 | T3 | TPXX |
| 1405 | CALCIUM SILICIDE | 4.3 | III |  | T1 | TPXX |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | III |  | T1 | TPXX |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 | III |  | T1 | TPXX |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 | III |  | T1 | TPXX |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 | III |  | T1 | TPXX |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | III |  | T1 | TPXX |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | T1 | TPXX |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | III |  | T1 | TPXX |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | III | 4.2 | T1 | TPXX |
| 1435 | ZINC ASHES | 4.3 | III |  | T1 | TPXX |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | III | 8 | T1 | TPXX |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | III |  | T1 | TPXX |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 | III |  | T1 | TPXX |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | T1 | TPXX |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | T1 | TPXX |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | T1 | TPXX |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | III | 6.1 | T1 | TPXX |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | III | 6.1 | T1 | TPXX |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 | III |  | T1 | TPXX |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | III | 4.2 | T1 | TPXX |
| 1475 | MAGNESIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 1496 | SODIUM CHLORITE | 5.1 | II |  | T3 | TPXX |
| 1495 | SODIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1494 | SODIUM BROMATE | 5.1 | II |  | T3 | TPXX |
| 1473 | MAGNESIUM BROMATE | 5.1 | II |  | T3 | TPXX |
| 1472 | LITHIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1471 | LITHIUM HYPOCHLORITE, DRY or LITHIUM HYPOCHLORITE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 2468 | TRICHLOROISOCYANURIC ACID, DRY | 5.1 | II |  | T3 | TPXX |
| 2465 | DICHLOROISOCYANURIC ACID, DRY or DICHLOROISOCYANURIC ACID SALTS | 5.1 | II |  | T3 | TPXX |
| 1439 | AMMONIUM DICHROMATE | 5.1 | II |  | T3 | TPXX |
| 1462 | CHLORITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1463 | CHROMIUM TRIOXIDE, ANHYDROUS | 5.1 | II | 8 | T3 | TPXX |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1509 | STRONTIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1450 | BROMATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1457 | CALCIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1484 | POTASSIUM BROMATE | 5.1 | II |  | T3 | TPXX |
| 1485 | POTASSIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 3212 | HYPOCHLORITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 3247 | SODIUM PEROXOBORATE, ANHYDROUS | 5.1 | II |  | T3 | TPXX |
| 1490 | POTASSIUM PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 1489 | POTASSIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1488 | POTASSIUM NITRITE | 5.1 | II |  | T3 | TPXX |
| 1493 | SILVER NITRATE | 5.1 | II |  | T3 | TPXX |
| 1512 | ZINC AMMONIUM NITRITE | 5.1 | II |  | T3 | TPXX |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | II | 8 | T3 | TPXX |
| 1449 | BARIUM PEROXIDE | 5.1 | II | 6.1 | T3 | TPXX |
| 1469 | LEAD NITRATE | 5.1 | II | 6.1 | T3 | TPXX |
| 2573 | THALLIUM CHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | II | 6.1 | T3 | TPXX |
| 2741 | BARIUM HYPOCHLORITE with more than 22% available chlorine | 5.1 | II | 6.1 | T3 | TPXX |
| 2719 | BARIUM BROMATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1446 | BARIUM NITRATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1448 | BARIUM PERMANGANATE | 5.1 | II | 6.1 | T3 | TPXX |
| 2464 | BERYLLIUM NITRATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1445 | BARIUM CHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1447 | BARIUM PERCHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1470 | LEAD PERCHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1515 | ZINC PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1502 | SODIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1503 | SODIUM PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 2721 | COPPER CHLORATE | 5.1 | II |  | T3 | TPXX |
| 2723 | MAGNESIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1514 | ZINC NITRATE | 5.1 | II |  | T3 | TPXX |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED, or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% but not more than 10% water | 5.1 | II |  | T3 | TPXX |
| 1516 | ZINC PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1513 | ZINC CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1506 | STRONTIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1508 | STRONTIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1453 | CALCIUM CHLORITE | 5.1 | II |  | T3 | TPXX |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1487 | POTASSIUM NITRATE AND SODIUM NITRITE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 1452 | CALCIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1476 | MAGNESIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | II |  | T3 | TPXX |
| 1456 | CALCIUM PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 2626 | CHLORIC ACID, AQUEOUS SOLUTION with not more than 10% chloric acid | 5.1 | II |  | T3 | TPXX |
| 2627 | NITRITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1455 | CALCIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1442 | AMMONIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1466 | FERRIC NITRATE | 5.1 | III |  | T1 | TPXX |
| 1492 | POTASSIUM PERSULPHATE | 5.1 | III |  | T1 | TPXX |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | III |  | T1 | TPXX |
| 2208 | CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 10% but not more than 39% available chlorine | 5.1 | III |  | T1 | TPXX |
| 1444 | AMMONIUM PERSULPHATE | 5.1 | III |  | T1 | TPXX |
| 1465 | DIDYMIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1438 | ALUMINIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1505 | SODIUM PERSULPHATE | 5.1 | III |  | T1 | TPXX |
| 2469 | ZINC BROMATE | 5.1 | III |  | T1 | TPXX |
| 2726 | NICKEL NITRITE | 5.1 | III |  | T1 | TPXX |
| 1451 | CAESIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1474 | MAGNESIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1499 | SODIUM NITRATE AND POTASSIUM NITRATE MIXTURE | 5.1 | III |  | T1 | TPXX |
| 2720 | CHROMIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1507 | STRONTIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1511 | UREA HYDROGEN PEROXIDE | 5.1 | III | 8 | T1 | TPXX |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | III | 8 | T1 | TPXX |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | III | 6.1 | T1 | TPXX |
| 1500 | SODIUM NITRITE | 5.1 | III | 6.1 | T1 | TPXX |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1481 | PERCHLORATES, INORGANIC, N.O.S | 5.1 | III |  | T1 | TPXX |
| 2722 | LITHIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1486 | POTASSIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 2724 | MANGANESE NITRATE | 5.1 | III |  | T1 | TPXX |
| 2725 | NICKEL NITRATE | 5.1 | III |  | T1 | TPXX |
| 1498 | SODIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1872 | LEAD DIOXIDE | 5.1 | III |  | T1 | TPXX |
| 2728 | ZIRCONIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1454 | CALCIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1467 | GUANIDINE NITRATE | 5.1 | III |  | T1 | TPXX |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE | 5.1 | III |  | T1 | TPXX |
| 3110 | ORGANIC PEROXIDE TYPE F, SOLID | 5.2 | II |  | T23 | TPXX |
| 3120 | ORGANIC PEROXIDE TYPE F, SOLID, TEMPERATURE CONTROLLED | 5.2 | II |  | T23 | TPXX |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1575 | CALCIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 2642 | FLUOROACETIC ACID | 6.1 | I |  | T6 | TPXX |
| 2630 | SELENATES or SELENITES | 6.1 | I |  | T6 | TPXX |
| 2629 | SODIUM FLUOROACETATE | 6.1 | I |  | T6 | TPXX |
| 2628 | POTASSIUM FLUOROACETATE | 6.1 | I |  | T6 | TPXX |
| 1698 | DIPHENYLAMINE CHLOROARSINE | 6.1 | I |  | T6 | TPXX |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1570 | BRUCINE | 6.1 | I |  | T6 | TPXX |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1565 | BARIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3048 | ALUMINIUM PHOSPHIDE PESTICIDE | 6.1 | I |  | T6 | TPXX |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1889 | CYANOGEN BROMIDE | 6.1 | I | 8 | T6 | TPXX |
| 1699 | DIPHENYLCHLOROARSINE, SOLID | 6.1 | I |  | T6 | TPXX |
| 2570 | CADMIUM COMPOUND | 6.1 | I |  | T6 | TPXX |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | I | 8 | T6 | TPXX |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | I | 8 | T6 | TPXX |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | I | 5.1 | T6 | TPXX |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | I | 4.3 | T6 | TPXX |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | I | 4.1 | T6 | TPXX |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1692 | STRYCHNINE or STRYCHNINE SALTS | 6.1 | I |  | T6 | TPXX |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | I | 4.2 | T6 | TPXX |
| 2471 | OSMIUM TETROXIDE | 6.1 | I |  | T6 | TPXX |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1713 | ZINC CYANIDE | 6.1 | I |  | T6 | TPXX |
| 1626 | MERCURIC POTASSIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2316 | SODIUM CUPROCYANIDE, SOLID | 6.1 | I |  | T6 | TPXX |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | I |  | T6 | TPXX |
| 1680 | POTASSIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 1689 | SODIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 1694 | BROMOBENZYL CYANIDES, SOLID | 6.1 | I |  | T6 | TPXX |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2567 | SODIUM PENTACHLOROPHENATE | 6.1 | II |  | T3 | TPXX |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1678 | POTASSIUM ARSENITE | 6.1 | II |  | T3 | TPXX |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2671 | AMINOPYRIDINES (o-, m-, p,) | 6.1 | II |  | T3 | TPXX |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2657 | SELENIUM DISULPHIDE | 6.1 | II |  | T3 | TPXX |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1636 | MERCURY CYANIDE | 6.1 | II |  | T3 | TPXX |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2863 | SODIUM AMMONIUM VANADATE | 6.1 | II |  | T3 | TPXX |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | II | 5.1 | T3 | TPXX |
| 2859 | AMMONIUM METAVANADATE | 6.1 | II |  | T3 | TPXX |
| 1651 | NAPHTHYLTHIOUREA | 6.1 | II |  | T3 | TPXX |
| 2673 | 2-AMINO-4-CHLOROPHENOL | 6.1 | II |  | T3 | TPXX |
| 2931 | VANADYL SULPHATE | 6.1 | II |  | T3 | TPXX |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2587 | BENZOQUINONE | 6.1 | II |  | T3 | TPXX |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2645 | PHENACYL BROMIDE | 6.1 | II |  | T3 | TPXX |
| 2647 | MALONONITRILE | 6.1 | II |  | T3 | TPXX |
| 2861 | AMMONIUM POLYVANADATE | 6.1 | II |  | T3 | TPXX |
| 2649 | 1,3-DICHLOROACETONE | 6.1 | II |  | T3 | TPXX |
| 2570 | CADMIUM COMPOUND | 6.1 | II |  | T3 | TPXX |
| 1617 | LEAD ARSENATES | 6.1 | II |  | T3 | TPXX |
| 1684 | SILVER CYANIDE | 6.1 | II |  | T3 | TPXX |
| 2027 | SODIUM ARSENITE, SOLID | 6.1 | II |  | T3 | TPXX |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1679 | POTASSIUM CUPROCYANIDE | 6.1 | II |  | T3 | TPXX |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | II | 4.2 | T3 | TPXX |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S | 6.1 | II | 4.1 | T3 | TPXX |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | II | 4.3 | T3 | TPXX |
| 1895 | PHENYLMERCURIC NITRATE | 6.1 | II |  | T3 | TPXX |
| 2727 | THALLIUM NITRATE | 6.1 | II | 5.1 | T3 | TPXX |
| 1751 | CHLOROACETIC ACID, SOLID | 6.1 | II | 8 | T3 | TPXX |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | II | 8 | T3 | TPXX |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | II | 8 | T3 | TPXX |
| 1567 | BERYLLIUM POWDER | 6.1 | II | 4.1 | T3 | TPXX |
| 1885 | BENZIDINE | 6.1 | II |  | T3 | TPXX |
| 1704 | TETRAETHYL DITHIOPYROPHOSPHATE | 6.1 | II |  | T3 | TPXX |
| 1691 | STRONTIUM ARSENITE | 6.1 | II |  | T3 | TPXX |
| 1707 | THALLIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1712 | ZINC ARSENATE, ZINC ARSENITE or ZINC ARSENATE AND ZINC ARSENITE MIXTURE | 6.1 | II |  | T3 | TPXX |
| 2864 | POTASSIUM METAVANADATE | 6.1 | II |  | T3 | TPXX |
| 1688 | SODIUM CACODYLATE | 6.1 | II |  | T3 | TPXX |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1685 | SODIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1894 | PHENYLMERCURIC HYDROXIDE | 6.1 | II |  | T3 | TPXX |
| 1639 | MERCURY NUCLEATE | 6.1 | II |  | T3 | TPXX |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1683 | SILVER ARSENITE | 6.1 | II |  | T3 | TPXX |
| 3155 | PENTACHLOROPHENOL | 6.1 | II |  | T3 | TPXX |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1665 | NITROXYLENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1586 | COPPER ARSENITE | 6.1 | II |  | T3 | TPXX |
| 1587 | COPPER CYANIDE | 6.1 | II |  | T3 | TPXX |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1590 | DICHLOROANILINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1597 | DINITROBENZENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1606 | FERRIC ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1653 | NICKEL CYANIDE | 6.1 | II |  | T3 | TPXX |
| 1674 | PHENYLMERCURIC ACETATE | 6.1 | II |  | T3 | TPXX |
| 1658 | NICOTINE SULPHATE, SOLID | 6.1 | II |  | T3 | TPXX |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1585 | COPPER ACETOARSENITE | 6.1 | II |  | T3 | TPXX |
| 1656 | NICOTINE HYDROCHLORIDE, solid | 6.1 | II |  | T3 | TPXX |
| 1657 | NICOTINE SALICYLATE | 6.1 | II |  | T3 | TPXX |
| 1652 | NAPHTHYLUREA | 6.1 | II |  | T3 | TPXX |
| 1638 | MERCURY IODIDE | 6.1 | II |  | T3 | TPXX |
| 1637 | MERCURY GLUCONATE | 6.1 | II |  | T3 | TPXX |
| 1607 | FERRIC ARSENITE | 6.1 | II |  | T3 | TPXX |
| 1634 | MERCURY BROMIDES | 6.1 | II |  | T3 | TPXX |
| 1608 | FERROUS ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1630 | MERCURY AMMONIUM CHLORIDE | 6.1 | II |  | T3 | TPXX |
| 1629 | MERCURY ACETATE | 6.1 | II |  | T3 | TPXX |
| 1627 | MERCUROUS NITRATE | 6.1 | II |  | T3 | TPXX |
| 1625 | MERCURIC NITRATE | 6.1 | II |  | T3 | TPXX |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1620 | LEAD CYANIDE | 6.1 | II |  | T3 | TPXX |
| 1664 | NITROTOLUENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1642 | MERCURY OXYCYANIDE, DESENSITIZED | 6.1 | II |  | T3 | TPXX |
| 1572 | CACODYLIC ACID | 6.1 | II |  | T3 | TPXX |
| 1631 | MERCURY BENZOATE | 6.1 | II |  | T3 | TPXX |
| 1646 | MERCURY THIOCYANATE | 6.1 | II |  | T3 | TPXX |
| 1645 | MERCURY SULPHATE | 6.1 | II |  | T3 | TPXX |
| 1644 | MERCURY SALICYLATE | 6.1 | II |  | T3 | TPXX |
| 1677 | POTASSIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1643 | MERCURY POTASSIUM IODIDE | 6.1 | II |  | T3 | TPXX |
| 1624 | MERCURIC CHLORIDE | 6.1 | II |  | T3 | TPXX |
| 1641 | MERCURY OXIDE | 6.1 | II |  | T3 | TPXX |
| 1574 | CALCIUM ARSENATE AND CALCIUM ARSENITE MIXTURE, SOLID | 6.1 | II |  | T3 | TPXX |
| 1623 | MERCURIC ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1659 | NICOTINE TARTRATE | 6.1 | II |  | T3 | TPXX |
| 1622 | MAGNESIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1621 | LONDON PURPLE | 6.1 | II |  | T3 | TPXX |
| 1640 | MERCURY OLEATE | 6.1 | II |  | T3 | TPXX |
| 1611 | HEXAETHYL TETRAPHOSPHATE | 6.1 | II |  | T3 | TPXX |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1573 | CALCIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1618 | LEAD ARSENITES | 6.1 | II |  | T3 | TPXX |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1562 | ARSENICAL DUST | 6.1 | II |  | T3 | TPXX |
| 1561 | ARSENIC TRIOXIDE | 6.1 | II |  | T3 | TPXX |
| 1559 | ARSENIC PENTOXIDE | 6.1 | II |  | T3 | TPXX |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | II |  | T3 | TPXX |
| 1555 | ARSENIC BROMIDE | 6.1 | II |  | T3 | TPXX |
| 1554 | ARSENIC ACID, SOLID | 6.1 | II |  | T3 | TPXX |
| 1558 | ARSENIC | 6.1 | II |  | T3 | TPXX |
| 1546 | AMMONIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1577 | CHLORODINITROBENZENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1578 | CHLORONITROBENZENES, solid | 6.1 | II |  | T3 | TPXX |
| 1596 | DINITROANILINES | 6.1 | II |  | T3 | TPXX |
| 1650 | beta-NAPHTHYLAMINE | 6.1 | II |  | T3 | TPXX |
| 1661 | NITROANILINES (o-, m-, p-) | 6.1 | II |  | T3 | TPXX |
| 1671 | PHENOL, SOLID | 6.1 | II |  | T3 | TPXX |
| 1708 | TOLUIDINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1711 | XYLIDINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1843 | AMMONIUM DINITRO-o-CRESOLATE | 6.1 | II |  | T3 | TPXX |
| 2018 | CHLOROANILINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 2038 | DINITROTOLUENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE | 6.1 | II |  | T3 | TPXX |
| 2261 | XYLENOLS, solid | 6.1 | II |  | T3 | TPXX |
| 2306 | NITROBENZOTRIFLUORIDES, solid | 6.1 | II |  | T3 | TPXX |
| 2669 | CHLOROCRESOLS, solid | 6.1 | II |  | T3 | TPXX |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 3243 | SOLIDS CONTAINING TOXIC LIQUID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2076 | CRESOLS, SOLID | 6.1 | II | 8 | T3 | TPXX |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2862 | VANADIUM PENTOXIDE, non-fused form | 6.1 | III |  | T1 | TPXX |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2871 | ANTIMONY POWDER | 6.1 | III |  | T1 | TPXX |
| 2875 | HEXACHLOROPHENE | 6.1 | III |  | T1 | TPXX |
| 2876 | RESORCINOL | 6.1 | III |  | T1 | TPXX |
| 2853 | MAGNESIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2855 | ZINC FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1550 | ANTIMONY LACTATE | 6.1 | III |  | T1 | TPXX |
| 2854 | AMMONIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 1548 | ANILINE HYDROCHLORIDE | 6.1 | III |  | T1 | TPXX |
| 1551 | ANTIMONY POTASSIUM TARTRATE | 6.1 | III |  | T1 | TPXX |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2570 | CADMIUM COMPOUND | 6.1 | III |  | T1 | TPXX |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2716 | 1,4-BUTYNEDIOL | 6.1 | III |  | T1 | TPXX |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2516 | CARBON TETRABROMIDE | 6.1 | III |  | T1 | TPXX |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE | 6.1 | III |  | T1 | TPXX |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2713 | ACRIDINE | 6.1 | III |  | T1 | TPXX |
| 2674 | SODIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 2660 | NITROTOLUIDINES (MONO) | 6.1 | III |  | T1 | TPXX |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2659 | SODIUM CHLOROACETATE | 6.1 | III |  | T1 | TPXX |
| 2655 | POTASSIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2233 | CHLOROANISIDINES | 6.1 | III |  | T1 | TPXX |
| 2512 | AMINOPHENOLS (o-, m-, p-) | 6.1 | III |  | T1 | TPXX |
| 2505 | AMMONIUM FLUORIDE | 6.1 | III |  | T1 | TPXX |
| 2473 | SODIUM ARSANILATE | 6.1 | III |  | T1 | TPXX |
| 2446 | NITROCRESOLS | 6.1 | III |  | T1 | TPXX |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2237 | CHLORONITROANILINES | 6.1 | III |  | T1 | TPXX |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | III |  | T1 | TPXX |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2020 | CHLOROPHENOLS, SOLID | 6.1 | III |  | T1 | TPXX |
| 1884 | BARIUM OXIDE | 6.1 | III |  | T1 | TPXX |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2433 | CHLORONITROTOLUENES, SOLID | 6.1 | III |  | T1 | TPXX |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1616 | LEAD ACETATE | 6.1 | III |  | T1 | TPXX |
| 1663 | NITROPHENOLS (o-, m-, p-) | 6.1 | III |  | T1 | TPXX |
| 1673 | PHENYLENEDIAMINES (o-, m-, p-) | 6.1 | III |  | T1 | TPXX |
| 1690 | SODIUM FLUORIDE | 6.1 | III |  | T1 | TPXX |
| 1709 | 2,4-TOLUYLENEDIAMINE | 6.1 | III |  | T1 | TPXX |
| 1812 | POTASSIUM FLUORIDE | 6.1 | III |  | T1 | TPXX |
| 2074 | ACRYLAMIDE | 6.1 | III |  | T1 | TPXX |
| 2235 | CHLOROBENZYL CHLORIDES | 6.1 | III |  | T1 | TPXX |
| 2239 | CHLOROTOLUIDINES, solid | 6.1 | III |  | T1 | TPXX |
| 2651 | 4,4'-DIAMINODIPHENYLMETHANE | 6.1 | III |  | T1 | TPXX |
| 2662 | HYDROQUINONE | 6.1 | III |  | T1 | TPXX |
| 2729 | HEXACHLOROBENZENE | 6.1 | III |  | T1 | TPXX |
| 2730 | NITROANISOLES, SOLID | 6.1 | III |  | T1 | TPXX |
| 2732 | NITROBROMOBENZENES, SOLID | 6.1 | III |  | T1 | TPXX |
| 2753 | N-ETHYLBENZYLTOLUIDINES, SOLID | 6.1 | III |  | T1 | TPXX |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | I |  | T6 | TPXX |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | I |  | T6 | TPXX |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | I | 5.1 | T6 | TPXX |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | I |  | T6 | TPXX |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | I | 6.1 | T6 | TPXX |
| 1905 | SELENIC ACID | 8 | I |  | T6 | TPXX |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | I | 4.3 | T6 | TPXX |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | I | 4.1 | T6 | TPXX |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | I | 4.2 | T6 | TPXX |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | I |  | T6 | TPXX |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | II |  | T3 | TPXX |
| 2680 | LITHIUM HYDROXIDE MONOHYDRATE | 8 | II |  | T3 | TPXX |
| 2682 | CAESIUM HYDROXIDE | 8 | II |  | T3 | TPXX |
| 2691 | PHOSPHORUS PENTABROMIDE | 8 | II |  | T3 | TPXX |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | II |  | T3 | TPXX |
| 2583 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with more than 5% free sulphuric acid | 8 | II |  | T3 | TPXX |
| 2678 | RUBIDIUM HYDROXIDE | 8 | II |  | T3 | TPXX |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 1756 | CHROMIC FLUORIDE, SOLID | 8 | II |  | T3 | TPXX |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 1839 | TRICHLOROACETIC ACID | 8 | II |  | T3 | TPXX |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | II |  | T3 | TPXX |
| 2033 | POTASSIUM MONOXIDE | 8 | II |  | T3 | TPXX |
| 1794 | LEAD SULPHATE with more than 3% free acid | 8 | II |  | T3 | TPXX |
| 1847 | POTASSIUM SULPHIDE, HYDRATED with not less than 30% water of crystallization | 8 | II |  | T3 | TPXX |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | II |  | T3 | TPXX |
| 1770 | DIPHENYLMETHYL BROMIDE | 8 | II |  | T3 | TPXX |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | II | 6.1 | T3 | TPXX |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | II | 5.1 | T3 | TPXX |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | II | 4.3 | T3 | TPXX |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | II | 4.2 | T3 | TPXX |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | II | 4.1 | T3 | TPXX |
| 1806 | PHOSPHORUS PENTACHLORIDE | 8 | II |  | T3 | TPXX |
| 1725 | ALUMINIUM BROMIDE, ANHYDROUS | 8 | II |  | T3 | TPXX |
| 2670 | CYANURIC CHLORIDE | 8 | II |  | T3 | TPXX |
| 2506 | AMMONIUM HYDROGEN SULPHATE | 8 | II |  | T3 | TPXX |
| 1825 | SODIUM MONOXIDE | 8 | II |  | T3 | TPXX |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | II |  | T3 | TPXX |
| 2509 | POTASSIUM HYDROGEN SULPHATE | 8 | II |  | T3 | TPXX |
| 1813 | POTASSIUM HYDROXIDE, SOLID | 8 | II |  | T3 | TPXX |
| 1823 | SODIUM HYDROXIDE, SOLID | 8 | II |  | T3 | TPXX |
| 1727 | AMMONIUM HYDROGENDIFLUORIDE, SOLID | 8 | II |  | T3 | TPXX |
| 1726 | ALUMINIUM CHLORIDE, ANHYDROUS | 8 | II |  | T3 | TPXX |
| 1807 | PHOSPHORUS PENTOXIDE | 8 | II |  | T3 | TPXX |
| 1939 | PHOSPHORUS OXYBROMIDE | 8 | II |  | T3 | TPXX |
| 2308 | NITROSYLSULPHURIC ACID, SOLID | 8 | II |  | T3 | TPXX |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | II |  | T3 | TPXX |
| 2439 | SODIUM HYDROGENDIFLUORIDE | 8 | II |  | T3 | TPXX |
| 3244 | SOLIDS CONTAINING CORROSIVE LIQUID, N.O.S. | 8 | II |  | T3 | TPXX |
| 2508 | MOLYBDENUM PENTACHLORIDE | 8 | III |  | T1 | TPXX |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 1805 | PHOSPHORIC ACID, SOLID | 8 | III |  | T1 | TPXX |
| 3253 | DISODIUM TRIOXOSILICATE | 8 | III |  | T1 | TPXX |
| 1773 | FERRIC CHLORIDE, ANHYDROUS | 8 | III |  | T1 | TPXX |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | III |  | T1 | TPXX |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | III |  | T1 | TPXX |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | III |  | T1 | TPXX |
| 1907 | SODA LIME with more than 4% sodium hydroxide | 8 | III |  | T1 | TPXX |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | III |  | T1 | TPXX |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | III | 6.1 | T1 | TPXX |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | III |  | T1 | TPXX |
| 2578 | PHOSPHORUS TRIOXIDE | 8 | III |  | T1 | TPXX |
| 2905 | CHLOROPHENOLATES, SOLID or PHENOLATES, SOLID | 8 | III |  | T1 | TPXX |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 | III |  | T1 | TPXX |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 2865 | HYDROXYLAMINE SULPHATE | 8 | III |  | T1 | TPXX |
| 2802 | COPPER CHLORIDE | 8 | III |  | T1 | TPXX |
| 2507 | CHLOROPLATINIC ACID, SOLID | 8 | III |  | T1 | TPXX |
| 2503 | ZIRCONIUM TETRACHLORIDE | 8 | III |  | T1 | TPXX |
| 2475 | VANADIUM TRICHLORIDE | 8 | III |  | T1 | TPXX |
| 2331 | ZINC CHLORIDE, ANHYDROUS | 8 | III |  | T1 | TPXX |
| 1910 | CALCIUM OXIDE | 8 | III |  | T1 | TPXX |
| 2698 | TETRAHYDROPHTHALIC ANHYDRIDES with more than 0.05% of maleic anhydride | 8 | III |  | T1 | TPXX |
| 2967 | SULPHAMIC ACID | 8 | III |  | T1 | TPXX |
| 2812 | SODIUM ALUMINATE, SOLID | 8 | III |  | T1 | TPXX |
| 2803 | GALLIUM | 8 | III |  | T1 | TPXX |
| 2440 | STANNIC CHLORIDE PENTAHYDRATE | 8 | III |  | T1 | TPXX |
| 2214 | PHTHALIC ANHYDRIDE with more than 0.05% of maleic anhydride | 8 | III |  | T1 | TPXX |
| 2215 | MALEIC ANHYDRIDE | 8 | III |  | T1 | TPXX |
| 2280 | HEXAMETHYLENEDIAMINE, SOLID | 8 | III |  | T1 | TPXX |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | III |  | T1 | TPXX |
| 2511 | 2-CHLOROPROPIONIC ACID, SOLID | 8 | III |  | T1 | TPXX |
| 2579 | PIPERAZINE | 8 | III |  | T1 | TPXX |
| 2823 | CROTONIC ACID | 8 | III |  | T1 | TPXX |
| 2834 | PHOSPHOROUS ACID | 8 | III |  | T1 | TPXX |
| 3335 | AVIATION REGULATED SOLID, N.O.S. | 9 |  |  | T1 | TPXX |
| 2969 | CASTOR BEANS or CASTOR MEAL or CASTOR POMACE or CASTOR FLAKE | 9 | II |  | T3 | TPXX |
| 2212 | BLUE ASBESTOS (crocidolite) or BROWN ASBESTOS (amosite, mysorite) | 9 | II |  | T3 | TPXX |
| 3152 | POLYHALOGENATED BIPHENYLS, SOLID or POLYHALOGENATED TERPHENYLS, SOLID | 9 | II |  | T3 | TPXX |
| 2590 | WHITE ASBESTOS (chrysotile, actinolite, anthophyllite, tremolite) | 9 | III |  | T1 | TPXX |
| 2216 | FISH MEAL (FISH SCRAP), STABILIZED | 9 | III |  | T1 | TPXX |
| 1931 | ZINC DITHIONITE (ZINC HYDROSULPHITE) | 9 | III |  | T1 | TPXX |
| 1841 | ACETALDEHYDE AMMONIA | 9 | III |  | T1 | TPXX |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S. | 9 | III |  | T1 | TPXX |
| 2211 | POLYMERIC BEADS, EXPANDABLE, evolving flammable vapour | 9 | III |  | T1 | TPXX |

Annex 3

Currently assigned tank provisions that would need to be changed in the Model Regulations based on the rationalized approach

| UN# | Name | Class | PG | Sub-Risk | EXISTING | PROPOSED |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | TI | TP | TI | TP |
| 1422 | POTASSIUM SODIUM ALLOYS | 4.3 | I |  | T9 | TP3 TP7 | T6 | TP7, TPXX |
| 1428 | SODIUM | 4.3 | I |  | T9 | TP3 TP7 | T6 | TP7, TPXX |
| 2257 | POTASSIUM | 4.3 | I |  | T9 | TP3 TP7 | T6 | TP7, TPXX |
| 1445 | BARIUM CHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 | TPXX |
| 1447 | BARIUM PERCHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 | TPXX |
| 1470 | LEAD PERCHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 | TPXX |
| 1811 | POTASSIUM HYDROGENDIFLUORIDE | 8 | II | 6.1 | T7 | TP2 | T3 | TPXX |
| 2076 | CRESOLS, SOLID | 6.1 | II | 8 | T7 | TP2 | T3 | TPXX |

Annex 4 - Solid substances proposed for transport in tanks that were addressed by

comments from the Working Group as requiring further consideration

| UN# | PROPER SHIPPING NAME | PG | Class | SR | Proposed UN T-Code |
| --- | --- | --- | --- | --- | --- |
| UN1374 | Fish meal, unstablized [or] Fish scrap, unstabilized | II | 4.2 |  | T3, TPXX |
| UN2008 | Zirconium powder, dry | II | 4.2 |  | T3, TPXX |
| UN2545 | Hafnium powder, dry | II | 4.2 |  | T3, TPXX |
| UN2546 | Titanium powder, dry | II | 4.2 |  | T3, TPXX |
| UN2008 | Zirconium powder, dry | III | 4.2 |  | T1, TPXX |
| UN2545 | Hafnium powder, dry | III | 4.2 |  | T1, TPXX |
| UN2546 | Titanium powder, dry | III | 4.2 |  | T1, TPXX |
| UN2881 | Metal catalyst, dry | III | 4.2 |  | T1, TPXX |
| UN1389 | Alkali metal amalgam, solid | I | 4.3 |  | T6, TP7, TPXX |
| UN1391 | Alkali metal dispersions, [or] Alkaline earth metal dispersions | I | 4.3 |  | T6, TP7, TPXX |
| UN1392 | Alkaline earth metal amalgams | I | 4.3 |  | T6, TP7, TPXX |
| UN1402 | Calcium carbide | I | 4.3 |  | T6, TP7, TPXX |
| UN1404 | Calcium hydride | I | 4.3 |  | T6, TP7, TPXX |
| UN1407 | Cesium [or] Caesium | I | 4.3 |  | T6, TP7, TPXX |
| UN1409 | Metal hydrides, water reactive, n.o.s. | I | 4.3 |  | T6, TP7, TPXX |
| UN1410 | Lithium aluminum hydride | I | 4.3 |  | T6, TP7, TPXX |
| UN1413 | Lithium borohydride | I | 4.3 |  | T6, TP7, TPXX |
| UN1414 | Lithium hydride | I | 4.3 |  | T6, TP7, TPXX |
| UN1415 | Lithium | I | 4.3 |  | T6, TP7, TPXX |
| UN1420 | Potassium, metal alloys | I | 4.3 |  | T6, TP7, TPXX |
| UN1422 | Potassium sodium alloys | I | 4.3 |  | T6, TP7, TPXX |
| UN1423 | Rubidium | I | 4.3 |  | T6, TP7, TPXX |
| UN1426 | Sodium borohydride | I | 4.3 |  | T6, TP7, TPXX |
| UN1427 | Sodium hydride | I | 4.3 |  | T6, TP7, TPXX |
| UN1428 | Sodium | I | 4.3 |  | T6, TP7, TPXX |
| UN1870 | Potassium borohydride | I | 4.3 |  | T6, TP7, TPXX |
| UN2010 | Magnesium hydride | I | 4.3 |  | T6, TP7, TPXX |
| UN2257 | Potassium | I | 4.3 |  | T6, TP7, TPXX |
| UN2463 | Aluminum hydride | I | 4.3 |  | T6, TP7, TPXX |
| UN2806 | Lithium nitride | I | 4.3 |  | T6, TP7, TPXX |
| UN2813 | Water-reactive solid, n.o.s. | I | 4.3 |  | T6, TP7, TPXX |
| UN3208 | Metallic substance, water-reactive, n.o.s. | I | 4.3 |  | T6, TP7, TPXX |
| UN3132 | Water-reactive solid, flammable, n.o.s. | I | 4.3 | 4.1 | T6, TP7, TPXX |
| UN1418 | Magnesium, powder [or] Magnesium alloys, powder | I | 4.3 | 4.2 | T6, TP7, TPXX |
| UN1436 | Zinc powder [or] Zinc dust | I | 4.3 | 4.2 | T6, TP7, TPXX |
| UN3135 | Water-reactive solid, self-heating, n.o.s. | I | 4.3 | 4.2 | T6, TP7, TPXX |
| UN3209 | Metallic substance, water-reactive, self-heating, n.o.s. | I | 4.3 | 4.2 | T6, TP7, TPXX |
| UN3131 | Water-reactive solid, corrosive, n.o.s. | I | 4.3 | 8 | T6, TP7, TPXX |
| UN1402 | Calcium carbide | II | 4.3 |  | T3, TPXX |
| UN1409 | Metal hydrides, water reactive, n.o.s. | II | 4.3 |  | T3, TPXX |
| UN2813 | Water-reactive solid, n.o.s. | II | 4.3 |  | T3, TPXX |
| UN3208 | Metallic substance, water-reactive, n.o.s. | II | 4.3 |  | T3, TPXX |
| UN3132 | Water-reactive solid, flammable, n.o.s. | II | 4.3 | 4.1 | T3, TPXX |
| UN1418 | Magnesium, powder [or] Magnesium alloys, powder | II | 4.3 | 4.2 | T3, TPXX |
| UN1436 | Zinc powder [or] Zinc dust | II | 4.3 | 4.2 | T3, TPXX |
| UN3135 | Water-reactive solid, self-heating, n.o.s. | II | 4.3 | 4.2 | T3, TPXX |
| UN3209 | Metallic substance, water-reactive, self-heating, n.o.s. | II | 4.3 | 4.2 | T3, TPXX |
| UN3134 | Water-reactive solid, toxic, n.o.s. | II | 4.3 | 6.1 | T3, TPXX |
| UN3131 | Water-reactive solid, corrosive, n.o.s. | II | 4.3 | 8 | T3, TPXX |
| UN2813 | Water-reactive solid, n.o.s. | III | 4.3 |  | T1, TPXX |
| UN3208 | Metallic substance, water-reactive, n.o.s. | III | 4.3 |  | T1, TPXX |
| UN3132 | Water-reactive solid, flammable, n.o.s. | III | 4.3 | 4.1 | T1, TPXX |
| UN1418 | Magnesium, powder [or] Magnesium alloys, powder | III | 4.3 | 4.2 | T1, TPXX |
| UN1436 | Zinc powder [or] Zinc dust | III | 4.3 | 4.2 | T1, TPXX |
| UN3135 | Water-reactive solid, self-heating, n.o.s. | III | 4.3 | 4.2 | T1, TPXX |
| UN3209 | Metallic substance, water-reactive, self-heating, n.o.s. | III | 4.3 | 4.2 | T1, TPXX |
| UN3134 | Water-reactive solid, toxic, n.o.s. | III | 4.3 | 6.1 | T1, TPXX |
| UN3131 | Water-reactive solid, corrosive, n.o.s. | III | 4.3 | 8 | T1, TPXX |
| UN1442 | Ammonium perchlorate | II | 5.1 |  | T3, TPXX |
| UN1479 | Oxidizing solid, n.o.s. | II | 5.1 |  | T3, TPXX |
| UN3087 | Oxidizing solid, toxic, n.o.s. | II | 5.1 | 6.1 | T3, TPXX |
| UN3085 | Oxidizing solid, corrosive, n.o.s. | II | 5.1 | 8 | T3, TPXX |
| UN1479 | Oxidizing solid, n.o.s. | III | 5.1 |  | T1, TPXX |
| UN3087 | Oxidizing solid, toxic, n.o.s. | III | 5.1 | 6.1 | T1, TPXX |
| UN3085 | Oxidizing solid, corrosive, n.o.s. | III | 5.1 | 8 | T1, TPXX |
| UN2930 | Toxic solids, flammable, organic, n.o.s. | I | 6.1 | 4.1 | T6, TPXX |
| UN1611 | Hexaethyl tetraphosphate, [solid] | II | 6.1 |  | T3, TPXX |
| UN2930 | Toxic solids, flammable, organic, n.o.s. | II | 6.1 | 4.1 | T3, TPXX |
| UN3095 | Corrosive solids, self-heating, n.o.s. | I | 8 | 4.2 | T6, TPXX |
| 1811 | Potassium hydrogendifluoride | 8 | II | 6.1 | T3 |
| UN1847 | Potassium sulfide, hydrated [with not less than 30 percent water of crystallization] | II | 8 |  | T3, TPXX |
| UN3095 | Corrosive solids, self-heating, n.o.s. | II | 8 | 4.2 | T3, TPXX |
| UN1910 | Calcium oxide | III | 8 |  | T1, TPXX |
| UN2812 | Sodium aluminate, solid | III | 8 |  | T1, TPXX |
| UN2216 | Fish meal, stabilized [or] Fish scrap, stabilized | III | 9 |  | T1, TPXX |

_________________

# Text boxes

STSTE

Secretariat