Distr.

GÉNÉRALE

ST/SG/AC.10/C.3/2002/75

13 septembre 2002

FRANÇAIS

Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT
DES MARCHANDISES DANGEREUSES
ET DU SYSTÈME GÉNÉRAL HARMONISÉ
DE CLASSIFICATION ET D’ÉTIQUETAGE
DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport
des marchandises dangereuses
(Vingt-deuxième session, 2-6 décembre 2002,
point 4 a) de l’ordre du jour)

NOUVELLES PROPOSITIONS

Questions en suspens

Transport en citernes mobiles des matières solides

Communication de l’expert des États-Unis d’Amérique

1.	À la vingt et unième session du Sous-Comité, l’expert des États-Unis d’Amérique a accepté d’élaborer une proposition révisée visant à prendre en compte le transport en citernes mobiles des marchandises dangereuses solides, et étant fondée sur les observations qui avaient été formulées et examinées par un groupe de travail informel. Une proposition finale d’amendements au Règlement type est donc présentée. L’annexe 1 contient une démarche rationalisée où sont indiquées les règles qui ont été employées pour attribuer aux matières solides des dispositions spéciales pour le transport en citernes mobiles. À l’annexe 2 sont énoncées les attributions proposées, compte tenu de la démarche rationalisée donnée à l’annexe 1. L’annexe 3 présente une liste des dispositions actuellement attribuées pour le transport en citernes, qui devraient être modifiées dans le Règlement type eu égard à la démarche rationalisée.

Propositions

2.	La nouvelle disposition spéciale suivante pour le transport en citernes mobiles est proposée pour les matières solides granuleuses ou pulvérulentes et pour les matières solides qui sont chargées à des températures supérieures à leur point de fusion, puis sont réfrigérées et transportées comme une masse solide:

«TPXX  L’instruction de transport en citernes mobiles attribuée à cette matière s’applique aux matières solides granuleuses ou pulvérulentes et aux matières solides qui sont chargées à des températures supérieures à leur point de fusion, puis sont réfrigérées et transportées comme une masse solide. En ce qui concerne les matières solides qui sont transportées à des températures supérieures à leur point de fusion, voir la sous-section 4.2.1.18.»

3.	Ajouter la nouvelle sous-section 4.2.1.18, libellée comme suit:

«4.2.1.18	Dispositions supplémentaires applicables au transport de matières solides à des températures supérieures à leur point de fusion

4.2.1.18.1 La température la plus élevée atteinte pendant le remplissage, la vidange ou le transport doit être utilisée, si elle est supérieure à 65 °C, lors du calcul de la pression de service maximale autorisée et de la pression de calcul, telles que définies au 6.7.2.1.

4.2.1.18.2	Protection contre les explosions

a)	La température à la surface de l’élément de chauffage dans le cas d’un système de chauffage interne ou la température sur le réservoir de la citerne mobile dans le cas d’un système de chauffage externe, ne doit en aucun cas dépasser 80 % de la température d’inflammation spontanée de la matière transportée. Les éléments de chauffage internes ne doivent pas être alimentés en énergie à moins d’être complètement immergés.

b)	Si le système de chauffage électrique est installé à l’intérieur de la citerne mobile, il convient de prévoir un disjoncteur de perte à la masse dont le courant de déclenchement soit inférieur à 100 mA.

c)	Les boîtiers des commutateurs électriques montés sur les citernes mobiles ne doivent pas avoir de raccordement direct avec l’intérieur de la citerne mobile et doivent disposer d’une protection équivalant au moins à la protection de type IP 56 conformément à la norme CEI 144 ou CEI 529.

4.2.1.18.3	Le système de chauffage doit être soumis à des inspections et à des épreuves, notamment à des épreuves de pression sur serpentins ou conduites de chauffage, selon le cas.

4.2.1.18.4	Les matières solides transportées à des températures supérieures à leur point de fusion, auxquelles il n’est pas attribué d’instruction de transport en citernes mobiles dans la colonne 10 de la Liste des marchandises dangereuses ou pour lesquelles l’instruction de transport en citernes mobiles attribuée ne s’applique pas au transport à des températures supérieures à leur point de fusion peuvent être transportées en citernes mobiles à condition que les matières solides soient telles qu’elles:

a)	Sont classées dans les divisions 4.1, 4.2, 4.3, 5.1 ou 6.1 ou dans les classes 8 ou 9 et ne présentent pas de risque subsidiaire autre que ceux de la division 6.1 ou de la classe 8;

b)	Appartiennent aux groupes d’emballage II ou III;

c)	Sont agréées pour le transport en citernes mobiles par l’autorité compétente, conformément aux dispositions du 6.7.1.3.

4.2.1.18.5	Sauf indication contraire dans la Liste des marchandises dangereuses au chapitre 3.2, les citernes mobiles employées pour le transport de ces matières solides doivent être conformes aux dispositions de l’instruction de transport en citernes mobiles T4 pour les matières solides du groupe d’emballage III ou T7 pour les matières solides du groupe d’emballage II. Une citerne mobile qui garantit un niveau de sécurité équivalent ou supérieur peut être choisie conformément au 4.2.5.2.5. Le taux de remplissage maximal (en %) doit être déterminé conformément au 4.2.1.9.5 (TP3)».
À la suite des observations formulées par le groupe de correspondance, le texte proposé inclut les dispositions énoncées aux paragraphes 4.2.1.18.1 à 4.2.1.18.3 du Code IMDG. Le Sous-Comité est prié de vérifier si l’insertion de ce texte est justifiée.

Amendements corollaires

4.	Les amendements corollaires suivants sont proposés:

a)	Section 1.2.1, ajouter la définition suivante:

Matière à température élevée, une matière qui est transportée ou est offerte au transport:

- Dans un état liquide à une température supérieure ou égale à 100 °C;

- Dans un état liquide ayant un point d’éclair supérieur ou égal à 60,5 °C et qui est volontairement chauffée jusqu’à une température supérieure ou égale à son point d’éclair;

- Dans un état solide à une température supérieure ou égale à 240 °C:

b)	Paragraphe 4.2.1.4, remplacer la deuxième phrase par «Si nécessaire, le réservoir doit être muni d’une isolation thermique».

Paragraphe 4.2.1.9.5.1, modifier comme suit: «Le taux de remplissage maximal (en %) pour les matières solides transportées à des températures supérieures à leur point de fusion et pour les liquides à température élevée doit être déterminé au moyen de la formule suivante: …»

c)	Sous-section 4.2.5.3, modifier la disposition spéciale TP3 comme suit:

TP3  Le taux de remplissage maximal (en %) pour les matières solides transportées à des températures supérieures à leur point de fusion et pour les liquides à température élevée doit être déterminé conformément au 4.2.1.9.5.

d)	Sous-section 6.7.2.1, modifier la définition de Pression de calcul en supprimant à l’alinéa b i les mots «à température élevée».

e)	Sous-section 6.7.2.1, modifier la définition de L’intervalle de température de calcul en supprimant les mots «Pour les matières transportées à température élevée».

____________

Annexe 1

Proposition de démarche rationaliser pour l’attribution aux matières solides des
instructions de transport en citernes

| Démarche rationalisée pour le transport des matières solides |
| --- |
| Classe ou division/matières autoréactives | Groupe d’emballage | Instruction de transport | Dispositions spéciales |
| 4.1 | I | Non autorisé |  |
|  | II | T3** | TPXX |
|  | III | T1* | TPXX |
| 4.2 | I | T21* | TP7, TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 4.3/6.1 | I | Non autorisé | - |
| 4.3 | I | T9* | TP7, TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 5.1 | I | Non autorisé |  |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 5.2 | - | T23*** | TPXX |
| 6.1 | I | T6 | TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 8 | I | T6 | TPXX |
|  | II | T3 | TPXX |
|  | III | T1 | TPXX |
| 9 | II | T3 | TPXX |
|  | III | T1 | TPXX |

* 	Il n’est pas attribué de code T à certaines matières de cette catégorie T en raison du risque que présente le transport.

**	Les matières mouillées qui peuvent avoir des propriétés explosives ne sont pas autorisées. Il n’est pas attribué de code T à certaines matières de cette catégorie T en raison du risque que présente le transport.

***	Seuls les peroxydes organiques de type F sont autorisés.

Les matières solides qui ne conviennent pas au transport en citernes sont notamment les matières suivantes:

- Explosifs, explosifs flegmatisés et matières autoréactives, à l’exception des matières de type F;

- Hypochlorites secs ou en mélange (à savoir, les numéros ONU 1471, 1748, 2208, 2880);

- Matières de la division 5.2, à l’exception de celles de type F;

- Matières de la division 6.2;

- Matières de la classe 7, à l’exception des matières de faible activité spécifique (LSA) non fissiles ou fissiles exceptées; et

- No ONU 3255, Hypochlorite de tert-butyle, no ONU 2907, dinitrate d’isosorbide en mélange, no ONU 2956, tert-butyl-5 trinitro-2,4,6 m-xylène (musc-xylène), no ONU 3241, bromo-2 nitro-2 propanediol-1,3 et no ONU 3251, mononitrate-5 d’isosorbide.

Annex 2

Proposed T-Codes for Solids not Currently Assigned T-Codes

| UN# | Name/Description | Class | PG | SR | Proposed UN T-Code | Proposed TP Note(s) |
| --- | --- | --- | --- | --- | --- | --- |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | II |  | T3 | TPXX |
| 1323 | FERROCERIUM | 4.1 | II |  | T3 | TPXX |
| 1341 | PHOSPHORUS SESQUISULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 | TPXX |
| 1343 | PHOSPHORUS TRISULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 | TPXX |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 1437 | ZIRCONIUM HYDRIDE | 4.1 | II |  | T3 | TPXX |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | II |  | T3 | TPXX |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | II | 6.1 | T3 | TPXX |
| 1868 | DECABORANE | 4.1 | II | 6.1 | T3 | TPXX |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | II | 6.1 | T3 | TPXX |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | II | 8 | T3 | TPXX |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | II | 8 | T3 | TPXX |
| 1339 | PHOSPHORUS HEPTASULPHIDE, free from yellow and white phosphorus | 4.1 | II |  | T3 | TPXX |
| 1345 | RUBBER SCRAP or RUBBER SHODDY, powdered or granulated, not exceeding 840 microns and rubber content exceeding 45% | 4.1 | II |  | T3 | TPXX |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 1326 | HAFNIUM POWDER, WETTED with not less than 25% water | 4.1 | II |  | T3 | TPXX |
| 1352 | TITANIUM POWDER, WETTED with not less than 25% water | 4.1 | II |  | T3 | TPXX |
| 1358 | ZIRCONIUM POWDER, WETTED with not less than 25% water | 4.1 | II |  | T3 | TPXX |
| 1871 | TITANIUM HYDRIDE | 4.1 | II |  | T3 | TPXX |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | II |  | T3 | TPXX |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 | III |  | T1 | TPXX |
| 1330 | MANGANESE RESINATE | 4.1 | III |  | T1 | TPXX |
| 1328 | HEXAMETHYLENETETRAMINE | 4.1 | III |  | T1 | TPXX |
| 1314 | CALCIUM RESINATE, FUSED | 4.1 | III |  | T1 | TPXX |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 2213 | PARAFORMALDEHYDE | 4.1 | III |  | T1 | TPXX |
| 1869 | MAGNESIUM or MAGNESIUM ALLOYS with more than 50% magnesium in pellets, turnings or ribbons | 4.1 | III |  | T1 | TPXX |
| 1332 | METALDEHYDE | 4.1 | III |  | T1 | TPXX |
| 2538 | NITRONAPHTHALENE | 4.1 | III |  | T1 | TPXX |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 2687 | DICYCLOHEXYLAMMONIUM NITRITE | 4.1 | III |  | T1 | TPXX |
| 2001 | COBALT NAPHTHENATES, POWDER | 4.1 | III |  | T1 | TPXX |
| 2714 | ZINC RESINATE | 4.1 | III |  | T1 | TPXX |
| 2878 | TITANIUM SPONGE GRANULES or TITANIUM SPONGE POWDERS | 4.1 | III |  | T1 | TPXX |
| 1318 | COBALT RESINATE, PRECIPITATED | 4.1 | III |  | T1 | TPXX |
| 3180 | FLAMMABLE SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.1 | III | 8 | T1 | TPXX |
| 1338 | PHOSPHORUS, AMORPHOUS | 4.1 | III |  | T1 | TPXX |
| 1313 | CALCIUM RESINATE | 4.1 | III |  | T1 | TPXX |
| 1312 | BORNEOL | 4.1 | III |  | T1 | TPXX |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 | III |  | T1 | TPXX |
| 3097 | FLAMMABLE SOLID, OXIDIZING, N.O.S. | 4.1 | III | 5.1 | T1 | TPXX |
| 2925 | FLAMMABLE SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.1 | III | 8 | T1 | TPXX |
| 3179 | FLAMMABLE SOLID, TOXIC, INORGANIC, N.O.S. | 4.1 | III | 6.1 | T1 | TPXX |
| 2717 | CAMPHOR, synthetic | 4.1 | III |  | T1 | TPXX |
| 1334 | NAPHTHALENE, CRUDE or NAPHTHALENE, REFINED | 4.1 | III |  | T1 | TPXX |
| 1346 | SILICON POWDER, AMORPHOUS | 4.1 | III |  | T1 | TPXX |
| 2715 | ALUMINIUM RESINATE | 4.1 | III |  | T1 | TPXX |
| 2926 | FLAMMABLE SOLID, TOXIC, ORGANIC, N.O.S. | 4.1 | III | 6.1 | T1 | TPXX |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 | III |  | T1 | TPXX |
| 1350 | SULPHUR | 4.1 | III |  | T1 | TPXX |
| 3254 | TRIBUTYLPHOSPHANE | 4.2 | I |  | T21 | TP 7,TPXX |
| 2881 | METAL CATALYST, DRY | 4.2 | I |  | T21 | TP 7,TPXX |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | I |  | T21 | TP 7,TPXX |
| 1854 | BARIUM ALLOYS, PYROPHORIC | 4.2 | I |  | T21 | TP 7,TPXX |
| 1383 | PYROPHORIC METAL, N.O.S. or PYROPHORIC ALLOY, N.O.S. | 4.2 | I |  | T21 | TP 7,TPXX |
| 3200 | PYROPHORIC SOLID, INORGANIC, N.O.S. | 4.2 | I |  | T21 | TP 7,TPXX |
| 2870 | ALUMINIUM BOROHYDRIDE | 4.2 | I | 4.3 | T21 | TP 7,TPXX |
| 3342 | XANTHATES | 4.2 | II |  | T3 | TPXX |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | II |  | T3 | TPXX |
| 1369 | p-NITROSODIMETHYLANILINE | 4.2 | II |  | T3 | TPXX |
| 1385 | SODIUM SULPHIDE, ANHYDROUS or SODIUM SULPHIDE with less than 30% water of crystallization | 4.2 | II |  | T3 | TPXX |
| 2940 | 9-PHOSPHABICYCLONONANES (CYCLOOCTADIENE PHOSPHINES) | 4.2 | II |  | T3 | TPXX |
| 2318 | SODIUM HYDROSULPHIDE with less than 25% water of crystallization | 4.2 | II |  | T3 | TPXX |
| 1923 | CALCIUM DITHIONITE (CALCIUM HYDROSULPHITE) | 4.2 | II |  | T3 | TPXX |
| 1374 | FISH MEAL (FISH SCRAP), UNSTABILIZED | 4.2 | II |  | T3 | TPXX |
| 1431 | SODIUM METHYLATE | 4.2 | II | 8 | T3 | TPXX |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | II | 8 | T3 | TPXX |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | II | 8 | T3 | TPXX |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | II | 6.1 | T3 | TPXX |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | II | 6.1 | T3 | TPXX |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | II | 5.1 | T3 | TPXX |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | II | 8 | T3 | TPXX |
| 1929 | POTASSIUM DITHIONITE (POTASSIUM HYDROSULPHITE) | 4.2 | II |  | T3 | TPXX |
| 2546 | TITANIUM POWDER, DRY | 4.2 | II |  | T3 | TPXX |
| 2881 | METAL CATALYST, DRY | 4.2 | II |  | T3 | TPXX |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | II |  | T3 | TPXX |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | II |  | T3 | TPXX |
| 1384 | SODIUM DITHIONITE (SODIUM HYDROSULPHITE) | 4.2 | II |  | T3 | TPXX |
| 3341 | THIOUREA DIOXIDE | 4.2 | II |  | T3 | TPXX |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 1382 | POTASSIUM SULPHIDE, ANHYDROUS or POTASSIUM SULPHIDE with less than 30% water of crystallization | 4.2 | II |  | T3 | TPXX |
| 2004 | MAGNESIUM DIAMIDE | 4.2 | II |  | T3 | TPXX |
| 1361 | CARBON, animal or vegetable origin | 4.2 | II |  | T3 | TPXX |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | II |  | T3 | TPXX |
| 1378 | METAL CATALYST, WETTED with a visible excess of liquid | 4.2 | II |  |  | TPXX |
| 3088 | SELF-HEATING SOLID, ORGANIC, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3192 | SELF-HEATING SOLID, CORROSIVE, INORGANIC, N.O.S. | 4.2 | III | 8 | T3 | TPXX |
| 3206 | ALKALI METAL ALCOHOLATES, SELF-HEATING, CORROSIVE, N.O.S. | 4.2 | III | 8 | T3 | TPXX |
| 3126 | SELF-HEATING SOLID, CORROSIVE, ORGANIC, N.O.S. | 4.2 | III | 8 | T3 | TPXX |
| 1376 | IRON OXIDE, SPENT or IRON SPONGE, SPENT obtained from coal gas purification | 4.2 | III |  | T1 | TPXX |
| 3341 | THIOUREA DIOXIDE | 4.2 | III |  | T1 | TPXX |
| 1932 | ZIRCONIUM SCRAP | 4.2 | III |  | T1 | TPXX |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGETABLE or SYNTHETIC, N.O.S. with oil | 4.2 | III |  | T1 | TPXX |
| 1361 | CARBON, animal or vegetable origin | 4.2 | III |  | T1 | TPXX |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3205 | ALKALINE EARTH METAL ALCOHOLATES, N.O.S. | 4.2 | III |  | T1 | TPXX |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | III | 5.1 | T1 | TPXX |
| 3313 | ORGANIC PIGMENTS, SELF-HEATING | 4.2 | III |  | T1 | TPXX |
| 3128 | SELF-HEATING SOLID, TOXIC, ORGANIC, N.O.S. | 4.2 | III | 6.1 | T1 | TPXX |
| 3174 | TITANIUM DISULPHIDE | 4.2 | III |  | T1 | TPXX |
| 2210 | MANEB or MANEB PREPARATION with not less than 60% maneb | 4.2 | III | 4.3 | T1 | TPXX |
| 3342 | XANTHATES | 4.2 | III |  | T1 | TPXX |
| 1362 | CARBON, ACTIVATED | 4.2 | III |  | T1 | TPXX |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 | III |  | T1 | TPXX |
| 2545 | HAFNIUM POWDER, DRY | 4.2 | III |  | T1 | TPXX |
| 2546 | TITANIUM POWDER, DRY | 4.2 | III |  | T1 | TPXX |
| 2881 | METAL CATALYST, DRY | 4.2 | III |  | T1 | TPXX |
| 3191 | SELF-HEATING SOLID, TOXIC, INORGANIC, N.O.S. | 4.2 | III | 6.1 | T1 | TPXX |
| 1422 | POTASSIUM SODIUM ALLOYS | 4.3 | I |  | T9 | TP3, TP7 |
| 1428 | SODIUM | 4.3 | I |  | T9 | TP 3, TP7 |
| 2257 | POTASSIUM | 4.3 | I |  | T9 | TP3, TP7 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | T3 | TPXX |
| 1400 | BARIUM | 4.3 | II |  | T3 | TPXX |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | II | 8 | T3 | TPXX |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | II | 6.1 | T3 | TPXX |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | II | 6.1 | T3 | TPXX |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | II | 4.2 | T3 | TPXX |
| 1401 | CALCIUM | 4.3 | II |  | T3 | TPXX |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | T3 | TPXX |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | T3 | TPXX |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 1405 | CALCIUM SILICIDE | 4.3 | II |  | T3 | TPXX |
| 2624 | MAGNESIUM SILICIDE | 4.3 | II |  | T3 | TPXX |
| 2830 | LITHIUM FERROSILICON | 4.3 | II |  | T3 | TPXX |
| 2835 | SODIUM ALUMINIUM HYDRIDE | 4.3 | II |  | T3 | TPXX |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | II |  | T3 | TPXX |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | T3 | TPXX |
| 3078 | CERIUM, turnings or gritty powder | 4.3 | II |  | T3 | TPXX |
| 1394 | ALUMINIUM CARBIDE | 4.3 | II |  | T3 | TPXX |
| 2805 | LITHIUM HYDRIDE, FUSED SOLID | 4.3 | II |  | T3 | TPXX |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | II |  | T3 | TPXX |
| 1390 | ALKALI METAL AMIDES | 4.3 | II |  | T3 | TPXX |
| 1402 | CALCIUM CARBIDE | 4.3 | II |  | T3 | TPXX |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | II |  | T3 | TPXX |
| 1417 | LITHIUM SILICON | 4.3 | II |  | T3 | TPXX |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | II | 4.2 | T3 | TPXX |
| 1340 | PHOSPHORUS PENTASULPHIDE, free from yellow and white phosphorus | 4.3 | II | 4.1 | T3 | TPXX |
| 1405 | CALCIUM SILICIDE | 4.3 | III |  | T1 | TPXX |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | III |  | T1 | TPXX |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 | III |  | T1 | TPXX |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 | III |  | T1 | TPXX |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 | III |  | T1 | TPXX |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | III |  | T1 | TPXX |
| 3372 | ORGANOMETALLIC COMPOUND, SOLID, WATER-REACTIVE, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | T1 | TPXX |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | III |  | T1 | TPXX |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | III | 4.2 | T1 | TPXX |
| 1435 | ZINC ASHES | 4.3 | III |  | T1 | TPXX |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | III | 8 | T1 | TPXX |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | III |  | T1 | TPXX |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 | III |  | T1 | TPXX |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | T1 | TPXX |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | T1 | TPXX |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | T1 | TPXX |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | III | 6.1 | T1 | TPXX |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | III | 6.1 | T1 | TPXX |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 | III |  | T1 | TPXX |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | III | 4.2 | T1 | TPXX |
| 1475 | MAGNESIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 1496 | SODIUM CHLORITE | 5.1 | II |  | T3 | TPXX |
| 1495 | SODIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1494 | SODIUM BROMATE | 5.1 | II |  | T3 | TPXX |
| 1473 | MAGNESIUM BROMATE | 5.1 | II |  | T3 | TPXX |
| 1472 | LITHIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1471 | LITHIUM HYPOCHLORITE, DRY or LITHIUM HYPOCHLORITE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 2468 | TRICHLOROISOCYANURIC ACID, DRY | 5.1 | II |  | T3 | TPXX |
| 2465 | DICHLOROISOCYANURIC ACID, DRY or DICHLOROISOCYANURIC ACID SALTS | 5.1 | II |  | T3 | TPXX |
| 1439 | AMMONIUM DICHROMATE | 5.1 | II |  | T3 | TPXX |
| 1462 | CHLORITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1463 | CHROMIUM TRIOXIDE, ANHYDROUS | 5.1 | II | 8 | T3 | TPXX |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1509 | STRONTIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1450 | BROMATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1457 | CALCIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1484 | POTASSIUM BROMATE | 5.1 | II |  | T3 | TPXX |
| 1485 | POTASSIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 3212 | HYPOCHLORITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 3247 | SODIUM PEROXOBORATE, ANHYDROUS | 5.1 | II |  | T3 | TPXX |
| 1490 | POTASSIUM PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 1489 | POTASSIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1488 | POTASSIUM NITRITE | 5.1 | II |  | T3 | TPXX |
| 1493 | SILVER NITRATE | 5.1 | II |  | T3 | TPXX |
| 1512 | ZINC AMMONIUM NITRITE | 5.1 | II |  | T3 | TPXX |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | II | 8 | T3 | TPXX |
| 1449 | BARIUM PEROXIDE | 5.1 | II | 6.1 | T3 | TPXX |
| 1469 | LEAD NITRATE | 5.1 | II | 6.1 | T3 | TPXX |
| 2573 | THALLIUM CHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | II | 6.1 | T3 | TPXX |
| 2741 | BARIUM HYPOCHLORITE with more than 22% available chlorine | 5.1 | II | 6.1 | T3 | TPXX |
| 2719 | BARIUM BROMATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1446 | BARIUM NITRATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1448 | BARIUM PERMANGANATE | 5.1 | II | 6.1 | T3 | TPXX |
| 2464 | BERYLLIUM NITRATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1445 | BARIUM CHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1447 | BARIUM PERCHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1470 | LEAD PERCHLORATE | 5.1 | II | 6.1 | T3 | TPXX |
| 1515 | ZINC PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1502 | SODIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1503 | SODIUM PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 2721 | COPPER CHLORATE | 5.1 | II |  | T3 | TPXX |
| 2723 | MAGNESIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1514 | ZINC NITRATE | 5.1 | II |  | T3 | TPXX |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED, or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% but not more than 10% water | 5.1 | II |  | T3 | TPXX |
| 1516 | ZINC PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1513 | ZINC CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1506 | STRONTIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1508 | STRONTIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1453 | CALCIUM CHLORITE | 5.1 | II |  | T3 | TPXX |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1487 | POTASSIUM NITRATE AND SODIUM NITRITE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 1452 | CALCIUM CHLORATE | 5.1 | II |  | T3 | TPXX |
| 1476 | MAGNESIUM PEROXIDE | 5.1 | II |  | T3 | TPXX |
| 1748 | CALCIUM HYPOCHLORITE, DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 39% available chlorine (8.8% available oxygen) | 5.1 | II |  | T3 | TPXX |
| 1456 | CALCIUM PERMANGANATE | 5.1 | II |  | T3 | TPXX |
| 2626 | CHLORIC ACID, AQUEOUS SOLUTION with not more than 10% chloric acid | 5.1 | II |  | T3 | TPXX |
| 2627 | NITRITES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | II |  | T3 | TPXX |
| 1455 | CALCIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1442 | AMMONIUM PERCHLORATE | 5.1 | II |  | T3 | TPXX |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE | 5.1 | II |  | T3 | TPXX |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1466 | FERRIC NITRATE | 5.1 | III |  | T1 | TPXX |
| 1492 | POTASSIUM PERSULPHATE | 5.1 | III |  | T1 | TPXX |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 | III |  | T1 | TPXX |
| 2208 | CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 10% but not more than 39% available chlorine | 5.1 | III |  | T1 | TPXX |
| 1444 | AMMONIUM PERSULPHATE | 5.1 | III |  | T1 | TPXX |
| 1465 | DIDYMIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1438 | ALUMINIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1505 | SODIUM PERSULPHATE | 5.1 | III |  | T1 | TPXX |
| 2469 | ZINC BROMATE | 5.1 | III |  | T1 | TPXX |
| 2726 | NICKEL NITRITE | 5.1 | III |  | T1 | TPXX |
| 1451 | CAESIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1474 | MAGNESIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1499 | SODIUM NITRATE AND POTASSIUM NITRATE MIXTURE | 5.1 | III |  | T1 | TPXX |
| 2720 | CHROMIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1507 | STRONTIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1511 | UREA HYDROGEN PEROXIDE | 5.1 | III | 8 | T1 | TPXX |
| 3085 | OXIDIZING SOLID, CORROSIVE, N.O.S. | 5.1 | III | 8 | T1 | TPXX |
| 3087 | OXIDIZING SOLID, TOXIC, N.O.S. | 5.1 | III | 6.1 | T1 | TPXX |
| 1500 | SODIUM NITRITE | 5.1 | III | 6.1 | T1 | TPXX |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1481 | PERCHLORATES, INORGANIC, N.O.S | 5.1 | III |  | T1 | TPXX |
| 2722 | LITHIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1486 | POTASSIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 2724 | MANGANESE NITRATE | 5.1 | III |  | T1 | TPXX |
| 2725 | NICKEL NITRATE | 5.1 | III |  | T1 | TPXX |
| 1498 | SODIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1872 | LEAD DIOXIDE | 5.1 | III |  | T1 | TPXX |
| 2728 | ZIRCONIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1454 | CALCIUM NITRATE | 5.1 | III |  | T1 | TPXX |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | III |  | T1 | TPXX |
| 1467 | GUANIDINE NITRATE | 5.1 | III |  | T1 | TPXX |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE | 5.1 | III |  | T1 | TPXX |
| 3110 | ORGANIC PEROXIDE TYPE F, SOLID | 5.2 | II |  | T23 | TPXX |
| 3120 | ORGANIC PEROXIDE TYPE F, SOLID, TEMPERATURE CONTROLLED | 5.2 | II |  | T23 | TPXX |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1575 | CALCIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 2642 | FLUOROACETIC ACID | 6.1 | I |  | T6 | TPXX |
| 2630 | SELENATES or SELENITES | 6.1 | I |  | T6 | TPXX |
| 2629 | SODIUM FLUOROACETATE | 6.1 | I |  | T6 | TPXX |
| 2628 | POTASSIUM FLUOROACETATE | 6.1 | I |  | T6 | TPXX |
| 1698 | DIPHENYLAMINE CHLOROARSINE | 6.1 | I |  | T6 | TPXX |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1570 | BRUCINE | 6.1 | I |  | T6 | TPXX |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1565 | BARIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3048 | ALUMINIUM PHOSPHIDE PESTICIDE | 6.1 | I |  | T6 | TPXX |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1889 | CYANOGEN BROMIDE | 6.1 | I | 8 | T6 | TPXX |
| 1699 | DIPHENYLCHLOROARSINE, SOLID | 6.1 | I |  | T6 | TPXX |
| 2570 | CADMIUM COMPOUND | 6.1 | I |  | T6 | TPXX |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | I | 8 | T6 | TPXX |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | I | 8 | T6 | TPXX |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | I | 5.1 | T6 | TPXX |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | I | 4.3 | T6 | TPXX |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | 6.1 | I | 4.1 | T6 | TPXX |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1692 | STRYCHNINE or STRYCHNINE SALTS | 6.1 | I |  | T6 | TPXX |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | I | 4.2 | T6 | TPXX |
| 2471 | OSMIUM TETROXIDE | 6.1 | I |  | T6 | TPXX |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1713 | ZINC CYANIDE | 6.1 | I |  | T6 | TPXX |
| 1626 | MERCURIC POTASSIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 2316 | SODIUM CUPROCYANIDE, SOLID | 6.1 | I |  | T6 | TPXX |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | I |  | T6 | TPXX |
| 1680 | POTASSIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 1689 | SODIUM CYANIDE | 6.1 | I |  | T6 | TPXX |
| 1694 | BROMOBENZYL CYANIDES, SOLID | 6.1 | I |  | T6 | TPXX |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | I |  | T6 | TPXX |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | I |  | T6 | TPXX |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | I |  | T6 | TPXX |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2567 | SODIUM PENTACHLOROPHENATE | 6.1 | II |  | T3 | TPXX |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1678 | POTASSIUM ARSENITE | 6.1 | II |  | T3 | TPXX |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2671 | AMINOPYRIDINES (o-, m-, p,) | 6.1 | II |  | T3 | TPXX |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2657 | SELENIUM DISULPHIDE | 6.1 | II |  | T3 | TPXX |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1636 | MERCURY CYANIDE | 6.1 | II |  | T3 | TPXX |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 2863 | SODIUM AMMONIUM VANADATE | 6.1 | II |  | T3 | TPXX |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | 6.1 | II | 5.1 | T3 | TPXX |
| 2859 | AMMONIUM METAVANADATE | 6.1 | II |  | T3 | TPXX |
| 1651 | NAPHTHYLTHIOUREA | 6.1 | II |  | T3 | TPXX |
| 2673 | 2-AMINO-4-CHLOROPHENOL | 6.1 | II |  | T3 | TPXX |
| 2931 | VANADYL SULPHATE | 6.1 | II |  | T3 | TPXX |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2587 | BENZOQUINONE | 6.1 | II |  | T3 | TPXX |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2645 | PHENACYL BROMIDE | 6.1 | II |  | T3 | TPXX |
| 2647 | MALONONITRILE | 6.1 | II |  | T3 | TPXX |
| 2861 | AMMONIUM POLYVANADATE | 6.1 | II |  | T3 | TPXX |
| 2649 | 1,3-DICHLOROACETONE | 6.1 | II |  | T3 | TPXX |
| 2570 | CADMIUM COMPOUND | 6.1 | II |  | T3 | TPXX |
| 1617 | LEAD ARSENATES | 6.1 | II |  | T3 | TPXX |
| 1684 | SILVER CYANIDE | 6.1 | II |  | T3 | TPXX |
| 2027 | SODIUM ARSENITE, SOLID | 6.1 | II |  | T3 | TPXX |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1679 | POTASSIUM CUPROCYANIDE | 6.1 | II |  | T3 | TPXX |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | II | 4.2 | T3 | TPXX |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S | 6.1 | II | 4.1 | T3 | TPXX |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | II | 4.3 | T3 | TPXX |
| 1895 | PHENYLMERCURIC NITRATE | 6.1 | II |  | T3 | TPXX |
| 2727 | THALLIUM NITRATE | 6.1 | II | 5.1 | T3 | TPXX |
| 1751 | CHLOROACETIC ACID, SOLID | 6.1 | II | 8 | T3 | TPXX |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | 6.1 | II | 8 | T3 | TPXX |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | 6.1 | II | 8 | T3 | TPXX |
| 1567 | BERYLLIUM POWDER | 6.1 | II | 4.1 | T3 | TPXX |
| 1885 | BENZIDINE | 6.1 | II |  | T3 | TPXX |
| 1704 | TETRAETHYL DITHIOPYROPHOSPHATE | 6.1 | II |  | T3 | TPXX |
| 1691 | STRONTIUM ARSENITE | 6.1 | II |  | T3 | TPXX |
| 1707 | THALLIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1712 | ZINC ARSENATE, ZINC ARSENITE or ZINC ARSENATE AND ZINC ARSENITE MIXTURE | 6.1 | II |  | T3 | TPXX |
| 2864 | POTASSIUM METAVANADATE | 6.1 | II |  | T3 | TPXX |
| 1688 | SODIUM CACODYLATE | 6.1 | II |  | T3 | TPXX |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1685 | SODIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1894 | PHENYLMERCURIC HYDROXIDE | 6.1 | II |  | T3 | TPXX |
| 1639 | MERCURY NUCLEATE | 6.1 | II |  | T3 | TPXX |
| 1693 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1683 | SILVER ARSENITE | 6.1 | II |  | T3 | TPXX |
| 3155 | PENTACHLOROPHENOL | 6.1 | II |  | T3 | TPXX |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1665 | NITROXYLENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1586 | COPPER ARSENITE | 6.1 | II |  | T3 | TPXX |
| 1587 | COPPER CYANIDE | 6.1 | II |  | T3 | TPXX |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1590 | DICHLOROANILINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1597 | DINITROBENZENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1606 | FERRIC ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1653 | NICKEL CYANIDE | 6.1 | II |  | T3 | TPXX |
| 1674 | PHENYLMERCURIC ACETATE | 6.1 | II |  | T3 | TPXX |
| 1658 | NICOTINE SULPHATE, SOLID | 6.1 | II |  | T3 | TPXX |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1585 | COPPER ACETOARSENITE | 6.1 | II |  | T3 | TPXX |
| 1656 | NICOTINE HYDROCHLORIDE, solid | 6.1 | II |  | T3 | TPXX |
| 1657 | NICOTINE SALICYLATE | 6.1 | II |  | T3 | TPXX |
| 1652 | NAPHTHYLUREA | 6.1 | II |  | T3 | TPXX |
| 1638 | MERCURY IODIDE | 6.1 | II |  | T3 | TPXX |
| 1637 | MERCURY GLUCONATE | 6.1 | II |  | T3 | TPXX |
| 1607 | FERRIC ARSENITE | 6.1 | II |  | T3 | TPXX |
| 1634 | MERCURY BROMIDES | 6.1 | II |  | T3 | TPXX |
| 1608 | FERROUS ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1630 | MERCURY AMMONIUM CHLORIDE | 6.1 | II |  | T3 | TPXX |
| 1629 | MERCURY ACETATE | 6.1 | II |  | T3 | TPXX |
| 1627 | MERCUROUS NITRATE | 6.1 | II |  | T3 | TPXX |
| 1625 | MERCURIC NITRATE | 6.1 | II |  | T3 | TPXX |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 1620 | LEAD CYANIDE | 6.1 | II |  | T3 | TPXX |
| 1664 | NITROTOLUENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1642 | MERCURY OXYCYANIDE, DESENSITIZED | 6.1 | II |  | T3 | TPXX |
| 1572 | CACODYLIC ACID | 6.1 | II |  | T3 | TPXX |
| 1631 | MERCURY BENZOATE | 6.1 | II |  | T3 | TPXX |
| 1646 | MERCURY THIOCYANATE | 6.1 | II |  | T3 | TPXX |
| 1645 | MERCURY SULPHATE | 6.1 | II |  | T3 | TPXX |
| 1644 | MERCURY SALICYLATE | 6.1 | II |  | T3 | TPXX |
| 1677 | POTASSIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1643 | MERCURY POTASSIUM IODIDE | 6.1 | II |  | T3 | TPXX |
| 1624 | MERCURIC CHLORIDE | 6.1 | II |  | T3 | TPXX |
| 1641 | MERCURY OXIDE | 6.1 | II |  | T3 | TPXX |
| 1574 | CALCIUM ARSENATE AND CALCIUM ARSENITE MIXTURE, SOLID | 6.1 | II |  | T3 | TPXX |
| 1623 | MERCURIC ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1659 | NICOTINE TARTRATE | 6.1 | II |  | T3 | TPXX |
| 1622 | MAGNESIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1621 | LONDON PURPLE | 6.1 | II |  | T3 | TPXX |
| 1640 | MERCURY OLEATE | 6.1 | II |  | T3 | TPXX |
| 1611 | HEXAETHYL TETRAPHOSPHATE | 6.1 | II |  | T3 | TPXX |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1573 | CALCIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1618 | LEAD ARSENITES | 6.1 | II |  | T3 | TPXX |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 1562 | ARSENICAL DUST | 6.1 | II |  | T3 | TPXX |
| 1561 | ARSENIC TRIOXIDE | 6.1 | II |  | T3 | TPXX |
| 1559 | ARSENIC PENTOXIDE | 6.1 | II |  | T3 | TPXX |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | II |  | T3 | TPXX |
| 1555 | ARSENIC BROMIDE | 6.1 | II |  | T3 | TPXX |
| 1554 | ARSENIC ACID, SOLID | 6.1 | II |  | T3 | TPXX |
| 1558 | ARSENIC | 6.1 | II |  | T3 | TPXX |
| 1546 | AMMONIUM ARSENATE | 6.1 | II |  | T3 | TPXX |
| 1577 | CHLORODINITROBENZENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1578 | CHLORONITROBENZENES, solid | 6.1 | II |  | T3 | TPXX |
| 1596 | DINITROANILINES | 6.1 | II |  | T3 | TPXX |
| 1650 | beta-NAPHTHYLAMINE | 6.1 | II |  | T3 | TPXX |
| 1661 | NITROANILINES (o-, m-, p-) | 6.1 | II |  | T3 | TPXX |
| 1671 | PHENOL, SOLID | 6.1 | II |  | T3 | TPXX |
| 1708 | TOLUIDINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1711 | XYLIDINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 1843 | AMMONIUM DINITRO-o-CRESOLATE | 6.1 | II |  | T3 | TPXX |
| 2018 | CHLOROANILINES, SOLID | 6.1 | II |  | T3 | TPXX |
| 2038 | DINITROTOLUENES, SOLID | 6.1 | II |  | T3 | TPXX |
| 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE | 6.1 | II |  | T3 | TPXX |
| 2261 | XYLENOLS, solid | 6.1 | II |  | T3 | TPXX |
| 2306 | NITROBENZOTRIFLUORIDES, solid | 6.1 | II |  | T3 | TPXX |
| 2669 | CHLOROCRESOLS, solid | 6.1 | II |  | T3 | TPXX |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | II |  | T3 | TPXX |
| 3243 | SOLIDS CONTAINING TOXIC LIQUID, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | II |  | T3 | TPXX |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | II |  | T3 | TPXX |
| 2076 | CRESOLS, SOLID | 6.1 | II | 8 | T3 | TPXX |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2862 | VANADIUM PENTOXIDE, non-fused form | 6.1 | III |  | T1 | TPXX |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2871 | ANTIMONY POWDER | 6.1 | III |  | T1 | TPXX |
| 2875 | HEXACHLOROPHENE | 6.1 | III |  | T1 | TPXX |
| 2876 | RESORCINOL | 6.1 | III |  | T1 | TPXX |
| 2853 | MAGNESIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2855 | ZINC FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1550 | ANTIMONY LACTATE | 6.1 | III |  | T1 | TPXX |
| 2854 | AMMONIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 1548 | ANILINE HYDROCHLORIDE | 6.1 | III |  | T1 | TPXX |
| 1551 | ANTIMONY POTASSIUM TARTRATE | 6.1 | III |  | T1 | TPXX |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2570 | CADMIUM COMPOUND | 6.1 | III |  | T1 | TPXX |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2716 | 1,4-BUTYNEDIOL | 6.1 | III |  | T1 | TPXX |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2516 | CARBON TETRABROMIDE | 6.1 | III |  | T1 | TPXX |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2783 | ORGANOPHOSPHORUS PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE | 6.1 | III |  | T1 | TPXX |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2713 | ACRIDINE | 6.1 | III |  | T1 | TPXX |
| 2674 | SODIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 2660 | NITROTOLUIDINES (MONO) | 6.1 | III |  | T1 | TPXX |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2659 | SODIUM CHLOROACETATE | 6.1 | III |  | T1 | TPXX |
| 2655 | POTASSIUM FLUOROSILICATE | 6.1 | III |  | T1 | TPXX |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 2233 | CHLOROANISIDINES | 6.1 | III |  | T1 | TPXX |
| 2512 | AMINOPHENOLS (o-, m-, p-) | 6.1 | III |  | T1 | TPXX |
| 2505 | AMMONIUM FLUORIDE | 6.1 | III |  | T1 | TPXX |
| 2473 | SODIUM ARSANILATE | 6.1 | III |  | T1 | TPXX |
| 2446 | NITROCRESOLS | 6.1 | III |  | T1 | TPXX |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2237 | CHLORONITROANILINES | 6.1 | III |  | T1 | TPXX |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | III |  | T1 | TPXX |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2020 | CHLOROPHENOLS, SOLID | 6.1 | III |  | T1 | TPXX |
| 1884 | BARIUM OXIDE | 6.1 | III |  | T1 | TPXX |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 2433 | CHLORONITROTOLUENES, SOLID | 6.1 | III |  | T1 | TPXX |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 1616 | LEAD ACETATE | 6.1 | III |  | T1 | TPXX |
| 1663 | NITROPHENOLS (o-, m-, p-) | 6.1 | III |  | T1 | TPXX |
| 1673 | PHENYLENEDIAMINES (o-, m-, p-) | 6.1 | III |  | T1 | TPXX |
| 1690 | SODIUM FLUORIDE | 6.1 | III |  | T1 | TPXX |
| 1709 | 2,4-TOLUYLENEDIAMINE | 6.1 | III |  | T1 | TPXX |
| 1812 | POTASSIUM FLUORIDE | 6.1 | III |  | T1 | TPXX |
| 2074 | ACRYLAMIDE | 6.1 | III |  | T1 | TPXX |
| 2235 | CHLOROBENZYL CHLORIDES | 6.1 | III |  | T1 | TPXX |
| 2239 | CHLOROTOLUIDINES, solid | 6.1 | III |  | T1 | TPXX |
| 2651 | 4,4'-DIAMINODIPHENYLMETHANE | 6.1 | III |  | T1 | TPXX |
| 2662 | HYDROQUINONE | 6.1 | III |  | T1 | TPXX |
| 2729 | HEXACHLOROBENZENE | 6.1 | III |  | T1 | TPXX |
| 2730 | NITROANISOLES, SOLID | 6.1 | III |  | T1 | TPXX |
| 2732 | NITROBROMOBENZENES, SOLID | 6.1 | III |  | T1 | TPXX |
| 2753 | N-ETHYLBENZYLTOLUIDINES, SOLID | 6.1 | III |  | T1 | TPXX |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 | III |  | T1 | TPXX |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3280 | ORGANOARSENIC COMPOUND, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3281 | METAL CARBONYLS, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, N.O.S., solid | 6.1 | III |  | T1 | TPXX |
| 3283 | SELENIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | III |  | T1 | TPXX |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | I |  | T6 | TPXX |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | I |  | T6 | TPXX |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | I | 5.1 | T6 | TPXX |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | I |  | T6 | TPXX |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | I | 6.1 | T6 | TPXX |
| 1905 | SELENIC ACID | 8 | I |  | T6 | TPXX |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | I | 4.3 | T6 | TPXX |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | I | 4.1 | T6 | TPXX |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | I |  | T6 | TPXX |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | I |  | T6 | TPXX |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | II |  | T3 | TPXX |
| 2680 | LITHIUM HYDROXIDE MONOHYDRATE | 8 | II |  | T3 | TPXX |
| 2682 | CAESIUM HYDROXIDE | 8 | II |  | T3 | TPXX |
| 2691 | PHOSPHORUS PENTABROMIDE | 8 | II |  | T3 | TPXX |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | II |  | T3 | TPXX |
| 2583 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with more than 5% free sulphuric acid | 8 | II |  | T3 | TPXX |
| 2678 | RUBIDIUM HYDROXIDE | 8 | II |  | T3 | TPXX |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 1756 | CHROMIC FLUORIDE, SOLID | 8 | II |  | T3 | TPXX |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | II |  | T3 | TPXX |
| 1839 | TRICHLOROACETIC ACID | 8 | II |  | T3 | TPXX |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | II |  | T3 | TPXX |
| 2033 | POTASSIUM MONOXIDE | 8 | II |  | T3 | TPXX |
| 1794 | LEAD SULPHATE with more than 3% free acid | 8 | II |  | T3 | TPXX |
| 1847 | POTASSIUM SULPHIDE, HYDRATED with not less than 30% water of crystallization | 8 | II |  | T3 | TPXX |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | II |  | T3 | TPXX |
| 1770 | DIPHENYLMETHYL BROMIDE | 8 | II |  | T3 | TPXX |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | II | 6.1 | T3 | TPXX |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | 8 | II | 5.1 | T3 | TPXX |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | II | 4.3 | T3 | TPXX |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | II | 4.2 | T3 | TPXX |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | 8 | II | 4.1 | T3 | TPXX |
| 1806 | PHOSPHORUS PENTACHLORIDE | 8 | II |  | T3 | TPXX |
| 1725 | ALUMINIUM BROMIDE, ANHYDROUS | 8 | II |  | T3 | TPXX |
| 2670 | CYANURIC CHLORIDE | 8 | II |  | T3 | TPXX |
| 2506 | AMMONIUM HYDROGEN SULPHATE | 8 | II |  | T3 | TPXX |
| 1825 | SODIUM MONOXIDE | 8 | II |  | T3 | TPXX |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | II |  | T3 | TPXX |
| 2509 | POTASSIUM HYDROGEN SULPHATE | 8 | II |  | T3 | TPXX |
| 1813 | POTASSIUM HYDROXIDE, SOLID | 8 | II |  | T3 | TPXX |
| 1823 | SODIUM HYDROXIDE, SOLID | 8 | II |  | T3 | TPXX |
| 1727 | AMMONIUM HYDROGENDIFLUORIDE, SOLID | 8 | II |  | T3 | TPXX |
| 1726 | ALUMINIUM CHLORIDE, ANHYDROUS | 8 | II |  | T3 | TPXX |
| 1807 | PHOSPHORUS PENTOXIDE | 8 | II |  | T3 | TPXX |
| 1939 | PHOSPHORUS OXYBROMIDE | 8 | II |  | T3 | TPXX |
| 2308 | NITROSYLSULPHURIC ACID, SOLID | 8 | II |  | T3 | TPXX |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | II |  | T3 | TPXX |
| 2439 | SODIUM HYDROGENDIFLUORIDE | 8 | II |  | T3 | TPXX |
| 3244 | SOLIDS CONTAINING CORROSIVE LIQUID, N.O.S. | 8 | II |  | T3 | TPXX |
| 2508 | MOLYBDENUM PENTACHLORIDE | 8 | III |  | T1 | TPXX |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 1805 | PHOSPHORIC ACID, SOLID | 8 | III |  | T1 | TPXX |
| 3253 | DISODIUM TRIOXOSILICATE | 8 | III |  | T1 | TPXX |
| 1773 | FERRIC CHLORIDE, ANHYDROUS | 8 | III |  | T1 | TPXX |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 | III |  | T1 | TPXX |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | III |  | T1 | TPXX |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 | III |  | T1 | TPXX |
| 1907 | SODA LIME with more than 4% sodium hydroxide | 8 | III |  | T1 | TPXX |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 | III |  | T1 | TPXX |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | III | 6.1 | T1 | TPXX |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 | III |  | T1 | TPXX |
| 2578 | PHOSPHORUS TRIOXIDE | 8 | III |  | T1 | TPXX |
| 2905 | CHLOROPHENOLATES, SOLID or PHENOLATES, SOLID | 8 | III |  | T1 | TPXX |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 | III |  | T1 | TPXX |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 | III |  | T1 | TPXX |
| 2865 | HYDROXYLAMINE SULPHATE | 8 | III |  | T1 | TPXX |
| 2802 | COPPER CHLORIDE | 8 | III |  | T1 | TPXX |
| 2507 | CHLOROPLATINIC ACID, SOLID | 8 | III |  | T1 | TPXX |
| 2503 | ZIRCONIUM TETRACHLORIDE | 8 | III |  | T1 | TPXX |
| 2475 | VANADIUM TRICHLORIDE | 8 | III |  | T1 | TPXX |
| 2331 | ZINC CHLORIDE, ANHYDROUS | 8 | III |  | T1 | TPXX |
| 1910 | CALCIUM OXIDE | 8 | III |  | T1 | TPXX |
| 2698 | TETRAHYDROPHTHALIC ANHYDRIDES with more than 0.05% of maleic anhydride | 8 | III |  | T1 | TPXX |
| 2967 | SULPHAMIC ACID | 8 | III |  | T1 | TPXX |
| 2812 | SODIUM ALUMINATE, SOLID | 8 | III |  | T1 | TPXX |
| 2803 | GALLIUM | 8 | III |  | T1 | TPXX |
| 2440 | STANNIC CHLORIDE PENTAHYDRATE | 8 | III |  | T1 | TPXX |
| 2214 | PHTHALIC ANHYDRIDE with more than 0.05% of maleic anhydride | 8 | III |  | T1 | TPXX |
| 2215 | MALEIC ANHYDRIDE | 8 | III |  | T1 | TPXX |
| 2280 | HEXAMETHYLENEDIAMINE, SOLID | 8 | III |  | T1 | TPXX |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | III |  | T1 | TPXX |
| 2511 | 2-CHLOROPROPIONIC ACID, SOLID | 8 | III |  | T1 | TPXX |
| 2579 | PIPERAZINE | 8 | III |  | T1 | TPXX |
| 2823 | CROTONIC ACID | 8 | III |  | T1 | TPXX |
| 2834 | PHOSPHOROUS ACID | 8 | III |  | T1 | TPXX |
| 3335 | AVIATION REGULATED SOLID, N.O.S. | 9 |  |  | T1 | TPXX |
| 2969 | CASTOR BEANS or CASTOR MEAL or CASTOR POMACE or CASTOR FLAKE | 9 | II |  | T3 | TPXX |
| 2212 | BLUE ASBESTOS (crocidolite) or BROWN ASBESTOS (amosite, mysorite) | 9 | II |  | T3 | TPXX |
| 3152 | POLYHALOGENATED BIPHENYLS, SOLID or POLYHALOGENATED TERPHENYLS, SOLID | 9 | II |  | T3 | TPXX |
| 2590 | WHITE ASBESTOS (chrysotile, actinolite, anthophyllite, tremolite) | 9 | III |  | T1 | TPXX |
| 2216 | FISH MEAL (FISH SCRAP), STABILIZED | 9 | III |  | T1 | TPXX |
| 1931 | ZINC DITHIONITE (ZINC HYDROSULPHITE) | 9 | III |  | T1 | TPXX |
| 1841 | ACETALDEHYDE AMMONIA | 9 | III |  | T1 | TPXX |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S. | 9 | III |  | T1 | TPXX |
| 2211 | POLYMERIC BEADS, EXPANDABLE, evolving flammable vapour | 9 | III |  | T1 | TPXX |

Annex 3

Currently assigned tank provisions that would need to be changed in the Model Regulations based on the rationalized approach

| UN# | Name | Class | PG | Sub-Risk | EXISTING | PROPOSED |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | TI | TP | TI | TP |
| 1445 | BARIUM CHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 | TPXX |
| 1447 | BARIUM PERCHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 | TPXX |
| 1470 | LEAD PERCHLORATE | 5.1 | II | 6.1 | T4 | TP1 | T3 | TPXX |
| 1811 | POTASSIUM HYDROGENDIFLUORIDE | 8 | II | 6.1 | T7 | TP2 | T3 | TPXX |
| 2076 | CRESOLS, SOLID | 6.1 | II | 8 | T7 | TP2 | T3 | TPXX |

-----

# Text boxes

NATIONS

UNIES

## Secrétariat

ST