#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.4/2002/15/Add.1

24 September 2002

# ENGLISH ONLY

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

##### Sub-Committee of Experts on the

# Transport of Dangerous Goods

# (Fourth session, 9-11 December 2002,

# agenda item 3 )

PROGRAMME OF WORK FOR THE BIENNIUM

Decision logic Hazard Statements - Precautionary Statements

Transmitted by the experts from Austria and Germany

Annex to the document ST/SG/AC.10/C.4/2002/15

EXPLOSIVES

Division 1.1	Explosive; mass explosion hazard

#### Division 1.2		Explosive; severe projection hazard

Division 1.3	Explosive; fire, blast or projection hazard

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace | Keep away from heat. Keep away from sources of ignition - No smoking. Keep at temperature not exceeding ...°C (to be specified by the manufacturer). Keep wetted with ... (appropriate material to be specified by the manufacturer). | Store and transport according to packing list of dangerous chemicals. Keep away from [fire] [sources of ignition]. |
| use/private | not allowed |  |
| use/occupational | Handle and open container with care. | Avoid [shock] [impact] [friction] [rough handling]. No [open flames] [sparks] [smoking]. Do not use sparking tools. Do not use compressed air for filling, discharging or handling. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

EXPLOSIVES

Division 1.4	Fire or projection hazard

Division 1.5	May explode in fire

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace | Keep away from sources of ignition - No smoking. | Store and transport according to packing list of dangerous chemicals. Keep away from [fire] [sources of ignition]. |
| use/private | not allowed |  |
| use/occupational |  | No [open flames] [sparks] [smoking]. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

FLAMMABLE GASES

Extremely flammable gas

Flammable gas

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep container in a well-ventilated place. | Keep out of the reach of children. Keep container/package in a well-ventilated place. Keep from direct sunlight. |
| storage/workplace | Keep container in a well-ventilated place. | Keep container/package [closed] [in a well-ventilated place]. Keep [in a cool place] [from direct sunlight] [at a temperature not exceeding ….°C]. |
| use/private | Keep away from sources of ignition - No smoking | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| use/occupational | Keep away from sources of ignition - No smoking. Take precautionary measures against static discharges | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. Take precautionary measures against static charges. Do not use sparking tools. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

FLAMMABLE AEROSOLS

Extremely flammable aerosol

Flammable aerosol

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. Keep from direct sunlight. |
| storage/workplace |  | Keep in a cool place. Keep at a temperature not exceeding ….°C. |
| use/private | Keep away from sources of ignition - No smoking | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| use/occupational | Keep away from sources of ignition - No smoking. Take precautionary measures against static discharges | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. Take precautionary measures against static charges. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | This material and its container must be disposed of as hazardous waste |  |

OXIDIZING GASES

May cause or intensify fire; oxidizer

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  | Separate from [reducers] [halogens] [acids] [flammable/ combustible materials] [finely powdered metals] etc in storage and transport. |
| use/private | Keep away from combustible materials | Keep away from combustible material. |
| use/occupational | Keep away from combustible materials | Keep away from [combustible material] [(incompatible material to be specified by manufacturer)]. Keep from contact with clothing and other combustible materials to avoid fire. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

OXIDIZING SOLIDS

May cause fire or explosion; strong oxidizer

May intensify fire; oxidizer

May intensify fire; oxidizer

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep container tightly closed. | Keep out of the reach of children. |
| storage/workplace | Keep container tightly closed. | Separate from [reducers] [halogens] [acids] [flammable/combustible materials] [finely powdered metals] etc in storage and transport. |
| use/private | Keep away from combustible materials Handle and open container with care. | Keep away from combustible material. Keep from contact with clothing and other combustible materials to avoid fire. |
| use/occupational | Keep away from combustible materials | Keep away from [combustible material] [(incompatible material to be specified by manufacturer)]. Keep from contact with clothing and other combustible materials to avoid fire. Prevent contamination with readily oxidizable materials and polymerization accelerators. |
| personal protection | Wear eye/face protection. | Wear protective eyewear (goggles, face shield, or safety glasses). |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. (This material and its container must be disposed of as hazardous waste.) |  |

OXIDIZING LIQUIDS

May cause fire or explosion; strong oxidizer

May intensify fire; oxidizer

May intensify fire; oxidizer

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep container tightly closed. | Keep out of the reach of children. |
| storage/workplace | Keep container tightly closed. | Separate from [reducers] [halogens] [acids] [flammable/combustible materials] [finely powdered metals] etc in storage and transport. |
| use/private | Keep away from combustible materials Handle and open container with care. | Keep away from combustible material. Keep from contact with clothing and other combustible materials to avoid fire. |
| use/occupational | Keep away from combustible materials | Keep away from [combustible material] [(incompatible material to be specified by manufacturer)]. Keep from contact with clothing and other combustible materials to avoid fire. Drying of this product on clothing or combustible materials may cause fire. Prevent contamination with readily oxidizable materials and polymerization accelerators. |
| personal protection | Wear eye/face protection |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. (This material and its container must be disposed of as hazardous waste.) |  |

ORGANIC PEROXIDES

Type A	May cause an explosion

Type B	May cause a fire or explosion

Type C, D, E, F	May cause a fire

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. (Keep only in the original container.) Keep container tightly closed. | Keep out of the reach of children. Keep only in the original container/package in a cool well-ventilated place. Keep container tightly closed. |
| storage/workplace | Keep container tightly closed. (Keep only in the original container.) | Keep container tightly closed. (Keep only in the original container.) Separate from [reducers] [halogens] [acids] [flammable/ combustible materials] [finely powdered metals] etc in storage and transport. |
| use/private | Handle and open container with care. | Keep away from heat. Keep away from combustible material. |
| use/occupational | Do not mix with ... (to be specified by the manufacturer). | Keep away from heat. Keep away from [combustible material] [(incompatible material to be specified by manufacturer)]. Keep from contact with clothing and other combustible materials to avoid fire. Prevent contamination with readily oxidizable materials and polymerization accelerators. |
| personal protection | Wear eye/face protection |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. (This material and its container must be disposed of as hazardous waste.) |  |

GASES UNDER PRESSURE

Compressed gas	Contains gas under pressure; may explode if heated

Liquefied gas	under pressure; may explode if heated

Refrigerated liquefied gas	Contains refrigerated gas; may cause cryogenic burns or injury

Dissolved gas	Contains gas under pressure; may explode if heated

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep in a cool place. | Keep [in a cool place] [from direct sunlight] [at a temperature not exceeding ….°C]. |
| storage/workplace |  |  |
| use/private | refrigerated liquefied gas only: Avoid contact with skin. Avoid contact with eyes. |  |
| use/occupational |  |  |
| personal protection |  |  |
| medical first aid |  |  |
| disposal |  |  |

FLAMMABLE LIQIDS

Extremely flammable liquid and vapour

Highly flammable liquid and vapour

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep container tightly closed. Keep container in a well-ventilated place. | Keep out of the reach of children. Keep container tightly closed. Keep in a well-ventilated place. |
| storage/workplace | Keep container tightly closed Keep container in a well-ventilated place. | Keep container/package [closed] [in a well-ventilated place]. Keep [in a cool place] [from direct sunlight] [at a temperature not exceeding ….°C]. |
| use/private | Keep away from sources of ignition - No smoking. In case of fire use... (indicate in the space the precise type of fire-fighting equipment. If water increases the risk add: Never use water). | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| use/occupational | Keep away from sources of ignition - No smoking. Take precautionary measures against static discharges. In case of fire use... (indicate in the space the precise type of fire-fighting equipment. If water increases the risk add: Never use water). | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. Take precautionary measures against static charges. Do not use sparking tools. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Do not empty into drains Dispose of this material and its container to .... (to be specified by the manufacturer). This material and its container must be disposed of as hazardous waste |  |

FLAMMABLE LIQIDS

Flammable liquid and vapour

Combustible liquid

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep container tightly closed. Keep container in a well-ventilated place. | Keep out of the reach of children. Keep container tightly closed. Keep in a well-ventilated place. |
| storage/workplace | Keep container tightly closed Keep container in a well-ventilated place. | Keep container/package [closed] [in a well-ventilated place]. Keep [from direct sunlight] [in a cool place]. |
| use/private | Keep away from sources of ignition - No smoking. | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| use/occupational | Keep away from sources of ignition - No smoking. | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). This material and its container must be disposed of as hazardous waste |  |

FLAMMABLE SOLIDS

Flammable solid

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. Keep container/package closed. |
| storage/workplace |  | Keep container/package closed. |
| use/private | Keep away from sources of ignition - No smoking. | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| use/occupational | Keep away from sources of ignition - No smoking. | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | This material and its container must be disposed of as hazardous waste. (in special cases) |  |

SELF-REACTIVE SUBSTANCES

Type A	Heating may cause an explosion

Type B	Heating may cause a fire or explosion

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace | Keep away from living quarters Keep container tightly closed Keep in a cool place/Keep at temperature not exceeding ...°C (to be specified by the manufacturer) | Keep at temperature not exceeding ……°C. Do not store near combustible materials. Do not store and transport with flammable/combustible materials etc. |
| use/private | not allowed |  |
| use/occupational | Keep away from sources of ignition - No smoking. | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. Keep away from (incompatible material to be specified by manufacturer). Keep from contact with clothing and other combustible materials to avoid fire. Prevent contamination with readily oxidizable materials and polymerization accelerators. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

SELF-REACTIVE SUBSTANCES

Type C, D	Heating may cause a fire

Type E, F	Heating may cause a fire

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed | Keep in a cool place. |
| storage/workplace | Keep [in a cool place] [at temperature not exceeding ...°C (to be specified by the manufacturer)] | Keep [in a cool place] [at temperature not exceeding ...°C (to be specified by the manufacturer)] Do not store near combustible materials. Do not store and transport with flammable/combustible materials etc. |
| use/private | not allowed |  |
| use/occupational | Keep away from sources of ignition - No smoking. | Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. Keep away from (incompatible material to be specified by manufacturer). |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

PYROPHORIC LIQUIDS

PYROPHORIC SOLIDS

Catches fire spontaneously if exposed to air

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace | Keep contents under...(appropriate liquid to be specified by the manufacturer ) Keep under...(inert gas to be specified by the manufacturer) | Keep under [insert name of inert gas]. |
| use/private | not allowed |  |
| use/occupational |  | Do not allow contact with air. Protect from light, moisture and damage. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal |  | This material and its container must be disposed of as hazardous waste. |

SELF-HEATING SUBSTANCES

Self-heating; may catch fire

Self-heating in large quantities; may catch fire

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | as in storage/workplace if allowed |  |
| storage/workplace | Keep away from heat. | Keep away from incompatible material [to be specified by manufacturer)]. Keep at a temperature not exceeding [ ]. |
| use/private | as in use/occupational if allowed |  |
| use/occupational |  |  |
| personal protection |  |  |
| medical first aid |  |  |
| disposal |  |  |

SUBSTANCES, WHICH IN CONTACT WITH WATER, EMIT FLAMMABLE GASES

In contact with water releases flammable gases which may ignite spontaneously

In contact with water releases flammable gases

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | as in storage/workplace if allowed |  |
| storage/workplace | Keep container tightly closed. Keep container dry. Keep container in a well-ventilated place. | Keep container dry. Store [in a dry place] [protect from moisture]. |
| use/private | as in use/occupational if allowed |  |
| use/occupational | Keep away from sources of ignition - No smoking. Never add water to this product. In case of fire use... (indicate in the space the precise type of fire-fighting equipment. If water increases the risk add: Never use water). Use only in well-ventilated areas. | Keep from any possible contact with [water] [moisture]. Never add water to this product [while in a container because of violent reaction and possible flash fire]. Protect from damage. Handle under nitrogen, [protect from moisture]. Keep away from [sparks] [open flames] [heated surfaces]. No Smoking. Take precautionary measures against static charges. Do not use sparking tools. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal |  |  |

ACUTE TOXICITY: INHALATION

Fatal if inhaled

#### Toxic if inhaled

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | as in storage/workplace if allowed |  |
| storage/workplace | Keep locked up. Keep in a cool place. Keep container in a well-ventilated place. | Keep locked up. Keep container/package in a [cool] well-ventilated place. |
| use/private | as in use/occupational if allowed |  |
| use/occupational |  | Use only with [adequate] [closed system] ventilation. Do not enter areas where used or stored until adequately ventilated. |
| personal protection | In case of insufficient ventilation wear suitable respiratory equipment. During fumigation/spraying wear suitable respiratory equipment (appropriate wording to be specified by the manufacture). | During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). Have available emergency self-contained breathing apparatus or full-face airline respirator when using this chemical. Always wear a self-contained breathing apparatus or full-face airline respirator when using this chemical. Wear a mask or pesticide respirator jointly approved by ... . |
| medical first aid | In case of accident or if you feel unwell seek medical advice immediately (show the label where possible). In case of accident by inhalation: remove casualty to fresh air and keep at rest. | In case of accident by inhalation, remove casualty to fresh air and keep at rest. In case of accident or if you feel unwell, seek medical advice immediately (show the label where possible). Have the product container or label with you when calling a poison control center or doctor, or going for treatment. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

ACUTE TOXICITY: INHALATION

Harmful if inhaled

(May be harmful if inhaled)

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep container in a well-ventilated place. | Keep out of the reach of children. Keep container in a well-ventilated place. |
| storage/workplace | Keep container in a well-ventilated place. | Keep container in a well-ventilated place. |
| use/private | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). Use only in well-ventilated areas. | Do not breathe [dust] [vapor] [spray mist]. Use only in well ventilated areas. |
| use/occupational | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). Use only in well-ventilated areas. | Use adequate ventilation to remove [vapors] [fumes] [dust] etc). Do not breathe [dust] [vapor] [spray mist]. Use only in well ventilated areas. |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

ACUTE TOXICITY: DERMAL

Fatal in contact with skin

#### Toxic in contact with skin

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | as in storage/workplace if allowed |  |
| storage/workplace | Keep locked up. | Keep locked up. |
| use/private | as in use/occupational if allowed |  |
| use/occupational |  | Wash thoroughly with soap and water after handling. Avoid contact with skin (eyes or clothing). Do not get in eyes (skin) or on clothing. |
| personal protection | Wear suitable protective clothing. Wear suitable gloves. | Wear suitable [protective clothing] [gloves] [eye/face protection]. Wear protective clothing and gloves (specify protective clothing and type of gloves). Wear appropriate personal protective equipment, avoid direct contact. |
| medical first aid | Take off immediately all contaminated clothing. After contact with skin, wash immediately with plenty of...(to be specified by the manufacturer). In case of accident or if you feel unwell seek medical advice immediately (show the label where possible) | After contact with skin, take off immediately all contaminated clothing and flush skin with fresh water. Obtain medical attention immediately. Wash contaminated clothing before reuse. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

ACUTE TOXICITY: DERMAL

Harmful in contact with skin

#### (May be harmful in contact with skin)

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private | Avoid contact with skin. | Avoid contact with skin [eyes] [clothing]. Do not get on skin [in eyes] [on clothing]. |
| use/occupational | Avoid contact with skin | Avoid contact with skin [eyes] [clothing]. Do not get on skin [in eyes] [on clothing]. |
| personal protection | Wear suitable gloves. | Wear suitable [protective clothing] [gloves] [eye/face protection]. |
| medical first aid |  | Wash the contaminated area of body with soap and fresh water. Take off contaminated clothing. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

ACUTE TOXICITY: ORAL

Fatal if swallowed

#### Toxic if swallowed

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | as in storage/workplace if allowed |  |
| storage/workplace | Keep locked up. Keep away from food, drink and animal feedingstuffs. | Keep locked up. Keep only in the original container. Keep away from food, drink, and animal feedstuffs. |
| use/private | as in use/occupational if allowed |  |
| use/occupational | When using do not eat or drink. Do not breathe dust. | When using do not [smoke] [eat] [drink]. Wash hands before [eating] [drinking] [smoking]. Wash thoroughly after handling. |
| personal protection |  |  |
| medical first aid | In case of accident or if you feel unwell seek medical advice immediately (show the label where possible) | If swallowed, [seek medical advice immediately and show this container or label]. If conscious, [rinse mouth with water] [give (fluid to be specified by manufacturer) to drink]. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

ACUTE TOXICITY: ORAL

Harmful if swallowed

#### (May be harmful) if swallowed

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. | Keep away from food, drink, and animal feedstuffs. |
| storage/workplace | Keep away from food, drink and animal feedingstuffs. | Keep away from food, drink, and animal feedstuffs. |
| use/private | When using do not eat or drink. | When using do not [eat] [drink]. Wash hands before [eating] [drinking] [smoking]. Wash thoroughly after handling. |
| use/occupational |  |  |
| personal protection |  |  |
| medical first aid | If swallowed, seek medical advice immediately and show this container or label. | If swallowed, seek medical advice immediately and show this container or label. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

SKIN CORROSION/IRRITATION

Causes severe skin burns and eye damage

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep locked up. Keep out of the reach of children. | Keep locked up. Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private | When using do not eat or drink. Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | When using do not [eat] [drink]. Do not breathe [dust] [vapor] [spray mist]. |
| use/occupational | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Do not breathe [dust] [vapor] [spray mist]. |
| personal protection | Wear suitable protective clothing. Wear suitable gloves. Wear eye/face protection. | Wear suitable [protective clothing] [gloves] [eye/face protection]. Wear protective clothing and gloves (specify protective clothing and type of gloves). Wear appropriate personal protective equipment, avoid direct contact. |
| medical first aid | In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. Take off immediately all contaminated clothing. After contact with skin, wash immediately with plenty of...(to be specified by the manufacturer). If swallowed, rinse mouth with water, (only if the person is conscious). | After contact with skin, take off immediately all contaminated clothing and flush skin with fresh water. Wash contaminated clothing before reuse. If swallowed, rinse mouth with water [give (fluid to be specified by manufacturer) to drink]. Do not induce vomiting. In case of contact with eyes, hold eyelids apart and rinse immediately with plenty of water. Remove contact lenses if worn. In case of accident by inhalation, remove casualty to fresh air and keep at rest. If irritation develops and persists, get medical attention. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

SKIN CORROSION/IRRITATION

Causes skin irritation

(Causes mild skin irritation)

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private |  |  |
| use/occupational |  |  |
| personal protection | Wear suitable gloves. | Wear suitable gloves. |
| medical first aid |  |  |
| disposal |  |  |

SEVERE EYE DAMAGE/EYE IRRITATION

Causes severe eye damage

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private |  |  |
| use/occupational |  |  |
| personal protection | Wear eye/face protection. | Wear suitable eye/face protection. |
| medical first aid | In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. | In case of contact with eyes, hold eyelids apart and rinse immediately with plenty of water. Remove contact lenses if worn. Get medical attention if eye irritation develops or persists. |
| disposal |  |  |

SEVERE EYE DAMAGE/EYE IRRITATION

Causes severe eye irritation

Causes eye irritation

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private |  |  |
| use/occupational |  |  |
| personal protection |  |  |
| medical first aid | In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. | In case of contact with eyes, hold eyelids apart and rinse immediately with plenty of water. Remove contact lenses if worn. Get medical attention if eye irritation develops or persists. |
| disposal |  |  |

RESPIRATORY SENSITIZATION

May cause allergy or asthma symptoms or breathing difficulties if inhaled

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private | Use only in well-ventilated areas. Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Use only in well ventilated areas. Do not breathe [dust, vapor or spray mist]. |
| use/occupational | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Do not breathe [dust, vapor or spray mist]. Use only with [adequate] [closed system] ventilation. Do not enter areas where used or stored until adequately ventilated. |
| personal protection | During fumigation/spraying wear suitable respiratory equipment (appropriate wording to be specified by the manufacture). | During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). Always wear a self-contained breathing apparatus or full-face airline respirator when using this chemical. Wear a mask or pesticide respirator jointly approved by ... . |
| medical first aid | In case of accident or if you feel unwell seek medical advice immediately (show the label where possible) In case of accident by inhalation: remove casualty to fresh air and keep at rest. | In case of accident by inhalation, remove casualty to fresh air and keep at rest. Have the product container or label with you when calling a poison control center or doctor, or going for treatment. |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

DERMAL SENTIZATION

May cause allergic skin reaction

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. | Keep out of the reach of children. |
| storage/workplace |  |  |
| use/private |  |  |
| use/occupational |  |  |
| personal protection | Wear suitable protective clothing. Wear suitable gloves. | Wear suitable [protective clothing] [gloves]. Wear protective clothing and gloves (specify protective clothing and type of gloves). Wear appropriate personal protective equipment, avoid direct contact. |
| medical first aid |  | Have the product container or label with you when calling a poison control center or doctor, or going for treatment. |
| disposal |  |  |

TARGET ORGAN SYSTEMIC TOXICITY (SINGLE EXPOSURE)

Cat 1	Causes damage to < > if << >>

Cat 2	May cause damage to < > if << >>

< >	state all organs affected, or use a general statement where there is no definite evidence that other organs are not affected.

<< >>	state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard.

Cat 1:	It is assumed that Precautionary Statements can be derived from the corresponding Categories 1 to 3 of the Acute Toxicity Hazard Classes.

Cat 2:	It is assumed that Precautionary Statements can be derived from the corresponding Categorie 4 of the Acute Toxicity Hazard Classes.

TARGET ORGAN SYSTEMIC TOXICITY (REPEATED EXPOSURE)

Cat 1	Causes < > damage through prolonged or repeated exposure << >>

Cat 2	May cause < > damage through prolonged or repeated exposure << >>

< >	state all organs affected, or use a general statement where there is no definite evidence that other organs are not affected.

<< >>	state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard.

Cat 1:	It is assumed that Precautionary Statements can be derived from the corresponding Categories 1 to 3 of the Acute Toxicity Hazard Classes. EU provides the mandatory S36 (Wear suitable protective clothing) in any case for Supply & Use.

Cat 2:	It is assumed that Precautionary Statements can be derived from the corresponding Categorie 4 of the Acute Toxicity Hazard Classes.

CARCINOGENICITY

May cause cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard).

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace |  |  |
| use/private | not allowed |  |
| use/occupational | Avoid exposure - Obtain special instructions before use. |  |
| personal protection |  |  |
| medical first aid | In case of accident or if you feel unwell seek medical advice immediately (show the label where possible). |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

CARCINOGENICITY

Suspected of causing cancer (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard).

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. |
| storage/workplace |  |  |
| use/private | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Do not breathe [dust] [vapor] [spray mist]. |
| use/occupational | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Use adequate ventilation to remove [vapors] [fumes] [dust] etc). Do not breathe [dust] [vapor] [spray mist]. |
| personal protection | Wear suitable protective clothing. Wear suitable gloves. In case of insufficient ventilation wear suitable respiratory equipment. During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). | Wear suitable [protective clothing] [gloves]. Wear protective clothing and gloves (specify protective clothing and type of gloves). In case of insufficient ventilation, wear suitable respiratory equipment. During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

GERM CELL MUTAGENICITY

May cause genetic defects (state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard).

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace |  |  |
| use/private | not allowed |  |
| use/occupational | Avoid exposure - Obtain special instructions before use. |  |
| personal protection |  |  |
| medical first aid | In case of accident or if you feel unwell seek medical advice immediately (show the label where possible). |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

GERM CELL MUTAGENICITY

Suspected of causing genetic defects 
(state route of exposure if it is conclusively proven that no other routes of exposure cause the hazard).

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. |
| storage/workplace |  |  |
| use/private | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Do not breathe [dust] [vapor] [spray mist]. |
| use/occupational | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Use adequate ventilation to remove [vapors] [fumes] [dust] etc). Do not breathe [dust] [vapor] [spray mist]. |
| personal protection | Wear suitable protective clothing. Wear suitable gloves. In case of insufficient ventilation wear suitable respiratory equipment. During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). | Wear suitable [protective clothing] [gloves]. Wear protective clothing and gloves (specify protective clothing and type of gloves). In case of insufficient ventilation, wear suitable respiratory equipment. During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

TOXIC TO REPRODUCTION

May damage fertility or the unborn child
(state specific effect if known or route of exposure if it is conclusively proven that no other routes of exposure cause the hazard).

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | not allowed |  |
| storage/workplace |  |  |
| use/private | not allowed |  |
| use/occupational | Avoid exposure - Obtain special instructions before use. |  |
| personal protection |  |  |
| medical first aid | In case of accident or if you feel unwell seek medical advice immediately (show the label where possible). |  |
| disposal | Dispose of this material and its container to .... (to be specified by the manufacturer). |  |

TOXIC TO REPRODUCTION

Suspected of damaging fertility or the unborn child
(state specific effect if known or route of exposure if it is conclusively proven that no other routes of exposure cause the hazard).

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. | Keep out of the reach of children. Keep away from food, drink and animal feedingstuffs. |
| storage/workplace |  |  |
| use/private | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Do not breathe [dust] [vapor] [spray mist]. |
| use/occupational | Do not breathe dust. Do not breathe gas/fumes/spray vapours/ (appropriate words to be specified by the manufacturer). | Use adequate ventilation to remove [vapors] [fumes] [dust] etc). Do not breathe [dust] [vapor] [spray mist]. |
| personal protection | Wear suitable protective clothing. Wear suitable gloves. In case of insufficient ventilation wear suitable respiratory equipment. During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). | Wear suitable [protective clothing] [gloves]. Wear protective clothing and gloves (specify protective clothing and type of gloves). In case of insufficient ventilation, wear suitable respiratory equipment. During fumigation/spraying, wear suitable respiratory equipment (appropriate wording to be specified by the manufacturer). |
| medical first aid |  |  |
| disposal | Dispose of this material and its container to hazardous or special waste collection point. |  |

Additional Category		Effects on or via lactation

May cause harm to breast-fed children

Criteria under development; Precautionary Statements not yet determined.

AQUATIC TOXICITY (ACUTE)

Very toxic to aquatic life

Toxic to aquatic life

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home |  |  |
| storage/workplace |  |  |
| use/private |  |  |
| use/occupational |  |  |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | This material and its container must be disposed of as hazardous waste. Avoid release to the environment. Refer to special instructions/Safety data sheet. | Dispose of this material and its container as hazardous waste. Do not empty into drains. Do not allow into any sewer on the ground, or into any body of water. Refer to manufacturer/supplier for information on recovery/recycling. |

AQUATIC TOXICITY (ACUTE)

Harmful to aquatic life

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| disposal | This material and its container must be disposed of as hazardous waste. | Dispose of this material and its container as hazardous waste. |

AQUATIC TOXICITY (CHRONIC)

Very toxic to aquatic life with long lasting effects

Toxic to aquatic life with long lasting effects

Harmful to aquatic life with long lasting effects

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| storage/home |  |  |
| storage/workplace |  |  |
| use/private |  |  |
| use/occupational |  |  |
| personal protection |  |  |
| medical first aid |  |  |
| disposal | This material and its container must be disposed of as hazardous waste. Avoid release to the environment. Refer to special instructions/Safety data sheet. | Dispose of this material and its container as hazardous waste. Do not empty into drains. Do not allow into any sewer on the ground, or into any body of water. Refer to manufacturer/supplier for information on recovery/recycling. |

AQUATIC TOXICITY (CHRONIC)

May cause long lasting harmful effects to aquatic life

| Precautionary Statements | EU Phrases according to Directive 67/548/EEC | from IPCS CSC |
| --- | --- | --- |
| disposal | This material and its container must be disposed of as hazardous waste. | Dispose of this material and its container as hazardous waste. |

__________________

# Text boxes

STSTE

Secretariat