#### UNITED

# NATIONS

Distr.

# GENERAL

# TRANS/WP.15/AC.1/2002/36

# 25 June 2002

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the

Working Party on the Transport of Dangerous Goods

(Geneva, 9-13 September 2002)

CARRIAGE OF UNPACKAGED MATERIAL AND ARTICLES OF CLASS 7

Proposal submitted by the Government of the United Kingdom */

Proposal:

In the Table in 3.2.1, insert the following entries in column 17 opposite two entries as shown:

"UN 2912	VW/VV 15

UN 2913	VW/VV 16"

In 7.3.3, add the following VW/VV entries:

"VW/VV 15: 	Carriage in bulk is permitted in accordance with the provisions of 4.1.9.2.3

VW/VV 16: 	Carriage in bulk of SCO-I is permitted in accordance with the provisions of 4.1.9.2.3"

________

*/	Circulated by the Central Office  for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT/III/2002/36.

Justification

This proposal seeks to resolve the problem of two conflicting provisions in RID/ADR concerning the carriage of Class 7.

4.1.9.2.3 permits LSA-I material and SCO-I of UN 2912 and 2913 to be carried unpackaged (ie in bulk) subject to certain specified conditions.

7.3.1, however, states that "goods may not be carried in bulk in wagons/vehicles or containers unless a special provision, identified by the code VW/VV, explicitly authorizing this mode of carriage is indicated in Column (17) of Table A of Chapter 3.2 for these goods and unless the conditions of this special provision are satisfied." At present, there are no VW/VV entries for UN 2912 and UN 2913, and carriage in bulk is, therefore, prohibited.

This proposal creates two VW/VV codes for these item numbers to permit their carriage in bulk in accordance with 4.1.9.2.3.

________________

# Text boxes

E

Economic and Social

Council