| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.15/AC.2/2002/1/Add.8/Rev.1 25 March 2002 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport

of Dangerous Goods

Joint Meeting of Experts on the Regulations

annexed to the European Agreement concerning

the International Carriage of Dangerous Goods

by Inland Waterway (ADN)

(Sixtieth session, Geneva, 27-30 May 2002)*/

## RESTRUCTURING OF THE REGULATIONS ANNEXED TO ADN

# Table A: List of dangerous goods by numerical order

# Note by the secretariat**/

The secretariat presents below Table A of Chapter 3.2, Part 3 of the restructured ADN.

This table takes into account amendments to Chapter 3.2 of the restructured ADR, adopted by the Working Party on the Transport of Dangerous Goods at its seventy-first session (see TRANS/WP.15/168) to be entered into force on 1 January 2003, as well as corrigenda to ADR 2001.

*/	This meeting is organized jointly by the Economic Commission for Europe and the Central Commission for the Navigation of the Rhine.

**/	Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR-ZKR/ADN/WP.15/AC.2/2002/1/Add.8/Rev.1.

GE.02-

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 0004 | AMMONIUM PICRATE dry or wetted with less than 10% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0005 | CARTRIDGES FOR WEAPONS with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0006 | CARTRIDGES FOR WEAPONS with bursting charge | 1 | 1.1E |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0007 | CARTRIDGES FOR WEAPONS with bursting charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0009 | AMMUNITION, INCENDIARY with or without burster, expelling charge or propelling charge | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0010 | AMMUNITION, INCENDIARY with or without burster, expelling charge or propelling charge | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0012 | CARTRIDGES FOR WEAPONS, INERT PROJECTILE or CARTRIDGES, SMALL ARMS | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0014 | CARTRIDGES FOR WEAPONS, BLANK or CARTRIDGES, SMALL ARMS, BLANK | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0015 | AMMUNITION, SMOKE with or without burster, expelling charge or propelling charge | 1 | 1.2G |  | 1 | 204 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0016 | AMMUNITION, SMOKE with or without burster, expelling charge or propelling charge | 1 | 1.3G |  | 1 | 204 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0018 | AMMUNITION, TEAR-PRODUCING with burster, expelling charge or propelling charge | 1 | 1.2G |  | 1+6.1+8 | 802 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0019 | AMMUNITION, TEAR-PRODUCING with burster, expelling charge or propelling charge | 1 | 1.3G |  | 1+6.1+8 | 802 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0020 | AMMUNITION, TOXIC with burster, expelling charge or propelling charge | 1 | 1.2K |  |  |  | CARRIAGE FORBIDDEN |  |  |  |  |  |  |
| 0021 | AMMUNITION, TOXIC with burster, expelling charge or propelling charge | 1 | 1.3K |  |  |  | CARRIAGE FORBIDDEN |  |  |  |  |  |  |
| 0027 | BLACK POWDER (GUNPOWDER), granular or as a meal | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0028 | BLACK POWDER (GUNPOWDER), COMPRESSED or BLACK POWDER (GUNPOWDER), IN PELLETS | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0029 | DETONATORS, NON-ELECTRIC for blasting | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0030 | DETONATORS, ELECTRIC for blasting | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0033 | BOMBS with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0034 | BOMBS with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0035 | BOMBS with bursting charge | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0037 | BOMBS, PHOTO-FLASH | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0038 | BOMBS, PHOTO-FLASH | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0039 | BOMBS, PHOTO-FLASH | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0042 | BOOSTERS without detonator | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0043 | BURSTERS, explosive | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0044 | PRIMERS, CAP TYPE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0048 | CHARGES, DEMOLITION | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0049 | CARTRIDGES, FLASH | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0050 | CARTRIDGES, FLASH | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0054 | CARTRIDGES, SIGNAL | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0055 | CASES, CARTRIDGE, EMPTY, WITH PRIMER | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0056 | CHARGES, DEPTH | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0059 | CHARGES, SHAPED without detonator | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0060 | CHARGES, SUPPLEMENTARY, EXPLOSIVE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0065 | CORD, DETONATING, flexible | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0066 | CORD, IGNITER | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0070 | CUTTERS, CABLE, EXPLOSIVE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0072 | CYCLOTRIMETHYLENE-TRINITRAMINE (CYCLONITE; HEXOGEN; RDX), WETTED with not less than 15% water, by mass | 1 | 1.1D |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0073 | DETONATORS FOR AMMUNITION | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0074 | DIAZODINITROPHENOL, WETTED with not less than 40% water, or mixture of alcohol and water, by mass | 1 | 1.1A |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0075 | DIETHYLENEGLYCOL DINITRATE, DESENSITIZED with not less than 25% non-volatile, water-insoluble phlegmatizer, by mass | 1 | 1.1D |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0076 | DINITROPHENOL, dry or wetted with less than 15% water, by mass | 1 | 1.1D |  | 1+6.1 | 802 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0077 | DINITROPHENOLATES, alkali metals, dry or wetted with less than 15% water, by mass | 1 | 1.3C |  | 1+6.1 | 802 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0078 | DINITRORESORCINOL, dry or wetted with less than 15% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0079 | HEXANITRODIPHENYL- AMINE (DIPICRYLAMINE; HEXYL) | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0081 | EXPLOSIVE, BLASTING, TYPE A | 1 | 1.1D |  | 1 | 616 617 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0082 | EXPLOSIVE, BLASTING, TYPE B | 1 | 1.1D |  | 1 | 617 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0083 | EXPLOSIVE, BLASTING, TYPE C | 1 | 1.1D |  | 1 | 267 617 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0084 | EXPLOSIVE, BLASTING, TYPE D | 1 | 1.1D |  | 1 | 617 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0092 | FLARES, SURFACE | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0093 | FLARES, AERIAL | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0094 | FLASH POWDER | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0099 | FRACTURING DEVICES, EXPLOSIVE without detonator, for oil wells | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0101 | FUSE, NON-DETONATING | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0102 | CORD (FUSE), DETONATING, metal clad | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0103 | FUSE, IGNITER, tubular, metal clad | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0104 | CORD (FUSE), DETONATING, MILD EFFECT, metal clad | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0105 | FUSE, SAFETY | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0106 | FUZES, DETONATING | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0107 | FUZES, DETONATING | 1 | 1.2B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0110 | GRENADES, PRACTICE, hand or rifle | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0113 | GUANYLNITROSAMINO-GUANYLIDENE HYDRAZINE, WETTED with not less than 30% water, by mass | 1 | 1.1A |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0114 | GUANYLNITROSAMINO-GUANYLTETRAZENE (TETRAZENE), WETTED with not less than 30% water, or mixture of alcohol and water, by mass | 1 | 1.1A |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0118 | HEXOLITE (HEXOTOL), dry or wetted with less than 15% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0121 | IGNITERS | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0124 | JET PERFORATING GUNS, CHARGED, oil well, without detonator | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0129 | LEAD AZIDE, WETTED with not less than 20% water, or mixture of alcohol and water, by mass | 1 | 1.1A |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0130 | LEAD STYPHNATE (LEAD TRINITRORESORCINATE), WETTED with not less than 20% water, or mixture of alcohol and water, by mass | 1 | 1.1A |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0131 | LIGHTERS, FUSE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0132 | DEFLAGRATING METAL SALTS OF AROMATIC NITRODERIVATIVES, N.O.S. | 1 | 1.3C |  | 1 | 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0133 | MANNITOL HEXANITRATE (NITROMANNITE), WETTED with not less than 40% water, or mixture of alcohol and water, by mass | 1 | 1.1D |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0135 | MERCURY FULMINATE, WETTED with not less than 20% water, or mixture of alcohol and water, by mass | 1 | 1.1A |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0136 | MINES with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0137 | MINES with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0138 | MINES with bursting charge | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0143 | NITROGLYCERIN, DESENSITIZED with not less than 40% non-volatile water-insoluble phlegmatizer, by mass | 1 | 1.1D |  | 1+6.1 | 266 271 802 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0144 | NITROGLYCERIN SOLUTION IN ALCOHOL with more than 1% but not more than 10% nitroglycerin | 1 | 1.1D |  | 1 | 500 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0146 | NITROSTARCH, dry or wetted with less than 20% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0147 | NITRO UREA | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0150 | PENTAERYTHRITE TETRANITRATE (PENTAERYTHRITOL TETRANITRATE; PETN), WETTED with not less than 25% water, by mass, or DESENSITIZED with not less than 15% phlegmatizer, by mass | 1 | 1.1D |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0151 | PENTOLITE, dry or wetted with less than 15% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0153 | TRINITROANILINE (PICRAMIDE) | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0159 | POWDER CAKE (POWDER PASTE), WETTED with not less than 25% water, by mass | 1 | 1.3C |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0160 | POWDER, SMOKELESS | 1 | 1.1C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0161 | POWDER, SMOKELESS | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0167 | PROJECTILES with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0168 | PROJECTILES with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0169 | PROJECTILES with bursting charge | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0171 | AMMUNITION, ILLUMINATING with or without burster, expelling charge or propelling charge | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0173 | RELEASE DEVICES, EXPLOSIVE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0174 | RIVETS, EXPLOSIVE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0180 | ROCKETS with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0181 | ROCKETS with bursting charge | 1 | 1.1E |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0182 | ROCKETS with bursting charge | 1 | 1.2E |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0183 | ROCKETS with inert head | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 0186 | ROCKET MOTORS | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0190 | SAMPLES, EXPLOSIVE, other than initiating explosive | 1 |  |  |  | 16 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0191 | SIGNAL DEVICES, HAND | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0192 | SIGNALS, RAILWAY TRACK, EXPLOSIVE | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0193 | SIGNALS, RAILWAY TRACK, EXPLOSIVE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0194 | SIGNALS, DISTRESS, ship | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0195 | SIGNALS, DISTRESS, ship | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0196 | SIGNALS, SMOKE | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0197 | SIGNALS, SMOKE | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0204 | SOUNDING DEVICES, EXPLOSIVE | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0207 | TETRANITROANILINE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0208 | TRINITROPHENYLMETHYL-NITRAMINE (TETRYL) | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0209 | TRINITROTOLUENE (TNT), dry or wetted with less than 30% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0212 | TRACERS FOR AMMUNITION | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0213 | TRINITROANISOLE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0216 | TRINITRO-m-CRESOL | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0217 | TRINITRONAPHTHALENE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0218 | TRINITROPHENETOLE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0219 | TRINITRORESORCINOL (STYPHNIC ACID), dry or wetted with less than 20% water, or mixture of alcohol and water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0221 | WARHEADS, TORPEDO with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0222 | AMMONIUM NITRATE with more than 0.2% combustible substances, including any organic substance calculated as carbon, to the exclusion of any other added substance | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0224 | BARIUM AZIDE, dry or wetted with less than 50% water, by mass | 1 | 1.1A |  | 1+6.1 | 802 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0225 | BOOSTERS WITH DETONATOR | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0226 | CYCLOTETRAMETHYLENE-TETRANITRAMINE (HMX; OCTOGEN), WETTED with not less than 15% water, by mass | 1 | 1.1D |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0235 | SODIUM PICRAMATE, dry or wetted with less than 20% water, by mass | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0236 | ZIRCONIUM PICRAMATE, dry or wetted with less than 20% water, by mass | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0237 | CHARGES, SHAPED, FLEXIBLE, LINEAR | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0238 | ROCKETS, LINE-THROWING | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0240 | ROCKETS, LINE-THROWING | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0241 | EXPLOSIVE, BLASTING, TYPE E | 1 | 1.1D |  | 1 | 617 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0242 | CHARGES, PROPELLING, FOR CANNON | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0243 | AMMUNITION, INCENDIARY, WHITE PHOSPHORUS with burster, expelling charge or propelling charge | 1 | 1.2H |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0244 | AMMUNITION, INCENDIARY, WHITE PHOSPHORUS with burster, expelling charge or propelling charge | 1 | 1.3H |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0245 | AMMUNITION, SMOKE, WHITE PHOSPHORUS with burster, expelling charge or propelling charge | 1 | 1.2H |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0246 | AMMUNITION, SMOKE, WHITE PHOSPHORUS with burster, expelling charge or propelling charge | 1 | 1.3H |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0247 | AMMUNITION, INCENDIARY, liquid or gel, with burster, expelling charge or propelling charge | 1 | 1.3J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0248 | CONTRIVANCES, WATER-ACTIVATED with burster, expelling charge or propelling charge | 1 | 1.2L |  | 1 | 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0249 | CONTRIVANCES, WATER-ACTIVATED with burster, expelling charge or propelling charge | 1 | 1.3L |  | 1 | 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0250 | ROCKET MOTORS WITH HYPERGOLIC LIQUIDS with or without expelling charge | 1 | 1.3L |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0254 | AMMUNITION, ILLUMINATING with or without burster, expelling charge or propelling charge | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0255 | DETONATORS, ELECTRIC for blasting | 1 | 1.4B |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0257 | FUZES, DETONATING | 1 | 1.4B |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0266 | OCTOLITE (OCTOL), dry or wetted with less than 15% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0267 | DETONATORS, NON-ELECTRIC for blasting | 1 | 1.4B |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0268 | BOOSTERS WITH DETONATOR | 1 | 1.2B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0271 | CHARGES, PROPELLING | 1 | 1.1C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0272 | CHARGES, PROPELLING | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0275 | CARTRIDGES, POWER DEVICE | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0276 | CARTRIDGES, POWER DEVICE | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0277 | CARTRIDGES, OIL WELL | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0278 | CARTRIDGES, OIL WELL | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0279 | CHARGES, PROPELLING, FOR CANNON | 1 | 1.1C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0280 | ROCKET MOTORS | 1 | 1.1C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0281 | ROCKET MOTORS | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0282 | NITROGUANIDINE (PICRITE), dry or wetted with less than 20% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0283 | BOOSTERS without detonator | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0284 | GRENADES, hand or rifle, with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0285 | GRENADES, hand or rifle, with bursting charge | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0286 | WARHEADS, ROCKET with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0287 | WARHEADS, ROCKET with bursting charge | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0288 | CHARGES, SHAPED, FLEXIBLE, LINEAR | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0289 | CORD, DETONATING, flexible | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0290 | CORD (FUSE), DETONATING, metal clad | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0291 | BOMBS with bursting charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0292 | GRENADES, hand or rifle, with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0293 | GRENADES, hand or rifle, with bursting charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0294 | MINES with bursting charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0295 | ROCKETS with bursting charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0296 | SOUNDING DEVICES, EXPLOSIVE | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0297 | AMMUNITION, ILLUMINATING with or without burster, expelling charge or propelling charge | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0299 | BOMBS, PHOTO-FLASH | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0300 | AMMUNITION, INCENDIARY with or without burster, expelling charge or propelling charge | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0301 | AMMUNITION, TEAR-PRODUCING with burster, expelling charge or propelling charge | 1 | 1.4G |  | 1.4+6.1+8 | 802 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0303 | AMMUNITION, SMOKE with or without burster, expelling charge or propelling charge | 1 | 1.4G |  | 1.4 | 204 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0305 | FLASH POWDER | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0306 | TRACERS FOR AMMUNITION | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0312 | CARTRIDGES, SIGNAL | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0313 | SIGNALS, SMOKE | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0314 | IGNITERS | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0315 | IGNITERS | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0316 | FUZES, IGNITING | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0317 | FUZES, IGNITING | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0318 | GRENADES, PRACTICE, hand or rifle | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0319 | PRIMERS, TUBULAR | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0320 | PRIMERS, TUBULAR | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0321 | CARTRIDGES FOR WEAPONS with bursting charge | 1 | 1.2E |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0322 | ROCKET MOTORS WITH HYPERGOLIC LIQUIDS with or without expelling charge | 1 | 1.2L |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0323 | CARTRIDGES, POWER DEVICE | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0324 | PROJECTILES with bursting charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0325 | IGNITERS | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0326 | CARTRIDGES FOR WEAPONS, BLANK | 1 | 1.1C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0327 | CARTRIDGES FOR WEAPONS, BLANK or CARTRIDGES, SMALL ARMS, BLANK | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0328 | CARTRIDGES FOR WEAPONS, INERT PROJECTILE | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0329 | TORPEDOES with bursting charge | 1 | 1.1E |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0330 | TORPEDOES with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0331 | EXPLOSIVE, BLASTING, TYPE B | 1 | 1.5D |  | 1.5 | 617 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0332 | EXPLOSIVE, BLASTING, TYPE E | 1 | 1.5D |  | 1.5 | 617 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0333 | FIREWORKS | 1 | 1.1G |  | 1 | 645 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0334 | FIREWORKS | 1 | 1.2G |  | 1 | 645 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0335 | FIREWORKS | 1 | 1.3G |  | 1 | 645 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0336 | FIREWORKS | 1 | 1.4G |  | 1.4 | 645 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0337 | FIREWORKS | 1 | 1.4S |  | 1.4 | 645 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0338 | CARTRIDGES FOR WEAPONS, BLANK or CARTRIDGES, SMALL ARMS, BLANK | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0339 | CARTRIDGES FOR WEAPONS, INERT PROJECTILE or CARTRIDGES, SMALL ARMS | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0340 | NITROCELLULOSE, dry or wetted with less than 25% water (or alcohol), by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0341 | NITROCELLULOSE, unmodified or plasticized with less than 18% plasticizing substance, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0342 | NITROCELLULOSE, WETTED with not less than 25% alcohol, by mass | 1 | 1.3C |  | 1 | 105 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0343 | NITROCELLULOSE, PLASTICIZED with not less than 18% plasticizing substance, by mass | 1 | 1.3C |  | 1 | 105 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0344 | PROJECTILES with bursting charge | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0345 | PROJECTILES, inert with tracer | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0346 | PROJECTILES with burster or expelling charge | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0347 | PROJECTILES with burster or expelling charge | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |

| UN No. or ID No. | Name and description | Class | Classifi-cation Code | Packing group | Labels | Special provi- sions | Limited quantities | Carriage permitted | Equipment required | Ventilation | Provisions concerning loading, unloading and carriage | Number of cones, blue lights | Remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3.3 | 3.4.6 | 3.2.1 | 8.1.5 | 7.1.6 | 7.1.6 | 7.1.5 | 3.2.1 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) | (12) | (13) |
| 0348 | CARTRIDGES FOR WEAPONS with bursting charge | 1 | 1.4F |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0349 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4S |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0350 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4B |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0351 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4C |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0352 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4D |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0353 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4G |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0354 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.1L |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0355 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.2L |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0356 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.3L |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0357 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.1L |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0358 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.2L |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0359 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.3L |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0360 | DETONATOR ASSEMBLIES, NON-ELECTRIC for blasting | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0361 | DETONATOR ASSEMBLIES, NON-ELECTRIC for blasting | 1 | 1.4B |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0362 | AMMUNITION, PRACTICE | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0363 | AMMUNITION, PROOF | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0364 | DETONATORS FOR AMMUNITION | 1 | 1.2B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0365 | DETONATORS FOR AMMUNITION | 1 | 1.4B |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0366 | DETONATORS FOR AMMUNITION | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0367 | FUZES, DETONATING | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0368 | FUZES, IGNITING | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0369 | WARHEADS, ROCKET with bursting charge | 1 | 1.1F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0370 | WARHEADS, ROCKET with burster or expelling charge | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0371 | WARHEADS, ROCKET with burster or expelling charge | 1 | 1.4F |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0372 | GRENADES, PRACTICE, hand or rifle | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0373 | SIGNAL DEVICES, HAND | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0374 | SOUNDING DEVICES, EXPLOSIVE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0375 | SOUNDING DEVICES, EXPLOSIVE | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0376 | PRIMERS, TUBULAR | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0377 | PRIMERS, CAP TYPE | 1 | 1.1B |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0378 | PRIMERS, CAP TYPE | 1 | 1.4B |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0379 | CASES, CARTRIDGE, EMPTY, WITH PRIMER | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0380 | ARTICLES, PYROPHORIC | 1 | 1.2L |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0381 | CARTRIDGES, POWER DEVICE | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0382 | COMPONENTS, EXPLOSIVE TRAIN, N.O.S. | 1 | 1.2B |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0383 | COMPONENTS, EXPLOSIVE TRAIN, N.O.S. | 1 | 1.4B |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0384 | COMPONENTS, EXPLOSIVE TRAIN, N.O.S. | 1 | 1.4S |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0385 | 5-NITROBENZOTRIAZOL | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0386 | TRINITROBENZENE- SULPHONIC ACID | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0387 | TRINITROFLUORENONE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0388 | TRINITROTOLUENE (TNT) AND TRINITROBENZENE MIXTURE or TRINITROTOLUENE (TNT) AND HEXANITROSTILBENE MIXTURE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0389 | TRINITROTOLUENE (TNT) MIXTURE CONTAINING TRINITROBENZENE AND HEXANITROSTILBENE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0390 | TRITONAL | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0391 | CYCLOTRIMETHYLENE-TRINITRAMINE (CYCLONITE; HEXOGEN; RDX) AND CYCLOTETRAMETHYLENE-TETRANITRAMINE (HMX; OCTOGEN) MIXTURE, WETTED with not less than 15% water, by mass or DESENSITIZED with not less than 10% phlegmatiser by mass | 1 | 1.1D |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0392 | HEXANITROSTILBENE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0393 | HEXOTONAL | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0394 | TRINITRORESORCINOL (STYPHNIC ACID), WETTED with not less than 20% water, or mixture of alcohol and water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0395 | ROCKET MOTORS, LIQUID FUELLED | 1 | 1.2J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0396 | ROCKET MOTORS, LIQUID FUELLED | 1 | 1.3J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0397 | ROCKETS, LIQUID FUELLED with bursting charge | 1 | 1.1J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0398 | ROCKETS, LIQUID FUELLED with bursting charge | 1 | 1.2J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0399 | BOMBS WITH FLAMMABLE LIQUID with bursting charge | 1 | 1.1J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0400 | BOMBS WITH FLAMMABLE LIQUID with bursting charge | 1 | 1.2J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0401 | DIPICRYL SULPHIDE, dry or wetted with less than 10% water, by mass | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0402 | AMMONIUM PERCHLORATE | 1 | 1.1D |  | 1 | 152 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0403 | FLARES, AERIAL | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0404 | FLARES, AERIAL | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0405 | CARTRIDGES, SIGNAL | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0406 | DINITROSOBENZENE | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0407 | TETRAZOL-1-ACETIC ACID | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0408 | FUZES, DETONATING with protective features | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0409 | FUZES, DETONATING with protective features | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0410 | FUZES, DETONATING with protective features | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0411 | PENTAERYTHRITE TETRANITRATE (PENTAERYTHRITOL TETRANITRATE; PETN) with not less than 7% wax, by mass | 1 | 1.1D |  | 1 | 131 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0412 | CARTRIDGES FOR WEAPONS with bursting charge | 1 | 1.4E |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0413 | CARTRIDGES FOR WEAPONS, BLANK | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0414 | CHARGES, PROPELLING, FOR CANNON | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0415 | CHARGES, PROPELLING | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0417 | CARTRIDGES FOR WEAPONS, INERT PROJECTILE or CARTRIDGES, SMALL ARMS | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0418 | FLARES, SURFACE | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0419 | FLARES, SURFACE | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0420 | FLARES, AERIAL | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0421 | FLARES, AERIAL | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0424 | PROJECTILES, inert with tracer | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0425 | PROJECTILES, inert with tracer | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0426 | PROJECTILES with burster or expelling charge | 1 | 1.2F |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0427 | PROJECTILES with burster or expelling charge | 1 | 1.4F |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0428 | ARTICLES, PYROTECHNIC for technical purposes | 1 | 1.1G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0429 | ARTICLES, PYROTECHNIC for technical purposes | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0430 | ARTICLES, PYROTECHNIC for technical purposes | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0431 | ARTICLES, PYROTECHNIC for technical purposes | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0432 | ARTICLES, PYROTECHNIC for technical purposes | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0433 | POWDER CAKE (POWDER PASTE), WETTED with not less than 17% alcohol, by mass | 1 | 1.1C |  | 1 | 266 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0434 | PROJECTILES with burster or expelling charge | 1 | 1.2G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0435 | PROJECTILES with burster or expelling charge | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0436 | ROCKETS with expelling charge | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0437 | ROCKETS with expelling charge | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0438 | ROCKETS with expelling charge | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0439 | CHARGES, SHAPED, without detonator | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0440 | CHARGES, SHAPED, without detonator | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0441 | CHARGES, SHAPED, without detonator | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0442 | CHARGES, EXPLOSIVE, COMMERCIAL without detonator | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0443 | CHARGES, EXPLOSIVE, COMMERCIAL without detonator | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0444 | CHARGES, EXPLOSIVE, COMMERCIAL without detonator | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0445 | CHARGES, EXPLOSIVE, COMMERCIAL without detonator | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0446 | CASES, COMBUSTIBLE, EMPTY, WITHOUT PRIMER | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0447 | CASES, COMBUSTIBLE, EMPTY, WITHOUT PRIMER | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0448 | 5-MERCAPTOTETRAZOL-1-ACETIC ACID | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0449 | TORPEDOES, LIQUID FUELLED with or without bursting charge | 1 | 1.1J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0450 | TORPEDOES, LIQUID FUELLED with inert head | 1 | 1.3J |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0451 | TORPEDOES with bursting charge | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0452 | GRENADES, PRACTICE, hand or rifle | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0453 | ROCKETS, LINE-THROWING | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0454 | IGNITERS | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0455 | DETONATORS, NON-ELECTRIC for blasting | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0456 | DETONATORS, ELECTRIC for blasting | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0457 | CHARGES, BURSTING, PLASTICS BONDED | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0458 | CHARGES, BURSTING, PLASTICS BONDED | 1 | 1.2D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0459 | CHARGES, BURSTING, PLASTICS BONDED | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0460 | CHARGES, BURSTING, PLASTICS BONDED | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0461 | COMPONENTS, EXPLOSIVE TRAIN, N.O.S. | 1 | 1.1B |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0462 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.1C |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0463 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.1D |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0464 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.1E |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0465 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.1F |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0466 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.2C |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0467 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.2D |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0468 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.2E |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0469 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.2F |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0470 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.3C |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0471 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4E |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0472 | ARTICLES, EXPLOSIVE, N.O.S. | 1 | 1.4F |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0473 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.1A |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0474 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.1C |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0475 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.1D |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0476 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.1G |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0477 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.3C |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0478 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.3G |  | 1 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0479 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.4C |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0480 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.4D |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0481 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.4S |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0482 | SUBSTANCES, EXPLOSIVE, VERY INSENSITIVE (SUBSTANCES, EVI), N.O.S. | 1 | 1.5D |  | 1.5 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0483 | CYCLOTRIMETHYLENE-TRINITRAMINE (CYCLONITE; HEXOGEN; RDX), DESENSITIZED | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0484 | CYCLOTETRAMETHYLENE-TETRANITRAMINE (HMX; OCTOGEN), DESENSITIZED | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0485 | SUBSTANCES, EXPLOSIVE, N.O.S. | 1 | 1.4G |  | 1.4 | 178 274 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0486 | ARTICLES, EXPLOSIVE, EXTREMELY INSENSITIVE (ARTICLES, EEI) | 1 | 1.6N |  | 1.6 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0487 | SIGNALS, SMOKE | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0488 | AMMUNITION, PRACTICE | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0489 | DINITROGLYCOLURIL (DINGU) | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0490 | NITROTRIAZOLONE (NTO) | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0491 | CHARGES, PROPELLING | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0492 | SIGNALS, RAILWAY TRACK, EXPLOSIVE | 1 | 1.3G |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0493 | SIGNALS, RAILWAY TRACK, EXPLOSIVE | 1 | 1.4G |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0494 | JET PERFORATING GUNS, CHARGED, oil well, without detonator | 1 | 1.4D |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0495 | PROPELLANT, LIQUID | 1 | 1.3C |  | 1 | 224 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0496 | OCTONAL | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0497 | PROPELLANT, LIQUID | 1 | 1.1C |  | 1 | 224 | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0498 | PROPELLANT, SOLID | 1 | 1.1C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0499 | PROPELLANT, SOLID | 1 | 1.3C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0500 | DETONATOR ASSEMBLIES, NON-ELECTRIC for blasting | 1 | 1.4S |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 0 |  |
| 0501 | PROPELLANT, SOLID | 1 | 1.4C |  | 1.4 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0502 | ROCKETS with inert head | 1 | 1.2C |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 3 |  |
| 0503 | AIR BAG INFLATORS or AIR BAG MODULES or SEAT-BELT PRETENSIONERS | 1 | 1.4G |  | 1.4 | 235 289 | LQ0 |  | PP |  | LO01 | HA01, HA03, HA04, HA05, HA06 |  | 1 |  |
| 0504 | 1H-TETRAZOLE | 1 | 1.1D |  | 1 |  | LQ0 |  | PP |  | LO01 | HA01, HA02, HA03, HA04, HA05, HA06 |  | 3 |  |
| 1001 | ACETYLENE, DISSOLVED | 2 | 4F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1002 | AIR, COMPRESSED | 2 | 1A |  | 2.2 | 292 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1003 | AIR, REFRIGERATED LIQUID | 2 | 3O |  | 2.2+5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1005 | AMMONIA, ANHYDROUS | 2 | 2TC |  | 2.3+8 | 23 | LQ0 | T | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1006 | ARGON, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1008 | BORON TRIFLUORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1009 | BROMOTRIFLUORO- METHANE (REFRIGERANT GAS R 13B1) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1010 | 1,2-BUTADIENE, STABILIZED or 1,3-BUTADIENE , STABILIZED or MIXTURES OF 1,3-BUTADIENE AND HYDROCARBONS, STABILIZED, having a vapour pressure at 70 °C not exceeding 1.1 Mpa (11 bar) and a density at 50 °C not lower than 0.525 kg/l | 2 | 2F |  | 2.1 | 618 | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1011 | BUTANE | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1012 | BUTYLENES MIXTURE or 1-BUTYLENE or CIS-2-BUTYLENE or TRANS-2-BUTYLENE | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1013 | CARBON DIOXIDE | 2 | 2A |  | 2.2 | 584 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1014 | CARBON DIOXIDE AND OXYGEN MIXTURE, COMPRESSED | 2 | 1O |  | 2.2+5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1015 | CARBON DIOXIDE AND NITROUS OXIDE MIXTURE | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1016 | CARBON MONOXIDE, COMPRESSED | 2 | 1TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1017 | CHLORINE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1018 | CHLORODIFLUORO-METHANE (REFRIGERANT GAS R 22) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1020 | CHLOROPENTAFLUORO- ETHANE (REFRIGERANT GAS R 115) | 2 | 2A |  | 2.2 |  | LQ1 | T | PP |  |  |  |  | 0 |  |
| 1021 | 1-CHLORO-1,2,2,2-TETRAFLUOROETHANE (REFRIGERANT GAS R 124) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1022 | CHLOROTRIFLUORO- METHANE (REFRIGERANT GAS R 13) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1023 | COAL GAS, COMPRESSED | 2 | 1TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1026 | CYANOGEN | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1027 | CYCLOPROPANE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1028 | DICHLORODIFLUORO- METHANE (REFRIGERANT GAS R 12) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1029 | DICHLOROFLUORO- METHANE (REFRIGERANT GAS R 21) | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1030 | 1,1-DIFLUOROETHANE (REFRIGERANT GAS R 152a) | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1032 | DIMETHYLAMINE, ANHYDROUS | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1033 | DIMETHYL ETHER | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1035 | ETHANE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1036 | ETHYLAMINE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1037 | ETHYL CHLORIDE | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1038 | ETHYLENE, REFRIGERATED LIQUID | 2 | 3F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1039 | ETHYL METHYL ETHER | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1040 | ETHYLENE OXIDE | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1040 | ETHYLENE OXIDE WITH NITROGEN up to a total pressure of 1 MPa (10 bar) at 50 °C | 2 | 2TF |  | 2.3+2.1 |  | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1041 | ETHYLENE OXIDE AND CARBON DIOXIDE MIXTURE with more than 9% but not more than 87% ethylene oxide | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1043 | FERTILIZER AMMONIATING SOLUTION with free ammonia | 2 |  |  |  |  |  | forbidden |  |  |  |  |  |  |  |
| 1044 | FIRE EXTINGUISHERS with compressed or liquefied gas | 2 | 6A |  | 2.2 | 225 594 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1045 | FLUORINE, COMPRESSED | 2 | 1TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1046 | HELIUM, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1048 | HYDROGEN BROMIDE, ANHYDROUS | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1049 | HYDROGEN, COMPRESSED | 2 | 1F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1050 | HYDROGEN CHLORIDE, ANHYDROUS | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1051 | HYDROGEN CYANIDE, STABILIZED containing less than 3% water | 6.1 | TF1 | I | 6.1+3 | 603 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1052 | HYDROGEN FLUORIDE, ANHYDROUS | 8 | CT1 | I | 8+6.1 | 802 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1053 | HYDROGEN SULPHIDE | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1055 | ISOBUTYLENE | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1056 | KRYPTON, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1057 | LIGHTERS or LIGHTER REFILLS containing flammable gas | 2 | 6F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1058 | LIQUEFIED GASES, non-flammable, charged with nitrogen, carbon dioxide or air | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1060 | METHYLACETYLENE AND PROPADIENE MIXTURE, STABILIZED such as mixture P1 or mixture P2 | 2 | 2F |  | 2.1 | 581 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1061 | METHYLAMINE, ANHYDROUS | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1062 | METHYL BROMIDE with not more than 2% chloropicrin | 2 | 2T |  | 2.3 | 23 | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1063 | METHYL CHLORIDE (REFRIGERANT GAS R 40) | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1064 | METHYL MERCAPTAN | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1065 | NEON, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1066 | NITROGEN, COMPRESSED | 2 | 1A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1067 | DINITROGEN TETROXIDE (NITROGEN DIOXIDE) | 2 | 2TOC |  | 2.3+5.1+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1069 | NITROSYL CHLORIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1070 | NITROUS OXIDE | 2 | 2O |  | 2.2+5.1 | 584 | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1071 | OIL GAS, COMPRESSED | 2 | 1TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1072 | OXYGEN, COMPRESSED | 2 | 1O |  | 2.2+5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1073 | OXYGEN, REFRIGERATED LIQUID | 2 | 3O |  | 2.2+5.1 |  | LQ0 |  | PP |  |  |  |  | 0 |  |
| 1075 | PETROLEUM GASES, LIQUEFIED | 2 | 2F |  | 2.1 | 274 583 639 | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1076 | PHOSGENE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1077 | PROPYLENE | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1078 | REFRIGERANT GAS, N.O.S., such as mixture F1, mixture F2 or mixture F3 | 2 | 2A |  | 2.2 | 274 582 | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1079 | SULPHUR DIOXIDE | 2 | 2TC |  | 2.3+8 |  | LQ0 |  | PP, EP, TOX, A | VE02 |  |  |  | 2 |  |
| 1080 | SULPHUR HEXAFLUORIDE | 2 | 2A |  | 2.2 |  | LQ1 |  | PP |  |  |  |  | 0 |  |
| 1081 | TETRAFLUOROETHYLENE, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1082 | TRIFLUOROCHLORO- ETHYLENE, STABILIZED | 2 | 2TF |  | 2.3+2.1 |  | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1083 | TRIMETHYLAMINE, ANHYDROUS | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1085 | VINYL BROMIDE, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1086 | VINYL CHLORIDE, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1087 | VINYL METHYL ETHER, STABILIZED | 2 | 2F |  | 2.1 |  | LQ0 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1088 | ACETAL | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1089 | ACETALDEHYDE | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1090 | ACETONE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1091 | ACETONE OILS | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1092 | ACROLEIN, STABILIZED | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1093 | ACRYLONITRILE, STABILIZED | 3 | FT1 | I | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1098 | ALLYL ALCOHOL | 6.1 | TF1 | I | 6.1+3 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1099 | ALLYL BROMIDE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 |  | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1100 | ALLYL CHLORIDE | 3 | FT1 | I | 3+6.1 | 802 | LQ0 | T | PP, EP, EX, TOX, A | VE01, VE02 |  |  |  | 2 |  |
| 1104 | AMYL ACETATES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1105 | PENTANOLS | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1105 | PENTANOLS | 3 | F1 | III | 3 |  | LQ7 | T | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1106 | AMYLAMINE | 3 | FC | II | 3+8 |  | LQ4 | T | PP, EP, EX, A | VE01 |  |  |  | 1 |  |
| 1106 | AMYLAMINE | 3 | FC | III | 3+8 |  | LQ7 |  | PP, EP, EX, A | VE01 |  |  |  | 0 |  |
| 1107 | AMYL CHLORIDE | 3 | F1 | II | 3 |  | LQ4 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1108 | 1-PENTENE (n-AMYLENE) | 3 | F1 | I | 3 |  | LQ3 | T | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1109 | AMYL FORMATES | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1110 | n-AMYL METHYL KETONE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |
| 1111 | AMYL MERCAPTAN | 3 | F1 | II | 3 |  | LQ4 |  | PP, EX, A | VE01 |  |  |  | 1 |  |
| 1112 | AMYL NITRATE | 3 | F1 | III | 3 |  | LQ7 |  | PP, EX, A | VE01 |  |  |  | 0 |  |