UNITED

NATIONS

Distr.

Economic and Social		GENERAL

Council

TRANS/WP.29/2002/46

12 April 2002

ENGLISH

Original:	ENGLISH and

FRENCH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-twenty-seventh session,

25-28 June 2002, agenda item 4.2.12.)

PROPOSAL FOR DRAFT SUPPLEMENT 2 TO THE 01 SERIES OF

AMENDMENTS TO REGULATION No. 79

(Steering equipment)

Transmitted by the Working Party on Brakes and Running Gear (GRRF)

Note:  The text reproduced below was adopted by GRRF at its fifty-first session, and is transmitted for consideration to WP.29 and to AC.1.  It is based on document TRANS/WP.29/GRRF/2002/2, not amended (TRANS/WP.29/GRRF/51, para. 33).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 6.2.6.2. the table, amend to read (provisions concerning M1, M2, N1 and N2 vehicles not modified):

#### "Table

STEERING CONTROL EFFORT REQUIREMENTS

| Vehicle Category | INTACT | WITH A FAILURE |
| --- | --- | --- |
|  | Maximum effort (daN) | Time (s) | Turning radius (m) | Maximum effort (daN) | Time (s) | Turning Radius (m) |
| M1 | ... | ... | ... | ... | ... | ... |
| M2 | ... | ... | ... | ... | ... | ... |
| M3 | 20 | 4 | 12 **/ | 45 */ | 6 | 20 |
| N1 | ... | ... | ... | ... | ... | ... |
| N2 | ... | ... | ... | ... | ... | ... |
| N3 | 20 | 4 | 12 **/ | 45 */ | 6 | 20 |

*/  50 for rigid vehicles with 2 or more steered axles excluding self-tracking

equipment

**/ or full lock if 12 m radius is not attainable."

____________

# Text boxes

E