Distr.

GENERAL

TRANS/WP.29/GRRF/2002/5/Add.1

5 July 2002

Original: ENGLISH

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-second session, 16-18 September 2002,

agenda item 5.)

## PROPOSAL FOR DRAFT AMENDMENT TO REGULATION No. 79

Addendum 1

(Steering equipment)

# Transmitted by the Expert from the International Organization of

Motor Vehicle Manufacturers (OICA)

Note:  The text reproduced below was prepared by the expert from OICA to amend the text of the proposal contained in document TRANS/WP.29/GRRF/2005/5 to which it refers.  It is based on the text of a document distributed without a symbol (Informal document No. 12) during the fifty-first session (TRANS/WP.29/GRRF/51, para. 36).

____________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

##### A.	PROPOSAL

Paragraphs 1.3. to 1.5., delete the word “systems” after “steering” (3 times).

Paragraph 2.3.4., amend to read:

" .... is required to remain alert to and to be or aware of ... "

Paragraph 2.5.2.4., amend to read:

"2.5.4.	"Additional steering equipment" means an independent a system, independent of the main steering system, by which the steering angle ..... "

Paragraph 3.2.3., amend to read:

" ......

....... shall be made available for discussion with manufacturer and the type approval authority .... "

Paragraph 5.2.3.1., amend the second and third sentences to read:

" ....... The data contacts of the ISO 7368 7638 connector shall be used … functions as specified in ISO 1192 11992… The braking and steering functions shall have priority and ..... "

Paragraph 5.3.2.1., amend to read:

" .... part of the transmission fails, with … greater than 10 km/h then, the requirements ....... "

Paragraph 5.3.3.3., amend to read:

"5.3.3.3.	In the event of a failure of the energy supply of a the control transmission system, it shall be possible ... "

Paragraph 5.3.3.4., amend to read:

" .... at a speed greater than 10 km/h then, the requirement of paragraph 6. with a for the system ..... "

Paragraph 5.5.1., to be put between square brackets.

Paragraph 5.5.2.1., amend to read:

" .... against simple unauthorized simple modification ...."

Annex 4, paragraph 2.2.1., amend to read:

" .... requirement of paragraphs 6 of this Regulation .... "

*    *    *

### B.	JUSTIFICATION

Ref. to paragraphs 1.3. to 1.5.:

### The definitions apply to the types of steering rather than to the steering systems.

Ref. to paragraph 2.3.4.:

As it was agreed by the GRRF EST informal group.

Ref. to paragraph 2.5.2.4.:

To improve the wording.

Ref. to paragraph 3.2.3.:

As it was agreed by the GRRF EST informal group.

Ref. to paragraphs 5.2.3.1., 5.3.2.1. and 5.5.2.1.:

Editorial corrections.

Ref. to paragraph 5.3.3.3.:

This paragraph addresses only the control transmission, in case of a failure in its energy supply.

Ref. to paragraph 5.5.1.:

The current paragraph 5.5.1. is inspired from the prescriptions for brakes.  The steering equipment does not need the same provisions as the brakes.  A proposal for a new wording is subject to a separate informal document.

____________