# UN/SCETDG/24/INF.61

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-fourth session

Geneva, 3-10 December 2003

Item 8 of the provisional agenda

HARMONIZATION WITH THE INTERNATIONAL ATOMIC ENERGY AGENCY (IAEA) REGULATIONS FOR THE SAFE TRANSPORT OF RADIOACTIVE MATERIAL

Changes to TS-R-1 recommended by the 10- 14 November 2003 Review Panel meeting for the 2005 edition of the IAEA Transport Regulations

Transmitted by the International Atomic Energy Agency

##### Recommended Changes to TS-R-1

This paper summarizes the changes to TS-R-1 recommended by the 10 – 14 November Review Panel meeting for the 2005 edition of the IAEA Transport Regulations.  These recommended changes resulted from a review of the proposed changes, presented last July as Working Paper ST/SG/AC.10/C.3/2003/3 and the comments received on those proposed changes.  As a result of the Review Panel meeting the number of recommended changes is considerably smaller than the original number of proposed changes.

These recommended changes are still subject to approval by the 22-26 March 2004 TRANSSC meeting.  At that time there may be some further amendments or deletions.

The TRANSSC approved changes will be presented to the UN SCETDG July 2004 meeting together with the minor changes that were approved already by the 2-6 September 2002 Review Panel meeting in Vienna and presented to the July 2003 UN SCETDG meeting as Working Paper ST/SG/AC.10/C.3/2003/2.  The combined approved changes that will be presented in July 2004 will represent all the changes recommended for the 2005 editions of both the IAEA and the UN Model Regulations.

The changes recommended by the 10 –14 November 2003 Review Panel meeting are presented in a table, in IAEA paragraph order. The related UN paragraphs are identified. The text has not yet been modified in accordance with UN format.  A summary of the corresponding changes in UN format is presented by the UN Secretariat in UN/SCETDG/24/INF.23.

The current IAEA text and the new IAEA text are presented side by side in order to easily identify what change has been recommended.  Where the change involves a deletion of text from the current regulations the part to be deleted is marked in bold in the current text.  Where the approved change involves new or revised text the new or revised part is marked in bold in the new text.

DECISIONS OF THE NOVEMBER 2003 REVIEW PANEL MEETING FOR APPROVAL BY TRANSSC IX

| Change | IAEA para | UN para | Existing text in TS-R-1 (2003) | Text Recommended by Review Panel No. 2 |
| --- | --- | --- | --- | --- |
| 1 | 204 | 2.72 | 204. Multilateral approval shall mean approval by the relevant competent authority both of the country of origin of the design or shipment and of each country through or into which the consignment is to be transported. The term “through or into” specifically excludes “over”, i.e. the approval and notification requirements shall not apply to a country over which radioactive material is carried in an aircraft, provided that there is no scheduled stop in that country. | 204. Multilateral approval shall mean approval by the relevant competent authority of the country of origin of the design or shipment, as applicable, and also, where the consignment is to be transported through or into any other country, approval by the competent authority of that country. The term “through or into” specifically excludes “over”, i.e. the approval and notification requirements shall not apply to a country over which radioactive material is carried in an aircraft, provided that there is no scheduled stop in that country. |
| 3 | 212 | Already in 5.4.1.3 | 212. Consignor shall mean any person, organization or government which prepares a consignment for transport, and is named as consignor in the transport documents. | 212. Consignor shall mean any person, organization or government which prepares a consignment for transport. 549. The consignor shall include in the transport documents with each consignment the identification of the consignor and consignee, including their names and addresses and the following information, as applicable in the order given: |
| 4 | 222 | 2.7.2 | Fissile material 222. Fissile material shall mean uranium-233, uranium-235, plutonium-239, plutonium-241, or any combination of these radionuclides. Excepted from this definition is: (a) natural uranium or depleted uranium which is unirradiated, and (b) natural uranium or depleted uranium which has been irradiated in thermal reactors only. | Fissile – nuclides, material 222. Fissile nuclides shall mean uranium-233, uranium-235, plutonium-239 and plutonium-241. Fissile material shall mean a material containing any of the fissile nuclides. Excepted from the definition of fissile material is: (a) natural uranium or depleted uranium which is unirradiated, and (b) natural uranium or depleted uranium which has been irradiated in thermal reactors only. |
| 5 | 222 related consequential changes in paras 226, 418, 543, 549, 559, 672, 831, 832, 833 and Table XII | Consequential changes in 2.7.7.1.7, 5.2.2.1.12.2, 5.4.1.5.7.1, 5.1.5.2.4(d), 6.4.11.2, 6.4.23.12,. 6.4.23.13,. 6.4.23.14, 6.4.11.2 | Proposed consequential change in para 226 not accepted by Review Panel 418. Packages containing fissile material shall not contain: (a) a mass of fissile material different from that authorized for the package design, (b) any radionuclide or fissile material different from those authorized for the package design, or (c) contents in a form or physical or chemical state, or in a spatial arrangement, different from those authorized for the package design, as specified in their certificates of approval where appropriate. 543 (b) Activity: The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with the appropriate SI prefix (see Annex II). For fissile material, the mass of fissile material in units of grams (g), or multiples thereof, may be used in place of activity. 549 (f) The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with an appropriate SI prefix (see Annex II). For fissile material, the mass of fissile material in units of grams (g), or appropriate multiples thereof, may be used in place of activity; 559 (e) The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with an appropriate SI prefix (see Annex II). For fissile material, the mass of fissile material in units of grams (g), or multiples thereof, may be used in place of activity. 672 (a) in formula, mass of other fissile material(g) 672 (a) (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile material in any 10 litre volume of material. 672 (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile material is distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. TABLE XII See appendix 1 831 (j) A specification of the authorized radioactive contents, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. 832 (j) A specification of the actual radioactive contents, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the total activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable . 833 (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. | 418. Packages containing fissile material shall not contain: (a) quantities of fissile material and/or fissile nuclides not authorized for the package design, (b) any radionuclide different from those authorized for the package design, or (c) contents in a form or physical or chemical state, or in a spatial arrangement, different from those authorized for the package design, as specified in their certificates of approval where appropriate. 543 (b) Activity: The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with the appropriate SI prefix (see Annex II). For fissile material, the mass of fissile nuclides in units of grams (g), or multiples thereof, may be used in place of activity. 549 (f) The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with an appropriate SI prefix (see Annex II). For fissile material, the mass of fissile nuclides in units of grams (g), or multiples thereof, may be used in place of activity; 559 (e) The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with an appropriate SI prefix (see Annex II). For fissile material, the mass of fissile nuclides in units of grams (g), or multiples thereof, may be used in place of activity. 672 (a) in formula, mass of other fissile nuclides(g) 672 (a) (i) each individual package contains not more than 15 g of fissile nuclides; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or (ii) the fissile material is a homogeneous hydrogenous solution or mixture where the ratio of fissile nuclides to hydrogen is less than 5% by mass, or (iii) there is not more than 5 g of fissile nuclides in any 10 litre volume of material. 672 (b) Uranium enriched in uranium-235 to a maximum of 1% by mass, and with a total plutonium and uranium-233 content not exceeding 1% of the mass of uranium-235, provided that the fissile nuclides are distributed essentially homogeneously throughout the material. In addition, if uranium-235 is present in metallic, oxide or carbide forms, it shall not form a lattice arrangement. TABLE XII See appendix 1 831 (j) A specification of the authorized radioactive contents, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material and/or fissile nuclides), and whether special form radioactive material or low dispersible radioactive material, if applicable. 832 (j) A specification of the actual radioactive contents, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the total activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material and/or fissile nuclides), and whether special form radioactive material or low dispersible radioactive material, if applicable . 833 (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material and/or fissile nuclides), and whether special form radioactive material or low dispersible radioactive material, if applicable. |
| 10 | 303 | 1.1.2.2.4 | 303. Workers shall receive appropriate training concerning the radiation hazards involved and the precautions to be observed in order to ensure restriction of their exposure and that of other persons who might be affected by their actions. | 303. Workers shall receive appropriate training concerning radiation protection and the precautions to be observed in order to control their occupational exposure and the exposure of other persons who might be affected by their actions. |
| 11 | 305 | 1.1.2.2.5 | 305. For occupational exposures arising from transport activities, where it is assessed that the effective dose: (a) is most unlikely to exceed 1 mSv in a year, neither special work patterns nor detailed monitoring nor dose assessment programmes nor individual record keeping shall be required; (b) is likely to be between 1 and 6 mSv in a year, a dose assessment programme via work place monitoring or individual monitoring shall be conducted; (c) is likely to exceed 6 mSv in a year, individual monitoring shall be conducted. When individual monitoring or work place monitoring is conducted, appropriate records shall be kept. | 305. For occupational exposures arising from transport activities, where it is assessed that the effective dose: (a) is likely to be between 1 and 6 mSv in a year, a dose assessment programme via work place monitoring or individual monitoring shall be conducted; (b) is likely to exceed 6 mSv in a year, individual monitoring shall be conducted. When individual monitoring or work place monitoring is conducted, appropriate records shall be kept. |
| 12 | Table I footnote (a) | Table 2.7.7.2.1 | (a) A1 and/or A2 values for these parent radionuclides include contributions from daughter radionuclides with half-lives less than 10 days. | (a) A1 and/or A2 values for these parent radionuclides include contributions from daughter radionuclides with half-lives less than 10 days, as listed in the following: Mg 28 Al 28 Ar 42 K 42 Ca 47 Sc 47 Ti 44 Sc 44 Fe 52 Mn 52m Fe 60 Co 60m Zn 69m Zn 69 Ge 68 Ga 68 Rb 83 Kr 83m Sr 82 Rb 82 Sr 90 Y 90 Sr 91 Y 91m Sr 92 Y 92 Y 87 Sr 87m Zr 95 Nb 95m Zr 97 Nb 97m, Nb 97 Mo 99 Tc 99m Tc 95m Tc 95 Tc 96m Tc 96 Ru 103 Rh 103m Ru 106 Rh 106 Pd 103 Rh 103m Ag 108m Ag 108 Ag 110m Ag 110 Cd 115 In 115m In 114m In 114 Sn 113 In 113m Sn 121m Sn 121 Sn 126 Sb 126m Te 118 Sb 118 Te 127m Te 127 Te 129m Te 129 Te 131m Te 131 Te 132 I 132 I 135 Xe 135m Xe 122 I 122 Cs 137 Ba 137m Ba 131 Cs 131 Ba 140 La 140 Ce 144 Pr 144m, Pr 144 Pm 148m Pm 148 Gd 146 Eu 146 Dy 166 Ho 166 Hf 172 Lu 172 W 178 Ta 178 W 188 Re 188 Re 189 Os 189m Os 194 Ir 194 Ir 189 Os 189m Pt 188 Ir 188 Hg 194 Au 194 Hg 195m Hg 195 Pb 210 Bi 210 Pb 212 Bi 212, Tl 208, Po 212 Bi 210m Tl 206 Bi 212 Tl 208, Po 212 At 211 Po 211 Rn 222 Po 218, Pb 214, At 218, Bi 214, Po 214 Ra 223 Rn 219, Po 215, Pb 211, Bi 211, Po 211, Tl 207 Ra 224 Rn 220, Po 216, Pb 212, Bi 212, Tl 208, Po 212 Ra 225 Ac 225, Fr 221, At 217, Bi 213, Tl 209, Po 213, Pb 209 Ra 226 Rn 222, Po 218, Pb 214, At 218, Bi 214, Po 214 Ra 228 Ac 228 Ac 225 Fr 221, At 217, Bi 213, Tl 209, Po 213, Pb 209 Ac 227 Fr 223 Th 228 Ra 224, Rn 220, Po 216, Pb 212, Bi 212, Tl 208, Po 212 Th 234 Pa 234m, Pa 234 Pa 230 Ac 226, Th 226, Fr 222, Ra 222, Rn 218, Po 214 U 230 Th 226, Ra 222, Rn 218, Po 214 U 235 Th 231 Pu 241 U 237 Pu 244 U 240, Np 240m Am 242m Am 242, Np 238 Am 243 Np 239 Cm 247 Pu 243 Bk 249 Am 245 Cf 253 Cm 249 |
| 13 | Table I footnote (b) | Table 2.7.7.2.1 | (b) Parent nuclides and their progeny included in secular equilibrium are listed in the following: Sr-90 Y-90 Zr-93 Nb-93m Zr-97 Nb-97 Ru-106 Rh-106 Cs-137 Ba-137m Ce-134 La-134 Ce-144 Pr-144 Ba-140 La-140 Bi-212 Tl-208 (0.36), Po-212 (0.64) Pb-210 Bi-210, Po-210 Pb-212 Bi-212, Tl-208 (0.36), Po-212 (0.64) Rn-220 Po-216 Rn-222 Po-218, Pb-214, Bi-214, Po-214 Ra-223 Rn-219, Po-215, Pb-211, Bi-211, Tl-207 Ra-224 Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Ra-226 Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 Ra-228 Ac-228 Th-226 Ra-222, Rn-218, Po-214 Th-228 Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-229 Ra-225, Ac-225, Fr-221, At-217, Bi-213, Po-213, Pb-209 Th-nat Ra-228, Ac-228, Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-234 Pa-234m U-230 Th-226, Ra-222, Rn-218, Po-214 U-232 Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) U-235 Th-231 U-238 Th-234, Pa-234m U-nat Th-234, Pa-234m, U-234, Th-230, Ra-226, Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 U-240 Np-240m Np-237 Pa-233 Am-242m Am-242 Am-243 Np-239 | (b) Parent nuclides and their progeny included in secular equilibrium are listed in the following: Sr-90 Y-90 Zr-93 Nb-93m Zr-97 Nb-97 Ru-106 Rh-106 Ag-108m Ag-108 Cs-137 Ba-137m Ce-144 Pr-144 Ba-140 La-140 Bi-212 Tl-208 (0.36), Po-212 (0.64) Pb-210 Bi-210, Po-210 Pb-212 Bi-212, Tl-208 (0.36), Po-212 (0.64) Rn-222 Po-218, Pb-214, Bi-214, Po-214 Ra-223 Rn-219, Po-215, Pb-211, Bi-211, Tl-207 Ra-224 Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Ra-226 Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 Ra-228 Ac-228 Th-228 Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-229 Ra-225, Ac-225, Fr-221, At-217, Bi-213, Po-213, Pb-209 Th-nat Ra-228, Ac-228, Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) Th-234 Pa-234m U-230 Th-226, Ra-222, Rn-218, Po-214 U-232 Th-228, Ra-224, Rn-220, Po-216, Pb-212, Bi-212, Tl-208 (0.36), Po-212 (0.64) U-235 Th-231 U-238 Th-234, Pa-234m U-nat Th-234, Pa-234m, U-234, Th-230, Ra-226, Rn-222, Po-218, Pb-214, Bi-214, Po-214, Pb-210, Bi-210, Po-210 Np-237 Pa-233 Am-242m Am-242 Am-243 Np-239 |
| 14 | 402 | 2.7.7.2.2 | 402. For individual radionuclides which are not listed in Table I the determination of the basic radionuclide values referred to in para. 401 shall require competent authority approval or, for international transport, multilateral approval. Where the chemical form of each radionuclide is known, it is permissible to use the A2 value related to its solubility class as recommended by the International Commission on Radiological Protection, if the chemical forms under both normal and accident conditions of transport are taken into consideration. Alternatively, the radionuclide values in Table II may be used without obtaining competent authority approval. | 402. For individual radionuclides which are not listed in Table I the determination of the basic radionuclide values referred to in para. 401 shall require multilateral approval. It is permissible to use an A2 value calculated using a dose coefficient for the appropriate lung absorption type, as recommended by the International Commission on Radiological Protection, if the chemical forms of each radionuclide under both normal and accident conditions of transport are taken into consideration. Alternatively, the radionuclide values in Table II may be used without obtaining competent authority approval. |
| 15 | TABLE II | Table 2.7.7.2.2 | TABLE II (first column) Radioactive contents Only beta or gamma emitting nuclides are known to be present Only alpha emitting nuclides are known to be present No relevant data are available | TABLE II (first column) Radioactive contents Only beta or gamma emitting nuclides are known to be present. Alpha emitting nuclides, but no neutron emitters are known to be present Neutron emitting nuclides are known to be present or no relevant data are available |
| 17 | 419 | 2.7.7.1.8 | 419. The mass of uranium hexafluoride in a package shall not exceed a value that would lead to an ullage smaller than 5% at the maximum temperature of the package as specified for the plant systems where the package shall be used. The uranium hexafluoride shall be in solid form and the internal pressure of the package shall be below atmospheric pressure when presented for transport. | 419. Packages containing uranium hexafluoride shall not contain:_ (a) a mass of uranium hexafluoride different from that authorized for the package design, (b) a mass of uranium hexafluoride greater than a value that would lead to an ullage smaller than 5% at the maximum temperature of the package as specified for the plant systems where the package shall be used, or (c) uranium hexafluoride other than in solid form or at an internal pressure above atmospheric pressure when presented for transport. |
| 18 | 502 | 5.1.5.1.2 | 502. Before each shipment of any package, the following requirements shall be fulfilled: (a) For any package it shall be ensured that all the requirements specified in the relevant provisions of these Regulations have been satisfied. (b) It shall be ensured that lifting attachments which do not meet the requirements of para. 607 have been removed or otherwise rendered incapable of being used for lifting the package, in accordance with para. 608. (c) For each Type B(U), Type B(M) and Type C package and for each package containing fissile material, it shall be ensured that all the requirements specified in the approval certificates have been satisfied. (d) Each Type B(U), Type B(M) and Type C package shall be held until equilibrium conditions have been approached closely enough to demonstrate compliance with the requirements for temperature and pressure unless an exemption from these requirements has received unilateral approval. (e) For each Type B(U), Type B(M) and Type C package, it shall be ensured by inspection and/or appropriate tests that all closures, valve and other openings of the containment system through which the radioactive contents might escape are properly closed and, where appropriate, sealed in the manner for which the demonstrations of compliance with the requirements of paras 656 and 669 were made. (f) For each special form radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. (g) For packages containing fissile material the measurement specified in para. 674(b) and the tests to demonstrate closure of each package as specified in para. 677 shall be performed where applicable. (h) For each low dispersible radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. | 502. Before each shipment of any package, the following requirements shall be fulfilled: (a) For any package it shall be ensured that all the requirements specified in the relevant provisions of these Regulations have been satisfied. (b) It shall be ensured that lifting attachments which do not meet the requirements of para. 607 have been removed or otherwise rendered incapable of being used for lifting the package, in accordance with para. 608. (c) For each package requiring competent authority approval, it shall be ensured that all the requirements specified in the approval certificates have been satisfied. (d) Each Type B(U), Type B(M) and Type C package shall be held until equilibrium conditions have been approached closely enough to demonstrate compliance with the requirements for temperature and pressure unless an exemption from these requirements has received unilateral approval. (e) For each Type B(U), Type B(M) and Type C package, it shall be ensured by inspection and/or appropriate tests that all closures, valve and other openings of the containment system through which the radioactive contents might escape are properly closed and, where appropriate, sealed in the manner for which the demonstrations of compliance with the requirements of paras 656 and 669 were made. (f) For each special form radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. (g) For packages containing fissile material the measurement specified in para. 674(b) and the tests to demonstrate closure of each package as specified in para. 677 shall be performed where applicable. (h) For each low dispersible radioactive material, it shall be ensured that all the requirements specified in the approval certificate and the relevant provisions of these Regulations have been satisfied. |
| 19 | 503 | 4.1.9.1.3 | 503. A package shall not contain any other items except such articles and documents as are necessary for the use of the radioactive material. This requirement shall not preclude the transport of low specific activity material or surface contaminated objects with other items. The transport of such articles and documents in a package, or of low specific activity material or surface contaminated objects with other items may be permitted provided that there is no interaction between them and the packaging or its radioactive contents that would reduce the safety of the package. | 503. A package may only contain other items that are necessary for the use of the radioactive material. The interaction between these other items and the package, under the conditions of transport applicable to the design, shall not reduce the safety of the package. |
| 20 | Table VIII footnote “c” | Included in Part 3 | Table VIII footnote “c” c UN 2977 and UN 2978 are special cases without a unique relationship with the Schedules. | Table VIII footnote “c” c In the case of non-fissile or fissile excepted uranium hexafluoride, the UN 2978 and the proper shipping name and description, “RADIOACTIVE MATERIAL, URANIUM HEXAFLUORIDE, non-fissile or fissile excepted,” takes precedence over other UN numbers applicable to non-fissile and fissile excepted. In the case of uranium hexafluoride that is fissile material the UN 2977 and the proper shipping name, “RADIOACTIVE MATERIAL, URANIUM HEXAFLUORIDE, FISSILE,” takes precedence over other UN numbers applicable to fissile material. |
| 22 | 537 | 5.2.1.5.4 | 537. Each package which conforms to: (a) an IP-1, an IP-2 or an IP-3 design shall be legibly and durably marked on the outside of the packaging with “TYPE IP-1”, “TYPE IP-2” or “TYPE IP-3” as appropriate; (b) a Type A package design shall be legibly and durably marked on the outside of the packaging with “TYPE A”; (c) an IP-2, an IP-3 or a Type A package design shall be legibly and durably marked on the outside of the packaging with the international vehicle registration code (VRI Code) of the country of origin of design and the name of the manufacturers, or other identification of the packaging specified by the competent authority. | 537. Each package which conforms to: (a) an IP-1, an IP-2 or an IP-3 design shall be legibly and durably marked on the outside of the packaging with “TYPE IP-1”, “TYPE IP-2” or “TYPE IP-3” as appropriate; (b) a Type A package design shall be legibly and durably marked on the outside of the packaging with “TYPE A”; (c) an IP-2, an IP-3 or a Type A package design shall be legibly and durably marked on the outside of the packaging with the international vehicle registration code (VRI Code) of the country of origin of design and either the name of the manufacturer or other identification of the packaging specified by the competent authority of the country of origin of design. |
| 23 | 566 | 7.1.7.3.3 | 566. Loading of freight containers and accumulation of packages, overpacks and freight containers shall be controlled as follows: (a) Except under the condition of exclusive use, the total number of packages, overpacks and freight containers aboard a single conveyance shall be so limited that the total sum of the transport indexes aboard the conveyance does not exceed the values shown in Table IX. For consignments of LSA-I material there shall be no limit on the sum of the transport indexes. (b) Where a consignment is transported under exclusive use, there shall be no limit on the sum of the transport indexes aboard a single conveyance. (c) The radiation level under routine conditions of transport shall not exceed 2 mSv/h at any point on, and 0.1 mSv/h at 2 m from, the external surface of the conveyance, except for consignments transported under exclusive use by road or rail, for which the radiation limits around the vehicle are set forth in para 572(b) and (c). (d) The total sum of the criticality safety indexes in a freight container and aboard a conveyance shall not exceed the values shown in Table X. | 566. Loading of freight containers and accumulation of packages, overpacks and freight containers shall be controlled as follows: (a) Except under the condition of exclusive use, and for consignments of LSA-I material, the total number of packages, overpacks and freight containers aboard a single conveyance shall be so limited that the total sum of the transport indexes aboard the conveyance does not exceed the values shown in Table IX. (b) The radiation level under routine conditions of transport shall not exceed 2 mSv/h at any point on, and 0.1 mSv/h at 2 m from, the external surface of the conveyance, except for consignments transported under exclusive use by road or rail, for which the radiation limits around the vehicle are set forth in para 572(b) and (c). (c) The total sum of the criticality safety indexes in a freight container and aboard a conveyance shall not exceed the values shown in Table X. |
| 24 | 622 and consequential changes in 624, 625, 627, 628 and 646b | 6.4.5.2 and consequential changes in 6.4.5.4.1 6.4.5.4.2 6.4.5.4.4 6.4.5.4.5 6.4.7.14 | 622. A package, to be qualified as a Type IP-2, shall be designed to meet the requirements for Type IP-1 as specified in para. 621 and, in addition, if it were subjected to the tests specified in paras 722 and 723, it would prevent: (a) loss or dispersal of the radioactive contents; and (b) loss of shielding integrity which would result in more than a 20% increase in the radiation level at any external surface of the package. | 622. A package, to be qualified as a Type IP-2, shall be designed to meet the requirements for Type IP-1 as specified in para. 621 and, in addition, if it were subjected to the tests specified in paras 722 and 723, it would prevent: (a) loss or dispersal of the radioactive contents; and (b) more than a 20% increase in the maximum radiation level at any external surface of the package. |
| 26 | 652 and 662 | 6.4.8.3 and 6.4.8.13 | 652. Except as required in para. 617 for a package transported by air, a package shall be so designed that, under the ambient condition specified in para. 653, the temperature of the accessible surfaces of a package shall not exceed 50°C, unless the package is transported under exclusive use. 662. Except as required in para. 617 for a package transported by air, the maximum temperature of any surface readily accessible during transport of a package shall not exceed 85°C in the absence of insolation under the ambient conditions specified in para. 653. The package shall be carried under exclusive use, as specified in para. 652, if this maximum temperature exceeds 50°C. Account may be taken of barriers or screens intended to give protection to persons without the need for the barriers or screens being subject to any test. | 652. A package shall be so designed that, under the ambient condition specified in para. 653 and in the absence of insolation, the temperature of the accessible surfaces of a package shall not exceed 50 °C, unless the package is transported under exclusive use. 652 bis. Except as required in para. 617 for a package transported by air, the maximum temperature of any surface readily accessible during transport of a package under exclusive use shall not exceed 85°C in the absence of insolation under the ambient conditions specified in para. 653. Account may be taken of barriers or screens intended to give protection to persons without the need for the barriers or screens being subject to any test. 662 : deleted and replaced with 652bis as above |
| 27 | 418 and 672 NOTE. In original proposal: Current para 672, as modified, becomes new para 417bis | 2.7.7.1.7 | 418. Packages containing fissile material shall not contain: (a) a mass of fissile material different from that authorized for the package design, (b) any radionuclide or fissile material different from those authorized for the package design, or (c) contents in a form or physical or chemical state, or in a spatial arrangement, different from those authorized for the package design, as specified in their certificates of approval where appropriate. | 418. Unless excepted by para. 672 packages containing fissile material shall not contain: (a) a mass of fissile material different from that authorized for the package design, (b) any radionuclide or fissile material different from those authorized for the package design, or (c) contents in a form or physical or chemical state, or in a spatial arrangement, different from those authorized for the package design, as specified in their certificates of approval where appropriate. 672. no change |
| 31 | 672 | 6.4.11.2 | 672 ……… (a)……. …..(iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium in hydrogenous material enriched in deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII. (b)Uranium enriched….. | 672 ……… (a)……. …..(iii) there is not more than 5 g of fissile material in any 10 litre volume of material. Neither beryllium nor deuterium shall be present in quantities exceeding 1% of the applicable consignment mass limits provided in Table XII, except for deuterium in natural concentration in hydrogen.. (b)Uranium enriched….. |
| 32 | 672 | 6.4.11.2 | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or ………………………………… …………or any combination of those radionuclides. | 672. Fissile material meeting one of the provisions (a)–(d) of this paragraph is excepted from the requirement to be transported in packages that comply with paras 673–682 as well as the other requirements of these Regulations that apply to fissile material. Only one type of exception is allowed per consignment. (a) A mass limit per consignment such that: mass of uranium-235 (g) + mass of other fissile material (g) ( 1 X Y where X and Y are the mass limits defined in Table XII, provided that the smallest external dimension of each package is not less than 10 cm and that either: (i) each individual package contains not more than 15 g of fissile material; for unpackaged material, this quantity limitation shall apply to the consignment being carried in or on the conveyance, or ………………………………… …………or any combination of those radionuclides. |
| 38 | 677 | 6.4.11.7 | 677. For a package in isolation, it shall be assumed that water can leak into or out of all void spaces of the package, including those within the containment system. However, if the design incorporates special features to prevent such leakage of water into or out of certain void spaces, even as a result of error, absence of leakage may be assumed in respect of those void spaces. Special features shall include the following: (a) Multiple high standard water barriers, each of which would remain watertight if the package were subject to the tests prescribed in para. 682(b), a high degree of quality control in the manufacture, maintenance and repair of packagings and tests to demonstrate the closure of each package before each shipment; or (b) For packages containing uranium hexafluoride only: (i) packages where, following the tests prescribed in para. 682(b), there is no physical contact between the valve and any other component of the packaging other than at its original point of attachment and where, in addition, following the test prescribed in para. 728 the valves remain leaktight; and (ii) a high degree of quality control in the manufacture, maintenance and repair of packagings coupled with tests to demonstrate closure of each package before each shipment. | 677. For a package in isolation, it shall be assumed that water can leak into or out of all void spaces of the package, including those within the containment system. However, if the design incorporates special features to prevent such leakage of water into or out of certain void spaces, even as a result of error, absence of leakage may be assumed in respect of those void spaces. Special features shall include the following: (a) Multiple high standard water barriers, each of which would remain watertight if the package were subject to the tests prescribed in para. 682(b), a high degree of quality control in the manufacture, maintenance and repair of packagings and tests to demonstrate the closure of each package before each shipment; or (b) For packages containing uranium hexafluoride, with maximum uranium enrichment of 5 mass percent uranium-235: (i) packages where, following the tests prescribed in para. 682(b), there is no physical contact between the valve and any other component of the packaging other than at its original point of attachment and where, in addition, following the test prescribed in para. 728 the valves remain leaktight; and (ii) a high degree of quality control in the manufacture, maintenance and repair of packagings coupled with tests to demonstrate closure of each package before each shipment. |
| 39 | 709 | 2.7.4.6 | 709. Specimens that comprise or simulate radioactive material enclosed in a sealed capsule may be excepted from: (a) The tests prescribed in paras 705 and 706 provided the mass of the special form radioactive material is less than 200 g and they are alternatively subjected to the Class 4 impact test prescribed in the International Organization for Standardization document ISO 2919: “Sealed Radioactive Sources —Classification” [11], and (b) The test prescribed in para. 708 provided they are alternatively subjected to the Class 6 temperature test specified in the International Organization for Standardization document ISO 2919: “Sealed radioactive sources —Classification” [11]. | 709. Specimens that comprise or simulate radioactive material enclosed in a sealed capsule may be excepted from: (a) The tests prescribed in paras 705 and 706 provided the mass of the special form radioactive material is less than 200 g and they are alternately subjected to the Class 4 impact test prescribed in the International Organization for Standardization document ISO 2919: “Sealed Radioactive Sources – Classification” [11], or is less than 500 g and they are alternately subjected to the Class 5 impact test prescribed in the International Organization for Standardization document ISO 2919: “Sealed Radioactive Sources – Classification” [11], and (b) The test prescribed in para. 708 provided they are alternatively subjected to the Class 6 temperature test specified in the International Organization for Standardization document ISO 2919: “Sealed radioactive sources —Classification” [11]. |
| 42 | 805 | 6.4.22.1 | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) After 31 December 2000, each design that meets the requirements of para. 632 shall require multilateral approval. After 31 December 2003, each design that meets the requirements of paras 629–631 shall require unilateral approval by the competent authority of the country of origin of the design; (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. | 805. The approval of designs for packages containing 0.1 kg or more of uranium hexafluoride requires that: (a) Each design that meets the requirements of para. 632 shall require multilateral approval. (a bis) Each design that meets the requirement of paras 629-631 shall require unilateral approval by the competent authority of the country of origin of the design, unless multilateral approval is otherwise required by these regulations. (b) The application for approval shall include all information necessary to satisfy the competent authority that the design meets the requirements of para. 629, and a specification of the applicable quality assurance programme as required in para. 310; (c) The competent authority shall establish an approval certificate stating that the approved design meets the requirements of para. 629 and shall attribute to that design an identification mark. |
| 47 | 814bis | Suggest new text for 5.1.5.3.1 and 6.4.23 | The proposal involves new text, complete with heading, (currently missing from the regulations) to be incorporated between existing paras 814 and 815 | APPROVAL OF RADIONUCLIDE VALUES 814bis. Each calculation of radionuclide values that are not listed in Table I shall require multilateral approval. 814bis+1. An application for approval shall include: (a) The effective dose rate coefficient to the skin for external dose due to photons calculated at 1m; (b) the equivalent dose rate coefficient for external dose due to beta emission calculated at 1m; (c) the effective dose coefficient for the inhalation of a 1 µm AMAD aerosol of the radionuclide by workers, in the most restrictive lung absorption category; (d) the equivalent dose coefficient to the skin for skin contamination; (e) if the radionuclide is a noble gas, the effective dose coefficient or the equivalent dose coefficient to the skin for submersion dose; and (f) the calculated values for A1 and A2 in TBq, the activity concentration for exempt material in Bq/g; and the activity limits for exempt consignments in Bq. 814bis+2. The competent authority shall establish an approval stating that the calculated radionuclide values are approved. 827 …shipment, package design and unlisted radionuclide values. |
| 49 | 817 | 6.4.24.3 | 817. Packagings manufactured to a package design approved by the competent authority under the provisions of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used until 31 December 2003, subject to: the mandatory programme of quality assurance in accordance with the requirements of para. 310; the activity limits and material restrictions of Section IV; and, for a package containing fissile material and transported by air, the requirement of para. 680. After this date use may continue subject, additionally, to multilateral approval of package design. Changes in the design of the packaging or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would significantly affect safety shall require that this Edition of the Regulations be met in full. All packagings for which manufacture begins after 31 December 2006 shall meet this Edition of the Regulations in full. | 817. Packagings manufactured to a package design approved by the competent authority under the provisions of the 1985 or 1985 (As Amended 1990) Editions of these Regulations may continue to be used, subject to: multilateral approval of package design, the mandatory programme of quality assurance in accordance with the requirements of para. 310; the activity limits and material restrictions of Section IV; and, for a package containing fissile material and transported by air, the requirement of para. 680. Changes in the design of the packaging or in the nature or quantity of the authorized radioactive contents which, as determined by the competent authority, would significantly affect safety shall require that this Edition of the Regulations be met in full. All packagings for which manufacture begins after 31 December 2006 shall meet this Edition of the Regulations in full. |
| 52 | 819 | 6.4.23.15 | 819. The competent authority shall be informed of the serial number of each packaging manufactured to a design approved under paras 806, 809, 812, and 816–817. The competent authority should, consistent with para. 311, maintain a register of such serial numbers. | 819. The competent authority shall be informed of the serial number of each packaging manufactured to a design approved under paras 806, 809, 812, and 816–817 |
| 54 | 820 | 5.1.5.2.2 | 820. Multilateral approval shall be required for: (a) the shipment of Type B(M) packages not conforming with the requirements of para. 637 or designed to allow controlled intermittent venting; (b) the shipment of Type B(M) packages containing radioactive material with an activity greater than 3000 A1 or 3000 A2, as appropriate, or 1000 TBq, whichever is the lower; (c) the shipment of packages containing fissile materials if the sum of the criticality safety indexes of the packages exceeds 50; and (d) radiation protection programmes for shipments by special use vessels according to para. 575(a). | 820. Multilateral approval shall be required for: (a) the shipment of Type B(M) packages not conforming with the requirements of para. 637 or designed to allow controlled intermittent venting; (b) the shipment of Type B(M) packages containing radioactive material with an activity greater than 3000 A1 or 3000 A2, as appropriate, or 1000 TBq, whichever is the lower; (c) the shipment of packages containing fissile materials if the sum of the criticality safety indexes of the packages in a single freight container or in a single conveyance exceeds 50. Excluded from this requirement shall be shipments by seagoing vessels, if the sum of the criticality safety indexes does not exceed 50 for any hold, compartment or defined deck area and the distance of 6m between groups of packages or overpacks as required in table X is met; and (d) radiation protection programmes for shipments by special use vessels according to para. 575(a). |
| 55 | 824 | 1.1.2.4.2 | 824. Each consignment transported internationally under special arrangement shall require multilateral approval. | 824. Each consignment transported under special arrangement shall require multilateral approval. |
| 56 | 833 | 6.4.23.14 | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (n) (bis) For packages containing more than 0.1 kg of uranium hexafluoride a statement specifying those prescriptions of para 632 that apply, if any, and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. |
| 57 | 833 | 6.4.23.14 | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. | 833. Each approval certificate of the design of a package issued by a competent authority shall include the following information: (a) Type of certificate. (b) The competent authority identification mark. (c) The issue date and an expiry date. (d) Any restriction on the modes of transport, if appropriate. (e) List of applicable national and international regulations, including the edition of the IAEA Regulations for the Safe Transport of Radioactive Material under which the design is approved. (f) The following statement: “This certificate does not relieve the consignor from compliance with any requirement of the government of any country through or into which the package will be transported.” (g) References to certificates for alternative radioactive contents, other competent authority validation, or additional technical data or information, as deemed appropriate by the competent authority. (h) A statement authorizing shipment where shipment approval is required under para. 820, if deemed appropriate. (i) Identification of the packaging. (j) Description of the packaging by a reference to the drawings or specification of the design. If deemed appropriate by the competent authority, a reproducible illustration, not larger than 21 cm by 30 cm, showing the make-up of the package should also be provided, accompanied by a brief description of the packaging, including materials of manufacture, gross mass, general outside dimensions and appearance. (k) Specification of the design by reference to the drawings. (l) A specification of the authorized radioactive content, including any restrictions on the radioactive contents which might not be obvious from the nature of the packaging. This shall include the physical and chemical forms, the activities involved (including those of the various isotopes, if appropriate), amounts in grams (for fissile material), and whether special form radioactive material or low dispersible radioactive material, if applicable. (l) (bis) A description of the containment system (m) Additionally, for packages containing fissile material: (i) a detailed description of the authorized radioactive contents; (i bis) A description of the confinement system (ii) the value of the criticality safety index; (iii) reference to the documentation that demonstrates the criticality safety of the contents; (iv) any special features, on the basis of which the absence of water from certain void spaces has been assumed in the criticality assessment; (v) any allowance (based on para. 674(b)) for a change in neutron multiplication assumed in the criticality assessment as a result of actual irradiation experience; and (vi) the ambient temperature range for which the package design has been approved. (n) For Type B(M) packages, a statement specifying those prescriptions of paras 637, 653, 654 and 657–664 with which the package does not conform and any amplifying information which may be useful to other competent authorities. (o) A detailed listing of any supplementary operational controls required for preparation, loading, carriage, unloading and handling of the consignment, including any special stowage provisions for the safe dissipation of heat. (p) Reference to information provided by the applicant relating to the use of the packaging or specific actions to be taken prior to shipment. (q) A statement regarding the ambient conditions assumed for purposes of design if these are not in accordance with those specified in paras 653, 654 and 664, as applicable. (r) A specification of the applicable quality assurance programme as required in para. 310. (s) Any emergency arrangements deemed necessary by the competent authority. (t) If deemed appropriate by the competent authority, reference to the identity of the applicant. (u) Signature and identification of the certifying official. |
| 59 | Schedules | Schedules are not in UN | Schedule 5, Part 9 (b) For unpackaged LSA-I in a freight container or tank, or where an exclusive use consignment in a freight container is packaged LSA-I and no other UN Number commodities are present in the freight container, the UN Number "2912" shall be displayed on all four sides of the freight container or tank, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. Schedule 6, Part 9 (b) Where an exclusive use consignment in a freight container is non-fissile or fissile-excepted LSA-II and no other UN Number commodities are present in the freight container, "3321" shall be displayed on all four sides of the freight container, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. In the case of fissile material transported as LSA-II, "3324" shall be displayed on the placards. Schedule 7, Part 9 (b) Where an exclusive use consignment in a freight container is non-fissile or fissile-excepted LSA-III and no other UN Number commodities are present in the freight container, "3322" shall be displayed on all four sides of the freight container, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. In the case of fissile material transported as LSA-III, "3325" shall be displayed on the placards. Schedule 9, Part 9 (c) Where an exclusive use consignment in a freight container is non-fissile or fissile-excepted radioactive material in Type A packages and no other UN Number commodities are present in the freight container, "2915" shall be displayed on all four sides of the freight container, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. In the case of fissile material transported in Type A packages, "3327" shall be displayed on the placards. | Schedule 5, Part 9 (b) For unpackaged LSA-I in a freight container or tank, or where an exclusive use consignment in a freight container is packaged LSA-I and no other UN Number commodities are present in the freight container, the UN Number "2912" shall be displayed on all four sides of the freight container or tank, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. However if the packages contain non-fissile or fissile-excepted uranium hexafluoride, “2978” shall be displayed. Schedule 6, Part 9 (b) Where an exclusive use consignment in a freight container is non-fissile or fissile-excepted LSA-II and no other UN Number commodities are present in the freight container, "3321" shall be displayed on all four sides of the freight container, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. In the case of fissile material transported as LSA-II, "3324" shall be displayed on the placards. However if the packages contain non-fissile or fissile-excepted uranium hexafluoride, “2978” shall be displayed. If the packages contain uranium hexafluoride that is fissile material, “2977” shall be displayed. Schedule 7, Part 9 (b) Where an exclusive use consignment in a freight container is non-fissile or fissile-excepted LSA-III and no other UN Number commodities are present in the freight container, "3322" shall be displayed on all four sides of the freight container, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. In the case of fissile material transported as LSA-III, "3325" shall be displayed on the placards. However if the packages contain non-fissile or fissile-excepted uranium hexafluoride, “2978” shall be displayed. If the packages contain uranium hexafluoride that is fissile material, “2977” shall be displayed. Schedule 9, Part 9 (c) Where an exclusive use consignment in a freight container is non-fissile or fissile-excepted radioactive material in Type A packages and no other UN Number commodities are present in the freight container, "2915" shall be displayed on all four sides of the freight container, either in the lower half of the placards shown in Fig. 6, and against the white background, or on the placards shown in Fig. 7. In the case of fissile material transported in Type A packages, "3327" shall be displayed on the placards. However if the Type A packages contain non-fissile or fissile-excepted uranium hexafluoride, “2978” shall be displayed. If the packages contain uranium hexafluoride that is fissile material, “2977” shall be displayed. |
| 61 | 302, 306, 307, 562 | 1.1.2.2.3, 7.1.7.1.1, 7.1.7.1.3 | NOTE. ONLY THE PARAGRAPHS WHICH THE REVIEW PANEL RECOMMENDS TO BE REVISED ARE LISTED HERE 302. In transport, protection and safety shall be optimized in order that the magnitude of individual doses, the number of persons exposed, and the likelihood of incurring exposure shall be kept as low as reasonably achievable, economic and social factors being taken into account, and doses to persons shall be below the relevant dose limits. A structured and systematic approach shall be adopted and shall include consideration of the interfaces between transport and other activities. 306. Radioactive material shall be segregated sufficiently from workers and from members of the public. The following values for dose shall be used for the purpose of calculating segregation distances or radiation levels: (a) for workers in regularly occupied working areas a dose of 5 mSv in a year; (b) for members of the public, in areas where the public has regular access, a dose of 1 mSv in a year to the critical group, taking account of exposures expected to be delivered by all other relevant sources and practices under control. 307. Radioactive material shall be sufficiently segregated from undeveloped photographic film. The basis for determining segregation distances for this purpose shall be that the radiation exposure of undeveloped photographic film due to the transport of radioactive material be limited to 0.1 mSv per consignment of such film. 562. Packages, overpacks and freight containers containing radioactive material shall be segregated during transport and during storage in transit: (a) from places occupied by persons and from undeveloped photographic film, for radiation exposure control purposes, in accordance with paras 306 and 307, and (b) from other dangerous goods in accordance with para. 506. | 302. In transport, doses to persons shall be below the relevant dose limits. Protection and safety shall be optimized in order that the magnitude of individual doses, the number of persons exposed, and the likelihood of incurring exposure shall be kept as low as reasonably achievable, economic and social factors being taken into account, within the restriction that the doses to individuals be subject to dose constraints. A structured and systematic approach shall be adopted and shall include consideration of the interfaces between transport and other activities. 306. deleted 307. deleted 562. Packages, overpacks and freight containers containing radioactive material and unpackaged radioactive material shall be segregated during transport and during storage in transit: (a) from workers in regularly occupied working areas by distances calculated using a dose criterion of 5 mSv in a year and conservative model parameters; (b) from members of the critical group of the public, in areas where the public has regular access, by distances calculated using a dose criterion of 1 mSv in a year and conservative model parameters; (c) from undeveloped photographic film by distances calculated using a radiation exposure criterion for undeveloped photographic film due to the transport of radioactive material of 0.1 mSv per consignment of such film; and (d) from other dangerous goods in accordance with para. 506. |
| 62 | 533, 533bis, 549 | 2.7.8.4, 5.4.1.5.7.1 other? | 533. Packages and overpacks shall be assigned to either category I-WHITE, II-YELLOW or III-YELLOW in accordance with the conditions specified in Table VII and with the following requirements: (a) For a package or overpack, both the transport index and the surface radiation level conditions shall be taken into account in determining which is the appropriate category. Where the transport index satisfies the condition for one category but the surface radiation level satisfies the condition for a different category, the package or overpack shall be assigned to the higher category. For this purpose, category I-WHITE shall be regarded as the lowest category. (b) The transport index shall be determined following the procedures specified in paras 526 and 527. (c) If the surface radiation level is greater than 2 mSv/h, the package or overpack shall be transported under exclusive use and under the provisions of paras 572(a), 574 or 578, as appropriate. (d) A package transported under a special arrangement shall be assigned to category III-YELLOW. (e) An overpack which contains packages transported under special arrangement shall be assigned to category III-YELLOW. 549. The consignor shall include in the transport documents with each consignment the following information, as applicable in the order given: (a) The proper shipping name, as specified in Table VIII; (b) The United Nations Class number “7”; (c) The United Nations number assigned to the material as specified in Table VIII, preceded by the letters “UN”; (d) The name or symbol of each radionuclide or, for mixtures of radionuclides, an appropriate general description or a list of the most restrictive nuclides; (e) A description of the physical and chemical form of the material, or a notation that the material is special form radioactive material or low dispersible radioactive material. A generic chemical description is acceptable for chemical form; (f) The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with an appropriate SI prefix (see Annex II). For fissile material, the mass of fissile material in units of grams (g), or appropriate multiples thereof, may be used in place of activity; (g) The category of the package, i.e. I-WHITE, II-YELLOW, III-YELLOW; (h) The transport index (categories II-YELLOW and III-YELLOW only); (i) For consignments including fissile material other than consignments excepted under para. 672, the criticality safety index; (j) The identification mark for each competent authority approval certificate (special form radioactive material, low dispersible radioactive material, special arrangement, package design, or shipment) applicable to the consignment; (k) For consignments of more than one package, the information contained in para. 549(a) to (j) shall be given for each package. For packages in an overpack, freight container, or conveyance, a detailed statement of the contents of each package within the overpack, freight container, or conveyance and, where appropriate, of each overpack, freight container, or conveyance shall be included. If packages are to be removed from the overpack, freight container, or conveyance at a point of intermediate unloading, appropriate transport documents shall be made available; (l) Where a consignment is required to be shipped under exclusive use, the statement “EXCLUSIVE USE SHIPMENT”; and (m) For LSA-II, LSA-III, SCO-I and SCO-II, the total activity of the consignment as a multiple of A2. | 533. Packages and overpacks shall be assigned to either category I-WHITE, II-YELLOW or III-YELLOW in accordance with the conditions specified in Table VII and with the following requirements: (a) For a package or overpack, both the transport index and the surface radiation level conditions shall be taken into account in determining which is the appropriate category. Where the transport index satisfies the condition for one category but the surface radiation level satisfies the condition for a different category, the package or overpack shall be assigned to the higher category. For this purpose, category I-WHITE shall be regarded as the lowest category. (b) The transport index shall be determined following the procedures specified in paras 526 and 527. (c) If the surface radiation level is greater than 2 mSv/h, the package or overpack shall be transported under exclusive use and under the provisions of paras 572(a), 574 or 578, as appropriate. (d) A package transported under a special arrangement shall be assigned to category III-YELLOW except under the provisions of para 533 bis. (e) An overpack which contains packages transported under special arrangement shall be assigned to category III-YELLOW except under the provisions of para 533 bis. 533 bis For each package the UN number and proper shipping name shall be determined (see Table VIII). In all cases of international transport of packages requiring competent authority design or shipment approval, for which different approval types apply in the different countries concerned by the shipment, the UN number, proper shipping name, labelling and marking shall be in accordance with the certificate of the country of origin of design. 549. The consignor shall include in the transport documents with each consignment the following information, as applicable in the order given: (a) The proper shipping name, as specified in accordance with the provisions of para 533 bis; (b) The United Nations Class number “7”; (c) The United Nations number assigned to the material as specified in accordance with the provisions of para 533 bis, preceded by the letters “UN”; (d) The name or symbol of each radionuclide or, for mixtures of radionuclides, an appropriate general description or a list of the most restrictive nuclides; (e) A description of the physical and chemical form of the material, or a notation that the material is special form radioactive material or low dispersible radioactive material. A generic chemical description is acceptable for chemical form; (f) The maximum activity of the radioactive contents during transport expressed in units of becquerels (Bq) with an appropriate SI prefix (see Annex II). For fissile material, the mass of fissile material in units of grams (g), or appropriate multiples thereof, may be used in place of activity; (g) The category of the package, i.e. I-WHITE, II-YELLOW, III-YELLOW; (h) The transport index (categories II-YELLOW and III-YELLOW only); (i) For consignments including fissile material other than consignments excepted under para. 672, the criticality safety index; (j) The identification mark for each competent authority approval certificate (special form radioactive material, low dispersible radioactive material, special arrangement, package design, or shipment) applicable to the consignment; (k) For consignments of more than one package, the information contained in para. 549(a) to (j) shall be given for each package. For packages in an overpack, freight container, or conveyance, a detailed statement of the contents of each package within the overpack, freight container, or conveyance and, where appropriate, of each overpack, freight container, or conveyance shall be included. If packages are to be removed from the overpack, freight container, or conveyance at a point of intermediate unloading, appropriate transport documents shall be made available; (l) Where a consignment is required to be shipped under exclusive use, the statement “EXCLUSIVE USE SHIPMENT”; and (m) For LSA-II, LSA-III, SCO-I and SCO-II, the total activity of the consignment as a multiple of A2. |

Appendix 1  Change # 5, Changes to TABLE XII (UN Table 6.4.11.2)

EXISTING TABLE XII

table XII.  Consignment mass limits for exceptions from the requirements for packages containing fissile material

Fissile material mass (g) mixed 	Fissile material mass (g) mixed

Fissile material	with substances having an	with substances having an

average hydrogen density less	average hydrogen density

than or equal to water	greater than water

Uranium-235 (X)	400	290

Other fissile material (Y)	250	180

RECOMMENDED TABLE XII (UN Table 6.4.11.2)

table XII.  Consignment mass limits for exceptions from the requirements for packages containing fissile MATERIAL

Fissile nuclide mass (g) mixed 	Fissile nuclide mass (g) mixed

Fissile nuclide	with substances having an	with substances having an

average hydrogen density less	average hydrogen density

than or equal to water	greater than water

Uranium-235 (X)	400	290

Other fissile nuclides (Y)	250	180