| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL TRANS/WP.15/AC.1/2003/53 12 June 2003 ENGLISH Original: FRENCH |

###### economic commission for europe

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Safety Committee and the
Working Party on the Transport of Dangerous Goods
(Geneva, 1-10 September 2003)

# PARAGRAPH 6.8.3.4.13

Transmitted by the Government of Switzerland*

The secretariat has received from the Central Office for International Carriage by Rail (OCTI) the proposal reproduced below.

# SUMMARY

Paragraph 6.8.3.4.13 defines the periodic inspections for battery wagons/vehicles and MEGCs.

The second sentence reads:  “The elements and the piping shall be tested at the periodicity defined in packing instruction P200 of 4.1.4.1 and in accordance with the requirements of 6.2.1.5.”

*  Circulated by the Central Office for International Carriage by Rail (OCTI) under the symbol OCTI/RID/GT-III/2003/53.

GE.03-22017  (E)    250603    070703

Proposal

The reference to 6.2.1.5 (“Initial inspection and test”) should be replaced by a reference to 6.2.1.6 (“Periodic inspection and test”).

Justification

Paragraph 6.8.3.4.13 applies to periodic tests and not to initial tests.  The reference seems incorrect.  Packing instruction P200 in 4.1.4.1 moreover refers to the “periodic test” of 6.2.1.6.

-----