|  | Informal Document No. 19 (53rd GRRF, 3-6 February 2003) Agenda Item 4 |
| --- | --- |
|  | Original: russian / english |

Proposal for Revision of the Document TRANS/WP.29/2002/27

With Regard to the Regulations No. 111

## Transmitted by the Russian Federation

Within October – December 2002, the experts of the Russian Federation at GRRF considered comments of the experts of Netherlands prepared in response to the document TRANS/WP.29/2002/27.

The major part of the comments was taken into account. Therefore it is proposed to modify the document TRANS WP/29/2002/27.

The revised version of the mentioned document is presented below. The changes proposed by the expert of Netherlands are typed in Italic.

- The following paragraphs should be added.

2.7. “Roll angle” means the roll angle of the sprung part of a vehicle with respect to the road surface or the tilt table platform.

2.7.1.  Roll angle is represented by the symbol  «».

2.8. “Rollover threshold” means the instant when all the wheels of one side of a vehicle have lost contact with the road or the tilt table surface.

2.8.1. The inclination angle of the tilt table surface is represented by the symbol «».

- The following insertions should be added:

- Into the paragraph 5.3.1.1 insert «=» before «23(».

- In the paragraph 5.3.1.1 after wording «in both tilt direction» insert wording «and roll angle  at those conditions shall not exceed  = 7(».

- Into the paragraph 5.3.1.2 add «roll angle, , at those conditions shall not exceed».

Annex 1

- The following insertions should be added.

p. 3.2. tank: make, model, effective volume ….

p. 8.1. Center of gravity height of a vehicle in running order …

p. 11.5. ESP device engaged … yes/no/not applicable.

p. 6.1.  Instead of parameter “mass of laden tank” insert parameter “mass of vehicle in running order” …

Annex 3

The text of the paragraph «Test procedure» is referred to p. 7.1.

The following p. 7.2 is inserted:

p. 7.2. If, during testing of a vehicle, which tank in case of full load (with respect to its mass) is not filled completely (with respect to its volume), the tilt table inclination angleis less than value of  or/and roll angle (when ) is more than value of , the test shall be repeated with the fully filled (with respect to its volume) tank.

The values of the recorded at the test tilt table inclination angle  and roll angle  (when ) shall be corrected by using the following formulas:

The value of  shall be higher, and the value of  shall be lower the corresponding critical values ().

In the formulas:

|  |  | vehicle weight in case of loading by normal fluid; |
| --- | --- | --- |
|  |  | vehicle weight in case of loading by water. |
| , |  | height of the vehicle center-of-gravity in case of loading by water and normal fluid, respectively; |
|  |  | theoretical wheel track at the vehicle cross section at the center-of-gravity point; |
|  |  | effective tank volume; |
|  |  | vertical stiffness of suspension at the center of gravity point; |
|  |  | mass of payload; |
|  |  | density of normal fluid; |
|  |  | density of water; |
|  |  | height of the center-of-gravity of the vehicle in running order. |

Annex 4

The p. 7.2 shall be partly modified. The revised text:

7.2. In case of semi-trailers separated from tractors, kingpin effects are calculated by using the following formula:

Kingpin trace width:

The kingpin roll stiffness, which is the roll stiffness of the tractor at the longitudinal position of the fifth wheel/kingpin, will be calculated by using a reference load dependent roll stiffness factor of 4 [m/rad]:

- Insert new paragraph 7.5.5 to read:

7.5.5. The vehicle roll angle when tilted on the tilt table in both directions with inclination angle  = 23(, calculated by using the following formula:

shall be less than  ( ( ).