Distr.
	GÉNÉRALE

ST/SG/AC.10/C.3/2004/12
	31 mars 2004

FRANÇAIS
	Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT DES 
MARCHANDISES DANGEREUSES ET DU SYSTÈME 
GÉNÉRAL HARMONISÉ DE CLASSIFICATION ET 
D’ÉTIQUETAGE DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport des marchandises dangereuses

Vingt-cinquième session, 5-14 juillet 2004
Point 6 de l’ordre du jour provisoire

INSCRIPTION, CLASSEMENT ET EMBALLAGE

Proposition d’ajouter de nouvelles rubriques ONU pour l’acide formique
(no ONU 1779) et l’acide propionique (no ONU 1848)

Communication de l’expert de l’Allemagne

Introduction

1.	Lors de la session de mars 2003 du Sous-Comité des marchandises dangereuses, des cargaisons solides et des conteneurs (Sous-Comité DSC) de l’Organisation maritime internationale (OMI), l’Allemagne a attiré l’attention sur un problème se posant à propos d’une matière très courante, l’acide propionique (no ONU 1848).

2.	Pour cette matière, la liste des marchandises dangereuses du Code IMDG donne dans sa colonne 17 les informations et observations suivantes: Liquide incolore inflammable à odeur piquante. Miscible à l’eau. Corrosif pour le plomb et la plupart des autres métaux. Cause des brûlures cutanées. Les vapeurs ont des effets irritants sur les muqueuses.

3.	Bien que cette matière soit décrite comme étant un liquide inflammable, aucun risque subsidiaire de la classe 3 n’est mentionné à la colonne 4 de la liste du Code IMDG.

4.	L’expert de l’Allemagne a été prié de résoudre ce problème en proposant un nouveau numéro ONU au Sous-Comité d’experts de l’ONU.

5.	Au cours des travaux concernant ce document, les industriels ont attiré l’attention des experts allemands sur une matière qui présente des propriétés semblables à celles de l’acide propionique. Il s’agit de l’acide formique (no ONU 1779).

6.	Les experts allemands ont donc réuni toutes les données nécessaires pour pouvoir classer ces deux matières. Ces données sont présentées dans les fiches de renseignements figurant dans les annexes 1 et 2, et des informations supplémentaires dans l’annexe 3.

7.	Pour tenir compte des données fournies par les fiches de renseignements et pour classer l’acide formique (no ONU 1779) et l’acide propionique (no ONU 1848) comme il convient, l’Allemagne propose d’apporter les amendements suivants à la liste des marchandises dangereuses du Règlement type de l’ONU.

Proposition

8.	No ONU 1779 ACIDE FORMIQUE
	Colonne (2), modifier le nom et la description comme suit:
	ACIDE FORMIQUE contenant plus de 85 % (masse) d’acide

9.	No ONU 1779 ACIDE FORMIQUE
	Colonne (4), ajouter la mention «3»

10.	ACIDE FORMIQUE
	Ajouter une nouvelle rubrique ainsi conçue:

| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| xxxx | ACIDE FORMIQUE contenant au moins 10 % et au plus 85 % (masse) d’acide | 8 |  | II |  | 1 L | P001 IBC02 |  | T7 | TP2 |
|  | ACIDE FORMIQUE contenant au moins 5 %, mais moins de 10 % (masse) d’acide | 8 |  | III |  | 5 L | P001 IBC03 LP01 |  | T7 | TP2 |

11.	No ONU 1848 ACIDE PROPIONIQUE

Colonne (2), modifier le nom et la description comme suit:
	ACIDE PROPIONIQUE contenant au moins 10 %, mais moins de 90 % (masse) d’acide

12.	Acide propionique

Ajouter dans la liste une nouvelle rubrique ainsi conçue:

| (1) | (2) | (3) | (4) | (5) | (6) | (7) | (8) | (9) | (10) | (11) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| yyyy | ACIDE PROPIONIQUE contenant au moins 90 % (masse) d’acide | 8 | 3 | II |  | 1 L | P001 IBC02 |  | T7 | TP2 |

ANNEXES (ENGLISH ONLY)

Annex 1

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	 Germany								Date  04-03-29

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions – if necessary state "not known" or "not applicable" – if data is not available in the form requested, provide what is available with details. Delete inappropriate words.

# Section 1.	SUBSTANCES IDENTITY

1.1	Chemical name	Formic acid

1.2	Chemical formula	CH2O2

1.3	Other names/synonyms	none

1.4.1	UN Number    1779		1.4.2	CAS number	64-18-6

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2)	Formic acid

1.5.2	class/division	   8	subsidiary risk(s)   3 for C > 85%

packing group	   II

class/division	   8 	subsidiary risk(s) no for 10%<C≤ 85%

packing group	   II

class/division	   8 	subsidiary risk(s)  no for 5%<C< 10%

packing group	   III

1.5.3	proposed special provisions, if any		none

1.5.4	proposed packing instruction(s)		PG II = P001/IBC02

PG III = P001/IBC03/LP01

# Section 2.	PHYSICAL PROPERTIES

2.1	Melting point or range	    8 °C

2.2	Boiling point or range	101 °C

2.3	Relative density at:

2.3.1	15 °C	not known

2.3.2	20 °C	1.220 g/cm3

2.3.3	50 °C	not known

2.4	Vapour pressure at:

2.4.1	20°C	4.2 kPa

50 °C	17.0 kPa

2.4.2	65 °C	not known

2.5	Viscosity at 20 °C		1.8 mPa*s

2.6	Solubility in water at 20 °C		complete	g/100 ml

2.7	Physical state at 20 °C (2.2.1.1)	solid / liquid / gas

  - Appearance at normal carriage temperatures, including colour and odour

colourless liquid, pungent odour

2.9	Other relevant physical properties	not known

# Section 3.	FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3)	 	see attachment

3.1.2	Is combustion sustained? (2.3.1.2)	yes / no

3.2	Autoignition temperature 		480 °C

3.3	Flammability range (LEL/UEL) 	12 / 38 % estimated

3.4	Is the substance a flammable solid? (2.4.2)	yes / no

3.4.1	If yes, give details ...

# Section 4.	CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity?	yes / no

If yes, state

4.1.1	Inhibitor/stabilizer used ...

4.1.2	Alternative method ...

4.1.3	Time effective at 55 °C ...

    - Conditions rendering it ineffective ...

4.2	Is the substance an explosive according to paragraph 2.1.1? (2.1)	yes / no

4.2.1	If yes, give details ...

4.3	Is the substance a desensitized explosive? (2.4.2.4)			yes / no

4.3.1	If yes, give details ...

4.4	Is the substance a self-reactive substance? (2.4.1)	yes / no

If yes, state

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.4.2.3.4)	yes / no

4.4.2	proposed control temperature for a 50 kg package ... °C

4.4.3	proposed emergency temperature for a 50 kg package ... °C

4.5	Is the substance pyrophoric? (2.4.3)	yes / no

4.5.1	If yes, give details ...

4.6	Is the substance liable to self-heating? (2.4.3)	yes / no

4.6.1	If yes, give details ...

4.7	Is the substance an organic peroxide (2.5.1)	yes / no

If yes state

4.7.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.5.3.4.1)		yes / no

4.7.2	proposed control temperature for a 50 kg package ... °C

4.7.3	proposed emergency temperature for a 50 kg package ... °C

4.8	Does the substance in contact with water emit flammable

gases (2.4.4)					yes / no

4.8.1	If yes, give details ...

4.9	Does the substance have oxidizing properties (2.5.1)		yes / no

4.9.1	If yes, give details ...

4.10	Corrosivity (2.8) to:

4.10.1	mild steel ...	C>5%	more than 6.25 mm/year at 55 °C

4.10.2	aluminium ...	C>5%	more than 6.25 mm/year at 55 °C

4.10.3	other packing materials

(specify) no		... mm/year at ...

...		... mm/year at ...

  - Other relevant chemical properties 	...not known...

# Section 5.	HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1)         730      	mg/kg	Animal species ...rat..

5.2	LD 50, dermal (2.6.2.1.2) .....x..	mg/kg	Animal species ...

x...not published (Patty’s Ind. Hyg. Toxicol. 4, 1994)

5.3	LC 50, inhalation (2.6.2.1.3) ...>14.8....	mg/litre	Exposure time .1.. hours

or  .......	ml/m3	Animal species ...

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3)	 41.7. ml/m3

5.5	Skin exposure (2.8) results:   corrosive

Exposure time ... x x				hours/minutes

x x...not published (Patty’s Ind. Hyg. Toxicol. 3, 1981)

Animal species ... rabbit

5.6	Other data ...

5.7	Human experience ...medical reports of acute exposures of workers show severe skin burns (C>90%) and mild to moderate skin burns (10%<C≤ 90%).

# Section 6.	SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents):

suitable are dry chemical powder, carbon dioxide, water spray and appropriate foam

    - Spillage:

Absorb on sand or vermiculite and place in closed containers for disposal; ventilate area and wash spill site after material pickup is complete

6.2	Is it proposed to transport the substance in:

6.2.1	Intermediate Bulk Containers (6.5)		yes / no

6.2.2	Portable tanks (6.7)			yes / no

If yes, give details in Sections 7. and/or 8.

# Section 7.  INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.1)

  - Proposed type(s)

PG II = IBC02

PG III = IBC03

# Section 8.	MULTIMODAL TANK TRANSPORT(only complete if yes in 6.2.2)

  - Description of proposed tank (including IMO tank type if known)

For 8(3), II  and  8, II and 8, III

T7

8.2.	Minimum test pressure 	4.0 bar

8.3	Minimum shell thickness  		see 6.7.2.4.2

8.4	Details of bottom openings, if any 	see 6.7.2.6.3

8.5	Pressure relief arrangements 		normal

8.6	Degree of filling 		TP2

8.7	Unsuitable construction materials 	no

* * * * *

Annex 2

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS
FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	 Germany								Date  04-03-25

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions – if necessary state "not known" or "not applicable" – if data is not available in the form requested, provide what is available with details. Delete inappropriate words.

# Section 1.	SUBSTANCES IDENTITY

1.1	Chemical name	Propionic acid

1.2	Chemical formula	C3H6O2

1.3	Other names/synonyms	Propanoic acid

1.4.1	UN Number	1848

1.4.2	CAS number	79-09-4

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2)	Propionic acid

1.5.2	class/division	   8	subsidiary risk(s)   3 for C ( 90%

packing group	   II

class/division	   8 	subsidiary risk(s) no for 10%<C< 90%

packing group	   III

1.5.3	proposed special provisions, if any		none

1.5.4	proposed packing instruction(s)		PG II = P001/IBC02

PG III = P001/IBC03/LP01

Section 2.	PHYSICAL PROPERTIES

2.1	Melting/freezing point or range    -20 °C

2.2	Boiling point or range	 141 °C

2.3	Relative density at:

2.3.1	15 °C	not known

2.3.2	20 °C	0.992 g/cm3

2.3.3	50 °C	not known

2.4	Vapour pressure at:

2.4.1	20 °C	0.5 kPa

50 °C	not known

2.4.2	65 °C	not known

2.5	Viscosity at 20 °C			10    mPas

2.6	Solubility in water at 20 °C			complete	g/100 ml

2.7	Physical state at 20 °C (2.2.1.1)		solid / liquid / gas

  - Appearance at normal carriage temperatures, including colour and odour

colourless liquid, pungent odour

2.9	Other relevant physical properties		not known

# Section 3.	FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3)	 		see attachment

3.1.2	Is combustion sustained? (2.3.1.2)	yes / no

3.2	Autoignition temperature 			485 °C

3.3	Flammability range (LEL/UEL) 		2.0 / 12.0 % estimated

3.4	Is the substance a flammable solid? (2.4.2)		yes / no

3.4.1	If yes, give details ...

Section 4.	CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity?	yes / no

If yes, state

4.1.1	Inhibitor/stabilizer used ...

4.1.2	Alternative method ...

4.1.3	Time effective at 55 °C ...

4.1.4	Conditions rendering it ineffective ...

4.2	Is the substance an explosive according to paragraph 2.1.1? (2.1)	yes / no

4.2.1	If yes, give details ...

4.3	Is the substance a desensitized explosive? (2.4.2.4)			yes / no

4.3.1	If yes, give details ...

4.4	Is the substance a self-reactive substance? (2.4.1)			yes / no

If yes, state

4.4.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.4.2.3.4)			yes / no

4.4.2	proposed control temperature for a 50 kg package ... °C

4.4.3	proposed emergency temperature for a 50 kg package ... °C

4.5	Is the substance pyrophoric? (2.4.3)				yes / no

4.5.1	If yes, give details ...

4.6	Is the substance liable to self-heating? (2.4.3)				yes / no

4.6.1	If yes, give details ...

4.7	Is the substance an organic peroxide (2.5.1)				yes / no

If yes state

4.7.1	exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ... °C

Is the temperature control required? (2.5.3.4.1)		yes / no

4.7.2	proposed control temperature for a 50 kg package ... °C

4.7.3	proposed emergency temperature for a 50 kg package ... °C

4.8	Does the substance in contact with water emit flammable gases (2.4.4)	yes / no

4.8.1	If yes, give details ...

4.9	Does the substance have oxidizing properties (2.5.1)		yes / no

4.9.1	If yes, give details ...

4.10	Corrosivity (2.8) to:

4.10.1	mild steel ...	C>10%	more than 6.25 mm/year at 55 °C

4.10.2	aluminium ...	C>10%	more than 6.25 mm/year at 55 °C

4.10.3	other packing materials

(specify) no		... mm/year at ...

…	... mm/year at ...

  - Other relevant chemical properties 	... not known...

# Section 5.	HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1) 	3500-4200   	mg/kg	Animal species 	rat..

5.2	LD 50, dermal (2.6.2.1.2) 	 500....	mg/kg	Animal species 	rabbit

5.3	LC 50, inhalation (2.6.2.1.3) >19.7....	mg/litre	Exposure time 	1. hours

or  .......	ml/m3	Animal species 	rat..

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3) 4.96 ml/m3

5.5	Skin exposure (2.8) results: corrosive

Exposure time ...1 + 5 + 15			hours/minutes

Animal species ... rabbit

5.6	Other data ...

5.7	Human experience ... medical reports of acute exposures of workers show moderate skin burns (C>25%).

# Section 6.	SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents):

suitable are dry chemical powder, carbon dioxide, water spray and appropriate foam

    - Spillage:

Absorb on sand or vermiculite and place in closed containers for disposal; ventilate area and wash spill site after material pickup is complete

6.2	Is it proposed to transport the substance in:

6.2.1	Intermediate Bulk Containers (6.5)		yes / no

6.2.2	Portable tanks (6.7)			yes / no

If yes, give details in Sections 7. and/or 8.

Section 7.		INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes 
in 6.2.1)

7.1	Proposed type(s)

PG II = IBC02

PG III = IBC03

Section 8.	MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.2)

  - Description of proposed tank (including IMO tank type if known)

for 8(3), II	for 8, III

T7	T4

8.2.	Minimum test pressure 		4.0 bar 		2.65 bar

8.3	Minimum shell thickness  		see 6.7.2.4.2 	see 6.7.2.4.2

8.4	Details of bottom openings, if any 	see 6.7.2.6.3 	see 6.7.2.6.3

8.5	Pressure relief arrangements 		normal 	normal

8.6	Degree of filling 		TP2 	TP1

8.7	Unsuitable construction materials 	no	no

* * * * *

Annex 3

UN 1779 Formic acid + UN 1848 Propionic acid

| Flashpoint as a function of the concentration |
| --- |
| Concentration % | Flashpoint of formic acid (UN 1779) | Flashpoint of propionic acid (UN 1848) |
| 100 | 48 | 50 |
| 95 | 51 | 54 |
| 90 | 57 | 61 |
| 85 | 65 | 72 |
| 80 | 82 | 91 |

-----

# Text boxes

NATIONS UNIES

Secrétariat

ST