#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2004/20

2 April 2004

# ORIGINAL: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-fifth session, 5-14 July 2004

# Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Addition of toxic subsidiary risk to chromium trioxide, anhydrous

Transmitted by the expert from United States of America

Background

Chromium trioxide, anhydrous (UN 1463) is used in chromates, wood treating, inks, paints, rubber pigments, catalysts, plating and anodizing applications, and as an oxidizing agent. It is listed in the Model Regulations as a Division 5.1, PG II oxidizer with a corrosive subsidiary risk.  The attached UN data sheet indicates that the substance meets criteria for Division 6.1, PG II dermal toxicity (LD50: 57 mg/kg (rabbits)) and Division 6.1, PG III oral toxicity (LD50: 52 mg/kg (rats)).  The values for acute dermal toxicity and acute oral toxicity were determined by testing consistent with the provisions of 2.6.2.1 of  the Model Regulations.  It is proposed that the entry be amended to include a 6.1 subsidiary risk.

Proposal

Amend the entry in the dangerous goods list for UN 1463 by adding "6.1" to column (4) so that the column would read "6.1, 8".

### Annex

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by . . .JITU GHANDI

TOM MAHAFFEY. . . . . . . . . . . . .                       Date  MARCH 6, 2002

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1.     SUBSTANCE IDENTITY

1.1	Chemical name CHROMIUM TRIOXIDE, ANHYDROUS

1.2	Chemical formula CrO3 (CHROMIUM OXIDE)

1.3	Other names/synonyms CHROMIC ACID, CHROMIUM (VI) OXIDE, CHROMIC ANHYDRIDE

1.4.1	UN number            1463

1.4.2	CAS number          1333-82-0

1.5	Proposed classification for the Recommendations

1.5.1	proper shipping name (3.1.2*)  CHROMIUM TRIOXIDE, ANHYDROUS

1.5.2	class/division  	5.1                       	subsidiary risk(s)  (8) (6.1)

packing group 	II

1.5.3	proposed special provisions, if any

1.5.4	proposed packing instruction(s)

Section 2.     PHYSICAL PROPERTIES

2.1	Melting point or range	197   °C

2.2	Boiling point or range	N/A  °C

2.3	Relative density at :

2.3.1	15 °C	85-90 LBS/CU FT (TAPPED)

2.3.2	20 °C

2.3.3	50 °C

2.4	Vapour pressure at :

2.4.1	50 °C	NOT APPLICABLE                                                                                         kPa

2.4.2	65 °C		 kPa

2.5		Viscosity at 20°C**                    N/A               m2/s

2.6		Solubility in water at 20 °C           63 g/100 ml

2.7		Physical state at 20 °C (2.2.1.1*)	solid/liquid/gas**

  - Appearance at normal transport temperatures, including colour and odour .SOLID DARK RED

FLAKES OR POWDER, NO ODOR

2.9	Other relevant physical properties………………………………………………………………….

Section 3.     FLAMMABILITY

3.1		Flammable vapour

3.1.1	Flash point (2.3.3*)      N/A   °C oc/cc

3.1.2	Is combustion sustained? (2.3.1.3)    yes/no

3.2		Autoignition temperature    N/A     °C

3.3		Flammability range (LEL/UEL)    N/A    %

3.4		Is the substance a flammable solid? (2.4.2*)

3.4.1	If yes, give details   NOT APPLICABLE

Section 4.     CHEMICAL PROPERTIES

4.1		Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?				yes/no

If yes, state

4.1.1	Inhibitor/stabilizer used…………………………………………………............................

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.1*)	yes/no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.4*)	yes/no

    - If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.1*) 	yes/no

If yes, state

4.4.1	exit box of flow chart	………………………………………………..

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is the temperature control required? (2.4.2.3.4*)	yes/no

4.4.2	proposed control temperature for a 50 kg package	°C

4.4.3	proposed emergency temperature for a 50 kg package	°C

4.5	Is the substance pyrophoric? (2.4.3*)	yes/no

4.5.1	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.3*)	yes/no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.1*)	yes/no

If yes state

4.7.1	exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package?	°C

Is temperature control required? (2.5.3.4.1*)	yes/no

4.7.2	proposed control temperature for a 50 kg package	°C

4.7.3	proposed emergency temperature for a 50 kg package	°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.4*)	yes/no

4.8.1	If yes give details

4.9	Does the substance have oxidizing properties (2.5.1*)	yes/no

4.9.1	If yes, give details  THIS PRODUCT IS A STRONG OXIDIZING AGENT

EVEN IN SOLUTION

4.10	Corrosivity (2.8*) to:           METALS

4.10.1	mild steel	mm/year   at 	°C

4.10.2	aluminium	mm/year   at	°C

4.10.3	other packaging materials

(specify)				mm/year   at

mm/year   at

4.11	Other relevant chemical properties  PRODUCT IS HYGROSCOPIC

Section 5.     HARMFUL BIOLOGICAL EFFECTS

5.1	LD 50, oral (2.6.2.1.1*) 	52            mg/kg	Animal species   RAT

5.2	LD 50, dermal (2.6.2.1.2*)	57            mg/kg	Animal species   RABBIT

5.3	LC 50, inhalation (2.6.2.1.3*)		mg/litre	Exposure time	 hours

or	ml/m3	Animal species

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.3*)		ml/m3

- 5.5	Skin exposure (2.8*) results	Exposure time 	 hours/minutes

Animal species

5.6	Other data

5.7	Human experience

Section 6.     SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

USE EXTINGUISHING AGENT APPROPRIATE FOR SURROUNDING FIRE

WEAR SELF-CONTAINED BREATH APPARATUS

    - Spillage IF SOLID, PICK UP FOR PROPAL DISPOSAL. IF LIQUID, NEUTRALIZE WITH WEAK BASE AND DISPOSE OF IN ACCORDANCE WITH APPLICABLE REGULATIONS

6.2	Is it proposed to transport the substance in:

6.2.1	Intermediate Bulk Containers (6.5*)?		yes/no

6.2.2	Portable tanks (6.7*)?		yes/no

If yes, give details in Sections 7 and/or 8.

Section 7.     INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.1*)

7.1	Proposed type(s) 		NOT APPLICABLE

Section 8.     MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.2)

8.1	Description of proposed tank (including IMO tank type if known)

8.2	Minimum test pressure

8.3	Minimum shell thickness

8.4	Details of bottom openings, if any

8.5	Pressure relief arrangements

8.6	Degree of filling

8.7	Unsuitable construction materials

______________

# Footnotes

*	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

*		This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

** 	See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

* 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

* 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

# Text boxes

STSTE

Secretariat